## Slide 1: Quantum sensors activities in IN2P3-France
I. Laktineh

## Slide 2
IN2P3
Institut National de La Physique des Particules et de la Physique Nucléaire
IN2P3 is one of the ten French CNRS institutes. It focuses on probing the two infinites from particles to cosmos
Although IN2P3 contributes to many activities that are directly or indirectly related to Quantum Sensors, there is no axis identified as such.
In 2024, I was appointed as a “délégué scientifique” for innovative detectors and I was asked to advise the IN2P3 direction on the Quantum Technologies in general and on Quantum Sensors in particular.
So in the next slides I will show the different activities I identified, up to now, that could either be considered as quantum activities oras important elements that can/may contribute to quantum technologies.

## Slide 3
Squeezed states for Gravitational waves
Several French labs are involved in Virgo and preparing the future (ET): IJCLAB, LAPP, APC, LMA, IP2I
Angélique Artaud (IJCLAB)
Jérôme Degallaix (LMA-IP2I)

## Slide 4
Squeezed states for Gravitational waves
The squeezing at a given frequency depends on two parameters: The length of FP cavity and its quality Q
In addition, optical loss reduces the impact of the squeezing performance.
Angélique Artaud (IJCLAB)
Jérôme Degallaix (LMA-IP2I)
In collaboration with LKB

## Slide 5
3D SRF cavities
D. Longuevergne (IJCLAB)
Akira Miyazaki (IJCLAB)
IJCLAB has an established knowledge of conceiving, producing and testing SRF cavities of high quality
Surface treatment
Annealing and baking
Cavities with very high Q0 are extraordinary tools in quantum technologies

## Slide 6: Thermal doping and alternative materials
Two methods are under study for High Qo et strong Gradient:
Les multi-couches (SIS)
Couches supraconductrices (NbN) séparées par une couche isolante (AlN) déposées par ALD
(élaborations via partenaires, analyses Vide&Surface)
Nb
Isolator
Superconductor
Isolator (AlN)
Superconductor (NbN)
~ 50 nm
~ 10 nm
Couches épaisses :
Dopage surfacique du Niobium par diffusion thermique
(Four SUPRATECH) => Haut Qo
Dépôt d’un matériaux supraconducteur alternatif (élaborations via partenaires, analyses Vide&Surface) => Haut Qo, Haut Gradient
Nb/Cu
Superconductor (doped Nb, other)
< 1 um
Nb as received
Doping
Materials | Tc (K) | Brf_limit (mT) | Coherence length (nm) | Comments
Nb | 9.2 | 220 | 28 | 
NbN | 17.1 | 215 | < 5 | Pour multi-layerss
MgB2 | 39 | 170 | 5 | 
Base Fer | 10-40 | < 760 | ? | Arsenic or Selenium
D. Longuevergne (IJCLAB)
Akira Miyazaki (IJCLAB)

## Slide 7
SRF cavities are excellent tools to search for DM at very low mass
IN2P3 is interested to join the efforts initiated at FERMILAB under the leadership of A. Grasselino.
We are discussing internally the best way to contribute to these efforts.
D. Longuevergne (IJCLAB)
Akira Miyazaki (IJCLAB)

## Slide 8
Superconducting circuits sensors
KID for microwave sky survey
mKIDs and their readout electronics were developed by LPSC in collaboration with NEEL institute in Grenoble to study the impact of dusty star-formation to the early formation of the early galaxy evolution.
Concerto is one of the experiments using this technology.
Andrea Catalano (LPSC)
Activities based on SQUIDS and low temperature electronics for astronomy applications are also developed at APC

## Slide 9
Superconducting circuits sensors
TES for DM
Experiments searching for Dark Matter based on bolometers such Edelweiss
and more recently RICOCCHET in Modane (LSM) provided the French groups
of IN2P3 with precious expertise on the use of cryogenics, Ge/Si and the
associated readout electronics .
IP2I, LPSC and IJCLAB have recently joined the TESSERACT collaboration which
intends to extend the DM search down to the meV level.
Different technologies are proposed. The French groups propose the Ge/Si technology
Julien Billard (IP2I)
Silvia Scorza (LPSC)

## Slide 10
Superconducting circuits sensors
TES for DM
TES technology will be used to detect athermal phonons
Julien Billard (IP2I)
Silvia Scorza (LPSC)
Ge/SI by detecting phonons and charges could improve on the detection performances by reducing the impact of LEE.
Ge/SI

## Slide 11
Clock distribution
IJCLAB collaborate with SYRTE and others to distribute clocks generated at SYRTE (3 optical clocks) in different places in France and Europe within the framework of the T+REFIMEVE project
Daniel Charlet (IJCLAB)
IJCLAB has led the development of IDROGEN board that uses the White-Rabbit protocol to regenerate the signal with high precision

## Slide 12
Clock distribution
2 IDROGEN boards on the WR switch configured in Grand Master and synchronized by T+ REFIMEVE fiber
from Paris Observatory (SYRTE
PPS time difference between two independent IDROGEN3 boards
Excellent long term stability : ~ 3E-18 s
On-going work: improve short term performances
Goal performances
Achieved performances
Daniel Charlet (IJCLAB)

## Slide 13
Penning&Paul traps
Penning and Paul traps are used as excellent tools for mass spectroscopy studies.
IJCLAB and LP2I have developed such traps for DESIR experiment to be installed in GANIL
The traps they conceived and the expertise they acquired could be exploited in two fields:
Precision study (QED, etc…)
Developing qubits system after introducing
LASER control system in collaboration with other
labs like CIML (Marseille University)
Enrique Minaya (IJCLAB)
Pauline Ascher (LP2I)

## Slide 14
Nuclear clocks
Vladimir Manea (IJCLAB)
Louis Lalanne (IPHC)
Simon Lechner (LP2I)
Sarina Geldhof (GANL)
IN2P3 is considering the possibility to join the efforts to develop nuclear clocks
By contributing to new ways of exploiting 229mTh
Looking for new clocks in which the isomer has energy difference with the fundamental state of the same order of that observed in 229mTh (8.338 eV) or slightly higher with equivalent stability. Collaboration with theorists will be ^recious

## Slide 15
Summary
Some quantum sensor activities at IN2P3 exist but remain relatively weak or isolated
We have started to organize these activities around a few projects
We will encourage the French groups to join DRD5 to build collaboration with others from other countries
We will organize workshops and summer schools so the new subatomic physicists can get the extraordinary potential of quantum sensors