## Slide 1: RILIS @ CRIS Collab
J. R. Reilly, A. Ajayakumar, M. Au, J. Berbalk, C. Bernerd, H. Büker, K. Chrysalidis, M. Elle, V. Fedosseev, L. T. Glöggler , M. V. U. Gonzalez, R. Heinke, A. A. H. Jaradat, R. Mancheva, R. Rossel, S. Rothe, A. Schmidt, J. Wessolek
Jan 2025

## Slide 2: Overview
The RILIS Team
RILIS in 2024 (Tm, Lu, Hg)
Developmental labs: YOL2, LARIS
Online: RILIS
What’s coming up

## Slide 3: The RILIS Team
Fellows
Staff
PhD Students
Legacy Member
PIJAS

## Slide 4: RILIS Online Period
22 experiments requiring laser ionized species
60% of campaigns throughout the running period and winter physics
Cl, Dy, In, Zn, Se, Ga, Au, Mg, Ca, Sn, Cd, Sb, Tm, Lu, Ho, Hg, Sr, Al, Be, Ac
1 x 3:00 am Chiller substitution
1 x LIST/PI-LIST campaign (Tm/Lu)
1 x 12-hour LIST target construction and change
1 x In-source spectroscopy campaign (Hg)
Many collaborative efforts with TISD/ISOLTRAP/IDS
Resonance Ionization Laser Ion Source

## Slide 5: PI-LIST: Ever growing demand!
Extension to the standard Ion source
Perpendicular illumination in the LIST interaction region
Repellers to suppress surface ionization (x106)
RILIS → LIST: 100 Loss factor
RILIS → PI-LIST (opt): 2000 Loss factor
Each PI-LIST target requires thorough troubleshooting
Construction of the LIST container
Coupling to ISOLDE target container
Vacuum Tests
Temperature calibration + Mechanical durability
Electronics and RF set up
Surface ion extraction and RF guiding
Laser access and laser ion extraction
Surface ion suppression: Ion guide mode vs LIST mode
PI-LIST configuration access
Offline 2
Transport
ISOLDE
Electronics and RF set up
Surface ion extraction and RF guiding
Laser access and laser ion extraction
Surface ion suppression: Ion guide mode vs LIST mode
PI-LIST configuration access
Perpendicular Illumination Laser Ion Source and Trap

## Slide 6: RILIS Results 2024
PI-LIST & In-source Campaigns on Lu, Tm and Hg
RILIS + IDS + ISOLTRAP
Tm: COLLAPS run towards shell closure (Sept 2024)
Lu: Scheme development and yield checks (Sep 2024)
Hg: New laser spec and decay spec on neutron-rich side (Oct 2024)
Courtesy of Kara Lynch!
Courtesy of Josh Wilson!
209Hg!

## Slide 7: Offline 2
New autoionizing states found in Ni!
Measured in Oct!
Oct 2024: Ni Scheme development – New AIs found with spectroscopy transition
December 2024: Accepted proposal to study Ni online with PI-LIST – investigate resolution limit in medium mass region offline
Providing more laser capabilities in YOL2 for Ni development as well as future endeavors:
4 x TiSa cavities ( 2 x BiFi + etalon, 1 x Grating, 1 x injection-seeded)
2 x Pump lasers
1 x Non-res 1064/532/355
2 x Diode lasers
Upgrading the YOL2 Laser Lab!
To meet the demands in YOL2, we had to borrow Grating from MEDICIS – temporary solution

## Slide 8: Offline 2
Also investigating PI-LIST developments:
RF + laser pulse synchronisation (Summer 2024)
Single pass vs Triple pass (Feb 2025)
Voltage offset: deployed online for Tm (Autumn 2024)
H-bridge current switching (Spring/Summer 2025)
New Transducer box (Manchester collaboration)
Not only lasers!
Also aim to duplicate electronics this year to have a permanent ISOLDE and YOL2 set-up

## Slide 9: LARIS
Returning ABU to its former glory!
Plans to add an extension to existing and new design:
deflectors/bending plates added to existing chamber
Retractable extraction electrode
ISOLDE target coupling capabilities
Anti-collinear access
Decrease demand on Offline 2
Not only LIST but other ISOLDE targets!

## Slide 10: LARIS
Frequency mixing: Covering Dye laser wavelengths with solid-state systems & non-linear optics
Process
Schematics
Phase-matching BiBO
Sum frequency generation
SFG
Difference frequency generation
DFG
Potential coverage :
SFG tested at RILIS and CRIS in 2023 Ag (532nm SM not stabilized)
Proof of principle with broadband 1064nm MIRUS laser from Mainz in LARIS in 2025
Test for intra-cavity frequency mixing
If successful : stabilized 1064nm SML → call for tender
ħω2
Slide provided by Cyril!

## Slide 11: RILIS DAQ: Spectroscopy
Slide provided by Cyril!
General upgrade of the RILIS Labview software environnent (contract with ANGARA)
Upgrade of the RILIS DAQ software for in-source spectroscopy:
  Work in progress by ANGARA
  Testing and debugging in February-March – To be ready for use in April
  Possibility to add new trigger configuration (time, proton bunch, supercycle…). Any suggestions ?
Old version
New version

## Slide 12: RILIS DAQ: Operation
New monitoring capabilities for RILIS
Monitoring of (when possible):
◦ Position XY ◦ Intensity (ref) ◦ Wavelength ◦ Timing
Values pushed through CERN middleware and accessible in Timber
timber.cern.ch
Slide provided by Cyril!

## Slide 13: What’s coming up?
Ever-growing demand for (PI)-LIST!
2 Confirmed PI-LIST campaigns: Ni + Pm
1 tbc PI-LIST campaign: Lu
1 In-source LIST campaign: Bi/Cu
1 LIST target Campaign: Tm (COLLAPS)
4 x LIST for Online + 1 Development
Not just the typical LIST targets:
1 W-lined for Ni
1 Neutron-converter for Bi/Cu

## Slide 14: What’s coming up?
A busy year for PI-LIST, with challenging laser Schemes!
Our plans to provide the high-res light:
Currently high-res seed light is provided by the CRIS Matisse
This year, we have purchase Toptica diode laser (DLPRO) + trying to revive TUI Optics diode laser
Diode lasers moved between RILIS/YOL2/LARIS – wear and tear on equipment
Purchasing + swapping diodes for 2025
Growing demand for high-res PI-LIST and busy schedule for CRIS puts a strain on Matisse + Locals
New Matisse to be housed in CRIS laser lab?
2025
Ar: 763.5 nm
In: 738 nm
Pm: 905 nm
Ni: 704 nm
Lu: 897 nm
Missing any??

## Slide 15: 10 kHz Fast Beamgates
Recent implementation of the cRIO
Mixing input TTL signals
RILIS T0, USER or Tape triggered beamgate
All inputs mixed for a single output
Recent upgrades allow proton triggered + proton counting triggered beamgate
Implementation on GPS this year!

## Slide 16: New online Database for Laser Ionisation schemes
Found here: https://rims-code.github.io
Or use the QR code!

## Slide 17: Conclusion
New accepted proposals on Ni and Pm
4 LIST Campaigns
Implementing high-res in YOL2
Construction of new ABU in LARIS
New High-res laser in CRIS laser lab
New RILIS DAQ
Busy year with 60% of ion beams at ISOLDE requiring RILIS
Exchange of lasers and many late nights
Ongoing developments for PI-LIST
10 kHz beamgates for ion beam improvements
New TiSa only Ni scheme
Experimental runs on Lu, Tm and Hg in 2024
Future Outlooks
Thank you!

## Slide 18: Back up Slides

## Slide 19: Ni Scheme Development
3 New autoionizing states in Ni observed
This scheme utilizes the laser spectroscopy transition used in literature
Motivated the submission of INTC proposal to study Ni using PI-LIST!
Scheme at least as efficient as production
New autoionizing states found in Ni!
Measured in Oct!

## Slide 20: Thank you! Questions?
Submitted proposals on Ni & Pm
Further upgrades to offline2 laser laboratory for high-resolution
Construction of new ABU in LARIS
Raman laser development
Conclusion
Busy year with 60% of ions beam at ISOLDE requiring RILIS
Exchange of lasers and many late nights
Ongoing developments for PI-LIST
In-trap decay & 10 kHz beamgates for ion beam improvements
First online deployment of intracavity triple TiSa
New TiSa only Ni scheme
Experimental runs on Lu, Tm and Hg
Future Outlooks

## Slide 21: First online deployment of intra-cavity tripling
65 mW of 304 nm laser light for the production of indium beams
  Stable operation for 7 days without intervention
  Compared to Dye lasers which need constant monitoring
Courtesy of Julius
Intracavity THG Single-Pass THG
25 cm
250 cm
100 cm
Chart: Time [h]
Long-term stability test for Au 2nd step @ 306nm and 10kHz has shown a slow decrease of power but easily recovered:
 | Beam Profile | Output Power | Stability | Ease of set up | Space | Cost
Intra |  |  |  |  |  | 
External |  |  |  |  |  | 

## Slide 22: Resonance Ionization Laser Ion Source
RILIS uses a variety of 10 kHz lasers
Unique atomic transitions to step-wise excite and ionize the element of interest
Coupled with mass selectivity for high resolving power

## Slide 23: MELISSA in 2024
Month | May |  |  |  | June |  |  |  | July |  |  |  |  | August |  |  |  | September |  |  |  | October | October |  |  |  | November |  |  |  | D
Week no | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49
Element |  | Tb Dy | Tb Dy | Tb Dy |  | Tb Dy | Sm |  | Cu | Tb Dy |  |  |  | Tm | Tm | Tb |  |  | Tm | Tb Dy |  |  | Gd Eu | Tb Dy | Tb Dy | Tb Dy |  | Tb Dy | Tb Dy | Sc | Sc
145Eu
149Gd
New 2024
Portfolio
Operation 2024
Operators 2024
2 new collections at MEDICIS in 2024: 145Eu and 149Gd
Validation of Eu laser scheme developed in RILIS (B. van Dingenen KU Leuven)
Raman laser : Final z-fold design
New 2024
Laser laboratory
Development 2024
Courtesy of Cyril

## Slide 24: In-trap Decay
LOI to investigate in-trap decay using ISCOOL RFQ
Provide non-produced and challenging to extract elements
Improve ion confinement by optimizing He gas pressure and potential well depth
Thanks to efforts of TISD/RILIS/ISOLTRAP!
Laser ionized Sr tested!
Original Plan
Revised Plan
Analysis ongoing!

## Slide 25
RILIS uses a variety of 10 kHz lasers
Unique atomic transitions to step-wise excite and ionize the element of interest
Coupled with mass selectivity for high resolving power
Properties of MESAs and Photonics are comparable
Future plan is to investigate TiSa performance using MESA vs Photonics vs Nanio in offline labs
Photonics
200
300
400
500
600
700
800
900