## Slide 1: ISOLDE TISD 2024 year in review
Running period: 2 April – 8 December
MD activities: HRS fast beamgate system, RP monitor proton scans, 2D proton scans
11 Target and Ion Source Development (TISD) beamtimes:
  Beam development: Pa, TbFx, in-trap decay,
  New target materials: nano ZrOx, TaC,
Beams for operation:
  First negative ions since LS2: Br-, Cl-
  Molecular beams: SnS, CeFx, YFx, RaF,
  Special target materials: Nb foils, Ti foils, nano CaO
  Special target units: #856 ∆T<20˚C, #861 LIST, #813 LIST, #810 hq, #879 cq, #820 liquid La
TISD team on shift
Nonstandard target/ development for operation

## Slide 2: ISOLDE TISD 2024: April-June
LOI258: External sample collaboration, first Pa beam at ISOLDE
TISD TbFx: Molecular Tb beams for medical applications
HRS fast beamgates: Installation and commissioning
In-trap decay: MD and preliminary tests
GANDALPH: First (only) negative ion run since LS2
CaOx nano: One-day turnaround for backup target
TISD ZrOx nano: Target material development
TISD team on shift
Nonstandard target/beam development for operation
Liquid Pb
Liquid La: #820
M. Au

## Slide 3: ISOLDE TISD 2024: July-August
SnS: sulphur oven development
#856 for IS745: ∆T < 17˚C
SnS: sulphur oven development
TISD ZrOx: Target material development
TISD team on shift
Nonstandard target/beam development for operation
Hot quartz
LIST Ta
TISD TaCx: Target material development
LIST Ta: offline development target as backup ~1 day turnaround
TISD TaCx: Target material development
RP monitor data and 2D proton scans
J.B. Frederiksen, M. Au, L. Le
https://cds.cern.ch/record/2908317
M. Au

## Slide 4: ISOLDE TISD 2024: October-December
RaF-: negative molecules through double charge-exchange
TISD team on shift
Nonstandard target/beam development for operation
Cold quartz
Nb foil target: target material development, yields for users
CeFx: molecular beam development
LOI270 in-trap decay: beam development
Winter physics: Fr from Ac decay
TISD: TbFx from tantalum foils
M. Au

## Slide 5: TISD online experiments
Contaminant ions
Contaminant neutrals
Isotope of interest
Neutral molecule of interest
Molecular ion of interest
Reactive gas
Buffer gas
ϒ
β
β
β
In-beam detector
4-π
Ge
Ion beam
Catherall, R. et al. (2017) J. Phys. G. 44, 9
ISOLDE FTS
ISOLTRAP
MR-ToF MS
ISOLTRAP
RFQ-cb
collections chamber
Mass separator
target
p+
Extraction electrode
Ion source
ISOLDE LA1
ISOLDE HRS
M. Au

## Slide 6: Fluoride beams current status
Image published in EP Newsletter, CERN (2020)
Z=9
F
Z=89
Ac
Actinium
Z=9
F
Z=9
F
Z=89
Ac
Actinium
Z=9
F
Z=8
O
Z=92
U
Uranium
?
?
Z=89
Pa
Protactinium
  RaFx: developed, available*
  AcFx: developed, available*
  NpFx, PuFx: observed
  PaFx, PaOx: external sources, development
  ThFx, UFx: long-lived only
  ScFx, TbFx: ongoing development
  VFx: requested
M. Au
Notes: Not to scale 

## Slide 7: Fundamental Symmetries collaboration
Precision measurement
RIB
Making radioactive molecules
  Beams, traps, targets
Techniques for bulk systems
Work in progress
  Fellow position closed
  collaboration
Roussy et al., Science 381, 46 (2023)
Fitch et al., Q.Sci.T. 6, 014006 (2021)
Morris et al., Phil. Trans. R. Soc. A. 3822 (2023)
Characterizing radioactive molecules
  Spectroscopy, chemistry
  Properties and states
Athanasakis-Kaklamanakis et al.,(2024) in preparation
Udrescu et al.,(2024) Nat. Phys. 20, 202
M. Au

## Slide 8: Developments in target materials
Slides and pictures provided by V. Berlin, M. Au
Sub-micron and nano materials development:
Valentina Berlin and Edgar Reis
CaO, ZrO2, La2O3,UCX,TaC,HfB,Ta foils…
La2O3
ZrO2
Nano lab
Gas injection
  Reactive/corrosive gases
Reactants
Mass markers
Target materials
Particle size
Open porosity

## Slide 9: Ion source developments
Molecular breakup and characterization studies
  FEBIAD-type ion sources [1,2]
  Electron energy and source optimization
  Ion source systematics
Photocathode ion sources [3]
  Cold (room-temperature) environments
In-source spectroscopy [4]
  PI-LIST: sub-Doppler hot-cavity in-source spectroscopy
  CERN-ISOLDE implementation
[1] Maldonado (2023) PhD thesis
[2] Martinez Palenzuela (2020) PhD thesis
[3] Ballof . ﻿et al., 2022) J. Phys.: Conf. Ser. 2244 012072
[4] Heinke et al. (2023) NIM B. 541 (8-12)
Slides and pictures provided by M. Au

## Slide 10: Molecular ion beam production Update on ISOLDE Offline 2
Justus Berbalk
CRIS Collaboration meeting 30-31 January 2025

## Slide 11: Layout of OFFLINE 2
Ion source
Beamgate
90° Magnet
RFQcb
Radio-frequency quadrupole cooler and buncher
~ 2 m
Magnetof
High Voltage racks
High Voltage racks
RILIS Lab

## Slide 12: The radiofrequency quadrupole cooler-buncher (RFQcb)
Inj. plate
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
24
23
25
extr. plate
Beamgate
RFQ
2
Example: 10 ms trapping
0
50 ms
100 ms
150 ms
12
V
TTL signal of Quantum Composer switches endcap electrode potential via high-voltage, high-current Behlke switch
He
He
He
He
Before: 0.5% transmission, no bunching, no cooling
100 us
Now: 50-60% transmission, bunching and cooling !

## Slide 13: Different Time-of-Fight for different species
39K
10 ms trapping time
85Rb
10 ms trapping time

## Slide 14: Time-of-Flight vs Mass
10 ms trapping
Beam @ 30 keV
Time-of-flight calibration with hot plasma ion source ongoing at the moment
39K
23Na
85Rb

## Slide 15: Trapping lifetime Counts per bunch per beamgate vs trap time
23Na
PRELIMINARY
After optimising for ~2h

## Slide 16: Long trapping times: molecule formation ?
1 ms trap
100 ms trap
1000 ms trap
5000 ms trap
10 000 ms trap
500 ms trap
0.8
23Na

## Slide 17: Under investigation
Influence of the potential well shape on cooling-bunching
Helium pressure
Incoming beam and beam gate duty cycle: linearity tests for overflowing the trap
BG: 2us, trap: 20us

## Slide 18: Towards high-precision molecular experiment at RIB facilities
Fundamental symmetries, Physics beyond colliders framework

## Slide 19: Fundamental Symmetries Collaboration
Precision measurement
RIB
Making radioactive molecules
  Beams, traps, targets
Techniques for bulk systems
Work in progress
  Fellow position closed
  collaboration
Roussy et al., Science 381, 46 (2023)
Fitch et al., Q.Sci.T. 6, 014006 (2021)
Morris et al., Phil. Trans. R. Soc. A. 3822 (2023)
Characterizing radioactive molecules
  Spectroscopy, chemistry
  Properties and states
Athanasakis-Kaklamanakis et al.,(2024) in preparation
Udrescu et al.,(2024) Nat. Phys. 20, 202
M. Au
March 24-25
https://indico.cern.ch/e/FunSy

## Slide 20: An idealised EDM experiment
Taken from Nick Hutzler’s talk at TRISEP (2022)
https://www.hutzlerlab.com/teaching/trisep-2022
Example: Implementation with BaF (NL-eEDM collaboration)
Taken from: Aggarwal, P., Bethlem, H. L., Borschevsky, A., Denis, M., Esajas, K., Haase, P. A. B., Hao, Y., Hoekstra, S., Jungmann, K., Meijknecht, T. B., Mooij, M. C., Timmermans, R. G. E., Ubachs, W., Willmann, L., Zapara, A., & The NL-eEDM collaboration. (2018). Measuring the electric dipole moment of the electron in BaF. The European Physical Journal D, 72(11), 197. https://doi.org/10.1140/epjd/e2018-90192-9

## Slide 21: Current layout
Ion source
Beamgate
90° Magnet
RFQcb
~ 2 m
Magnetof
High Voltage racks
High Voltage racks
RILIS Lab
Gas injection system

## Slide 22: In trap formation of molecules via atomic RIB Bridging the gap between high precision and RIB facilities
Ion source
Beamgate
90° Magnet
RFQcb
~ 2 m
Magnetof
RILIS Lab
Gas injection system
Reactive gases: CH3OH, H2O2,H2O,NH3
Inj. plate
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
24
23
25
extr. plate
V
He
He
He
He

## Slide 23: Projected new end of beamline
RILIS Lab
Hole in wall and second window through the magnet already exists !
Model by A.Schmidt

## Slide 24: New end of beamline: Phase one
RILIS Lab
Magnetof
installed ✅
ToF region ✅
Deflector to be designed 🛠️
Possible experiments:
Photodissociation of small molecules
Molecular breakup of SrF+ for n-deficient Sn and In
Dissociation thresholds
Ionisation of neutrals ?
Limited by ToF resolution (mass resolving power)
Image: Lukas Nies

## Slide 25: New end of beamline: Phase two
RILIS Lab
Emittance meter
available ✅
Wien filter
available ✅
Deflectors
Available/to buy ✅
Magnetof
installed ✅
Laser interaction region
Design phase🛠️
PMT + collection optics
Design phase 🛠️
Discussions with REBEL Lab
PI: Agi Koszorus
Einzel lens
to buy
Funding refused by SY department
Probing thermodynamics ensemble towards coherent state population for fundamental symmetry project
Model by A.Schmidt

## Slide 26
Funding refused by SY department (65k CHF)

## Slide 27
New end of beamline: Phase three
Long term :
Pulsing/ramping RFQ to ground
Pulsed drift tube
MR-ToF
Cryogenic trap, MOT
Your ideas
RILIS Lab
?
Model by A.Schmidt

## Slide 28
Acknowledgments
CERN:
Sebastian Rothe
Mia Au
Alex Schmidt
Line Le
Jordan Reilly
Reinhard Heinke
Katherina Chrysalidis
Sebastian Rothe
Simon Stegeman
Edgar Reis
Matthias Grasser
Valentina Berlin
Serdar Usta
Patricija Kalnina
Isabel Frank
SY-STI-LP
SY-STI-RBS groups
KU Leuven:
Gerda Neyens
Agi Koszorus
Ruben De Groote
& the entire
IKS Nuclear Moments group

## Slide 30
Supplemental
23Na
10ms trapping time

## Slide 31
Target container typically heated to ~2000o C
Transfer line controls transport to ion source, Ta, Cu or quartz
Ion source: surface, laser, plasma, …
Each target is custom-tailored to the physics experiment
30+ targets per year!
Target unit
[ER24]-mod
Slides and pictures from V. Berlin

## Slide 32: eEDM is symmetry violating
s
d
Spatial coordinates mirror
s
d
s
d
Time reversal
Inspired from Nick Hutzler’s talk at TRISEP (2022)
https://www.hutzlerlab.com/teaching/trisep-2022