## Slide 1
HL-LHC jumpers interfaces
Interfaces definition in the LHC tunnel
F. Merli (TE-CRG-ME)
on behalf of WP9 cryo-distribution team

## Slide 2
Scope
Junction Module region
(Under revision: LHC-QXLJ-EC-0001)
Inner Triplet region
D2 / Crab Cavities region

## Slide 3
Types of QXL jumper
Inner Triplet jumper
Jumper with Jumper Extension
Rigid jumper
Q2B, CP, D1
D2, CC-IP, CC-nonIP
DFX, DFM

## Slide 4
Inner Triplet Jumper
IP | Side | Jumper | H | L | D
 |  |  | [mm] | [mm] | [mm]
1 | Left | Q2B | 1188 | 1000 | 440
 |  | CP | 1188 |  | 
 |  | D1 | 1188 |  | 
 | Right | Q2B | 1188 |  | 
 |  | CP | 1188 |  | 
 |  | D1 | 1188 |  | 
5 | Left | Q2B | 1201 |  | 
 |  | CP | 1381 | 129 | 405
 |  | D1 | 1381 |  | 
 | Right | Q2B | 1201 |  | 
 |  | CP | 1381 | 129 | 405
 |  | D1 | 1381 |  | 
L
H
D
Layout:
  Different height
  Left and right side mirrored
Interfaces:
  different number and size of pipes
    Q2B: 7
    CP: 5
    D1: 7
  Left and right side mirrored
Q2B left
Q2B right
CP left
CP right
D1 left
D1 right

## Slide 5
Jumper with Jumper Extension
D2
Crab Cavities
HIP1=1234
HIP5=1427
440
380
HIP1=1234
HIP5=1427
Layout of the pipes at the interface with the jumper extension to be defined based on:
  Layout of pipes at interface with the cryogenic beamline component
  Methods and tooling employed by CERN to make the interconnection on site

## Slide 6
Jumper Extensions
D2
Crab Cavities
In the
interconnection
8 lines
7 lines

## Slide 7
Rigid Jumper
DFX
DFM

## Slide 8
QXL Jumper | IP | QXL Layout Drawing | Service Module Assembly Drawing | Service Module Equipment Drawing | Jumper Interface Drawing | Jumper Internal Interface Drawing
Q2B | 1L | LHCQXL_G0009 | - | LHCQXLAA0001 | LHCQXLZ_0001 | -
 | 1R | LHCQXL_G0010 | - | LHCQXLAB0001 | LHCQXLZ_0002 | -
 | 5L | LHCQXL_G0011 | - | LHCQXLAC0001 | LHCQXLZ_0003 | -
 | 5R | LHCQXL_G0012 | - | LHCQXLAD0001 | LHCQXLZ_0004 | -
CP | 1L | LHCQXL_G0009 | - | LHCQXLBA0001 | LHCQXLZ_0005 | -
 | 1R | LHCQXL_G0010 | - | LHCQXLBB0001 | LHCQXLZ_0006 | -
 | 5L | LHCQXL_G0011 | - | LHCQXLBC0001 | LHCQXLZ_0007 | -
 | 5R | LHCQXL_G0012 | - | LHCQXLBD0001 | LHCQXLZ_0008 | -
D1 | 1L | LHCQXL_G0009 | - | LHCQXLCA0001 | LHCQXLZ_0009 | -
 | 1R | LHCQXL_G0010 | - | LHCQXLCB0001 | LHCQXLZ_0010 | -
 | 5L | LHCQXL_G0011 | - | LHCQXLCC0001 | LHCQXLZ_0011 | -
 | 5R | LHCQXL_G0012 | - | LHCQXLCD0001 | LHCQXLZ_0012 | -
D2 | 1L | LHCQXL_G0009 | LHCQXLDA0002 | LHCQXLDA0001 | LHCQXLZ_0017 | LHCQXLZ_0019
 | 1R | LHCQXL_G0010 | LHCQXLDB0002 | LHCQXLDB0001 | LHCQXLZ_0018 | LHCQXLZ_0020
 | 5L | LHCQXL_G0011 | LHCQXLDC0002 | LHCQXLDC0001 | LHCQXLZ_0019 | LHCQXLZ_0019
 | 5R | LHCQXL_G0012 | LHCQXLDD0002 | LHCQXLDD0001 | LHCQXLZ_0020 | LHCQXLZ_0020
CC-IP | 1L | LHCQXL_G0009 | LHCQXLEA0002 | LHCQXLEA0001 | LHCQXLZ_0025 | LHCQXLZ_0027
 | 1R | LHCQXL_G0010 | LHCQXLEB0002 | LHCQXLEB0001 | LHCQXLZ_0026 | LHCQXLZ_0028
 | 5L | LHCQXL_G0011 | LHCQXLEC0002 | LHCQXLEC0001 | LHCQXLZ_0025 | LHCQXLZ_0027
 | 5R | LHCQXL_G0012 | LHCQXLED0002 | LHCQXLED0001 | LHCQXLZ_0026 | LHCQXLZ_0028
CC-noIP | 1L | LHCQXL_G0009 | LHCQXLFA0002 | LHCQXLFA0001 | LHCQXLZ_0026 | LHCQXLZ_0028
 | 1R | LHCQXL_G0010 | LHCQXLFB0002 | LHCQXLFB0001 | LHCQXLZ_0025 | LHCQXLZ_0027
 | 5L | LHCQXL_G0011 | LHCQXLFC0002 | LHCQXLFC0001 | LHCQXLZ_0026 | LHCQXLZ_0028
 | 5R | LHCQXL_G0012 | LHCQXLFD0002 | LHCQXLFD0001 | LHCQXLZ_0025 | LHCQXLZ_0027
Reference documents

## Slide 9
QXL Vs SQXL
Inner Triplet region reconfiguration
(EDMS 2827006)
SQXL installation lessons learnt
(EDMS 2768428)
Jumper design studies

## Slide 10
Jumper design studies
Technical notes
  Jumpers interconnection layout review
  Jumpers required flexibility evaluation
  Jumpers interconnection weld flanges structural verification
  Jumpers stiffness analysis
Engineering methods for installation
  QXL/QRL Jumper interfaces preparation for interconnection
  QXL/QRL Jumper interfaces alignment
  HL-LHC Jumpers interconnection
  QXL/QRL Installation requirements
  Jumper extension installation requirements
HL-LHC Jumpers interface specification
(EDMS 2419072)
Validation activities
  Jumpers mock-up
  Flexible hoses characterization tests (EDMS xxx)

## Slide 11
Installation methods
QXL/QRL
interface preparation
User
Installation
(1st positioning)
Jumper extension installation
Jumper
interface
alignment
Interface to magnet
interconnection
QXL
commissioning
magnets
interconnection
User final
positioning
(smoothing)
QXL/QRL
installation
Interface to
QXL/QRL
interconnection
QXL/QRL Installation requirements
QXL/QRL Jumper interfaces preparation for interconnection
Jumper extension installation
QXL/QRL Jumper interfaces alignment
HL-LHC Jumpers interconnection

## Slide 12
Removal of thermal shield endcap and MLI
Cutting of pipes overlength
Removal of pipe endcaps
Removal of piping internal support (optional)
Positioning of vacuum jacket sleeve
Cutting of vacuum jacket endcap
Opening of vacuum jacket valves
Cleaning and preservation
Jumper interfaces preparation for interconnection

## Slide 13
Jumpers interconnection
Initial configuration
Final configuration
Interconnection sequence

## Slide 14
Jumpers interconnection
Pipes with backing rings
Line | DN | Dp | Tube t | N. of Tubes | Welding technique
[-] | [-] | [mm] | [mm] | [-] | [-]
CC', KD | Φ10 | 10 | 1 | 32 | Orbital TIG
CY | DN6 | 12 | 1 | 16 | Orbital TIG
CY | DN8 | 13.5 | 1.6 | 8 | Manual TIG
CC', CY, EE, E'H, E'HFH, FF, KD | DN10 | 17.2 | 1.6 | 68 | Orbital TIG
EHE'H, E'HFH | Φ18 | 18 | 1.6 | 32 | Orbital TIG
EE, RD | Φ22 | 22 | 1 | 8 | Manual TIG
Installation sequence
Configurations
Repair

## Slide 15
Jumpers interconnection
Pipes with sliding sleeve
Line | DN | D3 | Dp | N. of Tubes | Welding technique
[-] | [-] | [mm] | [mm] | [-] | [-]
CS | DN15 | 37 | 41 | 16 | Orbital TIG
CS, EHE'H, EHKH, E'H, E'HFH | DN20 | 37 | 41 | 36 | Orbital TIG
SD | DN25 | 46 | 50 | 8 | Manual TIG
LD | DN32 | 54 | 58 | 16 | Manual TIG
CL | Φ43 | 54 | 58 | 12 | Manual TIG
LD | DN40 | 64 | 68 | 12 | Manual TIG
LD | Φ52 | TBD | TBD | 6 | Manual TIG
XB | DN50 | 73.5 | 77 | 8 | Manual TIG
XB | Φ63 | 73.5 | 77 | 16 | Manual TIG
XB | DN125 | 151 | 155 | 12 | Manual TIG
Installation sequence
Configurations
Repair
Line | DN | Cutting machine
[-] | [-] | [-]
CS | DN15 | PROTEM TTSRD_41
CS, EHE'H, EHKH, E'H, E'HFH | DN20 | PROTEM TTSRD_41
SD | DN25 | PROTEM TTSRD_71
LD | DN32 | PROTEM TTSRD_71
CL | Φ43 | PROTEM TTSRD_71
LD | DN40 | PROTEM TTSRD_71
LD | Φ52 | TBD
XB | DN50 | PROTEM TTSRD_78
XB | Φ63 | PROTEM TTSRD_78
XB | DN125 | TBD

## Slide 16
Jumpers flexibility requirements
Sources of required flexibility
QXL Jumper (QXL)
Jumper Extension (JE)
Cryogenic Beam Line Component (CBLC)
Interconnection (INT)
Vacuum Vessel (VV)
Process Pipes (PP)
Applicable: “X”
Not applicable: “-”
Jumper required flexibility definition
(EDMS 2724933)

## Slide 17
Machine tilt
The design of the jumpers is adapted to the machine tilt in P1 and P5 to limit the impact on the jumper flexibility requirement

## Slide 18
Vacuum Vessel
Process Pipes
Jumper Extensions
QXL manufacturing tolerances

## Slide 19
Magnets manufacturing tolerances

## Slide 20
Telescopic sleeve
 Increased interconnection accessibility
Additional length for flexible hoses
 Increased pipes flexibility
Relocated gimbal sleeve
QXL fixed point moved forward magnet fixed point
 Reduced differential thermal contraction
Inner triplet region reconfiguration

## Slide 21
B. Wong Luis and D. Duarte Ramos, TE-MSC
EDMS 2798916
Outcome of the study
Design displacements
  Vacuum jacket ✓
  Process pipes ✓
Loads on magnet’s cryostat
  Stress field ✓
  Global stability ✓
  Buckling ✓
Interconnection ✓
Vacuum jacket flexibility analysis
Pipes flexibility analysis
Interconnection accessibility study
~260
Inner triplet region reconfiguration

## Slide 22
Impact of new process scheme
  + 1 subcooling heat exchanger
+ 2 control valves
+ 3 process lines
    CY2 (DN10)
    CY2’ (DN10)
    XB2 (DN65)
Outcome of the study
Internal pipe routing ✓
Thermal contraction accommodation ✓
Pressure drops ✓
External constraints ✓
HXI dome
HXI dome
Jumper interconnection
Magnet interconnection
Q2B magnet Service Module
QXL Service Module
Inner triplet region reconfiguration

## Slide 23
SQXL installation lessons learnt

## Slide 24
Summary
Several activities have been performed to anticipate issues with jumper interconnections for the LHC tunnel, which implements requirements and return of experience from:
  QRL design and installation
  SQXL installation
  IT region reconfiguration
The outcome of these activities result in the current specification and the design has undergone different level of validation.
The current design of the QXL is significantly different from the one of the SQXL also thanks to experience gathered during the manufacturing and installation of the SQXL.
The current design requirements will avoid issues experienced in the interconnection operations in SM18, provided that they will be fulfilled.
Quality control to ensure that the new requirements are met will be fundamental to avoid issues in LS3.

## Slide 25
End of presentation