## Slide 1: FCC-hh cryogenics R&D and cooling schemes for sc magnets at 4.5 K – Cross section 2D modelling –
This project has received funding from the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754.
Patricia Borges de Sousa
Ximo Gallud Cidoncha
on behalf of CERN TE/CRG

## Slide 2: Heat load distributions
FCC-hh heat loads |  | 60 - 80 K (W/m) | 4 K (W/m)
Static | Supports | 2.4 | 0.13
 | Radiative Insulation |  | 0.13
 | Thermal Shield | 3.1 | 
 | Feedthrough and vacum barrier | 0.2 | 0.10
 | Beamscreens |  | 0.30
 | Distribution | 3.6 | 0.10
 | Total Static | 9.3 | 0.76
Dynamic | Synchrotron Radiations | 37 | 0.05
 | Image Currents | 3.4 | 
 | Resistive Heating |  | 0.30
 | Beam Gas Scattering |  | 0.45
 | Total Dynamic (no losses) | 40.4 | 0.80
 | Magnetization losses (eddy current) |  | 3.13
TOTAL (with mag. losses) |  | 49.7 | 4.69
Surface load distributed homogeneously along outer shell
Distributed homogeneously along inner core shell
Volumetrically distributed load in coils

## Slide 3: Preliminary geometrical placement of cooling channels:
Number of channels distribution .
Arbitrary diameter .
  Future optimization of and based on:
    Longitudinal pressure drop considerations.
    Convective heat transfer coefficient considerations for given .
Heat sinks at
No material modification (insulation material as prescribed).

## Slide 4: Cooling channels :
T (K)

## Slide 5: Cooling channels :
T (K)

## Slide 6: Cooling channels :
T (K)

## Slide 7: Cooling channels (top placement):
T (K)
(Second channel in
symmetry plane)

## Slide 8: Cooling channels (top placement):
T (K)

## Slide 9: Cooling channels (side and top):
T (K)

## Slide 10: Adding of Copper conducting layer of cooling channel size:
Number of channels distribution .
Arbitrary diameter mm.
Heat sinks at
Copper layer at midplane to distribute heat sink of varying thickness .

## Slide 11: Cooling channels (side and top):
T (K)
Copper layer thickness

## Slide 12: Cooling channels ():
T (K)

## Slide 13: Cooling channels ():
T (K)

## Slide 14: Cooling channels ():
T (K)

## Slide 15: Cooling channels ():
T (K)

## Slide 16: Cooling channels ():
T (K)

## Slide 17: Maximum magnet temperature vs. Cu thickness:

## Slide 18: Maximum magnet temperature vs. Cu thickness:

## Slide 19: Maximum magnet temperature vs. Cu thickness:
Minimum copper thickness for

## Slide 20: Summary of preliminary design exploration (, )
Layout |  | Max (K) | (mm) | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. | Symmetric heat loads. Accessible to higher diameter (lower ). | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | Above the 5 K limit. Constrained diameter (higher )
 | 4 | 5.05 | 50 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | More channels? Constrained diameter (higher )
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). | Shortest heat load path to sink (lower max ) | Non symmetric heat loads. Constrained diameter (higher )
Layout |  |  |  | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. |  | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). |  | 
 | 4 | 5.05 | 50 | Cooling channels in collar (top). |  | 
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). |  | 

## Slide 21: Summary of preliminary design exploration (, )
Layout |  | Max (K) | (mm) | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. | Symmetric heat loads. Accessible to higher diameter (lower ). | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | Above the 5 K limit. Constrained diameter (higher )
 | 4 | 5.05 | 50 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | More channels? Constrained diameter (higher )
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). | Shortest heat load path to sink (lower max ) | Non symmetric heat loads. Constrained diameter (higher )
Layout |  |  |  | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. |  | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). |  | 
 | 4 | 5.05 | 50 | Cooling channels in collar (top). |  | 
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). |  | 
max decreases

## Slide 22
Conclusions:
Preliminary placement of 4 cooling channels in collar for single aperture cross section (SMT) cools magnets below 5 K including ramping losses, when assuming:
    Cooling channel is a thermal sink at .
    A midplane copper layer to distribute sink of
    2D Heat transfer
Limited availability of cross section area limits hydraulic diameter to mm smashing pressure drop in magnet supply line up to 1 bar.

## Slide 23
Discussion items

## Slide 24
Discussion items:
What is:
    the maximum copper layer thickness (above )?
b) the smallest pipe allowance/placement to the magnet coil (tolerance)?
c) the maximum cross section area available for cooling channels?
That does not compromise any structural and magnetic field requirements.
(On the side):
    d) In which ways would any 3D model (conjugate heat transfer/turbulent single phase He flow) be helpful to devise possible hot spots/dangerous thermal gradients in magnet coils?

## Slide 25
Longitudinal considerations

## Slide 26: Summary of preliminary design exploration (, )
Layout |  | Max (K) | (mm) | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. | Symmetric heat loads. Accessible to higher diameter (lower ). | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | Above the 5 K limit. Constrained diameter (higher )
 | 4 | 5.05 | 50 | Cooling channels in collar (top). | Symmetric heat loads. Shorter heat load path to sink (lower max ) | More channels? Constrained diameter (higher )
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). | Shortest heat load path to sink (lower max ) | Non symmetric heat loads. Constrained diameter (higher )
Layout |  |  |  | Comments | Pros. | Cons.
 | 2 | 5.22 | 90 | Cooling channels in iron yoke. |  | Above the 5 K limit.
 | 2 | 5.07 | 40 | Cooling channels in collar (top). |  | 
 | 4 | 5.05 | 50 | Cooling channels in collar (top). |  | 
 | 4 | 4.98 | 40 | Cooling channels in collar (top and side). |  | 
Chosen as benchmark for recooling scheme update

## Slide 27
Cold mass cooling scheme PID (nomenclature):

## Slide 28
Parameter | Unit | FCC- hh cryog. report (2024) benchmark | 2D cross section preliminary benchmark
 | m | 4800 | 4800
 | m | 300 | 300
 | bar | 0.817 | 0.817
 | bar | 3 | 3
 | kg/s | 1.1 | 0.58
 | W | 4.5 | 2.28
Min. | K | 4.1 | 4.1
Max. | K | 4.5 | 4.5
N. Channels (as per ) | # | 1 | 4
N. Apertures | # | 2 | 1
 | mm | 120 | 40
 | mm | 230 | 230
 | mm | 125 | 125
Parameter | Unit | FCC- hh cryog. report (2024) benchmark | 2D cross section preliminary benchmark
 | m | 4800 | 4800
 | m | 300 | 300
 | bar | 0.817 | 0.817
 | bar | 3 | 3
 | kg/s | 1.1 | 0.58
 | W | 4.5 | 2.28
 | K | 4.1 | 4.1
 | K | 4.5 | 4.5
 | # | 1 | 4
N. Apertures | # | 2 | 1
 | mm | 120 | 40
 | mm | 230 | 230
 | mm | 125 | 125
Reminder of last update from cold mass cooling scheme input parameters:
(Due to single aperture heat load adjustment)

## Slide 29
FCC-hh report
benchmark
2D cross sec.
preliminary
benchmark
Magnet supply
Recooler supply
Gas return
Longitudinal grad. scheme results, from self code: