## Slide 1: HTS simulations
Simulation types:
Stand-alone quench simulations
Ramp up and down simulations
Thermal transient and steady-state sim.
3D HTS Magnets, FE
Types:
Single pancake
Stack of pancakes
Racetrack coils
Existing or planned abilities:
Eddy currents/iron yoke can be included
No/Patrial/Smart/Full Insulation
EE, QH, self-protected, capacitive discharge
Circuit coupling and co-simulation
Simple windings and parts generated parametrically
Complex(-ish) shapes imported from CAD
Very long term – include cables via ROHM/F
Domain Decomposition method to speed up!
Types:
Twisted Stack
CORC
Robel
Simulation types:
AC loss and magnetization
(differential) inductance
current sharing
Existing or planned abilities:
H-phi for tape level solution, potentially thin-shell
CATI method for the cable level solution
ROHM/F for homogenisation at the cable level
ROHM/F for homogenisation at winding cell
Parallel solution (HTCondor) to identify parameters
M. Wozniak, 23.01.2025
HTS Conductors
3D HTS Magnets, Non-FE
(Daniel Mayr, PhD work)
1st year
Full 3D EM calculation accounting for:
Source currents (BS most likely)
Non-linear B-H relation and eddy currents in metal structures (some hybrid method that combines BS with a method that can deal with iron, eddy currents, like BEM-FEM, VIM. It is too early to say exactly but it will be not just standard 3D FE with meshed air)
2nd year
Include analytical ROHM/F to deal with single tape and cable-based magnets.
Keep ability to have iron and eddies.
Rely on CATI to precompute ROHM/F homogenization parameters for a given HTS conductor.
3rd year
Study new protection methods, like CD, ESC, etc. applied to HTS magnets
Verify against other codes
Validate against measurements!