## Slide 1: Top-up injection performance between GHC and LCC
Sen Yue (SY-ABT-BTP)

## Slide 2: Injection settings for GHC and LCC
Lattice version: GHC V25.3.1
Injection setting for pure on-axis injection
  Optics at injection point:
  Energy offset:
Lattice version: LCC V105.0.0
Injection setting for pure on-axis injection
  Optics at injection point:
  Energy offset:

## Slide 3: Momentum acceptance
Momentum acceptance with only considering quantum SR
  LCC has larger momentum acceptance
Hybrid on-axis and off-axis injection
  Relation between energy offset and betatron offset:
GHC_V253.1
LCC_V105.0
Geometrical condition:
  5 sigma beam size
  2.8mm septum blade

## Slide 4: Tracking setting
Tracking setting:
  Lattice from acc-models-fcc-ee
  Only consider quantum SR
  Particle number of Injected beam: 1000
  Turns: 5000
Injected beam distribution
  X-Y coupling is kept
  Horizontal dispersion is removed
  Z- relation is removed
Injected beam orbit
  On-energy parameter:
    Strong nonlinear effect at injection point in GHC
GHC lattice
LCC lattice

## Slide 5: Injection efficiency -- GHC
Good injection efficiency for pure on-axis injection
  energy offset = 0.95%
Also good for some hybrid injection schemes
  energy offset: 0.5 - 1%
Impossible for pure off-axis injection
  According to MA, injection efficiency should not be 0 ?

## Slide 6: Injected beam evolution-- GHC
Best injection efficiency when
  Horizontal emittance blow-up still happens
Vertical emittance blow-up was observed when injected beam close to MA border
  Starts increase from , and larger when reduces

## Slide 7: Beam evolution-- GHC

## Slide 8: Injection efficiency -- LCC
Good injection efficiency for pure on-axis injection
  energy offset = 1.12%
Also good for some hybrid injection schemes
  energy offset: 0.7-1.2%
Possible for pure off-axis injection
  The injection efficiency looks not high enough: less than 80%

## Slide 9: Injected beam evolution-- LCC
Best injection efficiency when
  Horizontal emittance seems good
Vertical emittance blow up happens when close to the MA border
Injection efficiency for pure off-axis injection is less than 80%
  Still vertical emittance blow up but not that large

## Slide 10: Beam evolution-- LCC
In LCC, Maximum zeta offset is ~0.12 m when
In GHC, Maximum zeta offset is ~0.15 m when

## Slide 11: On-axis injection comparison
Injection setting
  GHC: , LCC:
GHC has evident horizontal emittance blow up
GHC has smaller energy offset but larger longitudinal emittance
LCC
GHC

## Slide 12: Hybrid injection with matched injected beam
Requirements for hybrid injection
  Relation between energy offset and betatron offset:
Possible for hybrid injection with the matched injected beam but less margin
Geometrical condition:
  : 5 sigma beam and 2.8mm septa
  is the increase part of the injected beam size
GHC_V253.1
LCC_V105.0

## Slide 13: Hybrid injection with shared oscillation
Reduce energy/betatron offset by introducing circulating beam oscillation
  Unchanged relation between circulating and injected beam:
      Injected beam oscillation:
      Circulating beam oscillation:
[1]
[1] Injection Status and Issue of SuperKEKB
Geometrical condition:
  : 5 sigma beam and 2.8mm septa
  increase of matched injected beam size
  reduction due to shared oscillation
GHC_V253.1
LCC_V105.0
May need to adjust the filling scheme since only inject 10% bunch

## Slide 14: Conclusion
Pure on-axis injection
  Good injection efficiency is achieved in both GHC and LCC
Hybrid on-axis and off-axis injection
  GHC: energy offset should be 0.5 - 1 %
  LCC: energy offset should be 0.7 -1.2% % or around 0
  It’s possible for LCC to switch to off-axis injection but not for GHC
It’s possible to use the fully matched injected beam in hybrid injection but less margin in MA
  For both GHC and LCC
Top-up injection with shared oscillation
  Can increase the space for on-axis/off-axis/hybrid injection
  Reduce the oscillation amplitude
  Need to study the influence on the circulating beam

## Slide 15: Conclusion of Lattice comparison report
Collider injection
  Injection efficiency: 100 % for both GHC and LCC
  orbit bump: not feasible for LCC, but is fine for 4 orbit bump
Collider extraction
  FSR has studied that of GHC
  The distance difference of extraction location between GHC and LCC is ~ 100m
  TL is more than 1000 m and should have minimum influence on the dump absorber location
Beam transfer from booster to collider
  GHC: booster extraction point at section center
    Positron and electron beam could share the same kicker
  LCC: booster extraction point at both section sides
  Common: Separate H&V deflection, similar TL length

## Slide 16: Back-up: Evolution-- LCC

## Slide 17: Back-up: Evolution-- LCC
Pure off-axis injection

## Slide 18: Back-up: Evolution-- GHC