## Slide 1: Novel energy-sensitive x-ray cameras, record fusion-plasmas, real-time monitoring and the need of radiation-hardened detectors
L. F. Delgado-Aparicio1, T. Barbui1, R. Barnsley2, D. Vezinet3, R. Dumont4, N. Fedorczak4, J. Morales4, T. Fonguetti4, P. Manas4, S. Mazzi4, X. Litaduon4, F. Imbeaux4, K. Hill1, M. Bitter1,
N. Pablant1, J. Wisniewski1, B. Luethi5, M. Rissi5, T. Donath5, L. Glatt5, P. Hofer5, and N. Pilet5
1 Princeton Plasma Physics Laboratory, Princeton, NJ, USA
2 ITER Organization, Saint-Paul-les-Durance Cedex, France
3 Commonwealth Fusion Systems, Devens, MA, USA
4 CEA, IRFM, Saint-Paul-les-Durance Cedex, France
5 DECTRIS Ltd., 5405 Baden-Dattwil, Switzerland
DRD3
Amsterdam, Netherlands
Tuesday, June 3rd, 2025

## Slide 2: Agenda
PPPL Advisory Board, November 14-15th, 2023
Long Pulse Operation (LPO) and example @ WEST
X-ray spectroscopy and tomography…back to the basics!
WEST and challenges of multi-energy program
Few results and physics
Eight drivers for the future…
Summary

## Slide 3: Long pulse operations (LPO) open a new era of expertise, training (e.g. physics and engineer) & collaborations
WEST, KSTAR, EAST & W7X… JT-60SA
*Pulsed machines
*

## Slide 4: Long pulse operations (LPO) open a new era of expertise, training (e.g. physics and engineer) & collaborations
tMHD ∼ 1 − 100 μs
tELM ≲ 1 ms
tUFO ~ 20-50 ms
tTransport ~ 1-20 ms
tE ∼ 50-70 ms
tEx:e,i ∼ 250 ms
tIp ∼ 100 s
tPMI ∼ 100’s s
Long pulse operation (LPO) redefines all our diagnostic timescales over eight-nine orders of magnitude
×(108-109)
March 2024

## Slide 5: Diagnostic community continues exploring innovative x-ray techniques for fusion power plants (FPPs)
PPPL Advisory Board, November 14-15th, 2023
Important % of the Pin is lost as radiation (~50%).
Prad,X is subset of Prad … high as 50-90%
Easier to get the signals out than the visible range !!!
X-rays: dominant source of radiation (hn=hc/l~Te):
100 eV<Te<20 keV ⇒ 0.5 Å < l <130 Å ⇒ X-rays!
20 keV< Ee< 200 keV ⇒ SXR to HXR
Measurement of Prad,x will enable:
⇒ Emiss[ph/cm2s, W/cm3], ne, nZ, Te, TZ, Vf, Vq & nRE
Engineer challenges: Ensure vacuum compatibility and in-situ calibration
⇒Important technological & engineer development

## Slide 6: Take home message: three x-ray concepts to remember!
#1: X-ray imaging crystal spectrometer

## Slide 7: Take home message: three x-ray concepts to remember!
#2: X-ray tomography
#3 Multi-energy x-ray imaging

## Slide 8: Conventional SXR tomography helps to study MHD: e- and ion fishbones

## Slide 9: Conventional SXR tomography helps to study MHD: (1,1) kinks, islands and LLMs
Raw DATA
DATA + reconstruction
Time history of mode-formation

## Slide 10: Conventional SXR tomography helps to study transport: particle (ne) and medium- to high-Z (nZ)

## Slide 11: Long pulse operation (LPO) at the WEST tokamak At CEA in France – next to ITER
Toroidal magnetic field
Bf~3.7 Tesla
Superconducting coil temperature @ 1.8 K (-271.4°C)
Plasma major radius
R0~2.5 m
Minor radius: a~5 m
Plasma volume: 18 m3
Plasma current <1 MA
Additional heating power: 15 MW
Plasma temperature
10-100 Million °C
Max plasma duration
1000 seconds
Task:
Measuring tens of million °C near the absolute zero!

## Slide 12
WEST is covered with tungsten plasma facing components (W-PFCs)

## Slide 13: GOALs for novel multi-energy technology
RT-centroid (R0, Z0) & shape (Y) through Shafranov-shift (DSS)
Detection & ID of UFO injections which impact performance
nZ & DZeff bracketing line radiation (BB)
Te & ne2Zeff sampling continuum (FF + FB)
ne,nM (e.g. ECCD, LHCD, runaways)
Real time and control
~exp(-E/Te)
EXAMPLE: no line-emission
(slope of continuum emission is ∝ Te or ne,fast)
Intensity ∝ nW
~exp(-E/Te)
0.1
10
Te
[keV]

## Slide 15: Novel x-ray detectors enable breakthrough of 100k pixels (minimum) at multiple energy ranges from 2-100 keV
“Constant” width of electronic response is a great improvement over the use of filters
New technology: electronics
EW~500 eV
Old technology: metal filters

## Slide 16: Novel x-ray detectors enable breakthrough of 100k pixels (minimum) at multiple energy ranges from 2-100 keV
Operates in single photon counting mode
CMOS hybrid pixel technology
developed originally for synchrotrons
CMOS
readout chip
Si-sensor
2D array pn diodes
In
balls
The comparator voltage of the readout chip (Vcmp) controls the global threshold energy.
The threshold energy can be individually refined/trimmed using and in-pixel 6-bits DAC (Vtrim).
2012
2024
technology

## Slide 17: Smart pixel-technology allows filtering spectra to measure line-emission and/or the continuum
2012-2016
2017 - nowadays
2018 - nowadays

## Slide 18: Main diagnostic challenge at WEST is to disentangle nW and Te-effects in recorded spectra
PPPL Advisory Board, November 14-15th, 2023
Zoom
“Smart” pixel
configuration

## Slide 19: Main diagnostic challenge at WEST is to disentangle nW and Te-effects in recorded spectra
PPPL Advisory Board, November 14-15th, 2023
“Filtering the spectra”

## Slide 20: Long pulse operations (LPO) open a new era of expertise, training (e.g. physics and engineer) & collaborations
Typical “1-min” shot
Hot temperature branch @ 4-5 keV with density nearly a factor 2 compared to its predecessor
Non-inductive (Vloop → 0) long-pulse discharges with no external input torque and particle source
Resilience to tungsten UFOs and an improved L-mode confinement (H98y,2 ∼ 1.0, bp∼1.6 & bN∼0.7) lasting 6 mins
Without W-wall conditioning and using a total of 1.146 GJ of injected energy.
March 2024

## Slide 21: Tungsten multi-energy brightness and emissivities measured for the first time at WEST
Line-integrated brightness
Local reconstructed emission
ToFu
ToFu

## Slide 22: Core multi-energy (ME) fits capture the Maxwellian part of the electron energy distribution function
⇒Te,0 ✓
Typical “1-min” shot
⟨Zeff⟩~2.2, Te,0~4.5 keV and H98y2~1
⟨Zeff⟩~2.7, Te,0~4.1 keV and H98y2~1.05
Notes: 7-point fit Te,0 measurement
Uncertainty: ±2%

## Slide 23: Driver #1: Demonstrated technology enables different options upon arrangements of threshold energies
Driver #2: Constrain W-transport physics in SS without perturbative experiments regardless of H & CD
Driver #3: Provide internal non-magnetic measurements to constrain equilibria: R0, Z0 and DSS
Driver #4: Constrain W-transport asymmetries with rotation or ICRH heating (V⊥ vs V|| effects)
Driver #5: Resolve fast-electron anisotropies from ECRH, LHCD, fast e- losses and runaway electrons
Driver #7: Adopt new technology with 4+ thresholds per pixel & RoI sampling (from 0.5 to 100 kHz)
Driver #8: All the above + DD&DT neutrons and g’s
Driver #6: Develop real-time capabilities

## Slide 24: Driver #1: Demonstrated technology enables different options upon arrangements of threshold energies
PPPL Advisory Board, November 14-15th, 2023
In rows: good spatial resolution
In columns: higher spatial resolution
“Meta”-pixel: 2D distribution
1D
1D
2 keV
4 keV
3 keV
5 keV
4D (x,y,t,E)

## Slide 25: Driver #6: Develop real-time capabilities <Te,0>L & Z0
New
results
March
2025
Real-time
Fr=10 Hz
± 0.2 keV
Sub-cm

## Slide 26: Driver #6: Develop real-time capabilities <Te,0>L & Z0

## Slide 27: Driver #7: Adopt new technology with 4+ thresholds per pixel & RoI sampling (from 0.5 to 100 kHz)
2012
2024
technology
2024
+
technology

## Slide 28: Driver #8: Develop radiation-hardened sensors and electronics for DOE labs, universities & private sector
Main issues: circumvent gamma- and neutron-induced noise, T- and B-limitations, as well as define LIFETIMES!
Si-detectors:
Used due to the availability of good quality homogeneous material and high charge carrier transport properties. Can only withstand 1012-1013 neq/cm2.
Lifetimes shortened:
  neutron damage
  Survivability at high temperatures
Forced to look for new solutions compatible with CERN’s very-high-luminosity experiments (up to 1016-1017 neq/cm2 ???).
ITER
DT

## Slide 29: Driver #8: Develop radiation-hardened sensors and electronics for DOE labs, universities & private sector
“Meta”-pixel
2 keV
4 keV
3 keV
5 keV
Neutron-flux for JT-60SA DD and SPARC- and ITER-DT scenarios can be as high as 1019-1020 n/s
ALARA: As Low As Reasonably Achievable
1 MW of DT neutrons: ~4.4×1017 n/s
For d=15 m ⇒ Fn ~ 1.5×1010 n/cm2/s
Dt=5-10 s ⇒ ~ 1011 n/cm2/shot
Si fluencemax ~ 1012-13 n/cm2/MeV
SPARC
DT
4D (x,y,t,E)

## Slide 30: ∴ Find synergies between fusion energy science (FES) and high-energy physics (HEP) communities
Semiconductor detectors will be exposed to hadron fluences to more than 1016 neq/cm2 (HL-LHC, 2024-26) and more than 7x1017 neq/cm2 (FCC, >2035)
Aiming at neutron hardness ≳1016 neq/cm2
Compare standard Si with: a) electrode configs. (e.g. Si3D), b) enrichment techniques (e.g. H, C, O, N, Ga) or c) other materials (e.g. Si vs Diamond±N, SiC, GaN, AlN, GaAlN, for high-T)
Radiated power, UV, low-, medium- and high-E x-rays and neutrons!!!
Applications for ultra-thin 3D silicon detectors:
Neutral particle analyzers (NPA)
Fast-ion loss detectors
UV and x-ray spectroscopy
BENEFIT: 100% detection efficiency and low sensitivity for the (n,g) background

## Slide 31: and… now we also have a wealthy private sector!!!
Tokamaks
MCF
Stellarators
FRCs
Mirrors
Other
ICF
Laser
Other

## Slide 32: Summary
With the selection of W for modern machines, understanding the sources, transport and confinement of high-Z impurities is crucial to SPARC and ITER success.
Prad ≳ ½ Pinput and Prad,X ≲ 90% Prad
Modern x-ray diagnostics help us probe: nZ, Te,i, Vf,q, Zeff & ne,fast and their profiles!
Urgent need of rad-hardened sensors (e.g. UV as well as soft & hard x-rays) !!!
Need better neutron monitors for DD and DT (2.5 vs 14.1 MeV): flux and spectra!!!
Now we have a private sector !!!