## Slide 1: Execution of large- scale projects in regards to logistic potentials
DI(FH) Robert Goliasch Business Unit Manager Plant & Equipment
© STRABAG, MAY 2025

## Slide 2: Content
  Project Overview
  North Yorkshire Polyhalite Project
  Rail-bounded Logistic
  Conveyor System
  Shaft System
  Koralm Tunnel LOT 2
  Shaft Logistic
  Conveyor System
  Logistic Concept
  Material Processing
  Summary

## Slide 3
  Division 3I Tunnel Construction & International:
  Austria/ Germany/ Switzerland
  Canada
  International Projects
  Membrane Department
  600+ colleagues
  Highlights:
  50+ years of experience
  worldwide projects
  sustainable
  innovative spirit
  trust & respect
Projects of STRABAG – ZÜBLIN; Division 3I
Koralm Tunnel - AT
York Potash - UK

## Slide 4: North Yorkshire Polyhalite Project
  Project Data:
  Mining the largest polyhalite deposit to produce fertilizer
  2018 – ongoing
  37km long segment lined tunnel
  6m TBM cutting diameter
  service – to deliver polyhalite from the mine to port facility
  Most Significant Challenges:
  geotechnically – 4 intersecting faults
  groundwater flows
  environmental sensitivity – Border of National Park, groundwater connection to local beck
  Tunnel logistic - from one portal and through shaft structures

## Slide 5: Rail-bounded logistic for 37km TBM-Tunnel
  Rail-bounded Logistic:
  37km long
  up to 4% gradient
  900mm track gauge
  One train about 180ton gross weight, rail-bounded with best resistance
  services – transport of segments, rail sets, consumables and staff
  Highlights:
  Use of California Crossings – for train crossings in single-lane tunnel
  Battery & plug-in-hybrid Loco’s - with recuperation while downhill drive
  Optimised ventilation – due to use of battery driven equipment
  Rescue train - parked on California-crossing at the rear end of the TBM
  Cycle times – every train is timed after TBM-production

## Slide 6: Conveyor System for 37km TBM-Tunnel
  Conveyor System:
  37km long
  208m height difference
  services – excavation material transport
  Most Significant Challenges:
  length & height – 4 booster stations needed
  space – little space to ventilation, train, survey window
  belt tension – complex measuring and adjustment

## Slide 7: INTERMEDiATE Shaft aditS
  Completed Shaft via Blind Boring:
  380m deep
  3.2m diameter
  services - ventilation, grout, power, water, elevator
  access - 12.8km/ 23km from tunnel entry point
  Most Significant Challenges:
  schedule – ventilation and power supply on TBM critical path
  groundwater flows – 2 unsuccessful grouting programmes previously
  connection tunnels – with drill and blast method

## Slide 8: Koralm tunnel Lot 2
Weststyria neogene
Lavanttal fault
Lavanttal neogene
Wolfsberg
Deutschlandsberg
Crystalline
Max. overburden: 1200 m (3937 ft)
  Project Data:
  Project of ÖBB Infrastructure, Twin Tunnel for High Speed Rail in Austria
  2011- 2021 – construction period Lot 2 - operation will start in Q4.2025
  2 x 32,9km lined tunnel – 2 x 19km Lot 2 executed by JV STRABAG-Jäger Bau
  8,6mio ton excavation material

## Slide 9: Shaft logistic
  Shaft structure, Conventional Excavation:
  60m deep
  700m² outbreak area of twin shaft structure
  services - ventilation, grout, cables, concrete, vertical conveyor with excavation material and segments
  Most Significant Challenges:
  sequence – of gantry cranes for TBM, D&B, concrete operations
  gantry cranes – 2 x 60ton + 2 x 35ton gantry cranes with recuperation
  vertical conveyor – 2 x vertical conveyors for TBM muck transport 1000ton/h

## Slide 10: Logistic Concept
  Logistic Concept:
  national train connection – for cement, pea gravel and excavation material
  tunnel train – transport of segments, back filling, consumables and staff
  gantry cranes – transport trough the shaft into the tunnel and on surface
  Highlights:
  75km – of railbounded logistic – 2 rails per tunnel
  120.500 – segments fabricated on site
  1,2mio ton - excavation material transported by train according to contract
  75% - of cement and pea gravel to be delivered by national train system

## Slide 11: Conveyor System
  Conveyor system:
  44km long
  1000ton/h / 2000ton/h design capacity
  services – excavation material transport
  Highlights:
  2 x vertical conveyor – in shaft
  belt scales – no. 15 scales used to record all material flows just in time
  dispose – of material flow from central control room
  sustainability – very economic and efficient way of mass transport

## Slide 12: Material processing – overall flow chart
gravel storage/ crushing plant
batch plants/ segment production
railway loading facility
screening plant
external peagravel delivery
TBM drive

## Slide 13: Material processing – Crushing process, plant overview
  Highlights:
  300 ton/hr – plant production capacity
  550.000 ton excavation material – reused in 3 years for segment production
  app. 600.000 ton excavation material – reused in 4 years for concrete lining
aggregate processing plant
aggregate silo and storage
Transfer to batch plant
  Material Crushing Process:
  pre-screening plant – integrated in conveyor system
  aggregate processing plant – just in time production of concrete aggregates from TBM excavation material
  three stage crushing plant and wet sieving process due to challenging crystalline geology

## Slide 14: Summary
Challenging Interface TBM drive and D&B method
Sustainable Concepts – Locos & Gantry Cranes
Complex Conveyor Systems
Supply Shafts
Focus on Site Process Sequence
Muck Material Processing
Focus on Logistic Tasks
Ventilation
Power and Water supply for Construction Phase