## Slide 1: Future High-Energy Collider Projects
Part 2
Roderik Bruce

## Slide 2: Outline
Introduction
  Considerations for collider design: particle type, energy, circular/linear…
  Limitations for future colliders
  European strategy for particle physics
ILC (International Linear Collider)
CLIC (Compact Linear Collider)
HL-LHC (High-Luminosity Large Hadron Collider)
FCC-hh (Future Circular collider, hadrons)
FCC-ee (Future Circular collider, e+e-)
CEPC/SppC (Circular Electron-Positron Collider / Super proton-proton Collider)
Muon collider
First lecture
Second lecture
Linear
Circular

## Slide 3
HL-LHC

## Slide 4: Reminder: LHC
27 km synchrotron, built to collide 7 TeV proton beams at 4 experiments
  Largest collider and highest energy to date
About 1 month per year: heavy-ion collisions
About 1200 superconducting dipole magnets (NbTi) with 8.3 T field, operating at 1.9 K
  In total, more than 9000 magnetic elements
Switzerland
France
LHC
CMS
ALICE
LHCb
ATLAS

## Slide 5: LHC layout
8 bent sections, arcs, and 8 straight sections, “insertion regions (IRs)”
4 experiments where beams collide (ATLAS – IR1, ALICE – IR2, CMS – IR5, LHCb – IR8)
2 IRs for beam cleaning (collimation), one for RF, one for beam extraction

## Slide 6: LHC main parameters
Design luminosity of 1×1034 cm-2s-1 surpassed by more than a factor 2
Collected in total more than 400 fb-1 of integrated luminosity at the high-luminosity experiments (ATLAS, CMS)
Parameter | 2025 | Design
Energy [TeV] | 6.8 | 7.0
No. of bunches | 2460 | 2808
p/bunch (typical value) [1011] | 1.6 | 1.15
Max. stored energy per beam (MJ) | 410 | 362
β* [cm] | 60/18 | 55
Typical normalized emittance [μm] | ~1.6 | 3.75
Peak luminosity [1034 cm-2s-1] | 2.2 (lev.) | 1.0
year
Tot. no. events

## Slide 7: HL-LHC
  High-luminosity LHC: Major upgrade of the LHC
  Main goals:
    achieve a total integrated luminosity of 3000 fb-1, a factor ~10 higher than what has been achieved so far since the start of the LHC
    Target an integrated luminosity of ~250 fb-1 per year
    Prepare machine for operation from 2029 and into the 2040's
 | LHC 2025 | HL-LHC
Protons per bunch | 1.6 x 1011 | 2.2 x 1011
Number of bunches | 2460 | 2750
Normalized emittance | 1.6 micron | 2.5 micron
Beta* | 60/18 cm (flat) | 15 cm
Full crossing angle | 320 microrad | 500 microrad
Geometric reduction factor F | 0.6 | 0.35
“Virtual” luminosity | 4.2 x 1034 cm-2s-1 | 2.4 x 1035 cm-2s-1
Levelled luminosity | 2.1 x 1034 cm-2s-1 | 5 x 1034 cm-2s-1

## Slide 8: Compensation of geometric reduction factor
Bunches experience electromagnetic force from the opposing beam at the collision point (head-on beam-beam) or nearby in common beam pipe (long-range beam-beam)
  Need crossing angle, not only to avoid parasitic collisions
Crossing angle at HL-LHC must be larger than at LHC, due to higher intensity
  Would cause very large loss in luminosity: F≈0.35
To compensate: use “crab cavities” that tilt the bunches longitudinally and ensure overlap at the collision point
Long-range
Head-on

## Slide 9: Crab cavities
Create a oscillating transverse electric field
Kick head and tail of the bunch in opposite directions

## Slide 10: HL-LHC interaction region
For smaller β*: need new triplet
All magnets and other equipment in IR1 and IR5 to be completely exchanged for HL-LHC

## Slide 11: Comparison: LHC triplets

## Slide 12: Luminosity leveling
Experiments can only cope with a certain maximum event rate before saturating
In LHC and HL-LHC, the achievable peak luminosity gives a significantly higher rate
Solution: artificially reduce luminosity to stay within limit of experiments – ”leveling”
  Can be done by changing offset between beams, β* (beam size – chosen option in HL-LHC) or crossing angle
Separation
leveling
β*-leveling

## Slide 13: Collimation and machine protection
Losses from the beam are inevitable, and could cause magnet quenches or even damage
With higher intensity in the HL-LHC, need to enforce machine protection
New collimators to be installed to better protect the machine
680 MJ =
Total energy in one HL-LHC beam =
kinetic energy of TGV train at 215 km/h

## Slide 14
FCC-ee

## Slide 15: Reminder: European strategy 2020
European strategy: “An electron-positron Higgs factory is the highest-priority next collider”
European strategy: “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. “

## Slide 16: FCC integrated program
FCC-ee
FCC-hh
stage 1: FCC-ee circular e+e- collider Higgs factory, but several other operational energies for different physics programs
stage 2: FCC-hh circular hadron collider (~100 TeV) as natural continuation at energy frontier, proton and ion collisions
Re-use the same civil engineering, build on CERN’s existing infrastructure

## Slide 17: Current working hypothesis on FCC placement
Overall layout and placement optimisation process: Many options being studied
Current baseline position based on:
  lowest risk for construction, fastest and cheapest construction
  feasible positions for large span caverns (most challenging structures)
  Total length is 90.7 km
  8 surface sites with few ha area each

## Slide 18: FCC-ee layout
Double ring collider with 8 straight sections
  4 collision points
  4 technical insertions for RF, beam dump, collimation
FCC-ee

## Slide 19: FCC-ee accelerator complex
Injector complex
  Electron & positron source, linacs for e- and e+, damping ring, high-energy linac to 20 GeV.
  On CERN Prevessin site
High Energy Booster (HEB)
  Additional ring installed on top of the collider with same circumference, 1.03 m vertical separation.
Collider
2025 DESIGN
F. Carra et al.
Collider
Booster

## Slide 20: FCC-ee operation modes
4 different operational energies are foreseen to perform precision measurements of Z, W and H bosons and the top quark
  Z-pole: 45.6 GeV
  WW pair production threshold: 80 GeV
  ZH production peak: 120 GeV
  ttbar production threshold: 182.5 GeV

## Slide 21: FCC-ee parameter table
parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340-350 | 365
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 70 | 64
total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 144 | 20 | 7.5 | 1.8 | 1.4
luminosity / year [ab-1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
total integrated luminosity [ab-1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
total number of events | 6 1012 Z | 2.4 108 WW (incl. WW at higher √s) | 2.2 106 ZH 65k WW → H | 2 106 + 370k ZH + 92k WW → H | 
parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340-350 | 365
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 70 | 64
total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 144 | 20 | 7.5 | 1.8 | 1.4
luminosity / year [ab-1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
total integrated luminosity [ab-1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
total number of events | 6 1012 Z | 2.4 108 WW (incl. WW at higher √s) | 2.2 106 ZH 65k WW → H |  | 
M. Benedikt

## Slide 22: FCC-ee operational sequence
Flexible sequence Z – W - H

## Slide 23: Luminosity comparison
To reach the physics goals, need to significantly increase luminosity w.r.t. previous lepton colliders
Can reach higher luminosity than linear colliders at lower energy
  The higher the energy, the more severe limitations from synchrotron radiation

## Slide 24: Synchrotron radiation in FCC-ee
Design choice: limit radiation power to 50 MW per beam (still huge!)
  RF cavities have a certain (in)efficiency  total RF power consumption for both beams up to about 160 MW
  Lower intensity at higher energy => lower luminosity
  Not critical for cooling – normal-conducting magnets
At highest energy, 182.5 GeV, loss of 9 GeV or ~5% per turn
  Also: particles that have lost energy are overbent by the dipoles => accumulate large transverse offsets, “saw tooth” orbit if nothing is done
Example horizontal orbit with radiation
B. Härer, A. Doblhammer, and B.J. Holzer, IPAC16, THPOR003

## Slide 25: Tapering
  To avoid large transverse offsets due to over-bending: “Tapering scheme”
  Vary magnetic strengths along the ring, so that we always match the beam energy
No tapering (note: positive energy offset)
Tapering: adjusting magnetic field to beam energy
B. Härer, A. Doblhammer, and B.J. Holzer, IPAC16, THPOR003

## Slide 26: Beamstrahlung
Particles radiate not only in magnets, but also due to electromagnetic field of opposing beam: “beamstrahlung”
FCC-ee will be the first collider where beamstrahlung plays a significant role in beam dynamics
  Collider must have sufficiently large momentum acceptance to hold a particle that loses its energy in a single photon emission due to beamstrahlung.
    A particle with 2% momentum deviation must still stay within the beampipe without touching it
Power of radiated photons reaches almost 400 kW – big engineering challenge!
  Photons hit downstream vacuum chamber in localized spot – engineering challenge to dispose of heat without material damage
  Different solutions under study: solid graphite absorber (might break), absorber with flowing liquid Pb
`
M. Calviani et al.

## Slide 27: FCC-ee power consumption
FCC-ee elecrtical energy consumption | Z | W | H | TT
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Peak power during beam operation [MW] | 250 | 275 | 297 | 381
Total FCC-ee yearly consumption [TWh] | 1.2 | 1.3 | 1.4 | 1.85
Power consumption dominated by RF
Total increase of power usage compared to LHC
Load to be distributed on three main sub-stations – concept confirmed with French electricity grid operator
Notes: Yearly consumption about 1.9 TWh (compare 1.2 TWh for CERN in 2016)

## Slide 28: Overall FCC timeline
Foreseen FCC timeline spans several decades
Remember: it took ~25 years from the start of the LHC design to the start of operation
2100?

## Slide 29: FCC documentation
FCC-Conceptual Design Reports (completed in 2018):
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 , EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382
Feasibility study report prepared for 2025, as input to European strategy
  Volume 1: Physics and Experiments is here
  Volume 2: Accelerators, technical infrastructure and safety is here
  Volume 3: Civil Engineering, Implementation and Sustainability is here

## Slide 30
FCC-hh

## Slide 31: FCC-hh general goals
European strategy: “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. “
FCC-hh: collide 42 (or up to 60) TeV protons (or heavy ions of equivalent magnetic rigidity)
  Factor ~6-8.5 higher energy than LHC, factor ~3 longer tunnel
  International FCC collaboration (CERN as host lab)
More than an order of magnitude higher peak luminosity than LHC; factor 6 higher than HL-LHC
Goal: Achieve integrated luminosity of 20 000 fb-1 per experiment collected over 25 years of operation (vs 3000 fb-1 for HL-LHC)

## Slide 32: FCC-hh layout
Insertions in FCC-hh
  Two high-luminosity experiments (A and G)
  Two other experiments (D and J)
  Two collimation insertions (F and H)
  One extraction insertion (B)
  One RF insertion (H)
Considered injector options
  New superconducting machine in the SPS tunnel
  modified faster-ramping LHC
  new 4 T machine in the LHC tunnel
  new 2 T superferric machine in the LHC tunnel

## Slide 33: FCC-hh parameter comparison

## Slide 34: FCC-hh magnets
Need 14-20 T dipole magnets – not feasible with today’s technology  big challenge for technological development!
  In LHC, 8.3 T, with NbTi superconductors
  Cannot to much higher with NbTi: need working point below “critical surface”
Rely on future developments of Nb3Sn superconductor technology
Alternative: high-temperature superconductors
  Could achieve higher fields and lower power consumption
  Significant technology development and cost reduction needed
Critical surface
for NbTi

## Slide 35: High-field magnet research
HTS R&D in various domains:
REBCO and IBS Conductor R&D
racetrack coil developments
Nb3Sn:
12- and 14-T short demonstrators
different coil geometries
tests scheduled for 2026

## Slide 36: Next challenge: FCC-hh machine protection
HL-LHC: total stored energy of beam = 680 MJ = kinetic energy of TGV train cruising at 215 km/h
FCC-hh: : total stored energy of beam = 8.3 GJ = kinetic energy of Airbus A380 (empty) cruising at 880 km/h
Big challenge: Protect the machine against beam losses –
need very efficient collimation system

## Slide 37: Beam dump
Need beam dump to safely extract and dispose of beam in case of any failure, or the remaining beam a the end of luminosity production
  Extract beam in separate dump channel using very fast dipole magnets
Need to dispose of 8.3 GJ!
  Enough to drill 300m long hole in copper
FCC-hh CDR

## Slide 38: Beam dump
Solution: as for LHC, distribute (“paint”) beam transversely, but over much larger surface than in LHC
  Dynamically changing magnetic field while beam is passing
  Beam-dump made of low-density graphite sheets, should not exceed 1500 deg C
LHC pattern (same scale)
1m
D. Schulte, W. Bartmann

## Slide 39: Synchrotron radiation in FCC-hh
FCC-hh first hadron collider where synchrotron radiation power has potentially limiting effects
  About 5 MW power loss per beam, lost continuously around the ring!
Need about 12 MW of RF power per beam to replenish lost energy
Need to cool away the 5MW heating power of lost photons around the ring
  Special beam screen design to intercept photons in a slit

## Slide 40: Electron cloud effects
Electrons inside vacuum chamber accelerated by field from passing bunch
Electrons hit inside of vacuum chamber, releasing more electrons, in turn accelerated => ever increasing cascasde of electrons
Causes heating, potential beam instabilities, worse vacuum...
Big challenge for LHC, even more for FCC-hh
Mitigations:
  Beam screen design, surface treatment, coatings
  If nothing else helps: increase spacing between bunches
a-C
LESS
G. Iadarola
Notes: Laser ablation surface engineering (LASE), or laser-engineered surface structures (LESS) are techniques that can be applied to the beam-facing surfaces of the beamscreen in order to mitigate the electron cloud

## Slide 41
CEPC / SppC

## Slide 42: CEPC (Circular Electron Positron Collider)
Chinese proposal for e+e- collider 90-240 GeV, 100 km ring
Four operation modes: H, Z, WW, ttbar
Two collision points, two RF insertions
Limit synchrotron radiation power to 30 MW per ring, option to go to 50 MW

## Slide 43: CEPC parameter table
More details technical design report , 2023

## Slide 44: SppC (Super proton-proton Collider)
100 km hadron collider to later be installed in the same tunnel as CEPC
Design report scenario:
  use 12 T high-temperature iron-based superconductors for high field dipole magnets => centre of mass energy of 75 TeV
  “ultimate” upgrade: 24T field, 150 TeV CMS energy
  Operating at 4.2 K
  Luminosity of 1035 cm–2 s–1
Baseline layout with 8 insertions for experiments, collimation, extraction, injection, RF
conceptual design report in 2018

## Slide 45
Muon collider

## Slide 46: Muon collider study
Could use heavier leptons than e+e- to minimize synchrotron radiation in a circular lepton collider
  Could reach much higher energy than with e+e- for the same radius, still with “cleaner” collisions than protons
  Or reach similar energies with a much smaller machine  cost- and energy-efficient
Use muons?
  mass = 106 MeV/c2 = 207 me
  Challenge 1: Unstable, 2.2 μs mean lifetime
    Need to very quickly accelerate them to high energy – with time dilation, factor γ longer lifetime
  Challenge 2: experimental backgrounds due to e+ and e- from muon decay
  Challenge 3: abundant neutrinos from muon decay could reach surface and interact, causing radiation
Production of muons – presently considered option:
  Let high-power proton beam hit a target
  Pions are produced, which later decay into muons
  Muons have relatively large transverse momentum spread  need to very quickly "cool" them to achieve small beam size for higher luminosity
    Challenge 4: very fast cooling of muon beam
protons
target
Many particles,
including π+, π-
Notes: At 5 TeV, gamma = 47322, mean lifetime is 95 ms
Muons should last about 1000 turns in main ring, I.e. ~30 ms. Lifetime at top energy is 95 ms for 5 TeV beams (10 TeV CMS)

## Slide 47: Muon collider concept
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
D. Schulte
Muon collider design studies ongoing in international collaboration
A lot of advancement lately, many challenges remain

## Slide 48: Summary
LHC will be upgraded to HL-LHC, and operate to ~2041
  Future collider projects on the table, but no decision yet
Main projects studied at CERN
  FCC-ee: circular e+e- collider
    e+e- Higgs factory is highest priority it European strategy
    Feasibility study report prepared as input to next European strategy
  FCC-hh: circular pp collider with ion option
    Second stage after FCC-ee
  CLIC: Linear e+e- collider
    Also fulfills priority on a Higgs factory in European strategy
    Conceptual design report exists, technology and concept demonstrated
  Muon collider: potential for high-energy circular lepton collider without radiation limitation, very challenging
  Other projects: LEP3, LHeC, …
  All machines have many interesting beam physics aspects and difficult challenges – I could cover only a few!
Initiatives in other parts of the world
  ILC: Linear e+e- collider, possibly hosted by Japan
    Mature design with technical design report; ready to be built. Awaiting political decisions
    Alternative placement at CERN under study
  CEPC / SppC: circular e+e- collider followed by hadron collider, Chinese initiative
    Technical design report exists. China will decide
  EIC: circular electron-ion collider, to be built in the US
    Approved project with conceptual design report

## Slide 49: Future colliders?
Particle collisions 50 years ago
Particle collisions today
Particle collisions in 50 years
574 TeV Pb beams colliding at ALICE, LHC
32 cm bubble chamber with liquid hydrogen, 16 GeV pion interacting with proton
https://cds.cern.ch/record/39474
We know only that we will need scientists and engineers to design, operate and optimize the machines, and to analyze the data