## Slide 1: Optics Update
HEMAC Meeting, 18/02/2025
L. Soubirou, A. Chance

## Slide 2: Recap and overview
Last update : Milestone n°5 (11/2024). Unrealistic QP gradient and very big apertures (>100mm for RCS 1&2 of Greenfield)
Work on different cell types :
  Normal FODO
  Hybrid FODO
  Combined function magnets (for normal RCS only)
Focus on feasibility (QP gradients, magnet lengths) and optimization towards minimization of the magnet apertures
  Beam size dominated by dispersion => focus on minimizing Dx .
Study for Greenfield and CERN-siting

## Slide 3: Types of cell
QP NC Foc
QP NC Defoc
DIPOLES
DIPOLES
QP SC
Defoc
QP SC
Foc
Lcell
QP NC Foc
QP NC Defoc
DIPOLES
DIPOLES
« Normal » FODO
« Hybrid » FODO
Interconnexion length
Insertion
DIPOLES
kf
Insertion
DIPOLES
-kd
Lsss
Combined Functions

## Slide 4: Normal and Hybrid FODO cell
« Normal » FODO (normal conducting QP):
  Old approach: minimizing total length of QP.
    Unrealistic gradient + aperture too large
  New optimization approach: QP occupy the maximum total length possible and we see « the best we can do » at minimizing Dx -> highlight limitation of normal FODO cells.
  Constraints : Bpole, QP NC < 1T, Ldip, SC > 2m, aperture margin (diam) Δx=20mm
« Hybrid » FODO (normal and superconducting QP) :
  Same approach: NC QP + SC QP at maximum occupancy
  Constraints : Bpole, QP NC < 1T, GQP, SC < 400 T/m, Ldip, SC > 2m, Lquad, SC/NC > 0.75m,
  aperture margin (diam) Δx=20mm

## Slide 5: Combined Functions magnet cell
Configuration only studied for normal RCS.
Goal : minimizing Dx.
Parameter to be optimized :
  Bending field Bbend, inj and Bbend, ext
  Phase advances µx and µy (or equivalently quadrupolar strength kf and kd in dipoles)
Constraints :
  Bpole = Bbend + G*r < 1.8 T
  µx, µy < 120°
  Assumes the gradient follows the reference trajectory when computing the apertures

## Slide 6: Normal RCS
Greenfield RCS1 and CERN RCS 1, 2

## Slide 7: Greenfield RCS1
Limiting factor
FODO

## Slide 8
« Normal » FODO
« Hybrid » FODO
Combined Functions
Effect of sagitta !

## Slide 9: CERN RCS 1
Limiting factor
FODO

## Slide 10: CERN RCS 2
Limiting factor
FODO

## Slide 11: Hybrid RCS: FODO Cells
Greenfield RCS 2,3,4 and CERN RCS 3

## Slide 12: Greenfield RCS 2
No difference between Normal and Hybrid FODO.
Limitations: Ldip,SC = 2 m.
  Restricts maximum nc: 41.6mm of trajectory excursion out of 85.3mm total aperture.

## Slide 13: Greenfield RCS 3
No such constraint on RCS3 (larger energy and bigger machine): rather small trajectory excursion.
Limitations:
  Hybrid : Ldip,SC
  Normal : BQP, NC
Global parameters for RCS 2/3 do not look optimized for apertures.

## Slide 14: Greenfield RCS 4
Same case as RCS 2
Limitations:
  Hybrid : Ldip,SC .
    Restricts maximum nc: 37mm of trajectory excursion out of total 68mm aperture.
  Normal : BQP, NC .

## Slide 15: CERN RCS 3
Limitations:
  Hybrid: BQP, SC
  Normal : BQP, NC

## Slide 16: Summary on horizontal apertures: Greenfield
Greenfield |  | Normal FODO | Hybrid FODO | Combined Functions
RCS 1 | Apert. NC Dipole | 99.1 | 67.1 | 60.6
 | Apert. SC Dipole | / | / | /
RCS 2 | Apert. NC Dipole | 85.3 | 85.3 | -
 | Apert. SC Dipole | 58.6 | 58.5 | -
RCS 3 | Apert. NC Dipole | 49.4 | 40.3 | -
 | Apert. SC Dipole | 40.2 | 33.9 | -
RCS 4 | Apert. NC Dipole | 85.9 | 68.1 | -
 | Apert. SC Dipole | 65.2 | 53.3 | -
Without the contribution of the sagitta !!
RCS 1 : Combined functions and Hybrid FODO much better than Normal FODO (the sagitta is not taken into account)
RCS 2 : No improvement made with Hybrid FODO (limiting RCS)
RCS 3 and 4 : Better performance with Hybrid FODO

## Slide 17: Summary on horizontal apertures: CERN-siting
CERN |  | Normal FODO | Hybrid FODO | Combined Functions
RCS 1 | Apert. NC Dipole | 79.1 | 58.2 | 49.8
 | Apert. SC Dipole | / | / | /
RCS 2 | Apert. NC Dipole | 42.8 | 34.0 | 36.4
 | Apert. SC Dipole | / | / | /
RCS 3 | Apert. NC Dipole | 88.2 | 60.0 | -
 | Apert. SC Dipole | 64.4 | 46.4 | -
Without the contribution of the sagitta !!
RCS 1 : Combined functions and Hybrid FODO much better than Normal FODO
RCS 2 : Equivalent apertures for Hybrid and combined functions, averall small apertures for all cells.
RCS 3 : Better performance with Hybrid FODO.

## Slide 18: Conclusion on limitations
Normal FODO: limitations on Bpole, QP NC = 1T(except RCS2 Greenfield)
Hybrid FODO:
  For normal RCS or “low energy machines” (Greenfield RCS1 and CERN RCS1, 2) : limitations on LQP, SC = 0.75m .
  For hybrid RCS or “high energy machines” (Greenfield RCS2, 3, 4 and CERN RCS3): limitations on Ldip, SC = 2m .
Combined Functions: limitations on Bpole = 1.8T.

## Slide 19: Discussion
List of constraints
Magnet lengths:
  Ldip, SC > 2m
  Lquad, SC/NC > 0.75m
Field and gradients :
  Bpole, QP NC < 1T
  GQP, SC < 400 T/m
Combined functions:
  Bpole = Bbend + G*r < 1.8 T
Open Questions
Do the constraints look realistic ?
For combined functions, would it be possible to bend NC magnets ?
Open question on magnet design : would it be worth decreasing magnet lengths to decrease dipole apertures ?
Discussion on the siting