## Slide 1: Beam Interlock System Operating scenarios and interlocking
Antoine Colinet
27/02/2025

## Slide 2: Motivations behind the BIS architecture change
An initial proposal for the Beam Interlock System in the NA was drafted in EDMS 2810115
A new BIS architecture is proposed to account for the following points:
P4 XTAX is now fixed
Consideration of the HI-ECN3 operating scenarios
Addition of the P4 beam stopper as an actuator
Reduced infrastructure costs (less fibres between BA80 and BA2)
Enhanced reliability (shorter connections)
Increased flexibility (requirements continuously changing -> more future-proof)

## Slide 3: New BIS architecture
Two matrices (in purple)
Two actuators
8 BICs before 2031
1 more after 2031
2 (or?) more after LS4
BA2
BA80
BA81
BA82
Post LS4
Post 2031

## Slide 4: Key for all schematics
BIC
BIC
The beam interlock controller ‘local permit’ must be TRUE
The beam interlock controller ‘local permit’ is ignored
Moveable Beam Intercepting Devices
Schematics example

## Slide 5: Beam to non-FTARGET destinations
Non-FTARGET destinations should not be affected by NA interlocks
The FTARGET destination from timing is used to differentiate NA cycles to any other SPS cycle. The MSE Imin check serves as a destination tag reinforcement to guarantee that a user in the timing network is not tagged with a wrong destination by mistake
 | non-FTARGET
Software Permit | TRUE
FTARGET destination | FALSE
MSE I<Imin | TRUE
Slow extraction Slave BIC | TRUE
TT21 UP BIC | don´t care
MBE2103 dipoles partial | don´t care
MBE2103 dipoles total | don´t care
TT21 TED in | don´t care
TT21 TED out | don´t care
TT21 DOWN MASTER BIC | don´t care
BA80 MATRIX BIC | don´t care

## Slide 6: Beam to TT20 TED (SFTPRO or SFTSHIP)
 | TED with MBE partial | TED with MBE total
Software Permit | TRUE | TRUE
FTARGET destination | TRUE | TRUE
MSE I<Imin | don´t care | don´t care
Slow extraction Slave BIC | TRUE | TRUE
TT21 UP BIC | TRUE | TRUE
MBE2103 dipoles partial | TRUE | FALSE
MBE2103 dipoles total | FALSE | TRUE
TT21 TED in | TRUE | TRUE
TT21 TED out | FALSE | FALSE
TT21 DOWN MASTER BIC | don´t care | don´t care
BA80 MATRIX BIC | don´t care | don´t care

## Slide 7: SFTPRO operating scenarios
A destination flag from timing will indicate if the cycle is shared (SFTPRO to TCC2) or dedicated (SFTSHIP to ECN3)
The beam must not hit the P4 stopper
The BIS will guarantee that the new MCB is off.
In theory, the SFTPRO beam must hit the P4 XTAX, but: wrong T4 wobbling settings can send the SFTPRO beam downstream the P4 TAX, towards the P4 stopper even with MCB off. Damage limits of P4 stopper to be assessed.
  software interlocks on the wobbling settings
  might have BLM as back-up
Machine elements need to be protected up to the stoppers (M2 TAX, P4 beam stopper, P42 dump (before 2031), experiments)
The SFTPRO beam can be sent to a moving TAX
A moving P4 beam stopper should not interrupt SFTPRO
Any combination of the M2 TAX in/out and P4 stopper in/out is possible, i.e. 4 equations

## Slide 8: SFTPRO with M2 TAX in + P4 stopper in
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Shared cycle (SFTPRO)
 | M2 in + P4 stopper in
Software Permit | TRUE
HI-ECN3 cycle (from timing) | FALSE
Vertical kicker I<Imin (off) | don´t care
MCB I<Imin (off) | TRUE
M2 TAX in | TRUE
M2 TAX out | FALSE
M2 MASTER BIC | don´t care
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | TRUE
P4 stopper out | FALSE
P42 MASTER BIC | don´t care
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 9: SFTPRO with M2 TAX out + P4 stopper in
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Shared cycle (SFTPRO)
 | M2 out + P4 stopper in
Software Permit | TRUE
HI-ECN3 cycle (from timing) | FALSE
Vertical kicker I<Imin (off) | don´t care
MCB I<Imin (off) | TRUE
M2 TAX in | FALSE
M2 TAX out | don´t care
M2 MASTER BIC | TRUE
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | TRUE
P4 stopper out | FALSE
P42 MASTER BIC | don´t care
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 10: SFTPRO with M2 TAX in + P4 stopper out
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Shared cycle (SFTPRO)
 | M2 in + P4 stopper out
Software Permit | TRUE
HI-ECN3 cycle (from timing) | FALSE
Vertical kicker I<Imin (off) | don´t care
MCB I<Imin (off) | TRUE
M2 TAX in | TRUE
M2 TAX out | FALSE
M2 MASTER BIC | don´t care
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | FALSE
P4 stopper out | don´t care
P42 MASTER BIC | TRUE
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 11: SFTPRO with M2 TAX out + P4 stopper out
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Shared cycle (SFTPRO)
 | M2 out + P4 stopper out
Software Permit | TRUE
HI-ECN3 cycle (from timing) | FALSE
Vertical kicker I<Imin (off) | don´t care
MCB I<Imin (off) | TRUE
M2 TAX in | FALSE
M2 TAX out | don´t care
M2 MASTER BIC | TRUE
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | FALSE
P4 stopper out | don´t care
P42 MASTER BIC | TRUE
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 12: SFTSHIP scenarios
The SFTSHIP beam must not hit the T4 target
  An Imin check on the vertical kicker serves as a ‘destination reinforcement’ for the dedicated/shared beams: vertical kicker must be off to bypass the T4 target
The SFTSHIP beam must not hit the P4 XTAX if I(SPS) > 1.5e13p
  The Safe Machine Parameter will provide an intensity-based flag for the protection of the P4 TAX
Splitting in TDC2: there is no guarantee that no beam goes towards TT23 and TT25, therefore all the corresponding interlocks in these beamlines need to be considered
  Will have FGC3 checks on the bumpers
  Will have BLMs as backup
  All magnets will be off in TT23 and TT25
Any combination of the M2 TAX in/out and P4 stopper in/out is possible, i.e. 4 equations

## Slide 13: SFTSHIP with M2 TAX out + P4 stopper in Destination: P4 XTAX
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Dedicated cycle (SFTSHIP)
 | M2 in + P4 stopper in
Software Permit | TRUE
HI-ECN3 cycle (from timing) | TRUE
Vertical kicker I<Imin (off) | TRUE
MCB I<Imin (off) | TRUE
M2 TAX in | TRUE
M2 TAX out | FALSE
M2 MASTER BIC | don´t care
P4 TAX SMP flag (I<threshold) | TRUE
P4 stopper in | TRUE
P4 stopper out | FALSE
P42 MASTER BIC | don´t care
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 14: SFTSHIP with M2 TAX out + P4 stopper in Destination: P4 XTAX
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Dedicated cycle (SFTSHIP)
 | M2 out + P4 stopper in
Software Permit | TRUE
HI-ECN3 cycle (from timing) | TRUE
Vertical kicker I<Imin (off) | TRUE
MCB I<Imin (off) | TRUE
M2 TAX in | FALSE
M2 TAX out | TRUE
M2 MASTER BIC | TRUE
P4 TAX SMP flag (I<threshold) | TRUE
P4 stopper in | TRUE
P4 stopper out | FALSE
P42 MASTER BIC | don´t care
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 15: SFTSHIP with M2 TAX out + P4 stopper in Destination: P42 Dump (<2031), ECN3 (>2031)
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Dedicated cycle (SFTSHIP)
 | M2 in + P4 stopper out
Software Permit | TRUE
HI-ECN3 cycle (from timing) | TRUE
Vertical kicker I<Imin (off) | TRUE
MCB I<Imin (off) | don´t care
M2 TAX in | TRUE
M2 TAX out | FALSE
M2 MASTER BIC | don´t care
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | FALSE
P4 stopper out | TRUE
P42 MASTER BIC | TRUE
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 16: SFTSHIP with M2 TAX out + P4 stopper in Destination: P42 Dump (<2031), ECN3 (>2031)
 | North Area
Software Permit | TRUE
FTARGET destination | TRUE
MSE I<Imin | don´t care
Slow extraction Slave BIC | TRUE
TT21 UP BIC | TRUE
MBE2103 dipoles partial | FALSE
MBE2103 dipoles total | TRUE
TT21 TED in | FALSE
TT21 TED out | TRUE
TT21 DOWN MASTER BIC | TRUE
BA80 MATRIX BIC | TRUE
 | Dedicated cycle (SFTSHIP)
 | M2 out + P4 stopper out
Software Permit | TRUE
HI-ECN3 cycle (from timing) | TRUE
Vertical kicker I<Imin (off) | TRUE
MCB I<Imin (off) | don´t care
M2 TAX in | FALSE
M2 TAX out | TRUE
M2 MASTER BIC | TRUE
P4 TAX SMP flag (I<threshold) | don´t care
P4 stopper in | FALSE
P4 stopper out | TRUE
P42 MASTER BIC | TRUE
Represented here after 2031
Before 2031, P42 Dump is in beam

## Slide 17: Operation between the end of LS3 to 2031
Before 2031:
The P42 Dump will be permanently in-beam
Its cooling will be interlocked by the BIS (EDMS 3049242)
The interlocks downstream the P42 Dump will be ignored
After 2031:
The P42 Dump will be realigned to allow the beam to go to ECN3.
Its cooling will no longer require to be interlocked as it will not see the beam anymore
During YETS 2030/2031, the interlocks downstream the P42 Dump will have to be connected, the BIC in BA82 will have to be linked to the BIC in BA80, all the interlocks for BDF/SHIP will have to be ready

## Slide 18: Actuators
Two actuators are connected to the BIS beam permit:
  M2 TAX
  P4 beam stopper
When the interlocks downstream these elements report a fault, then the BIS sends a beam permit to FALSE to them. The aim is to insert these stoppers in the beam so that operation can be resumed asap.
The latency to dump in the SPS will be much quicker than the movement of the P4 stopper, so that the beam is dumped in the SPS and not on the P4 stopper

## Slide 19: Conclusions
Next steps
Review the failure cases and mitigation measures related to post-LS3 start-up: interlocks in TCC2 and upstream of P42 dump
Freeze the architecture of the BIS
Follow-up with BID controls, EPC, WIC… on the latest updates
Follow-up on the outcome of the T4 review (WP2 meeting next week)
Define the intermediate interlocking strategy for BA81 between 2031 and LS4
Define the BDF/SHIP interlocks in a separate specification
Discuss the commissioning scenarios of SHIP, and its impacts on other beamlines
Next meeting proposal: 27th March
Review of the failure cases and mitigation measures

## Slide 20: Appendices

## Slide 21: Overall view of North Area BIS matrices
 | Shared cycle (SFTPRO) | Shared cycle (SFTPRO) | Shared cycle (SFTPRO) | Shared cycle (SFTPRO) | Dedicated cycle (SFTSHIP) | Dedicated cycle (SFTSHIP) | Dedicated cycle (SFTSHIP) | Dedicated cycle (SFTSHIP)
 | M2 in + P4 stopper in | M2 out + P4 stopper in | M2 in + P4 stopper out | M2 out + P4 stopper out | M2 in + P4 stopper in | M2 out + P4 stopper in | M2 in + P4 stopper out | M2 out + P4 stopper out
Software Permit | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE
HI-ECN3 cycle (from timing) | FALSE | FALSE | FALSE | FALSE | TRUE | TRUE | TRUE | TRUE
Vertical kicker I<Imin (off) | don´t care | don´t care | don´t care | don´t care | TRUE | TRUE | TRUE | TRUE
MCB I<Imin (off) | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE | don´t care | don´t care
M2 TAX in | TRUE | FALSE | TRUE | FALSE | TRUE | FALSE | TRUE | FALSE
M2 TAX out | FALSE | don´t care | FALSE | don´t care | FALSE | TRUE | FALSE | TRUE
M2 MASTER BIC | don´t care | TRUE | don´t care | TRUE | don´t care | TRUE | don´t care | TRUE
P4 TAX SMP flag (I<threshold) | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE | don´t care | don´t care
P4 stopper in | TRUE | TRUE | FALSE | FALSE | TRUE | TRUE | FALSE | FALSE
P4 stopper out | FALSE | FALSE | don´t care | don´t care | FALSE | FALSE | TRUE | TRUE
P42 MASTER BIC | don´t care | don´t care | TRUE | TRUE | don´t care | don´t care | TRUE | TRUE
 | non-FTARGET | TED with MBE partial | TED with MBE total | North Area
Software Permit | TRUE | TRUE | TRUE | TRUE
FTARGET destination | FALSE | TRUE | TRUE | TRUE
MSE I<Imin | TRUE | don´t care | don´t care | don´t care
Slow extraction Slave BIC | TRUE | TRUE | TRUE | TRUE
TT21 UP BIC | don´t care | TRUE | TRUE | TRUE
MBE2103 dipoles partial | don´t care | TRUE | FALSE | FALSE
MBE2103 dipoles total | don´t care | FALSE | TRUE | TRUE
TT21 TED in | don´t care | TRUE | TRUE | FALSE
TT21 TED out | don´t care | FALSE | FALSE | TRUE
TT21 DOWN MASTER BIC | don´t care | don´t care | don´t care | TRUE
BA80 MATRIX BIC | don´t care | don´t care | don´t care | TRUE
North Area
Slow extraction

## Slide 22: List of user inputs – Slow extraction
FTARGET destination
MSE I<Imin
Slow extraction Slave BIC
TT21 UP BIC
MBE2103 dipoles partial
MBE2103 dipoles total
TT21 TED in
TT21 TED out
TT21 DOWN MASTER BIC
BA80 MATRIX BIC
In BA2 matrix:
In BA2 slave BIC:
Extraction sextupoles current monitoring BA1 | Yes | Current monitoring for extraction sextupoles LSE.10602 and LSE.12402
Extraction sextupoles current monitoring BA2 | Yes | Current monitoring for extraction sextupoles LSE.20602 and LSE.22402
Extraction sextupoles current monitoring BA4 | Yes | Current monitoring for extraction sextupoles LSE.40602 and LSEN.42402
Extraction sextupoles current monitoring BA5 | Yes | Current monitoring for extraction sextupoles LSE.50602 and LSE.52402
Extraction sextupoles current monitoring BA6 | Yes | Current monitoring for extraction sextupole LSE.62402
Bumpers current monitoring | Yes | Current monitoring for extraction bumpers in BA2 (9x PCs located in BA2)
Masking matrix interlocks is not possible

## Slide 23: List of user inputs – TT21 Upstream
Input name | Maskable | Details
Vacuum TT21 before TED | No | Vacuum valves before the TT21 TED
WIC #1.1 | No | Electrical circuits before the TT21 TED
MSE/MST septa | No | Cooling pumps, temperatures, if power converter is ON, girder position, etc
ZS electrostatic septa | No | Interlock on ZS electrostatic septa
ACCESS TT20 EXTR | No | Access system covering TT20 up to the TED.210358
TT21 TED cooling | No | Eletta flow switch and thermocouples
BLM | Yes | BLMs before the TT21 TED
TT21 TQCD | Yes | Position interlock on the TQCD.201271 for the UA9 experiment
PC #BA2.1 | Yes | Current monitoring for TT21 before the TED
In BA2:

## Slide 24: List of user inputs – TT21 Downstream
Input name | Maskable | Details
TT21 downstream slave BIC | No | TT21 downstream slave BIC located in BA80
Vacuum TT21 after TED | No | Vacuum valve after TT21 TED controlled from BA2
WIC #1.2 | No | Warm magnet protection in TT21 after TED and TDC2
TT21 TBSE out | No | TT21 TBSE is out of beam or moving
ACCESS NORTH TRAN | No | Access system covering TT20 from the TED.210358, TCC2 and TDC2
PC #BA2.2 | Yes | TT21 after TED powered from BA2
PC #BA2.3 | Yes | TT21 after TED powered from BA2
In BA2:
In BA80:
Input name | Maskable | Details
Targets | No | T2/T4/T6 targets cooling interlocks + TBIU/D positions
TAXes cooling | No | P4/P6/M2/H2/H4/H6 TAX cooling
TCSC collimators | No | TDC2 splitter collimators cooling
TCX after T6 | No | TCX.61002 cooling
Vacuum TDC2, TT22, TT24, TT25 | No | Vacuum valves in TDC2, TT22, TT24 and TT25
WIC #2.1 | No | Warm magnet protection in TT22, TT23, TT24, TT25 + wobbling magnets
WIC #4.2 | No | Warm magnet protection in the start of M2 line
BLM TDC2/TCC2 | Yes | BLMs in TDC2/TCC2
PC #BA80.1 | Yes | TT21 after TED and TT22
PC #BA80.2 | Yes | TT23
PC #BA80.3 | Yes | T2 wobbling magnets and BA80_left PC spares
PC #BA80.4 | Yes | TT24
PC #BA80.5 | Yes | T4 wobbling magnets, NR22-004, NR22-001, NR22-007
PC #BA80.6 | Yes | TT25
PC #BA80.7 | Yes | End of TT25 and M2 before the M2 TAX
PC #BA80.9 | Yes | T4 bumper #2

## Slide 25: List of user inputs – BA80 matrix
In BA80:
HI-ECN3 cycle (from timing)
Vertical kicker I<Imin (off)
MCB I<Imin (off)
M2 TAX in
M2 TAX out
M2 MASTER BIC
P4 TAX SMP flag (I<threshold)
P4 stopper in
P4 stopper out
P42 MASTER BIC
Masking matrix interlocks is not possible

## Slide 26: List of user inputs – P42
In BA80:
Input name | Maskable | Details
P42 slave BIC | No | P42 slave BIC located in BA81
WIC #4.1 | No | Warm magnet protection in P4 and P4:P6 after P42 TAX
ACCESS TCC8-ECN3 | No | Access system covering TCC8 and ECN3
ECN3 BIC | No | HI-ECN3 BIC located in BA82 for SHIP/BDF
PC #BA80.8 | Yes | Current monitoring for P42 and BA80_right PC spares
In BA81
(post LS4):
WIC #5.1 | No | Warm magnet protection in P42 controlled from BA81. Only available in LS4
WIC #7.1 | No | Warm magnet protection in K12 controlled from BA82. Only available in LS4
PC #BA81.1 | Yes | Current monitoring for P42. Only available in LS4
PC #BA81.2 | Yes | Current monitoring for P42 and K12. Only available in LS4
PC #BA81.3 | Yes | Current monitoring for K12. Only available in LS4
PC #BA82.1 | Yes | Current monitoring for K12. Only available in LS4
In BA82
(post 2031):
Input name
WIC SHIP
PC #SHIP
Sweep monitor (?)
Target System (?)
BLM
Experiment (SC magnets)

## Slide 27: List of user inputs – M2
In BA80:
In BA82
(post LS4):
Input name | Maskable | Details
M2 slave BIC | No | M2 slave BIC located in BA82. Only available in LS4
WIC #4.3 | No | Circuits in M2 powered from BA80
WIC #6.1 | No | Circuits in M2 powered from BA81. Only available in LS4
Input name | Maskable | Details
WIC #7.2 | No | Circuits in M2 powered from BA82. Only available in LS4
WIC #7.3 | No | Circuits in EHN2 for SM1, SM2 and COMPASS. Only available in LS4
PC #82.2 | Yes | PC current monitoring for SM1, SM2, COMPASS. Only available in LS4

## Slide 28: From T4 review (link)