## Slide 1: Detector Development - Challenges - discussion
Grzegorz W. Deptuch,
FCCee workshop May 7-9, 2025
email: gdeptuch@bnl.gov

## Slide 2: Introduction
Directions for future detectors
Specifications and comparison
Challenges (all interwoven)
Material Lightweightness
High Granularity / Rate
Powering Methods
Power Consumption / Cooling
Timing Precision
Selective Readout
Radiation Hardness
Next-generation experiments in relativistic heavy-ion and particle physics demand trackers that combine high-rate capability, low material budget, spatial precision, and time stamping.

## Slide 3: Outline
Requirements
Front-End
Back-End
Readout
Powering
Power Distribution
require a two-order-of-magnitude enhancement in time stamping while preserving their light material budget (~50 μm thickness) and low power consumption (~50 mW/cm²).

## Slide 4: Requirements - 1
 | ALICE3 OT | Belle II trk | CBM trk | LHCb UT | FCCee trk
Position resolution | ~10 µm | <15 µm | ~10 µm | <10 µm | <10 µm
Pixel pitch (µm) | 50 | 50 | ~30 | 50 | 50
Hit rate (MHz/cm2) | 0.05 to 2 | <1 | 60/180 | 160 | <10
Data rate (Gb/s) |  |  | 8 | 20 | 
Time figure (ns) | 100 | ~1 | 25 | ~1 (<25) | 20 to 1000
Triggering | No | yes | no | no | ?
Power (mW/cm²) | ~20 | <50 | ~50 | <100 | ~20?
TID (kGy) | 50 | 10? | ~10 | 2400 | 10?
NIEL | 1014 | 1011? | few 1014 | 3x1015 | 1011?
ALICE3 [1], BelleII [2], CBM [3], EIC [4], FCCee [5], LHCb [6].
Belle II Pixel Vertex Detector (PXD)
ALICE 3: a heavy-ion detector for the 2030s
Geometry of the CBM experiment
Geometry of the LHCb experiment
The FCC-ee + IDEA detector with an ultra-thin solenoid inside the calorimeter

## Slide 5: Requirements - 2
References (examples)ALICE-3 [1], Belle-II [2], CBM [3], EIC [4], FCCee [5], LHCb [6]:
[1] R. Vertesi (ALICE Collaboration), “The ALICE 3 detector concept for LHC Runs 5 and 6 and its physics performance”, (2024), https://arxiv.org/abs/2409.12148, DOI:
https://doi.org/10.48550/arXiv.2409.12148 (ALICE3)
[2] H. Ye, F. Abudinen, K. Ackermann, P. Ahlburg, M. Albalawi, O. Alonso, et al., “Commissioning and performance of the Belle II pixel detector”, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, Vol. 987, (2021), DOI: https://doi.org/10.1016/j.nima.2020.164875 (Belle2)
[3] F. Matejcek, A.-M. Altingun, J. Andary, B. Arnoldi-Meadows, J. Baudot, G. Bertolone et al.,” Integration Concept of the CBM Micro Vertex Detector”, (2025), https://arxiv.org/abs/2502.04858, DOI: https://doi.org/10.48550/arXiv.2502.04858 (CBM)
[4] R. Abdul Khalek, A. Accardi, J. Adam, D. Adamiak, W. Akers, M. Albaladejo, et al., “Science Requirements and Detector Concepts for the Electron-Ion Collider “, Nuclear Physics A Volume 1026, October (2022), DOI: http://dx.doi.org/10.1016/j.nuclphysa.2022.122447 (EIC)
[5] A. Abada, M. Abbrescia, S.S. AbdusSalam, et al. “FCC-ee: The Lepton Collider”, Eur. Phys. J. Spec. Top. 228, 261–623 (2019) DOI: https://doi.org/10.1140/epjst/e2019-900045-4 (FCC)
[6] A.F. Prieto, P.V. Regueiro, K. Hennessy, J. Buytaert, M. van Beuzekom, et al., “Phase I Upgrade of the Readout System of the Vertex Detector at the LHCb Experiment”, IEEE Trans. Nucl. Sci. 67 (2020) 4, 732-739, DOI: 10.1109/TNS.2020.2970534 (LHCb)
The growing size and complexity of detectors introduce new challenges.

## Slide 6: MAPS ePIC SVT - Illustration
ePIC SVT detector layout configuration (in total sub 100B pixels, on ∼ 10 m2 of Si)
Baseline technology of choice: MAPS in TPSCo 65 nm process, following CERN’s ALICE ITS3 upgrade development of bent silicon
some numbers, mainly X/X0, are evolving due to stave approach and cooling.
Optimized layout
cables & services for mvertex & OuterBarrel layers + first 2 disks exit on a cone along 45o line and cables run in-front of MM
3 equal sized MM modules
MM cables can run on front or back face of MM
fewer sharp bends
MAPS Barrel + Disks
MPGD Barrels + Disks
AC-LGAD based ToF
G. Feofilov et al.,
ITS3 WP4 10 October 2023.
IB
OB
E-End Cap Disks
IB
OB
EE
H-End Cap Disks
HE
Upgrades of ePIC with needed improvements:
require an order-of-magnitude enhancement in time stamping, while preserving light material budget (~50 μm thickness) and low power consumption (~50 mW/cm²) 2-5 ms st Æ 100 ns)

## Slide 7: Front-End / Readout - 1
Low Power Front-End:
One of several versions of FE for ALICE-ITS3 F. Piro et al., IEEE TNS, VOL. 70, NO. 9, SEPT 2023)
small size <20 mm pixel’s pitch
low power ~50 nW/pixel Æ <50 mW/cm2
But
SLOW
Technology: 65 nm CMOS (TPSco)

## Slide 8: Front-End / Readout - 2
Comparison with RD53 A/B (fast 25ns resolution)
Technology: 65 nm CMOS (TSMC)
Pixel Size: 50 μm × 50 μm
Power Consumption: aiming at less than 1 W/cm², including losses from on-chip voltage regulators (Shunt-LDOs) and per-pixel analog and digital current consumption is approximately 4 μA each with Front-End Variants:
    Synchronous Front-End: total current, including latch, is close to 5.5 μA per pixel
    Linear Front-End: approximately 4 μA per pixel
    Differential Front-End: around 4 μA per pixel
Design Considerations: RD53 chips are to handle rates up to 3 GHz/cm² and radiation up to 500 Mrad. ​

## Slide 9: Front-End / Readout - 3
Vertex 2023, Sestri Levante, 2023
Precise timing needs two: sensor and front-end electronics —
— Elephant in the room: primary optimization factor for practical 4D tracking system (millions of readout channels) is power consumption (scales with # of channels not with detector area)
Main challenge for future 4D trackers remains front-end power consumption.

## Slide 10: Back-End /Readout - 1
ALICE
ITS
P. Fischer, Nuclear Instruments and Methods in Physics Research A 461 (2001) 499–504
P. Yang et al., Nuclear Instruments and Methods in Physics Research A 785, pp. 61–69, 2015
G.W.Deptuch, https://lss.fnal.gov/archive/test-tm/2000/fermilab-tm-2709-ppd.pdf
Mephisto
Token Passing - Timepix
T Poikela et al 2014 JINST 9 C01007
FRAME-BASED no intrinsic timing
POLLING intrinsic timing affected by varied latency

## Slide 11: Back-End / Readout - 2
Lot of attention given to event-driven readout
D. Gorni et al., “Event driven readout architecture with non-priority arbitration for radiation detectors,” Journal of Instrumentation, vol. 17,no. 04, p. C04027, 2022
D. S. Gorni et al., “Integration of EDWARD readout architecture in full-field fluorescence imaging detector,” Journal of Instrumentation, vol. 19,no. 04, p. C04035, 2024.
Event-driven readout can lower power and dead-time in radiation imagers, yet only if arbitration remains fast, fair, and clock-free.
EDWARD – Event-Driven With Access and Reset Decoder – developed at BNL (no priority – dynamic Priority Arbitration)
FRAME-LESS preserving intrinsic latency
E. Aguénounon, et al., “Design and Characterization of an Asynchronous Fixed Priority Tree Arbiter for SPAD Array Readout”, Sensors 2021, 21, 3949
SPARC – use of Fixed Priority Arbitration

## Slide 12: Powering - 1
Options:
Low-Voltage Parallel Powering
  Simple but faces high losses in resistive trace Æ need of accounting for sagging of power supply in providing operational voltage
  Material budget increase for providing satisfactory cross-section
DC-DC Power Converters (charge pumps or inductive converters)
  Increased complexity, but reduction of losses in resistive traces
  Concerns about electromagnetic interferences
  Large (coreless if operated in B-field) inductances and capacitors needed for high currents
Serial Powering
  Simple (when operating) conceptually with reduced losses in resistive traces as one trace instead of multiple allows providing larger cross-section
  Accumulated concerns:
    Risky startup:
      shunt regulator needs to be powered before switching main power (how to do it?);
      optimal ramping of current to avoid instabilities
    Need of multiple protection modes Å by-pass mode, overcurrent, overvoltage
    Low and nominal load operation mode needed
    Difficult indirect monitoring Å regulator need to be equipped with measurement features
  Complications Å NO common ground complicates:
    biasing sensors with High Voltage - especially difficult if precisely defined reverse bias is need – local bias generators are needed (negative voltage in ePIC) or accept multiple HV lines or differences in HV bias (ATLAS ITk) if delivered all from outside
    AC-coupling for slow control and data – restarting transmission requires synchronization (power off?)
DC-DC Power Converter Æ many power traces and small currents v.s. Serial Powering Æ one power trace and large current

## Slide 13: Powering - 2
Power supply sagging
in large area sensors/modules:
Serial powering
and DC-coupling (ePIC SVT):
Default AC-coupled
Opt. DC-coupled
Key: use PD-SOI process with ability to isolate each transistor in Deep Trench Isolation à la DMILL 
Significant supply and ground drops Å large sizes of devices:
  nonuniform distribution of biases
  spread of performances

## Slide 14: Power Disribution
Key Challenges in Power Distribution for High-Precision Timing ASICs:
Voltage Drops and IR Drop Effects: as ASICs scale up, maintaining uniform power distribution becomes challenging due to voltage drops across the power grid, leading to timing skews and degraded performance
High Instantaneous Current Demands: achieving picosecond timing resolution requires fast signal processing, which demands rapid current transients. Supplying these currents without inducing voltage fluctuations necessitates careful power network design
Thermal Management: increased power consumption leads to heat generation, affecting the performance and reliability of both the ASIC and the sensor. Effective thermal management strategies are essential to dissipate heat efficiently​
Radiation-Induced Effects: operating in radiation-rich environments introduces challenges like total ionizing dose effects and single-event upsets, impacting the power distribution network's reliability and necessitating radiation-hardened design techniques

## Slide 15
Sensing with electro-photonic signal conversion a) processing data on the fly b) and the end of the data route with electro-photonic computing c).
- Energy Efficiency
Data Reduction -
Readout - option