## Slide 1: Emittance and bunch length diagnostics for run 2c
J. Wolfenden, D. Ghosal, A-M. Guisao Betancur, C. Swain, and C. Welsch
22nd AWAKE Instrumentation meeting
11/03/2025

## Slide 2
Overview
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
2
Emittance - OTR/OSR measurements at CLEAR
Bunch length – CTR/CSR measurements at MAX IV

## Slide 3: Emittance

## Slide 4
Emittance – Review Oct. ‘23
4
Data from October ‘23 run provided PoC for the measurement procedure for the MLA
Benchmarking was done using quadrupole scans – inconsistencies in the data
Emittance varied wildly between all measurements
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
εx=15 mm mrad
εx =27 mm mrad

## Slide 5
Emittance – Review Jun. ‘24
5
MLA unchanged from previous run
DMD system updated with new camera and angular optics
Extensive quadrupole scan study undertaken with online analysis
A range of (magnetic) optics were captured
  inconsistencies highlighted online
“Consistent” benchmark values found:
  εx ≈ (15.6 ± 2.6) mm mrad
  εy ≈ (4.2 ± 0.7) mm mrad
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025

## Slide 6
Emittance – Review Jun. ‘24
6
Pincushion distortion found in images
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
“Correction”

## Slide 7
7
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
A final goal of the measurements was to test the potential for OSR from CLEAR
Modified setup on final afternoon, ended up with 20 minutes(!) of beam to test
Idea to return late 2024 to try non-invasive version of MLA/DMD
No screen on diverted beamline
Very quick alignment
No beam optimisation
Emittance – Review Jun. ‘24

## Slide 8
8
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
~19nC @ ~200 MeV
Signal definitely beam dependent
Couldn’t centre signal in the time we had
Not at focus – steered off screen by delay line
Very promising first glimpse!
Emittance – Review Jun. ‘24

## Slide 9
9
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Changed final imaging optic to a matched pair of air spaced achromats – removed pincushion distortion
Using high resolution sCMOS
Significantly simplified installation and alignment
Much better background shrouding (light) and shielding (radiation)
Took both OSR and OTR data
Emittance – CLEAR Dec. ‘24
Angular distribution
Micro-lens array
Spatial distribution

## Slide 10
10
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Emittance – CLEAR Dec. ‘24
Majority of measurements taken from 700pC to 2.2nC @ 200 MeV
  Went as low as <100pC @ <100MeV
Restricted beam optics for quad scans to “reliable range”
Found out following week that scatterer had been left in the beamline from the week before and unplugged
Positives are the PoC on the feasibility of OSR as a radiation source for this measurement
Confirmed beam time W/C April 28th

## Slide 11
11
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Emittance – OSR simulation
Full end-to-end simulations
Image Plane
MLA Focal Plane
SRW – Ansys Zemax OpticStudio Benchmarking with ideal lenses
Extraction scenarios for Run 2c

## Slide 12
Emittance - Outlook
12
5 days of beam time confirmed at CLEAR for W/C April 28th
OSR source has proven to be a viable option, measurements just need to be retaken
Online analysis codes of MLA almost complete
Assessment of # lenslets illuminated/energy spread impact on emittance/phase space
OSR simulations progressing well, should be completed prior to beam time
  Looking at reconstruction from OSR simulated image
  Ongoing work with Spectrometer Team regarding Run 2c installation options
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025

## Slide 13: Bunch length

## Slide 14
Bunch length – Experimental Review
14
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Pyrocam
HRFZ Si Lens
Pyrocam
[1]
Next steps:
New measurements with improved image resolution
Upgrade to OAP-based system
Test of ML-based analysis on experimental data

## Slide 15
Bunch length – Analysis Review
15
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
x100,000
Next steps:
Training with more realistic beam-based profiles
Application to CSR simulations
Application to CxR data
Ground Truth
Model Prediction

## Slide 16
Bunch length – MAX IV Feb. ‘25
16
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Upgrade!
Existing HRFZ Si system tidied up and adjusted before benchmarking
Replaced with x2 magnification confocal OAP system

## Slide 17
Bunch length – MAX IV Feb. ‘25
16
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
New CxR compression monitor installed by MAX IV (BCM)
Took comparative intensity measurements non-invasively – repeat previous measurements

## Slide 18
Bunch length – MAX IV Feb. ‘25
17
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Measurements taken single-shot with 90pC @ 3 GeV
Bunch lengths varied from ~150 fs to ~10 fs
Scanned fill time (phase) and sextupoles (LPS linearisation)
Benchmarking with TDC (and BCM)

## Slide 19
Bunch length – MAX IV Feb. ‘25
18
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Average of 20 shots

## Slide 20
Bunch length – MAX IV Feb. ‘25
19
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Single shot

## Slide 21
Bunch length – MAX IV Feb. ‘25
20
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Single shot TDC

## Slide 22
Bunch length – Simulations
21
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
(image credit: A-M Guisao Betancur)

## Slide 23
Bunch length – Simulations
22
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025
Ensemble methods show:
  Estimate of error from ML
  Variation of error across the longitudinal profile
Can extract small features and irregularities

## Slide 24
Bunch length - Outlook
23
Analysis of MAX IV data (>30,000 images)
Simulations of machine settings for each scan point
Comparisons of images, simulations, BCM intensity, and TDC output
Application of ensemble method to experimental data
Future return to MAX IV:
  Test CSR version
  Replace HRFZ Si window with something optically transmissive
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)
22nd AWAKE Instrumentation meeting 11/03/2025

## Slide 25: Thank you for your attention. Questions?
Special THANKS to CLEAR and MAX IV
J. Wolfenden (joseph.wolfenden@cockcroft.ac.uk)