## Slide 1: Bond Winding process & Impgregnation mold concept
N.Peray
18/02/2025

## Slide 2
Pole midplane interface
Winding process
Impregnation mold

## Slide 3
Pole midplane interface :
Only ground insulation (2x0.125mm Kapton)
Miplane shim (4mm of trace, gound insulation, fiber glass midplane shim)
1
2

## Slide 4
Pole midplane interface
Winding process
Impregnation mold

## Slide 5
Shims
Before winding

## Slide 6
First 6 turns of the lower layer

## Slide 7
Lower layer winding
Should we try it on the winding of the next SMC ?

## Slide 8
Upper layer winding

## Slide 9
Final step before reaction mold assembly
Head length measurement device ?
Splice length ? (twist pitch = 121+-3)

## Slide 10
Pole midplane interface
Winding process
Impregnation mold

## Slide 11
Impregnation needs :
To obtain a uniform stress at each interface, coils geometry should be the closest to perfection possible.
Due to the behavior of the cable during reaction, the position of the cable in the head cannot be fully guarantied.
Meaning that distance between cables and the pad in the head can vary and need to be filled for the final assembly.
Coil overlenght | Total shim thickness*
mm | mm
1 | 0.12
2 | 0.24
3 | 0.37
4 | 0.49
5 | 0.61
6 | 0.73
7 | 0.85
8 | 0.97
9 | 1.10
10 | 1.22
11 | 1.34
12 | 1.46
13 | 1.58
14 | 1.71
15 | 1.83
16 | 1.95
17 | 2.07
18 | 2.19
19 | 2.32
20 | 2.44
*Shim thickness to be split in two if equally spread at each end

## Slide 12
Option 1 : Filling the gaps before impregnation
Fiber glass or EP GC/GM
Seal web

## Slide 13
Option 2 : Adaptative mold
The gaps between the coil and the pad will need to be shimmed after impregnation
Custom spacer
Similar in some point to the technic used on TFD

## Slide 14
Option 3 : Impregnated pad
Machined after reaction to fit the coil overlength
Final pad
ESC Coil* or any filler
*If ESC coil, it needs to be fitted to the coil shape/overlength

## Slide 15
Thanks for your attention