## Slide 1: Electron cloud and ion effects
L. Mether

## Slide 2: Task overview
Electron cloud in Collider, Booster, Damping ring
Multipacting thresholds:
  Determine SEY thresholds and specify tolerances on bunch intensity, bunch spacing and train structure
Beam stability:
  Study beam stability and determine tolerance on electron cloud density
Photoemission:
  Determine photoemission yield (PEY) specifications based on data from photon tracking simulations (TE/VSC)
Ion trapping and instability in Collider, Booster, Damping rings, LINACs
Study ion trapping and instability to determine vacuum specifications and identify tolerances on bunch intensity, bunch spacing and train structure
All studies for Z operation only

## Slide 3: Electron cloud multipacting thresholds
Determine multipacting (SEY) thresholds and specify tolerances on bunch intensity, bunch spacing and train structure
COLLIDER
STATUS: Extensive studies of parameter space in arcs identified most critical requirements during injection
    Mitigation with train pattern confirmed: Carli-Bartosik filling, non-uniform bunch trains à la 8b+4e
TO DO: Requires continuous studies as long as the design continues to evolve, e.g.,
    Impact of shorter trains and gaps for reverse polarity operation with 2-cell RF cavities
    Impact of pilots in gaps between trains
Extend studies to special areas and equipment (longterm)
BOOSTER
STATUS: Studies in main arc elements found requirements compatible with surface design even for long trains
DAMPING RING
TO DO: Studies for 2.86 GeV option (FSR) with 4 x 25 ns + 82.5 ns train structure – confirm with INFN

## Slide 4: Electron cloud and beam stability
Study beam stability and determine tolerance on electron cloud density
COLLIDER
STATUS: Threshold density evaluation indicates that full e-cloud suppression in main elements is necessary
TO DO: Confirm thresholds with detailed electron cloud distributions from build up simulations
Study impact of mitigation measures (chromaticity, Landau damping, transverse feedback)
Study interaction with other effects (impedance, beam-beam)
BOOSTER
TO DO: Study stability at injection and extraction energy (less critical since e-cloud suppression is expected)
DAMPING RING
TO DO: Study stability (less critical if e-cloud build-up is suppressed)

## Slide 5: Photoemission
Determine photoemission yield (PEY) specifications based on data from photon tracking simulations (TE/VSC)
COLLIDER
STATUS: Preliminary studies with outdated chamber and photon absorbers give strong constraints on PEY
TO DO: Studies with up-to date photon flux data from photon tracking simulations
BOOSTER/DAMPING RING
TO DO: Study photoelectron emission (expected to be less critical than in collider)
GENERAL
TO DO: Improve photoemission modelling (EPFL/CERN-EPFL PhD?)
    Consider photon properties such as energy and angle of incidence in photoemission yield
    Interface ABP tools with photon tracking tools for improved workflow: Xsuite (photon generation)  Synrad+ (photon tracking)  PyECLOUD (photoelectron emission) (TBC)

## Slide 6: Ion effects
Study ion trapping and instability to determine vacuum specifications and identify tolerances on bunch intensity, bunch spacing and train structure
COLLIDER
STATUS: Analytical estimates show that trapping is not expected to occur (due to small emittance)
BOOSTER
STATUS: Analytical estimates suggest that even light ions are trapped at injection energy
    The flexibility in the filling scheme needs to be used for mitigation
TO DO: Simulation studies to verify analytical results and define vacuum specifications for different filling schemes
DAMPING RINGS/LINACS
TO DO: Evaluate trapping with analytical estimates and simulations (if needed)
GENERAL
Should beam-gas and/or beam-ion interactions be included under this task?

## Slide 7: Resources
Available and expected resources
Required resources for pre-TDR phase: 1.5 – 2 trained persons\year (dependent on rate of design updates)
Where | Who | When | Time (PY) | Tasks
CERN | 1 staff | 2025-2026 | 0.3 | Coordination, ion studies
CERN | 1 PhD | 2025-2026 | 0.3 | Ion studies
EPFL | 1 staff | - | 0.2 | Coordination
EPFL | 1 Postdoc | 2025 | 1 | Electron cloud studies
EPFL (TBC) | 1 PhD | 2025-2028 | 1 | Photoemission, electron cloud
Other collaborators (Turkey, Mexico, US) | ~4 staff | - | Best effort | Electron cloud studies