## Slide 2
BOND design status March 2025
BOND 14 T Dipole design meeting
Author: Juan Carlos Perez
Date: Tuesday March 4th

## Slide 3: Table of contents
BOND design status
Tooling and Mock-ups for BOND fabrication

## Slide 4: Scope of the Work Package
WP3.5: Nb3Sn 14 T Block dipole BOND
Demonstrate Nb3Sn performance in a 14 T block-type dipole at 1.9 K
Design and construction of a 14 T accelerator quality dipole model magnet
  The short model magnet should reach 15-15.5 T field
Explore alternatives and develop design and technology for Nb3Sn accelerator dipoles

## Slide 5: 14 T Block dipole BOND
BOND stands for BlOck coil Nb3Sn Dipole
BOND

## Slide 6: 14 T Block dipole BOND
Design requirements:
14 T bore field with ≈ 20 % load line margin
(1.9 K using HFM specs).
Protection time margin*1 > 40 ms.
Aperture = 50 mm.
Eq. coil width*2 < 60 mm → “accelerator coil size”.
Field quality within 10 units at all current levels (excluding PC effects).
Magnet OD:
  Double aperture, inter-beam distance: 250 mm.
  Cold mass OD: 800 mm and Magnet OD: 760 mm.
  For the 1 in 1, we will scale down.
Ti post
Al shell
Coil
Vertical pad
Horizontal pad
Key
Iron yoke
Courtesy of A. Haziot, J. Ferradas & E. Fernandez

## Slide 7: 14 T Block Dipole BOND
A first BOND conceptual design (2024) was investigated accounting for the use of a large cable made of 44 strands of 1.1 mm diameter. The cable would be the same as the Test Facility Dipole (TFD), manufactured at LBNL since the strand number exceeds the current capability of CERN’s Rutherford cabling machine.
In parallel, a second design based on a 40 strands cable (which can be manufactured at CERN) was also considered and initially kept as an alternative.
In December 2024, a decision was made to change the baseline for BOND design and proceed with the 40 strands (1.1 mm diam.) option, allowing for the internalization of the cable production.
BOND – 40 strands cable

## Slide 8: BOND Design Parameters
The 2D & 3D electromagnetic design for the single aperture configuration was completed in January 2025.
Magnet |  | Single | Double
Aperture | [mm] | 50 | 50
Intra-beam distance | [mm] | - | 250
Yoke diameter | [mm] | 540 | 680
Shell diameter | [mm] | 640 | 780
Nominal current | [kA] | 20.005 | 19.340
J overall | [A/mm2] | 360 | 348
J strand (eng.) | [A/mm2] | 526 | 509
Nominal field | [T] | 14.00 | 14.00
Peak field | [T] | 14.85 | 14.81
Ap. to peak field ratio | [%] | 6.0 | 5.7
Load line fraction @1.9 K | [%] | 82.7 | 81.7
Load line fraction @4.2 K | [%] | 92.6 | 91.2
Temperature margin | [K] | 3.99 | 4.11
Inductance | [mH/m] | 4.72 | 10.24
Stored energy | [MJ/m] | 1.031 | 2.064
Coil |  | Single | Double
No. of turns per pole |  | 52 | 
Insulated cable surface | [mm2] | 11572 | 
Equivalent coil width | [mm] | 53.4 | 
Coil efficiency *1 | [T.mm/A] | 0.00073 | 0.00075
Courtesy of A. Haziot

## Slide 9: BOND Mechanical Design
Coil to pole contact pressure at 14 T
X-component of stress (MPa) during assembly (left), cool down (centre), and at 14 T (right).
Von Mises stresses (MPa) during assembly (left), cool down (centre), and at 14 T (right).
Peak at RT = 91 MPa
Peak at CD = 177 MPa
Peak at 14 T = 150 MPa
Peak at RT = 86 MPa
Peak at CD = 175 MPa
Peak at 14 T = 140 MPa
Chart: Fx / F e.m.
| Keys | CD | Powering
Pole | 0.4909 | 0.87391 | 0.19961
Shell | 0.47067 | 1.0443 | 1.0698
Vpad+Vfiller+Pocket | -0.020228 | 0.17027 | -0.12982
Pole (frictionless) | 0.45951 | 1.0286 | 0.16271
Shell (frictionless) | 0.45951 | 1.0289 | 1.1627
Vpad + Vfiller + Pocket (frictionless) | 0 | 0 | 0
Courtesy of J. Ferradas

## Slide 10: BOND Coils Configuration and Field Profile
Flared end curvature radius | mm | 750
Flared end angle | º | 7
Flared end straight section | mm | 178.4

## Slide 11: Tooling & components design
Coil components and coil fabrication tooling design is well on track.
The 3D design will be completed by end of April.
First tooling delivered is expected by late summer 2025.
Winding
Reaction
Impregnation
Courtesy of N. Peray

## Slide 12: Mock-up design of sliding reaction tooling
Thanks to the experience gained during the construction of the Race-tracks, FRESCA2 and MQXF magnets, BOND tooling designed to compensate for dimensional variations during heat treatments is currently in the design phase.
The basic concepts will be validated using simplified mock-ups that replicate conditions close as possible to those that will be used during coil manufacturing.
Racetrack coil mock-up with integrated sliding system
Courtesy of N. Lusa, J. Ferradas & B. Pellet
Circular ceramic bearing
Linear ceramic bearing

## Slide 13: BOND Magnet development plan
Tests using Mock-ups
Coil 3D CAD Design
3D CAD Winding, reaction & splicing tooling
Q1_2025
Q2_2025
Q3_2025
Q4_2025
Q1_2026
Q2_2026
Q3_2026
Q4_2026
Trial Copper Coil
1st Nb3Sn Coil Winding
Today
Analysis
Iterative engineering design
Insulated Nb3Sn Cable delivery
First dummy copper cable at CERN
First Single Aperture Magnet #1 assembly
Cold Powering
Tests Magnet #1
Single Aperture Magnet #2 assembly
Powering tests Magnet #2
Double Aperture Magnet #1 assembly
Double Aperture Magnet Magnet #1 powering tests