## Slide 1: All About AXI
Oliver Bründler – Staff Engineer
oliver.bruendler@enclustra.com
Notes: Mention Wording:
AXI: Master/Slave – Manager/Subordinate
- Mention that I noticed recently but the presentation still is Master/Slave
- So is AMD
- This is not political
AXI4-Stream: Transmitter/Receiver (use)

## Slide 2
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 3
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 4
Introduction – Communication Needs
Memory Mapped
  Access to registers (slow)
  Access to memory (fast)
  AXI3/AXI4/AXI4-Lite
Streaming
  Point-to-point
  Decentral
  AXI4-Stream
Events
  E.g. IRQs
  Not covered by AXI
Notes: 2’
Total 3:30

## Slide 5
Before AXI
  Xilinx: PLB/LMB
  Altera: Avalon
  ARM: AHB
  Logic not portable!
AXI
  Driven by ARM
  SoCs made AXI an FPGA thing
  De-facto industry standard
  Used in FPGA, ASIC & uC (e.g. STM32)
Introduction – One for All
Notes: 2’ Total 5:00

## Slide 6
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 7
AXI Protocols – Common Properties
Synchronous Protocols
  Specification on a per-clock-cycle basis
  No timing information like setup and hold times
Endianness
  Officially byte-invariant endianness
  WDATA[7:0] -> Addr+0, WDATA[15:8] -> Addr+1
  What usually is referred to as little endian
Point to Point Capability
  Masters and slaves can be connected directly
Notes: 2’

## Slide 8
AXI Protocols – Common Properties
Interconnect Approach
  Logic (interconnect) required for connecting multiple endpoints
  Interconnect != Bus (there is logic)
  Multiple transactions possible simultaneously
Notes: 1’ Total 8:00

## Slide 9
AXI Protocols – AXI4-Stream
Aim of the Protocol
  Transfer data between two endpoints - TDATA
  Flow-control – TVALID, TREADY
  Support packetized data – TLAST
  Dynamic selection of destination – TDEST
  Handling multiple logical streams through one physical link – TID
  Data alignment and dynamic bus sizing – TKEEP, TSTRB
  Handling of application specific side-band information - TUSER
Notes: 1’

## Slide 10
Sample text |  |  |  | 
Sample text |  |  |  | 
AXI Protocols – AXI4-Stream
Signals
Signal | Optional | Direction | Description
ACLK | No | - | Clock, rising-edge active
ARESETn | Yes | - | Reset, low-active
TVALID | No | M → S | Indicates when the master has valid data
TREADY | Yes | S → M | Indicates when the slave is ready to receive data
TDATA | Yes | M → S | Data to be transferred
TSTRB | Yes | M → S | Indicates whether a byte contains data
TKEEP | Yes | M → S | Indicates whether a byte must be kept (not removed)
TLAST | Yes | M → S | Indicates the end of a packet
TID | Yes | M → S | Number of the logical stream
TDEST | Yes | M → S | Endpoint to route the packet to
TUSER | Yes | M → S | Use defined side-band signals
Notes: 30” Total: 10:35

## Slide 11
AXI Protocols – AXI4-Stream
Handshaking
  TREADY is optional
  Blocking the data-stream by TREADY=‘0’ is called back-pressure
Notes: 2’ Total: 12:00
Mention: Definition of a Data Beat

## Slide 12
AXI Protocols – AXI4-Stream
Packet Handling (TLAST)
  Valid together with TDATA
  The same applies to all signals except TVALID, TREADY, ACLK and ARESETn
Notes: 1’
Total: 13:00

## Slide 13
Byte Types (TKEEP/TSTRB)
  Data byte (TKEEP=1, TSTRB=1)
    Byte contains information
    Do not remove, do not modify
  Position byte (TKEEP=1, TSTRB=0)
    Byte not interpreted at destination
    Do not remove – but may be modified
  Null byte (TKEEP=0, TSTRB=0)
    Byte not interpreted at destination
    May be added, removed or modified
  TKEEP=0, TSTRB=1 is illegal
AXI Protocols – AXI4-Stream
Notes: 1’

## Slide 14
AXI Protocols – AXI4-Stream
Byte Types Example
Address | +3 | +2 | +1 | +0
0x00 | - | 0xD4 | 0x45 | 0x67
0x04 | 0x01 | 0x02 | 0x03 | 0x04
0x08 | - | - | 0xCC | 0xDD
Notes: 1’
Total: 16:30

## Slide 15
Most Important Rules
  TVALID shall not depend on TREADY
    … but TREADY may depend on TVALID
    Required to avoid dead-locks
  TVALID must be kept until TREADY
    … but TREADY may be de-asserted
  Signals must not be changed between TVALID and TREADY assertion
AXI Protocols – AXI4-Stream
Notes: 1’
Total 18:30

## Slide 16
Aim of the Protocol
  Memory mapped read and write
  Read/write independent and simultaneous
  Burst accesses of up to 256-beats
  Configurable data width up to 1024 bits
  Overlapping transfers
    Start one transfer before the last one is completed
  Taylored for
    Low latency
    High bandwidth
    NOT simplicity
AXI Protocols – AXI4
Notes: 1’
Total: 20:00

## Slide 17
AXI Protocols – AXI4
Concept
  5 Channels
  Each channel has xREADY/xVALID handshaking (analog to AXI4-Stream)
Notes: 1’ Total: 21:00

## Slide 18
Sample text |  |  |  | 
Sample text |  |  |  | 
AXI Protocols – AXI4
Global Signals
Present in all Channels
Signal | Optional (M/S) | Description
ACLK | No / No | Clock, rising-edge active
ARESETn | No / No | Reset, low-active
Signal | Optional (M/S) | Description
xID | Yes / No | ID signal, identifies the master that requested a transaction
xValid | No / No | Handshaking signal (according to AXI4-Stream)
xReady | No / No | Handshaking signal (according to AXI4-Stream)
xUser | Yes / Yes | User defined side-band signals (according to AXI4-Stream)
Notes: 30”

## Slide 19
Sample text |  |  |  | 
Sample text |  |  |  | 
AXI Protocols – AXI4
Read/Write Address Channel
Signal | Optional (M/S) | Description
xADDR | No / No | Address to access (for bursts: first address)
xLEN | Yes / No | Burst length minus 1 (e.g. 4 = burst of 5 beats)
xSIZE | Yes / No | Bytes per beat in 2x bytes (e.g. 2 = 4 bytes) – If != data width -> Narrow Burst
xBURST | Yes / No | Burst type (incrementing, fixed or wrapping)
xLOCK | Yes / Yes | Atomic access control, out of scope for this presentation
xCACHE | Yes / Yes | Cache control, out of scope for this presentation
xPROT | No / Yes | Used for security control, out of scope for this presentation
xQOS | Yes / Yes | Quality of service, out of scope for this presentation
xREGION | Yes / Yes | For handling of multiple logical interfaces in one physical IF, out of scope for this presentation
Notes: 1.30’

## Slide 20
Sample text |  |  |  | 
Sample text |  |  |  | 
AXI Protocols – AXI4
Write Data Channel
Read Data Channel
Write Response Channel
Signal | Optional (M/S) | Description
WSTRB | Yes / No | Byte-enable
WDATA | No / No | Write data
WLAST | No / Yes | One packet per AW command
Signal | Optional (M/S) | Description
RDATA | No / No | Read data
RRESP | Yes / Yes | Read response (signal errors if any)
RLAST | Yes / No | One packet per AR command
Signal | Optional (M/S) | Description
BRESP | Yes / Yes | Write response (signal errors if any)
Notes: 1’ Total: 24:00

## Slide 21
AXI Protocols – AXI4
Example Write Transaction
  32-bit access
  Write to 0xABCD0000
Notes: 1.30

## Slide 22
AXI Protocols – AXI4
Example Write Transaction
  16-bit access
  Write to 0xABCD0001
  Unaligned
Notes: 1.30

## Slide 23
Example Read Transaction
  Reads are always full-width
  Read from 0xABCD0000
AXI Protocols – AXI4
Notes: 30’

## Slide 24
Example Burst Write Transaction
  0x11111111 > 0xABCD0000
  0x22222222 > 0xABCD0004
  0x33333333 > 0xABCD0008
AXI Protocols – AXI4
Notes: 1’

## Slide 25
Example Burst Read Transaction
  0x11111111 < 0xABCD0000
  0x22222222 < 0xABCD0004
  0x33333333 < 0xABCD0008
AXI Protocols – AXI4
Notes: 1’
Total: 28:30

## Slide 26
Example Pipelined Transactions
AXI Protocols – AXI4
Notes: 1’

## Slide 27
Concurrent Read & Write
AXI Protocols – AXI4
Notes: 30’
Total: 30:30

## Slide 28
Most Important Rules
  No bursts across 4kB boundaries
  R-packets must match ARSIZE
    Even in case of errors
    No possibility to abort
  W-packets must match AWSIZE
    No possibility to abort
  B/R required for every AW/AR command
AXI Protocols – AXI4
Notes: 1’

## Slide 29
What is Skipped
  Cache control
  Exclusive/atomic access
  Transfer ordering scheme
  Access protection
  Narrow bursts
  Wrapping bursts
AXI Protocols – AXI4
Notes: 30’
Total: 33:00

## Slide 30
Sample text |  |  |  | 
Sample text |  |  |  | 
AXI Protocols – AXI4-Lite
AXI4 is Overkill for Simple Peripherals
  AXI4-Lite is simplified (e.g. no burst access)
  AXI4 signals below are omitted
Signal | Reason
xID | All transactions MUST happened in order
AxLEN | No bursts supported, only single word transactions
AxSIZE | All transactions have the same width as the data bus
AxBURST | No bursts supported, only single word transactions
AxLOCK | No atomic accesses supported
AxCACHE | No cache control
AxPROT | No access protection
AxQOS | No quality of service
AxREGION | Only one region per slave
xLAST | No bursts supported, only single word transactions
Notes: 1’
Total: 34:30

## Slide 31
Predecessor of AXI4
  Very similar to AXI4
  Burst size limited to 16 (instead of 256)
  Minor modifications like:
    Changed cache signaling
    Changed atomic/exclusive access signaling
    Region signaling not present in AXI3
    …
  AXI3 is still used in PS interconnects for
    Zynq-7000
    Zynq-UltraScale+ MPSoC
    Reduce burst size for accesses from PL to PS!
AXI Protocols – AXI3
Notes: 1’ Total: 36:00
Note: There is also AXI5 (adding parity protection and the like) – just that nobody uses it in the FPGA context.

## Slide 32
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 33
Single Interconnect Approach
  Is simple
  Matches table-based tools (EDK/PFD)
  Wastes either resources or bandwidth
    Resources waste being the default
  Causes timing problems and congestion hotspots
Multi Interconnect Approach
  Enhanced design structure
  Allows for optimization
NOC – Versal ACAP
Pitfalls – One-for-All Interconnect
Notes: 30’<
Total: 39:00

## Slide 34
What’s Wrong with This?
Pitfalls – One-for-All Interconnect

## Slide 35
It Boils down to This!
  Wide Crossbar
  Does the Memory Tester really need access to I2C?
Pitfalls – One-for-All Interconnect
10k LUT, 12.5k FF, 06:18
Notes: 1’
Mention: Systems are not separated – CPU needs DDR access

## Slide 36
We can Split the Interconnect
  Tools usually maximize bus-widths
  In Vivado the width converter must be added manually
  Saves 55% LUT
Pitfalls – One-for-All Interconnect
4.5k LUT, 5.7k FF, 04:12
Notes: 1’

## Slide 37
We can Optimize Converters
  Tools tend to full AXI4
  Saves 62% resp. 15% of LUT
Pitfalls – One-for-All Interconnect
3.8k LUT, 4.9k FF, 03:40
Notes: 1.30 Total: 45:30

## Slide 38
Sample text |  |  |  | 
Sample text |  |  |  | 
Pitfalls – AMD Smart Connect
Interconnect
SmartConnect
Design | LUT | FF | Runtime | Comment
Design 1 | 10.0k | 12.5k | 06:18 | -
Design 2 | 4.5k | 4.9k | 04:12 | Separate 32- and 512-bit domain
Design 3 | 3.8k | 4.9k | 03:40 | Reduce AXI4-Lite converters
Design | LUT | FF | Runtime | Comment
Design 1 | 20.9k | 28.8k | 11:42 | 209% LUT usage
Design 2 | 21.9k | 28.9k | 13:04 | 487% LUT usage
Design 3 | 19.2k | 27.8k | 15:07 | 505% LUT usage
Notes: 1’
SmartConnect LUTs:
Design 1:
  Main: 20.9k
Design 2:
  32-bit: 5.1k
  512-bit: 15.5k
Design 3:
  Splitter: 2.4k
  512-bit: 14.0k (???)
  AxiLite: 0.45k
InterConnect LUTs
Design 1:
  Main: 10.0k LUT
Design 2:
  32-bit: 1.4k
  512-bit: 1.4k
Design 3:
  Splitter: 0.56k
  512-bit: 1.4k
  AxiLite: 0.12k

## Slide 39
More Resource Consumption
More Performance
  Especially in cases with lots of small transactions
  MAMD instead of SAMD
  Back-to-back arbitration
  …
Pitfalls – AMD Smart Connect
Notes: Mention: You can build interconnect manually! 1.30 Total: 49:30

## Slide 40
Pitfalls – The NOC Exception
0.60k LUT, 0.85k FF, 11:04
The NOC is hardened
  Available on AMD Versal only
  “All-for-one” but super efficient
  Saves 94% resp. 85% of LUT
Versal and AXI
  Only SmartConnect
  No basic components
Notes: 1’

## Slide 41
Do not change AXI bandwidth without Packet buffers
  Gained bandwidth is wasted otherwise
Pitfalls – Bandwidth Changes
Notes: 1’

## Slide 42
Add Buffers on High-Bandwidth Side
  Compress transfers
  Free time for other transactions
Pitfalls– Bandwidth Changes
Notes: 30”

## Slide 43
Same for Clock Crossings
Pitfalls – Bandwidth Changes
Notes: 30”

## Slide 44
Same for Clock Crossings
Pitfalls – Bandwidth Changes
Notes: 30”
Total: 52:00

## Slide 45
Packet Buffers Add Latency
  It’s the common latency vs. bandwidth tradeoff
  More open transactions required
Packet Buffers May Require Resources
  Usually double-buffering
  2 x 4kB = 8kB = 64kb
Most Tools allow Configuring Buffers in AXI Infrastructure
  Clock crossings / with converters / interconnects
Does Only Apply to Interconnect Based Systems
  E.g. not for point-to-point AXI4-Stream
  Who else would use the freed up cycles?
Pitfalls – Bandwidth Changes
Notes: 1’
Total: 55:00

## Slide 46
Backpressure on System Level
  R backpressure must be propagated to AR
  Same for B and AW
  Is it obvious?
Pitfalls – Inter-Channel Dependencies
Notes: 1’
Total: 57:00

## Slide 47
During a Burst Write
  … no other master can access the same slave
During a Burst Read
  … a master can’t receive any other data
Pitfalls – Stalling Others

## Slide 48
Problem
Pitfalls – Stalling Others

## Slide 49
Solution
  Buffer data before initiating AXI Burst
  Applies to W and R channels
Low-Latency
  Exit strategy Dummy Data
  Exit strategy Error Response
No Fancy Concepts
  E.g. do not build a direct AXI/I2C bridge
Pitfalls – Stalling Others
Notes: 1:01:00

## Slide 50
Don’t Believe it Works only Because …
  … a simple testbench works
  … a test design works
  … the code was used before
Issues Often only Arise with …
  … heavy traffic load
  ... specific traffic shapes
Applies to …
  … AXI infrastructure
  … AXI endpoints
  NOT to fixed AXI4-Stream Pairs
Pitfalls – Testing Shortcuts
Notes: 2’
Total: 1:04:00

## Slide 51
Most Implementations do not 100% adhere to the AXI specification
Example:
  Spec defines narrow bursts
  This is complex (resources)
  … and seldom needed
  Most slaves do not support narrow bursts
  Nor do most interconnects
Check Limitations
  … don’t waste effort on unsupported things
Pitfalls – Blindly Believe the Spec
Notes: Other examples:
TKEEP containing zeros in AMD only allowed on last beat
Wrapping bursts

## Slide 52
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 53
Custom AXI Logic – Backpressure
Problem
Notes: 2’

## Slide 54
Custom AXI Logic – Backpressure
Solution 1
  Implement pipeline stages with two sets of registers
  “Two level FIFO” behavior
Notes: 2’

## Slide 55
Custom AXI Logic – Backpressure
Solution 1
?
Notes: -
Total: 1:08:00

## Slide 56
Custom AXI Logic – Backpressure
Solution
  Backpressure FIFO
  Stop sample injection when half full
  Compatible with legacy processing not support backpressure
  FIFO depth = 2 x N
Notes: 1’

## Slide 57
Custom AXI Logic – Backpressure
Solution
  Why depth = 2 x N
  After Out_TREADY goes high, first N samples must come from FIFO
    … before first data from Processing arrives at FIFO
  After Out_TREADY goes low, last N samples in processing must fit into FIFO
    … before no more samples arrive
    … we can’t realy on samples arriving (processing could be empty)
Notes: 2’
1:12:0
Mention:
Actually 2 x N + FIFO latency
In reality usually FIFO=LUTRAM, no change in resources up to 32 levels which is > 2 x N in most cases. Just round up.

## Slide 58
Use Software Existingly
  AXI Master/Slave
    Use IP provided by vendor
    Use HLS
    Use open-source implementation
  Decide what you use
    Get used to it and use the same again
    Ensure proper verification
    Plausibility review
Custom AXI Logic – USE
Notes: Total: 1:15

## Slide 59
Introduction
AXI Protocols
Pitfalls
Custom AXI Logic
04
07
33
53
Agenda

## Slide 60: Questions?

## Slide 61: Thank You!