## Slide 1
Upgrades and results from CIRCUS, the autonomous control system for complex experiments
Marco Volponi, Jakub Zielinski (the AEgIS Collaboration)

## Slide 2: The Aegis experiment
The Antimatter Experiment: Gravity, Interferometry, Spectroscopy (AEgIS) collaboration aims at performing spectroscopic studies and direct experimental tests of the Weak Equivalence Principle (WEP) using antimatter-containing neutral systems (anti-hydrogen, positronium atom, antiprotonic ions).

## Slide 3: Gravity on antihydrogen
Beam of antihydrogen via charge-exchange
Gravity detector: measure free-fall

## Slide 4: The CIRCUS: Computer Interface for Reliably Controlling, in an Unsupervised manner, Scientific experiments

## Slide 5: Two Founding Pillars
Distributed System
  Unifies all the single machines in a coordinated system
  Enhance reproducibility, stability and safety
  Enable possibility of smart automation
“Everything is a MicroService”
  Defined, clear scope and tasks
  Modularity
  Asynchronicity
  Code uniformation and standardisation

## Slide 6: CIRCUS Structure
ANALYSIS ENGINE

## Slide 7: Talos: total automation of labview operations for science
Actor Framework
Guardian = Root Actor
Flat Hierarchy
Power of class inheritance

## Slide 8: Main CIRCUS services
Error Manager: distributed system error concentrator
Scheduler: to create schedules of experiments (i.e. scripts + parameters)
Kasli Wrapper: encapsulate shell interaction with Kasli (FPGA)
Monkey: core of automation, execute experiments
Tamer: for multi-Kasli operation

## Slide 10: Autonomous parameter optimisation via live data feedback
Interface of Monkey with ALPACA (Data Analysis Engine) enabled autonomous parameter exploration to optimise pre-defined observable

## Slide 11: Upgrades

## Slide 12: Extraction of Circus services from Talos
Inserting them was a good idea, but underperforming
Extraction was a game changer for the development of TALOS
  Now it compiles in < 1 min instead of > 10 mins !
Loading from CIRCUS is also much faster
Best would be to make another separate PPL
  But a PPL with a PPL inside with a PPL inside doesn’t compile…

## Slide 13: Removal of TALOS Internal Shared Variables
Error Queue: now simply a message to Error Manager
  A ‘local Error Manager’ is needed, otherwise if the Distributed Error Manager is off, the error is lost
  Future: direct TCP connection between Error Managers could ensure hardening against congestions of general TALOS connection
Initial Guardian connection: a ‘send and hope’ message to TCP Server of that machine
  Message from the m-th starting machine will correctly arrive to the (N-m-1)-th machines already started

## Slide 14: Removal of TALOS Internal Shared Variables (part 2)
Abort: replaced the nomad singleton SV with a Guardian private data boolean, and added the Bearer flag
  Only the value of Abort of the “Bearer” Guardian is the valid one: the others Abort are used as “local copies”
  Only one Bearer in the network, propagated with the periodic Pat
  In case the Bearer disappears from the network, someone else take the burden
  In case of multiple Bearers, who’s after in alphabetical order resigns

## Slide 15: Huge code refactoring
More classes!

## Slide 16: results

## Slide 17: Boot up speed
No SVs
   no Datalogging and Supervisoy Control (DSC) module to load
   no SVs to deploy and to clean up
   TCP communication way faster than SVEngine
CIRCUS uServices not needed to be loaded on slower machines
 | CIRCUS 3.0 | CIRCUS 4.0 | Improvement
Single PC startup | 147±3 s | 43.6±0.5 s | ~330 %
AEgIS’ CIRCUS restart | 262±17 s | 107±2 s | ~250 %

## Slide 18: Abort is faster
Abort=True propagated as before, O(10 ms)
Abort=False now propagated (even if multiple Bearer) in O(10 ms) instead of O(s)!
Now multiple Bearer cleaning takes O(10 ms) and happen every second instead of 30 s  “singleton” recovered in seconds instead of minute(s)!

## Slide 19: 64 bit unlocked
DSC no more a dependency  now TALOS supports LV 64 bits!
Tested on LV 2024 Q3 64 bits
Finally we are back to the future!

## Slide 20: Physics improvements
Removing and shrinking delays in Python and in LabVIEW made possible to form antihydrogen every 2 ELENA shot instead of 3-4  > 33% higher efficiency
Full 10-dimensional optimisation of beam steering inside the apparatus  ~ 2x antiprotons captured per ELENA shot wrt 4D optimisation

## Slide 21: two publications

## Slide 22: NI Case study for academic and research solutions

## Slide 23: Important physics results
APS and CERN Press Release
In the top 5% of all research outputs scored by Altmetric
Huge media impact (social, TV, journals, …)

## Slide 24: The most important metric
 | Version 3.0 |  | Version 4.0 | 
 | VIs | Wires length | VIs | Wires length
TALOS | 939 | 1.51 km | 529 | 920 m
AEgIS CIRCUS | 801 | 1.48 km | 1396 | 2.97 km
Total | 1740 | 2.99 km | 1925 | 3.89 km
Using a corrected version of Piotr Demski’s Wirelength Calculator and a 24” full HD screen.

## Slide 25: Conclusions
TALOS is “finished” (as much as such a piece of code can be finished…)
Automation is opening new physics doors
  More to come!
Open source release
  CIRCUS: 10.5281/zenodo.10371799
  TALOS: 10.5281/zenodo.10371404
Deployment in other experiments (PSICO, Univ. Of Trento)

## Slide 26
Thank you!
Disclaimer: no animals have been mistreated for the creation of this project.
Just some scientists.

## Slide 27: Backup slides

## Slide 28: Aegis System Size
‘They grow so fast!’
 | PCs | uServices instances | uServices coded
Current | 6 | 130 | 49
Forecast end 2025 | 9 | ~210 | ~58

## Slide 29: Consistent performance

## Slide 30: Why autonomous?
ELENA works 24/7 😱
Unmanned system
More beamtime
Less shifters workload
More time for data analyses & physics 🚀

## Slide 31: A Boat with two captains
TALOS does overall coordination, but it’s “slow” (~ms)
Sinara is used to control the fast operations (~ns)
High integration:
  TALOS controls Sinara, so no humans need to feed it experiments scripts
  Sinara can ask TALOS to perform operations on hardware
  In case of any error, TALOS guarantees their handling
The helm is periodically switched between the two!

## Slide 32: Single uService testing

## Slide 33: Running in Hybrid (Debug) mode
Picture of TALOS with an anaconda shell opened with a script running?

## Slide 34: Running in autonomous mode: operations
Via the Scheduler, a list of scripts to be executed can be prepared (each with different parameters)
Then the Monkey takes over and executes the scripts one by one
In case an error is generated by a µService or the Kasli, the Monkey can:
  Continue
  Retry – run again the same script
  Skip – go to the next script in the schedule
  Stop – stop the execution of the scripts and idle
  Abort – stop the execution and put the entire system in Safe Mode

## Slide 35: ELENA automated beam Steering

## Slide 36: Performance tests
(Small Delta T) – the difference between start times of the nth script among Kaslis
Same duration - sync
Different duration - async
Different duration - sync
Same duration - async
36

## Slide 37: Add sblock - demo
Notes: Add sblock - demo

## Slide 38: Standard operation – demo
Notes: Standard operation - demo

## Slide 39: Parallel mode – demo
Notes: Parallel mode - demo

## Slide 40: uService = QMH

## Slide 41: ELENA automated beam Steering

## Slide 42: ... With dedicated palette!

## Slide 43: Criticality code
Each error is substituted with a custom defined error with associated criticality code:
0: Continue
1: Retry
2: Skip
3: Stop
4: ABORT

## Slide 44: SOLUTION – Introducing the tamer
Scheduler
Tamer
Kasli 1 Wrapper
Kasli 2
Kasli 1
Monkey
Kasli 3 Wrapper
Kasli 2 Wrapper
Kasli 3
Dynamically spawned as schedule requires
Standard operation
NOTE: only ONE Kasli at a time is operated!
HW

## Slide 45: SOLUTION – Introducing the tamer
Scheduler
Tamer
Kasli 1 Wrapper
Kasli 2
Kasli 1
Monkey Kasli 1
Kasli 3 Wrapper
Kasli 2 Wrapper
Kasli 3
Dynamically spawned as schedule requires
Monkey Kasli 2
Monkey Kasli 3
Parallel operation
HW

## Slide 46: operation
Scheduler
Prepare schedule(s)
Tamer
Init Run (Spawn Monkeys, Check Guardians,
Check uServices)
Monkey
Monkey
Passed
Failed

## Slide 47: operation
Tamer
Monkey
Monkey Kasli 2
Send schedule
Check script
Submit script
Report to Tamer
Kasli
Kasli
Kasli 1
Banana arrived
Script execution
Finish script
Update
Standard operation

## Slide 48: operation
Tamer
Monkey Kasli 1
Monkey Kasli 2
Send schedules
Check script
Submit script
Report to Tamer
Check script
Submit script
Report to Tamer
Kasli
Kasli
Kasli 1
Banana arrived
Script execution
Finish script
Update
Finish script
Parallel operation - asynchronous

## Slide 49: operation
Tamer
Monkey Kasli 1
Monkey Kasli 2
Send schedule
Check script
Submit script
Report to Tamer
Collect bananas
Check script
Submit script
Report to Tamer
Parallel operation - synchronous
Collect checks
Kasli
Kasli
Kasli 1
Banana arrived
Script execution
Finish script
Update
Finish script

## Slide 50: Double TCP Tunnel
Communication via shell breaks realtime operation
Solution: two monodirectional TCP tunnels between Kasli and TALOS
  No realtime breaking
  Faster than shell processing for TALOS (~ ms), immediate* for Kasli
  Being each tunnel monodirectional, no message delay
  Kasli can reach all uServices, with no wire drawn!
(*) The communication takes place between TALOS and the Kasli Host, so if Kasli schedules it well it literally takes no time

## Slide 51: TCP Library
All communication functions are immediately available by importing this library
Each function triggers a specific action from a specific uService
The entire bridge is created by simply encasing the experiment code inside two function, StartRun() and StopRun()

## Slide 52: What about the daq?
Operation mode | DAQ operator
Standard | Monkey (in the script, as before)
Parallel (Asynchronous) | Only dedicated ports supported (no run-specific DAQ)
Parallel (Synchronous) | Tamer (starts when the script checker is passed, stops when all bananas arrive)

## Slide 53
Tamer Flowchart

## Slide 54
Monkey Flowchart

## Slide 55: AEgIS Collaboration