## Slide 1
ENUBET (NP06)
Notes: <number>

## Slide 2
The ENUBET (Enhanced Neutrino Beams from kaon Tagging) project aims to develop monitored neutrino beams with a precision of around 1% in neutrino flux determination. This is achieved by measuring leptons produced in the decay tunnel, which is instrumented with a modular cylindrical calorimeter. Positrons from K+ → e+ π0 νe decays striking the tunnel walls are used to monitor the νe flux. Additionally, the hadron dump is instrumented to track muons from kaon and pion decays (K+ → μ+ νμ and π+ → μ+ νμ), contributing to νμ flux measurement.
The test beam goal is to evaluate fast micromegas based detectors (PICOSEC) for the instrumented hadron dump.
Schematic of the installation
<number>
ENUBET – Valerio Mascagna
User Meeting 2025
Scintillator (trigger) + strip detector (tracking)
Detector 1
Beam
Total length : 2.5 m
Total width : 1.5 m
Height of beam : 1.39 m (as previous years)
Detector 2
Small scinti (trigger)

## Slide 3
Beam Condition
<number>
User Meeting 2025
Particle | Polarity | Energy (0.1 to 15 GeV/c (T09) | High purity | Intensity | Beam size (Ømm) | Run number (if applicable
Pion/Muons/K (MIPs) | Negative | 3-6 GeV/c | NO | 1E4 to 1E6 per spill | 10 | 
ENUBET – Valerio Mascagna

## Slide 4
Services needed
<number>
User Meeting 2025
Tables
  Fix table : YES, 4 (computers, small electronics, tools, ...)
  Moving table : YES (1 DESY TABLE for the detectors under test)
  Purpose for the moving table: positioning + scanning
  Setup on the table: ~ (0.5 m x 0.5 m) , 20 kg (2 PICOSEC) + 1 scinti behind)
GAS : YES.
Typical gases are AR:CO2 (70:30) and (97:3), Ne:CF4:C2H6 (80:10:10), Ar:CO2:iC4H10 (93:5:2), Ne:iC4H10 (95:5) → Flammable + fluorinated → already in contact with be-dep-ea-gas@cern.ch since last year. We’ll provide the documentation in advance.
High Voltage : YES (max ~1 kV for micromegas and PMTs)
Instrumentation :
  Wire Chamber : NO
  Cherenkov signal : YES
  Scintillator signal : NO
Infrastructure
  Electronics rack in zone : YES (2)
ENUBET – Valerio Mascagna

## Slide 5
Contact during the run
<number>
User Meeting 2025
Contact :
Andrea Longhin, andrea.longhin@cern.ch
Francesco Terranova, francesco.terranova@cern.ch
Fabio Pupilli, fabio.pupilli@cern.ch
Valerio Mascagna, valerio.mascagna@cern.ch
ENUBET – Valerio Mascagna