## Slide 1: 3D Modelling of HTS Magnets using Equivalent Circuits
TE-MPE-PE Section Meeting
Leon Teichröb – University of Stuttgart
19.03.2025

## Slide 2: A quick reintroduction…
Technical student in the STEAM team for one year
Under the supervision of Tim Mulder
My task:
Find the protection limitations and failure modes
of large HTS magnets

## Slide 3: Agenda
Goals and Motivation
HETS
  The Idea of NICQS and HETS
  Design Overview
  Geometry Representation
  Homogenization
  Circuit Solver
Results
Other Contributions
The Future

## Slide 4: Goals
Evaluate non-insulated magnet concepts
  Muon Collider: 40T Cooling Magnet
  HFM: HTS racetrack coils
Generally, pave the way for new magnet designs → Reduce size → Increase attainable field → Improve stability

## Slide 5: Boundary Conditions
Limited simulation capability for NI HTS magnets
Large geometries to expensive to simulate
NICQS* giving interesting results, but asymmetry is essential!
Conclusion:
Extension of the NICQS solver to 3D
* NICQS is the 2D, non-insulated HTS-magnet simulator written by Tim Mulder

## Slide 6
An elegant adaptation of NICQS was not possible…

## Slide 7
An elegant adaptation of NICQS was not possible…
Moving to 3D:
Required a more sophisticated geometry data model
Invalidated the circuit model
Necessitated a new software architecture

## Slide 8
Homogenized Electrothermal Transients of Superconductors
https://gitlab.cern.ch/steam/hets
Notes: And so HETS was born

## Slide 9: The Design of HETS

## Slide 10: 1. The Idea of NICQS and HETS
Both NICQS and HETS use an equivalent circuit representation of the geometry
Current Flow
Radial Current

## Slide 11: 1. The Idea of NICQS and HETS
Both NICQS and HETS use an equivalent circuit representation of the geometry
  Not a Finite Element or Boundary Element method
  Like PEEC method
Lump conductors together, reducing element count
Direct magnetic field calculation
No meshing of free space

## Slide 12: 2. Design Overview
YAML File
YAML File
YAML File
…
Imports
Pre-processor
Solution
VTKs
Paraview
Solver
Post-processor
HETS
CAD Files
Plots
Plots
CSVs
Artifacts
Multi-Part Simulations
Notes: HETS is driven by YAML simulation definition files

## Slide 13: 2. Design Overview
Written in pure Python
  But still fast?
Speed-ups via
  Numba (highly recommended!)
  Julia (DifferentialEquations.jl)
  Numpy, Pytorch, etc.
  Lookup tables
Clearly structured processing steps. A Directed Acyclic Graph (DAG) drives the execution of the preprocessor.
A part of the HETS execution graph

## Slide 14: 2. Design Overview
HETS models:
  Thermals
  B-Field
  Voltage and Current
  Radial Current
  Screening Currents
  Inductive Coupling
  T- and B-dependent materials
  External circuitry

## Slide 15: 3. Geometry Representation
The homogenization method demands a specific kind of element
  Hexahedral mesh approximates geometry inaccurately
  High order elements incompatible
A swept section with arbitrary path is used
  Lines
  Splines
  Spirals
Very accurate for many NI-HTS geometries
Illustration of HETS geometry element
Notes: Electrical nodes at the ends. Each element is modelled as an electrical component with two terminals.

## Slide 16: 3. Geometry Representation
Currently the geometry is described in YAML format
Perhaps CAD import in the future

## Slide 17: 4. Homogenization
Electrically the model in NICQS is a spiral, like the real geometry
This model breaks down when lumping + asymmetry are permitted
We are actually modelling parallel tapes
Notes: KCL is violated in 3D and it can be demonstrated that it is a very fundamental issue.

## Slide 18: 4. Homogenization – New Technique
An exact solution to the current flowing azimuthally and radially at a selected bridging point is established under more accurate assumptions
As more conductors are lumped, only a small fraction passes into the next layer
Modelled as a generic circuit component with four terminals
  “Bridges”

## Slide 19: 4. Homogenization – New Technique
Multiple bridge-types are employed that model the exact distribution of current in the tape stack
The new technique is…
  Proven to fulfill KCL
  Proven to fulfill conservation of energy
  Exactly accurate in common cases (like slow ramping)
  Still works with a single current per element and a single voltage per node

## Slide 20: 5. Circuit Solver
In NICQS, the circuit was represented by an ODE
Thus, we were solving for
  This does not work for resistor loops which exist in 3D

## Slide 21: 5. Circuit Solver
In NICQS, the circuit was represented by an ODE
Thus, we were solving for
  This does not work for resistor loops which exist in 3D
Transition to Multi-Nodal Analysis (MNA) method in DAE form
  Similar to some SPICE solvers
and do not appear in the equation!

## Slide 22: 5. Circuit Solver
In NICQS, the circuit was represented by an ODE
Thus, we were solving for
  This does not work for resistor loops which exist in 3D
Transition to Multi-Nodal Analysis (MNA) method in DAE form
  Similar to some SPICE solvers
  Coupling of circuits with simulation is built in!

## Slide 23: What else…
Gitlab CI Pipeline for unit tests, system tests, coverage, etc.
A complete User Guide
Full Linux and Windows compatibility
Multithreaded + CUDA acceleration
Local resolution control

## Slide 24: Results

## Slide 25: Example: Low Energy-Density Quench in Pancake Coil
Notes: I do not have exact data for this one.

## Slide 26: Solver Comparison Benchmark
Ramp of simple pancake coil
Comparison of HETS, NICQS, COMSOL, FiQuS
3cm ID, 5cm OD
250 turns
Resolution
  16 azimuthal elements
  50 radial elements
  4 screening current divisions

## Slide 27: Solver Comparison Benchmark
Notes: We compared the results of a ramp of a non-insulated pancake coil
- Good agreement

## Slide 28: Solver Comparison Benchmark
Quantity | Average Error | Maximum Error
Elements | 3200 | 
B-Field | 6.9% | 8.6%
Voltage Delta | 0.8% | 1.3%
Stored Energy | 0.9% | 2.5%
Radial Losses | 0.5% | 2.4%
Quantity | Average Error | Maximum Error
Elements | 280 | 
B-Field | 8.2% | 11.7%
Voltage Delta | 0.6% | 2.6%
Stored Energy | 1.3% | 3.8%
Radial Losses | 0.6% | 2.2%
Notes: We compared the results of a ramp of a non-insulated pancake coil
Good agreement
Using coarse elements, the result is practically the same!

## Slide 29: Example: Racetrack Quenches
15 Meters
Elements | 1344
Inner Width | 30mm
Outer Width | 80mm
Turns | 80
Energy Density | 17.3 kJ/kg
Current | 10.000A

## Slide 30: Example: Racetrack Quenches
15 Meters
HETS operates at great scales
Solves in 90-100s!
Elements | 1344
Inner Width | 30mm
Outer Width | 80mm
Turns | 80
Energy Density | 17.3 kJ/kg
Current | 10.000A

## Slide 31: Example: Racetrack Quenches
There is no time constant that would protect this magnet
Not enough of the racetrack is quenched
  Not enough energy is dissipated
Energy Extraction Region
Insufficient Dissipation!
Notes: For low time constants, ramping down of the PSU behaves like an energy extraction system and high voltages are induced.
For high time constants the magnet does not dissipate energy autonomously.
Both do not work.

## Slide 32: Example: Racetrack Quenches
Far below quench threshold!
Current

## Slide 33: Other contributions

## Slide 34: STEAM Material Library
Refactored, cleaned out legacy files
Added multiplatform support for Windows and Linux
Numerous fixes
Worked on STEAM material library pipeline
  Automatic release builds
  Automatic PyPI deployment
Transition to CMake for compilation
…

## Slide 35: The Future

## Slide 36: The Future
Validation!
  Against real measurements and other solvers
  For more interesting cases
Then: Apply to more real problems
  Capacitor discharge protection?
  Protection parameter study
Matrix-free methods…
Iron-effects…
CAD import…
Thermal transfer models…

## Slide 37: Questions?
Leon Teichröb
University of Stuttgart leon.teichroeb@{cern.ch, protonmail.com}

## Slide 38: Poster Art 🚀

## Slide 39: Poster Art 🚀

## Slide 40: Poster Art 🚀

## Slide 41: Poster Art 🚀