## Slide 1: Grayloc Discussion
10/03/2025

## Slide 2: BDF Target complex integration
Mobile Shielding
Target
Upstream Shielding
Collimator
Vacuum confinement
In-Ground Shielding
Target station
Target area
Confinement wall
Access chicane
Diluted Proton beam from SPS
Space for shielding temporary storage
Beam instrumentation
SHIP experiment
Water cooled proximity shielding
Magnetised
shielding
Above Coil Shielding

## Slide 3: Vacuum Vessel Overview
Vacuum vessel containing helium-cooled target and water-cooled proximity shielding with a 10-3mbar vacuum
3.16 m
1.58 m
Cooling Pipes
1.5m Tungsten Target
Copper Alloy Proximity Shielding
2050mm
6410mm
2965mm

## Slide 4: Feedthrough Connections
DN200 Bellow
Grayloc connection to be fitted onwards from the bellows
Target Helium Cooling
Proximity Shielding water cooling
Extra feedthroughs for instrumentation

## Slide 5: Foreseen Parameters
Pipe Size: DN50
Pipe thickness: potentially 8-10mm
Pressure: 16 bar (a)
Temperature: 200 °C
Radiation level in this area: 1-5kGy/year
Flow rate: 400g/s
Leak rate: 10^-6 mbar.l/s
Medium: Helium gas
Expected lifetime: at least 15 years