## Slide 1: Challenges from collective effects in the design and modelling of Muon Colliders
D. Amorim, E. Métral
Thanks to S. Albright, F. Batsch, J. S. Berg, F. Boattini, C. Barbagallo, L. Bottura, X. Buffat, C. Carli, A. Chancé, H. Damerau, E. de la Fuente, M. Gast, A. Grudiev, I. Karpov, E. Kvikne, E. Lamb, N. Mounet, T. Pieloni, C. Rogers, G. Rumolo, M. Seidel, D. Schulte, L. Soubirou, K. Skoufaris, R. Taylor, L. Thiele, M. Vanwelde
BE seminar, 14th March 2025
This work was performed under the auspices and with support from the Swiss Accelerator Research and Technology (CHART) program (www.chart.ch).

## Slide 2
Overview of the Muon Collider
Some examples of collective effects
Collective effects in the Muon Collider

## Slide 3
Overview of the Muon Collider
Some examples of collective effects
Collective effects in the Muon Collider

## Slide 4: Overview of the Muon Collider complex
Muon decay with a lifetime of 𝝉0=𝟐.𝟐𝝁𝒔 but thanks to special relativity, the lifetime in the laboratory frame becomes 𝝉=𝛾𝜏0=47323⋅2.2𝜇𝑠=𝟏𝟎𝟒 𝒎𝒔 at 5 TeV
The challenge is to generate muon bunches with low emittance and accelerate them quickly enough to a high luminosity experiment
High power proton driver to generate high intensity muon beams
6D muon cooling to reach target emittances
Fast acceleration in Recirculating Linacs and Rapid Cycling Synchrotrons to counter-balance the muon decay
In the collider ring, small β* are needed to reach the luminosity target

## Slide 5: Proton driver and target
Generate high power proton beam, two options at 2 MW or 4 MW
  5 GeV or 10 GeV, 5⋅1014 protons on target, 2 ns bunch length, 5 Hz repetition rate
  Comparable to ESS: 5MW, 2 GeV, 14 Hz
Graphite target, surrounded by a tungsten shield and immerged in a strong solenoid field generated by High Temperature Superconductors
  Must withstand radiation flux and dissipate generated heat load
Graphite target
Tungsten shield
HTS solenoid
p+
µ+, µ-, π+, π-
C. Accettura et al.
Notes: https://ieeexplore.ieee.org/document/10443443
https://indico.cern.ch/event/1325963/contributions/5792975/attachments/2818936/4922081/IMCC_March2024.pdf

## Slide 6: Muon Cooling
Ionization cooling provided by Liquid Hydrogen wedge absorbers
Warm RF cavities to restore the beam longitudinal momentum
Solenoid magnet to focus the beam at the absorber location
R. Taylor
From Interim Report
Notes: From Interim report: https://arxiv.org/abs/2407.12450
Chris Rogers prensetation?

## Slide 7: Rapid Cycling Synchrotrons (RCS)
Large RF voltage are required to accelerate the beams: many RF cavities in each machine. E.g., 90 GV and 3000 cavities in RCS 4
  Fast ramping magnets are needed: e.g., 4200 T/s in RCS 1
Hybrid synchrotrons for RCS 2, 3 and 4: alternate fixed-field 10 T superconducting dipoles and pulsed 1.8T normal conducting dipoles to increase the energy swing
  This creates large orbit excursion in the dipole magnets
Machine parameters | RCS 1 | RCS 2 | RCS 3 | RCS 4
Circumference [km] | 6 | 6 | 10.7 | 35
Injection energy [GeV] | 63 | 313.8 | 750 | 1500
Energy increase per turn [GeV] | 14.7 | 7.9 | 11.3 | 63.6
Bunch intensity at injection [1012 muons] | 2.7 | 2.4 | 2.2 | 2.0
εt [µm rad] / εl [eV s] | 25 / 0.025 |  |  | 
L. Soubirou
Notes: Lisa Soubirou annual meeting: https://indico.cern.ch/event/1325963/contributions/5806746/attachments/2817648/4921129/Status_RCS_geometry_LSoubirou.pdf

## Slide 8: Collider
Achieve high luminosity, both instantaneous and integrated
  Small β* (1.5 mm), high bunch intensity 1.8·1012, 5 Hz repetition rate
Must minimize intensity losses per turn from muon decay
  Compact ring with high average dipole field
Challenging lattice design with strong final focus magnets creating large chromatic aberrations
Parameters | Stage 1 Collider 3 TeV | Stage 2 Collider 10 TeV
Circumference [km] | 4.5 | 10
Beam energy [TeV] | 1.5 | 5
Instantaneous luminosity [1034 cm-2s-1] | 2.1 | 21
Bunch intensity at injection [1012 muons] | 2.2 | 1.8
Repetition rate [Hz] | 5 | 5
Bunch length at IP [mm] | 5 | 1.5
β* at IP [mm] | 5 | 1.5
εt [µm rad] / εl [eV s] | 25 / 0.025 | 
K. Skoufaris, M. Vanwelde
Notes: Marion presentation: https://indico.cern.ch/event/1325963/contributions/5806746/attachments/2817648/4921129/Status_RCS_geometry_LSoubirou.pdf
Kyriacos:

## Slide 9: Implementation studies
Muon Collider collaboration is based on a “Greenfield” facility
Studies have been started to implement a Muon Collider on CERN site or Fermilab site
  Could reuse existing tunnels and fit most of the facility on CERN lands
  Collider placement need to be carefully assessed to mitigate neutrino flux
Implementation of a muon cooling test facility at CERN is also studied

## Slide 10
Overview of the Muon Collider
Some examples of collective effects
Collective effects in the Muon Collider

## Slide 11: Direct space charge
In a bunch, particles are subject to Coulomb repulsion Once in motion, the induced magnetic field creates an attractive force But at low energies this force does not sufficiently compensate the Coulomb force
This force depends on the transverse distribution of the particles and is non-linear for Gaussian bunches
K. Schindl, Space Charge

## Slide 12: Impedance / Wakefields
The charged bunches interact electromagnetically with their environment: vacuum chamber, RF cavities, flanges etc.
Impedance (frequency domain)/wakefields (time domain) characterize these interactions
  They can be computed with 3D electromagnetic simulations or analytical models
These fields can perturb the following bunch, or the bunch itself
Careful design of the accelerator equipment can reduce these parasitic fields
E. de la Fuente
Cavity transverse impedance model
Turn-by-turn headtail signal
Notes: Add

## Slide 13: Beam-beam interactions
Bunches generate an electromagnetic field
When two bunches cross each other, the fields generated by one bunch perturb the other bunch
These effects are non-linear, and depend on the particle distribution, the number of bunches etc.
Muons
Antimuons
Interaction Point
Amplitude
W. Herr and T. Pieloni, Beam-beam effects

## Slide 14
Overview of the Muon Collider
Some examples of collective effects
Collective effects in the Muon Collider

## Slide 15: Collective effect challenges identified for the Muon Collider
Collaboration roadmap in 2021 identified twelve items for beam dynamics and collective effects, based on studies previously done by the US Muon Accelerator Program
R. Ryne, T. Raubenheimer, E. Métral

## Slide 16: Collective effects challenges in the Rapid Cycling Synchrotrons (RCS)
Large RF voltage are required to accelerate the beams: many RF cavities in each machine. E.g., 90 GV and 3000 cavities in RCS 4
  Synchrotron tune in RCS 1 at injection, well above the longitudinal phase space stability criteria
  The cavities must be distributed along the ring to preserve longitudinal focusing
Fast ramping magnets are needed: e.g., 4200 T/s in RCS 1
  The vacuum chamber must be designed to both minimize eddy current effects and beam coupling impedance

## Slide 17: Impedance model for the RF cavities
Wake function for the two types of cavity studied
Impedance function for the Low Loss cavity HOMs
1.3GHz superconducting TESLA cavity has been considered for the studies for their high gradient (30 MV/m per cavity is assumed)
The High Order Modes (HOMs) of the cavities are the main concern for transverse stability
Two variants of this cavity have been studied: the classic TESLA and the Low Loss type
  TESLA cavities are used at European XFEL and are ILC baseline
  Low Loss type have been studied to reach higher accelerating gradient, at the cost of stronger HOMs
1 σz
Notes: TESLA cavity: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.3.092001

## Slide 18: Vacuum chamber design constraints for the pulsed magnets
Ramp rate are large e.g. 4200 T/s in RCS 1, therefore, large eddy current losses would appear in a classic metallic vacuum chamber
A ceramic chamber must be used, with longitudinal stripes to maintain continuity for the beam image current
Eddy current losses are drastically reduced and become acceptable for thinner stripes
M. Kinsho, J-PARC
E. Kvikne
Notes: Erik Kvikne: https://indico.cern.ch/event/1437002/contributions/6061674/attachments/2903847/5093368/Wrap-up_on_Eddy_Current_E
JPARC: https://indico.fnal.gov/event/16269/contributions/36516/attachments/22688/28130/J-PARC-RCS-Vacuum-Chambers.pdfffects_in_the_NC_RCS_Vacuum_Chamber.pdf

## Slide 19: Impedance model for the RCS vacuum chamber
Impedance and its impact on transverse beam stability must be assessed
Provide the magnet and vacuum team with design input such as metallic coating thickness or minimum chamber radius
Chamber impedance is computed with ImpedanceWake2D
Example study to check the impact of a metallic coating.
  Radius constant at 10mm, ceramic thickness set to 5mm
Iron yoke
Ceramic
RF shield
100mm
30mm
Copper
Ceramic
10mm
5mm
Impedance model
Notes: Ref: Erik presentation annual meeting
Ref: IW2D

## Slide 20: Impedance model for the RCS vacuum chamber
Transverse dipolar impedance for 1m of chamber
An uncoated ceramic (blue curve) created strong resonances: detrimental for impedance
Adding a 100 nm inner metallic coating (green curve) damps these resonances
E. Kvikne

## Slide 21: Tracking simulations for the RCS chain
We must ensure that bunch intensity and transverse emittance are preserved through the acceleration chain
Macroparticle tracking simulations are performed using the Xsuite framework
  A single muon bunch is tracked through the chain of four accelerators
  The RF cavities (700 in RCS 1, 3000 in RCS 4) and their wakefield elements are regularly placed in 32 stations along the ring
17 turns
55 turns
66 turns
55 turns
RCS 1
63 – 313 GeV
RCS 2
313 - 750 GeV
RCS 3
750 -1500 GeV
RCS 4
1.5 -5.0 TeV
Beam monitor
RF station and Impedance
Transverse damper
Notes: Ref xsuite

## Slide 22: Particle tracking simulations for the RCS chain
Macroparticle tracking allows to simulate the effect of the RF cavities wakefield on the beam
  Simulations showed here only include the RF cavity wakefield

## Slide 23: Particle tracking simulations for the RCS chain
Bunch is matched longitudinally at injection into RCS 1
Some particles are lost in the first turns after injection
There is longitudinal emittance blow-up
Macroparticle tracking allows to simulate the effect of the RF cavities wakefield on the beam
  Simulations showed here only include the RF cavity wakefield

## Slide 24: Particle tracking simulations for the RCS chain
Large horizontal bunch oscillation
Transverse emittance blow-up in RCS 1
Macroparticle tracking allows to simulate the effect of the RF cavities wakefield on the beam
  Simulations showed here only include the RF cavity wakefield
The large number of RF cavities create strong, short range wakefields
A fast transverse instability can develop in the RCS and generate emittance blow-up and beam losses

## Slide 25: Particle tracking simulations for the RCS chain
The large number of RF cavities create strong, short range wakefields
A fast transverse instability can develop in the RCS and generate emittance blow-up and beam losses
Introducing positive chromaticity and a transverse damper can mitigate the instability
Transverse oscillations are damped
No emittance blow-up

## Slide 26: Impact of the different type of RF cavities
The large number of RF cavities create strong, short range wakefields
A fast transverse instability can develop in the RCS and generate emittance blow-up and beam losses
Introducing positive chromaticity and a transverse damper can mitigate the instability
Parametric tracking simulations were performed, investigating the impact of transverse damper, chromaticity, initial beam offset or RF cavity type
Chromaticity Q’=0
Chromaticity Q’=+20
Heatmap of emittance growth through the RCS chain, scanning transverse damping time and bunch offset
Low Loss cavity
TESLA cavity

## Slide 27: Collective effects challenges for the 10 TeV collider
Short bunch length σz=1.5 mm and large Δp/p0 = 10-3
  Very large RF voltage would be needed, even with small slippage factor (GV range with η ~ 10-6) → unpractical
  Operation with minimal RF (to compensate synchrotron radiation losses) is foreseen. It implies correcting η to zero to obtain an isochronous ring
Resistive wall would be the main contributor to transverse impedance
Tungsten liner is required to shield the superconducting coils from muon decay products
D. Calzolari

## Slide 28: 10 TeV collider impedance model
Assume 10 km resistive wall impedance for the collider
Scan the chamber radius and the copper coating thickness
Goal: find the minimum chamber radius and coating thickness admissible for transverse coherent stability
 | Tungsten 300K | Copper 300 K
Resistivity [nΩ m] | 54.4 | 17.9
23 mm chamber radius Different copper coating thickness
Copper
Tungsten
Scan
40 mm

## Slide 29: Particle tracking simulation for the collider
Muon half-life at 5 TeV is t1/2 = ln(2)·ɣ·τ0 = ln(2)·47323·2.2μs = 72 ms
  In the 10 km collider ring, this corresponds to ~2200 turns
  The luminosity quickly decreases after the bunch injection
The muon decay effect was added to transverse stability simulations
It is essential to preserve the transverse emittance to maximize luminosity at the interaction points
Despite the bunch intensity reduction over time, a beam break-up instability can appear
Example here with a 23 mm radius, copper coated tungsten chamber

## Slide 30: Particle tracking simulation for the collider
Introducing some small, positive or negative chromaticity helps mitigate the instability by introducing some tune spread
Parametric tracking simulations were performed to evaluate the impact of different chromaticities, transverse damper strength or initial bunch offset
Heatmap of emittance growth through after 1600 turns in the collider, scanning transverse damping time and bunch offset
Notes: See p. 561 of K.Y. Ng book, https://doi.org/10.1142/5835

## Slide 31: Minimum vacuum chamber radius admissible in the collider
Use tracking simulations to assess transverse stability limitation versus chamber radius and coating thickness
With 10 μm copper coating, the chamber radius must be at least 16 mm (without damper)
A. Lechner et al., Design meeting 09/2023
Requirement from optics
It is below the 23.5 mm assumed in the dipole magnet radial build, constrained by the lattice design

## Slide 32: Collective effect challenges identified for the Muon Collider
Collaboration roadmap in 2021 identified twelve items on beam dynamics and collective effects
Items showed in this presentation
Impedance models and beam dynamic simulations available at gitlab.cern.ch/muon-collider-bd/muc-impedance
Mitigation measures: sextupoles and damper are needed in the RCS
R. Ryne, T. Raubenheimer, E. Métral

## Slide 33: Collective effect challenges identified for the Muon Collider
R. Ryne, T. Raubenheimer, E. Métral
Collaboration roadmap in 2021 identified twelve items on beam dynamics and collective effects
Initial beam-beam studies for the 10 TeV collider
RCS chain parameter optimization: python package developed with RF, powering and optics team available at gitlab.cern.ch/muon-collider-bd/rcsparameters and web tool at rcsparameters.web.cern.ch
Comparison of different approaches for analytical coherent space charge estimation in the proton driver (IPAC 25 proceeding to be published)
Other items addressed

## Slide 34: Collective effect challenges identified for the Muon Collider
R. Ryne, T. Raubenheimer, E. Métral
Collaboration roadmap in 2021 identified twelve items on beam dynamics and collective effects
Collective effects in the ionization cooling
  High bunch intensity up to 40·1012 muons/anti-muons at start of cooling
  Many RF cavities to maintain the beam energy
  Wakefield effects in the liquid hydrogen absorbers
Two beam wakefield in the RCS, with multiple RF stations
Items currently investigated

## Slide 35: Conclusion and outlook
The Muon Collider complex hosts a variety of accelerators with different beam dynamics regime
  The high bunch intensity, the cooling and the quick acceleration pose unique challenges for the high-energy part of the chain
Collective effects studies are critical to ensure that the collider performance can be reached
  Providing input for the RF, magnet, vacuum and optics design teams
  With the proper mitigation measures and careful design choices, transverse beam stability can be ensured in the RCS chain and the 10 TeV collider
  Still a lot of effects to be investigated in the high energy part: beam-beam in the RCS, two beam wakefield etc.
Collective effects in the muon cooling are now the focus: high bunch intensity, low energy (β~0.9), large number of cavities, wakefield effect inside absorbers

## Slide 36: References
Transverse impedance and beam stability studies for the muon collider ring, IPAC 23
Transverse impedance and beam stability studies for the muon collider Rapid Cycling Synchrotrons, IPAC 23
Transverse Coherent Instability Studies for the High-Energy Part of the Muon Collider Complex, HB 2023
Transverse Collective Effects studies for a Muon Collider, ICHEP 2024
Coherent Beam-Beam effects in a Muon Collider, Beam Beam workshop 2024
IMCC and MuCol annual meeting 2024
IMCC annual meeting 2023
IMCC annual meeting 2022
Interim report for the International Muon Collider Collaboration (IMCC)
MuCol Milestone Report 5: Preliminary parameters

## Slide 38: Beam and machine parameters for the RCS
Machine parameters | Unit | RCS 1 | RCS 2 | RCS 3 | RCS 4
Circumference | m | 5990 | 5990 | 10700 | 35000
NC magnet length | m | 3655 | 2539 | 4366 | 20376
Bunch intensity | 1012 | 2.7 | 2.7 | 2.7 | 2.7
Beam momentum | GeV/c | 63 | 313.8 | 750 | 1500
Energy increase per turn | GeV | 14.7 | 7.9 | 11.3 | 63.6
Rev. frequency | kHz | 50 | 50 | 28 | 8.6
RF frequency | MHz | 1300 | 1300 | 1300 | 1300
Harmonic number |  | 25957 | 25957 | 46295 | 151433
RF voltage | GV | 20.9 | 11.22 | 16.1 | 90.0
Number of RF stations |  | 32 | 32 | 32 | 32
αp |  | 0.0024 | 0.0024 | 0.001 | 0.001
Avg. beta x/y | m | 50 / 50 | 50 / 50 | 50 / 50 | 50 / 50
Chromaticity Q’x/Q’y |  | scan | scan | scan | scan
Detuning from octupoles x/y | m-1 | 0 / 0 | 0 / 0 | 0 / 0 | 0 / 0
Parameters from F. Batsch RCS tables
Beam parameters | Unit | Value
Bunch length 1σ | mm | 5.7
Bunch intensity | Particles per bunch | 2.7e12
εx / εy | μm rad | 25
# of macropaticles |  | 400k
# of turns wakefield |  | 5
# of slices wakefield |  | 2000

## Slide 39: Beam and machine parameters for the Collider
Machine parameters | Unit | Collider 10 TeV
Circumference | m | 10000
Bunch intensity | 1012 | 1.8
Beam momentum | GeV/c | 5000.0
Energy increase per turn | GeV | 0
Rev. frequency | kHz | 30
RF frequency | MHz | 1300
Harmonic number | - | 43478
RF voltage | GV | 0
αp | - | 0.0
Avg. beta x/y | m | 85 / 51
Chromaticity Q’x/Q’y |  | Scan Q’x/Q’y=0
Detuning from octupoles x/y | m-1 | 0 / 0
Beam parameters | Unit | Value
Bunch length 1σ | mm | 1.5
Bunch Δp/p0 1σ | - | 1e-3
Bunch intensity at inejction | Particles per bunch | 1.8e12
Longitudinal emittance εl = σzσE | MeV m | 7.5
Transverse emittance εx / εy | μm rad | 25
# of macropaticles | - | 200k
# of turns wakefield | - | 5
# of slices wakefield | - | 2000
Not relevant since RF voltage is set to zero

## Slide 40: High order momentum compaction
Higher order terms can impact the longitudinal beam dynamic
Example effect of higher order momentum compaction factor on RF bucket (with RF votage)