## Slide 1: Ηλεκτρονικά συστήματα λήψης δεδομένων στα Πειράματα Φυσικής Υψηλών Ενεργειών
Kostas Kloukinas
CERN
Electronics System for Experiments group
Microelectronics section

## Slide 2: Η αποστολή του CERN
LHC
CERN Site (Meyrin)
SPS
Έρευνα & Ανακάλυψη
Εκπαίδευση & Κατάρτιση
Τεχνολογία
Συνεργασία

## Slide 3: Μέθοδοι της Σωματιδιακής Φυσικής
Τα Σωματίδια συγκρούονται με ταχύτητες παραπλήσιες με αυτή του φωτός με αποτέλεσμα την παραγωγή νέων σωματιδίων
Τα νέα σωματίδια περνούν μέσα από το χώρο των ανιχνευτών των πειραμάτων και παράγουν ηλεκτρικά σήματα

## Slide 4: Εγκάρσια τομή του πειράματος CMS
4 T magnetic field in the tracker to bend the particle tracks

## Slide 5: Τα Ηλεκτρονικά των Πειραμάτων
Ανίχνευση και Ενίσχυση Σήματος
  Οι αλληλεπιδράσεις των σωματιδίων δημιουργούν ασθενή ηλεκτρικά σήματα στους ανιχνευτές.
  Προενισχυτές χαμηλού θορύβου ενισχύουν τα σήματα σε μετρήσιμα επίπεδα
Επεξεργασία Σήματος και Λήψη Δεδομένων (DAQ)
  Ψηφιοποίηση και επεξεργασία για την εξαγωγή σημαντικών πληροφοριών, όπως η ενέργεια, ο χρόνος και η θέση της αλληλεπίδρασης των σωματιδίων.
  Τα συστήματα σκανδαλισμού (Τrigger) εντοπίζουν σημαντικά γεγονότα, φιλτράροντας τον θόρυβο του υποβάθρου και μειώνοντας τον όγκο των δεδομένων πριν από την αποθήκευση.
Μετάδοση και Συγχρονισμός Δεδομένων
  Τα επεξεργασμένα δεδομένα πρέπει να μεταδοθούν αποτελεσματικά σε κεντρικά υπολογιστικά συστήματα για περαιτέρω ανάλυση.
  Ο ακριβής χρονισμός και ο συγχρονισμός είναι κρίσιμος για τη συσχέτιση σημάτων από διαφορετικά μέρη του ανιχνευτή.

## Slide 6: Συλλογή & Διαλογή των Δεδομένων
40x106 φωτογραφίες /sec
20 συγκρούσεις ανά φωτογραφία
Το πρώτο φιλτράρισμα των μετρήσεων γίνεται στους ανιχνευτές δίνοντας 100x103 φωτογραφίες /sec
Το δεύτερο φιλτράρισμα των μετρήσεων γίνεται από συστοιχίες υπολογιστών δίνοντας 1 φωτογραφία /sec για εγγραφή και μετέπειτα ανάλυση
Τα πειράματα του LHC παράγουν 10-15 Petabytes δεδομένων κάθε χρόνο (20 εκατομμύρια CDs!)
Για την ανάλυση των δεδομένων χρειάζεται η υπολογιστική ισχύς που αντιστοιχεί σε ~100,000 γρήγορους μοντέρνους επεξεργαστές.

## Slide 7: Η ροή των δεδομένων

## Slide 8: Το Παγκόσμιο Υπολογιστικό Δίκτυο

## Slide 9: Microchips for Megastructures
CMS experiment at the LHC accelerator at CERN
Silicon Tracker Hybrid
On-detector ASIC
Off-detector electronics
Notes: Since the career we are reviewing today is buillt on detector electronics I believe that it is appropriate to spend a couple of minutes to introduce you to the world of electronics for particle physics experiments in hadron colliders.
These electronics are generaly divided in two distinct parts. The on-detector electronics and the off detector electronics. The on-detector electronics are realised with Application Specific Integrated Circuits (ASICs) and their role is to amplify the weak electrical signals that the particles generate with their passage through the sensors, to digitize them, perform some signal processing and finaly transmit them to the off-detector electronics for further processing.

## Slide 10: ASICs στη Φυσική Υψηλών Ενεργειών
ASIC Application-Specific Integrated Circuits Ολοκληρωμένα Κυκλώματα εξειδικευμένης εφαρμογής
Ιδιαίτερα εξειδικευμένες λειτουργίες
  Ειδικές τεχνικές επεξεργασίας σήματος
  Υψηλή ανάλυση και μεγάλο δυναμικό εύρος
Πολύ μεγάλος αριθμός καναλιών ανάγνωσης
  Χαμηλή κατανάλωση ενέργειας
Περιβάλλον έντονης σωματιδιακής ακτινοβολίας
  TID (Total Ionizing Dose) of 500 Mrads up to 1 Grad
    Space applications requirements: up to 200 Krads
  SEE (Single Event Effects)
    Particle fluence ~1015 cm-2 (inner tracker layers)

## Slide 11: Silicon Strip Detector electronics
Pre-amplifier
Shaper
Discriminator
or ADC
Threshold
Pipeline memory
LHC clock
40 MHz
Other channels
Multiplexer
Optical Transmission
On-detector electronics
ASIC (Application Specific Integrated Circuit)
Silicon-strip detector
1/0
Threshold
Very small signal (~fC) Needs amplification
Digitized signal (1/0) Signal above a preset threshold
t(ns)
Cf
+
-

## Slide 12: Cms preshower detector
The case of the

## Slide 13: Analog Electronics
Analog ASIC (Application Specific Integrated Circuit)
Ανιχνευτής λωρίδων πυριτίου
6cm x 2mm Si strip, 300um thick, produces ~4fC/mip*
*mip: minimum ionizing particle
Πολύ ασθενές σήμα για μετάδοση σε 100 μέτρα

## Slide 14: Digital Electronics
ADC: Ψηφιοποίηση των παλμών
Συγχώνευση, μορφοποίηση και μετάδοση με οπτικές ίνες
Το μεγαλύτερο πλεονέκτημα των ψηφιακών ηλεκτρονικών έναντι των αναλογικών είναι η ανθεκτικότητα στον θόρυβο και η ακεραιότητα του σήματος.

## Slide 15: Digital ASIC
Λειτουργικό Διάγραμμα Ψηφιακού ολοκληρωμένου
Μικροφωτογραφία του ολοκληρωμένου

## Slide 16: Sensor modules with ASICs

## Slide 17: Μητρική κάρτα με 10 ανιχνευτές

## Slide 18: Συναρμολόγηση του ανιχνευτή

## Slide 19: Συναρμολόγηση του ανιχνευτή

## Slide 20: Pixel Detector electronics
Velopix readout ASIC for the LHCb detector

## Slide 21: CMS Pixel Inner Tracker

## Slide 22: Pixel Sensors in Medical Imaging
New X-ray technology produces striking 3D images in full colour
A new medical imaging device uses technology developed by particle physicists to produce full colour, 3D images of the human body.
A hybrid detector capable of counting each individual particle hitting the pixels and measure its energy.

## Slide 23: Cms outer tracker @ HL-LHC
The case of the

## Slide 24: Phase-2 upgrade challenges
  LHC  HL-LHC: sustained luminosity of 5x1034 cm-2s-1
  From 20  200 pileup events per BX
  μ, e and jets at exceedingly high rates
    Add tracking information to the Level-1 trigger decision to keep trigger rate at an acceptable level
    Performance of trigger algorithms degrades with increasing pile-up
    Reject locally signals from low-pT particles (< 2GeV/c)
    Reduce data volume by one order of magnitude making transmission feasible for the available power budget
    Simplify track finding algorithms
⟨Pile-up⟩ ~ 20
⟨Pile-up⟩ ~ 200
Notes: The capacity of performing quick recognition of particles with high transverse momentum in the inner tracker is essential to keep CMS trigger rate at an acceptable level
A possible option is to anticipate the use of tracking information in the Level-1 selection, along the lines of what is done today in the HLT

## Slide 25: Intelligent particle tracking system
The CMS OT detector working principle of pT discrimination
  Exploit the strong magnetic field of CMS
  Correlate signals between two closely spaced sensors to identify “stubs”
  Stubs defined as a track coordinate + angle based on tracking window on parallel sensor
  Transmit stub coordinates and momentum instead of a multiplicity of hits
FE
Stub finding
L1 triggered data (up to 106 events/s)
Stream data of encoded information of high pT particles (40 MHz frame rate)
3.8T provided by the superconducting solenoid
2 mm
Interaction point
> 200 mm
ʘ
B
Pipeline memory
L1 Trigger @ 1MHz (max)
Τοπικό φιλτράρισμα τροχιών
με βάση την εγκάρσια ορμή (PT) των σωματιδίων
και μετάδοση στο Σύστημα Σκανδαλισμού
μόνο των ενδιαφερόντων ιχνών

## Slide 26: MPA-SSA Readout Concept
Two distinct data paths:
*DAQ: Async transmission 1 MHz event rate, 320 Mbps data rate
*Trigger: Sync transmission 40 MHz frame rate,
1 Gbps data rate
MPA
FE
SRAM
Data
Formatting
Binary
Readout
Stub Finding Logic
FE
Binary
Readout
SSA
Strips
Pixels
Level-1 accept
SRAM
Encoder Logic
DAQ* path
Trigger*
path
Level-1 accept
Level-1 accept
SSA-to-MPA interconnect
40MHz LHC clock
40MHz LHC clock
40MHz LHC clock

## Slide 27: CMS Tracker Pixel-Strip (PS) module
MPA
SSA
CIC
2.8 mm
6.5 mm
Design Teams
  CERN (MPA, SSA, CIC)
    Alessandro Caratelli
    Davide Ceresa
    Jan Kaplon
    Gianmario Bergamin
    Simone Scarfi
    Kostas Kloukinas
  Lyon IPNL/IN2P3 (CIC)
    Luigi Caponetto
    Geoffrey Galbit
    Benedetta Nodari
    Sebastian Viret
Challenging project
  Interoperability and event-by-event synchronization of all ASICs
  MPA ASIC design challenges due to large die size
  Low Power consumption
CMS Outer Tracker PS-Module
  MPA: Macro Pixel ASIC
  SSA: Short Strip ASIC
  CIC: Concentrator ASIC
Notes: Coming to the more recent years of my career, and perhaps the most interesting and more challenging project in my career is the development of the on-detector ASICs for the HL-LHC upgrades of the CMS Outer Tracker.
The Outer tracker detector is novel detector featuring real-time on-detector event processing and filtering thus enabling the inclusion of tracking information in the trigger system. By exploiting the CMS strong magnetic field and correlating signals between two closely spaced sensors (a pixel sensor and a strip sensor) we can reject locally from low Pt particles.
The project requires the development of three ASICs. The MPA; the pixel sensor readout ASIC, the SSA; the strip sensor ASIC and the CIC; data concentrator ASIC.
In this project I am the principal ASIC & system engineer and I manage to AASIC design teams. One at CERN, being responsible for the MPA and SSA chips and one in Lyon being responsible for the CIC.
There are two main challenges in this project: You need to achieve clock-cycle synchronization across the chipset for the coincidence and cluster finding operations to work and to implement the MPA ASIC which has a die size similar to a CPU of a computer.

## Slide 28: MPA wafers

## Slide 29: MPA ASIC wafer probe test
MPA ASIC
Production 1,000 wafers

## Slide 30: PS module assembly
13 296 Modules
44 Mstrips + 174 Mpixels
200m2 of silicon area

## Slide 31: Σχεδίαση για τα πειράματα Φυσικής
ASIC Design Teams
Fabrication Plant
EDA Software
Dicing and shorting

## Slide 32: Some examples of ASICs in CMS

## Slide 33: Some examples of ASICs in ATLAS

## Slide 34: Example ASICs for HL-LHC

## Slide 35: modern microelectronics

## Slide 36: Το βασικό στοιχείο: Transistor
FET : Field Effect Transistor Τρανζίστορ επίδρασης πεδίου
FET ως ενισχυτής σε Αναλογικά κυκλώματα
FET ως διακόπτης σε Ψηφιακά κυκλώματα
Δημιουργία αγώγιμου καναλιού

## Slide 37: CMOS Transistors
NMOS
PMOS
CMOS : Complementary Metal Oxide Field Effect Transistor
Η πράξη της αναστροφής (INVERT) στην ψηφιακή λογική με χρήση συμπληρωματικών τρανζίστορ CMOS
Input | Output
0 | 1
1 | 0
0
1
1
0

## Slide 38: CMOS Logic Gates
Basic CMOS Logic Gates and their truth table
Basic CMOS Logic Gate Symbols

## Slide 39: Logic Gate Circuit examples
4-bit Adder with fast carry
Binary to 7-segment display decoder

## Slide 40: O πρώτος επεξεργαστής
1971
2,300 transistors

## Slide 41: Εξέλιξη των επεξεργαστών
16-core CPU with
12 performance cores with up to 4.06 GHz AND
4 efficiency cores with 2.8 GHz.

## Slide 42: Moore’s Law
The observation is named after Gordon Moore, the co-founder of Fairchild Semiconductor and Intel

## Slide 43: Feature Size and Process Node
Feature Size measured in Nanometers The size of the features (the elements that make up the transistors) are measured in nanometers Historically, the feature size referred to the length of the silicon channel between source and drain in field-effect transistors. Today, the feature size is typically the smallest element in the transistor.
A 25 nm process technology refers to features 25 nm or 0.025 µm in size. Also called a "technology node" and "process node”.

## Slide 44: ASIC development costs
* According to the survey from the International Business Strategy Corporation (IBS), the increase of design cost for each generation technology has exceeded 50% after 22 nm process, including EDA, design verification, IP core, tape-out, and so forth.
Chip Design and Manufacturing Cost under Different Process Nodes: Data Source from IBS*
2004
2011
2019
2017
2015

## Slide 45: Διαδικασία κατασκευής ημιαγωγών

## Slide 46: CMOS Photomask Lithography
US$378 million EUV lithography machine
Photomasks

## Slide 47: CMOS Fabrication

## Slide 48: Semiconductor Foundry (Plant)
Construction cost of a modern Plant: $5 - $20 billion

## Slide 49: A Major semiconductor manufacturer

## Slide 50: Semiconductor Industry
Source: WSTS and SIA analysis
[1] McKinsey & Company. The semiconductor decade: A trillion-dollar industry. April 1, 2022.

## Slide 51: Επίλογος
Η ηλεκτρονική και ιδιαίτερα η μικροηλεκτρονική είναι τεχνολογίες κλειδιά στην οργανολογία των πειραμάτων φυσικής σωματιδίων.
Οι επόμενες γενιές πειραμάτων θα απαιτούν μεγαλύτερη επεξεργασία σήματος σε προγραμματικό χρόνο από τα ηλεκτρονικά των ανιχνευτών και ενδεχομένως χρήση Machine Learning
Η πρόσβαση σε τεχνολογίες αιχμής και η προσέλκυση εφευρετικών τεχνολόγων, μηχανικών και φυσικών αποτελούν τα εχέγγυα των κατασκευών των μελλοντικών πειραμάτων
CMS Tracker 2006

## Slide 52
Thank You