## Slide 1: Current design status of the Synchrotron Radiation Absorber of the FCC-ee
Stefania Grozavu, Marco Morrone
TE-VSC Seminar
17th June 2025

## Slide 2
FCC-ee: Synchrotron Radiation
accelerator center
N↓
S↓
γ
dipole

## Slide 3
accelerator center
N↓
S↓
γ
Beam enery loss: Synchrotron Radiation (SR)
dipole
FCC-ee: Synchrotron Radiation

## Slide 4
γ
Beam enery loss: Synchrotron Radiation (SR)
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
FCC-ee: Synchrotron Radiation

## Slide 5
γ
Beam enery loss: Synchrotron Radiation (SR)
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
FCC-ee: Synchrotron Radiation
_______
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
Running Mode | Z | WW | ZH | 
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Energy loss / turn [GeV] | 0.039 | 0.369 | 1.86 | 9.94
Synchrotron radiation power [MW] | 100 | 100 | 100 | 100
highest SR surface power density

## Slide 6
γ
Synchrotron Radiation Absorber (SRA)
vacuum chamber (VC)
SRA
Placement | localized absorber placed in the external winglet of the VC
Integration | laser welding of SRA into dedicated aperture
Design | slanted SR impinging surface with saw tooth profile
Manufacturing | Powder Bed Fusion 3D Printing
Material | CuCrZr
Cooling | water circuit
Conceptual design of the SRA:
water cooling circuit
saw tooth profile
⌀ 60 mm
390 mm
0.2 mm
⌀ 14 mm

## Slide 7
SF · < 500 MPa
Synchrotron Radiation
Absorber (SRA)
Dipole
Dipole
Quad & Correctors
Cooling Circuit Design
Arc Half-Cell Layout
SynRad+ Simulations
SRA geometry and cooling circuit design
SRA Thermo-mechanical characterization with FEM simulations
SRAs Locations
SR power deposition [W/mm²]
SRA geometrical model
Temperature and stress ()
Experimental validation
Real performance
Material Properties of CuCrZr
Yield Strength ~ 500 MPa

## Slide 8
2D Thermo-Mechanical Simulation
Heat convection: heat transfer coefficient, h [W/(m2K)]
(1)
SR Power [W/m]
CuCrZr
k = 360 W/(m*K) - thermal conductivity
α = 20.3e-6 1/K - thermal expansion
Copper
Experimental correlations from literature:
Heat conduction
(2)
Combining equations (1) and (2):
The objective is to minimize
conduction term
convection term

## Slide 9
2D Thermo-Mechanical Simulation
100
200
300
400
500
600
700
800
0
58.7
117.4
176.1
234.8
293.5
0
Asymptotic limit
1.00
1.25
1.50
SF
[MPa]
[gr/s]
Temperature [°C]
Von Mises stress [MPa]
500 =
450
400
350
300
250
200
150
100
0
220
180
140
100
60
27 =
Dittus and Boelter correlation: smooth channel
Manglik and Bergles correlation: twisted tape insert
n. of channels
0 1 2 3 4 5
= 15500 W/(m2K)
= 22000 W/(m2K)
adding channels
improving positioning
remove channel
h↑
remove channel
adding tapes
adding fins
Circular channels with d = 5 mm

## Slide 10
Fluid Thermo-Dynamics Simulations
Computational Fluid Dynamics (CFD)
Heat transfer coefficient:
Nusselt number:
where and
hydrodynamic field
thermal field

## Slide 11
Fluid Thermo-Dynamics Simulations
CFD potential for the SRA design:
Hydrodynamic characterization:
  Pressure and velocity distribution
  Developing flow regions (bends and cross-section variations)
  Backflow or stagnant fluid (source of vibrations)
Thermal characterization:
  Temperature distribution
  Heat transfer coefficient (substituting empirical correlations)

## Slide 12
near-wall region
fluid domain
Fluid Thermo-Dynamics Simulations
14000
16000
18000
20000
22000
24000
26000
12000
1
2
3
4
5
0
Exact Asymptotic CFD Solution
Mesh size [Million Elements]
6
Heat Transfer coefficient, h [W/m²K]
0.8% error
2.0% error
5.1% error
12.6% error
60.0% error
CFD results
Mesh Sensitivity Study
Perform simulation on ≥ 3 levels of mesh refinement
Extract value of a representative variable for comparison
Extrapolate the exact asymptotic CFD Solution
Asses the error committed for each refinement level
Decide the adequate mesh size
mesh refinement
coarse
fine
Refinement ratio: 1.25
Element size:
Smooth Circular Channel

## Slide 13
Experimental Validation
Measurement capabilities of the test setup:
Pressure drop:
Heat power absorption:
Heat transfer coefficient:
convergence
control valve
water tank
pump
test specimen
mixing section
flow meter
T
P
temperature sensor
pressure sensor

## Slide 14
Experimental Validation
After mastering the experimental validation for the benchmark case…
Experimental Validation Goals:
Asses cooling performance of different channels geometry
Asses thermo-mechanical performance of locally heated SRA
twisted-tape
double twisted-tape
lattice
waves
thermal bridge
4 x 1kW cartridges

## Slide 15
Key Takeaways
Current design status:
Cooling circuit current design: 3 cooling channels of 5-mm-diameter with twisted-tape
  Maximum mean velocity: 3 m/s (due to copper erosion limitation)
  Flow rate: 176 g/s /absorber → 352 g/s /cooling line
  Cooling water inlet temperature: 27°C
  Mean fluid temperature increase: 4.75°C /absorber
Thermo-mechanical results:
  Maximum temperature: 184°C
  Maximum Von Misses Stress: 360 MPa (Safety Factor of 1.4) (highly localized)
  Pressure drop: 0.7 bar /absorber
Work in progress:
CFD simulations on the different geometries
Coupled simulations of fluid and solid domain on the SRA
Upgrade and fine tunning of the test setup
Experimental characterization of different geometries of the cooling channels
Experimental characterization of the heated absorber
= 360 MPa
= 184°C

## Slide 16: Thank you for your attention!