## Slide 1
RPC and (M)RPC:
an historical-conceptual approach
Marcello Abbrescia
University and INFN Bari, Italy
DRD1 gaseous detector school
FTD, University of Bonn, Germany, September 17-24, 2025

## Slide 2
Ingredients for a gaseous detector
2
Marcello Abbrescia
DRD1 school 2025
2. An electric field:
  ion-electron recombination in its absence;
  must be intense enough (order of 1 MV/m) to allow multiplication processes;
  multiplication processes are necessary because number of primary ion-electron pairs is just few tens/mm (to be compared with 23400 electrons-hole pairs in 300 μm of Si).
1. A gas volume:
  where (almost) everything takes place;
  in principle can have arbitrary shape.
3. Suitable readout electrodes:
  readout electrodes sometimes coincide with high voltage electrodes, but they are conceptually different.

## Slide 3
Working principles of gaseous detectors
3
Marcello Abbrescia
DRD1 school 2025
Drift and amplification
due to electric field
Detection of an impinging particle takes place because this ionizes the gas, generating ion-electron pairs.

## Slide 4
First gaseous detectors
4
Marcello Abbrescia
DRD1 school 2025
From the historical point of view, the first gaseous detector had a cylindrical shape.
E(a)=5.18 x 10 6 V/m
Multiplication takes place essentially close to the central wire
only the region with a distance from it less then 400 μm, namely around 0.2% of the detector volume, is active for multiplication.
Indeed you can manufacture a detector like this
Using «typical» parameters
A = 80 μm
B = 10 cm
HV = 2000 V

## Slide 5
Cylindrical gaseous detector
5
Marcello Abbrescia
DRD1 school 2025
Cylindrical gaseous detectors, with a central wire, immediately had a tremendous success, and are widely used nowdays.
- A variation of this principle was the invention of the Multi-Wire Propotional Chamber, worth the Nobel prize to George Charpak.
Drift chambers used in the CMS experiment (with a squared section).

## Slide 6
Limitations of cylindrical gaseous detectors
6
Marcello Abbrescia
DRD1 school 2025
Time resolution in cylindrical gaseous detectors is limited by the variable amount of time the electrons need to drift from the points where they are produced to the region where multiplication takes place.
A 1 cm drift length variability, considering a drift velocity vd ≈ 5 cm/μs, implies a time uncertainty of around 200 ns.
Electrons drift and arrive at the wire, one after another, depending on drift distance.
The signal on the wire comprises a series of signals (and typically the first is used for timing)

## Slide 7
HV electrodes
Using a uniform electric field
7
Marcello Abbrescia
DRD1 school 2025
It was clear from the beginning that the way to increase time resolution was using a uniform electric field.
If the electric field is intense enough everywhere, avalanches can grow everywhere
All clusters drift toward the anode with the same velocity and simultaneosly originate avalanches.

## Slide 8
REMIND
8
Marcello Abbrescia
DRD1 school 2025
In ANY detector the signal is NOT generated when the charges are collected by the readout electrodes.
The signal is generated when the charges drift in the detector volume: when they are collected by the readout electrodes, everything is OVER.
1 V
O V
O V
Vd
Since avalanches develop at the same time, the total signal is the SUM of the signal generated by multiple avalanches.

## Slide 9
An important difference
9
Marcello Abbrescia
DRD1 school 2025
First change of paradygm:
passing from 1/r electric fields to uniform electric fields.
From cylindrical gaseous detectors  planar gaseous detectors
In a planar gaseous detector the whole detector volume is at the SAME time drift region and multiplication region
In wire chambers and MPGD drift region and multiplication region are separated.

## Slide 10
Let’s dimension such a detector
10
Marcello Abbrescia
DRD1 school 2025
Using a 1 cm gap, in order to reach an electric field around 5.18 x 10 6 V/m, we would need 51.8 kV
A problem even for nowdays power suppliers.
Therefore a suitable solution is to reduce the gap thickness
Typically down to 1-2 mm
1 mm gas gap  ≈ 5 kV of applied voltage
Primary ionization follows Poisson statistics, therefore the probability of NOT having any primary ion-electron pair in a thickness g (intrinsic inefficiency) is:
Where λ is the number of primaries per unit lenght (around 5-6/mm for the gas typically used in these devices).
For 1 mm,
For 0.5 mm,
(!!!)

## Slide 11
Keuffel’s PPC
11
Marcello Abbrescia
DRD1 school 2025
Built for the first time in 1949. Quite similar to planar capacitors.
First prototype: two Molibdenium disks separated by 3 mm and with an area of 31 cm2
Subsequently, Keuffel used two Copper plates (or iron/copper plated plates): d=2.5 mm, A=35 cm2
Gas mixture: xilene (C6H12(CH3)2) pparz = 6 mmHg
argon ptot = 0.5 Atm
World record time resolution for gaseous detectors

## Slide 12
Pros and conts of Keuffel’s PPC
12
Marcello Abbrescia
DRD1 school 2025
Characteristics of Keuffel’s PPC:
large signals ≈ 100 V (on 50 )
time resolution ≈ 5  10-9 s
efficiency ≈ 90%
plateau from 0.9 to 3 kV
Problems:
To get intense electric fields, the electrodes are at few mm distance
Detector lifetime: few months
Limited because of the formation of a (micro) point on the electrodes where a discharge always originates
Extremely laborious surface preparation
cleaning of the electrodes with increasingly fine sandpaper;
washing with xylene
vacuum tube assembly
re-washing with xylene, alcohol, and distilled water;
evacuation of the tube under vacuum and heating for two hours at 200 °C
introduction of hydrogen (to reduce any oxides)
evacuation down to 10⁻⁵ mm Hg (or better)
cooling
filling with the active mixture: first xylene and then Ar, to form a layer of xylene on the electrodes

## Slide 13
Choice of the gas filling
13
Marcello Abbrescia
DRD1 school 2025
New avalanches
Continuos discharge
De-excitation of noble gases can happen via photo-emission; for instance, Ar produces 11.6 eV photons.
This can be large then the extraction energy for many metals: Cu - 7.7 eV
Noble gases are preferentially used due to the absence of vibrational and rotational states ionization dominates.
Possible electron multiplication at low electric field
Choose cheap noble gases with low ionization potential

## Slide 14
Quencher gases
14
Marcello Abbrescia
DRD1 school 2025
Solution: add poly-atomic gases as “quenchers”
Because of the presence of many vibrational and rotational levels, these gases absorb photons in a wide range of energy.
Methane: absorption band between 7.9 and 14.5 eV
The result is that photons are prevented from covering long distances, and electron photo-production is reduced.

## Slide 15
A game of Switch on and off
15
Marcello Abbrescia
DRD1 school 2025
A typical PPC is a planar capacitor: hence the equivalent circuit is an RC circuit.
Differently to what happens in cylindrical gaseous detectors, in planar gaseous detectors a discharge continues until the applied HV is removed.
A discharge in the gas volume behaves like a short circuit connecting anode and cathode of the capacitor.
PPC
After the passage of an ionizing particle, the applied HV was removed for a certain time (0.01-0.05 s)  suitable switch-off electronic circuits (Franzinetti e Bella, Focardi, Torelli, Rubbia ...)
The time needed to charge up again a capacitor is related to the time constant of the circuit τ=RC
The maximum frequency of particle detection (rate capability) is limited.

## Slide 16
Conversi’s flash chambers
16
Marcello Abbrescia
DRD1 school 2025
Planar gaseous detector had an incredible success. Here one curious example (1955).
Shielding
HV electrodes
Wireless tubes filled with Ne

=
Since Ne produces fluorescence photons during a discharge it was possible directly visualize the particles
e+e-

## Slide 17
OK, this is really nice.
BUT
Is there a smarter way than continuously switching OFF and ON the detectors
17
Marcello Abbrescia
DRD1 school 2025

## Slide 18
Include resistive elements in gaseous detectors
18
Marcello Abbrescia
DRD1 school 2025
Put in front of the HV metallic planar electrodes, resistive plates of suitable material.
In this configuration, the detector is still a planar capacitor, but partially filled with a resistive material.

## Slide 19
As usual, put some numbers
19
Marcello Abbrescia
DRD1 school 2025
The electrical equivalent of an RPC is the following:
Once that the capacitor representing the gas gap is discharged because of the passage of an ionizing particle and subseguent discharge, its re-charging time is related to the time constant of this circuit:
d is the thickness of the resistive plates
g is the thickness of the gas gap
For d=g=2 mm and ρ = 10 11 Ωcm, τ is few ms (milliseconds)!
Electrons are collected on the anode in times of the order of few tens of ns
Ions are collected on the anode in times of the order of few tens of μs

## Slide 20
From the practical point of view
20
Marcello Abbrescia
DRD1 school 2025
This means that during the discharge, and well after even the ions are collected, the resistive material behaves like an insulator.
Also, after the electrons are collected on the anode, they remain there for «ages» before they are neutralized by the current flowing from the HV electrodes.
Locally, the electric field goes to zero.
If another ionizing particle passes close the «dead» area, it cannot be revealed because the electric field is under threshold for multiplication
There is no more a short circuit between anode and cathod.
No need to switch ON and OFF the applied HV voltage.

## Slide 21
Limitation in rate capability
21
Marcello Abbrescia
DRD1 school 2025
In a Parallel Plate Detector, with metallic electrodes, the whole electrodes as discharged as a consequence of the development of a discharge.
In a Resistive Plate Chamber (RPC), only a localized region is discharged, with dimensions close to the avalanche disk size.
BUT it remains discharged for much longer time, because the resistive component of the time constant τ is much (MUCH) larger.
Low resistivity
High resistivity
Net result is a decrease of the efficiency vs. rate of impinging particles, depending on the resistivity value.
Note: this is a result of the beginning of 1990s: now we can do much better!

## Slide 22
Inclusion of resistive elements
in gaseous detectors
22
Marcello Abbrescia
DRD1 school 2025
Crazy guys even wanted to write a book on this revolutionary concept.
THANKS Paulo and Vladimir: writing this book was the most exciting, instructive and rewarding experience in my entire academic life!
Including resistive elements in gaseous detectors was (and is) a major breakthrough in GD R&D
Disclaimer: this is NOT advertising. The book is available for FREE at the CERN library.

## Slide 23
Pestov’s Planar Spark Chambers (PSC)
23
Marcello Abbrescia
DRD1 school 2025
They were the first (1970) implementation of a planar gaseous detector with ONE resistive (glass) plate.
100 μm gap «compensated» by the use of a Ar/Ne/quencher gas mixture at 10 Atm
Exceptional time resolution!
Used in NA49 with limited lifetime

## Slide 24
Signals in planar gaseous detectors
24
Marcello Abbrescia
DRD1 school 2025
Ionization probabilty (and gain) are not the only parameters to be optimized in gaseous detectors: time resolution is quite relevant.
Given the fact that the electric field is uniform in the gas gap of a planar gaseous detector (at least at low rate), semi-analytical description of its behaviour can be found. Signals developed can be approximated like follows:
Here, we neglect saturation effects (correct if we consider the initial stages of the avalanches), and:
  vd is the electron drift velocity (assumed constant with time);
  Ew is the weighting field (assumed uniform in space);
  η is the first effective Townsend coefficient
  Mj is the avalanche fluctuation coefficient
  t is the time elapsed since the passage of the ionizing particle

## Slide 25
Time resolution in RPCs
25
Marcello Abbrescia
DRD1 school 2025
Inverting the previous equation (with some approximations), one can deduce an estimate for the time resolution of an RPC:
Factors under the square root depend on the specific gas or statistic and little can be done.
Here it is clear what an experimentalist can do to improve time resolution:
Improve drift velocity vd
(choose the suitable gas, since it tends to saturate at high fields)
Increase first Townsend coefficient  high electric fields
The applied HV is somehow limited by technological reasons, so the way that Pestov choose was to use a very narrow gap with a quite intense electric field.
Results do NOT come by chance!

## Slide 26
Finally… the RPCs
26
Marcello Abbrescia
DRD1 school 2025
They are made by two plates of «bakelite» (HPL, high pressure phenolic laminates), a plastic material widely used, obtained impregnating paper with phenolic resins.
  Later on glass was used
Bakelite plates were coated from one side with graphite, to manufacture the HV electrodes.
On the side toward the gas gap they were coated with linseed oil
They were typically readout by means of copper readout strips or pads.
Bakelite of resistivity 10 10- 10 12 cm
HV electrodes
Readout strips
Copper strips

## Slide 27
Finally… the RPCs
27
Marcello Abbrescia
DRD1 school 2025
Invented at the beginning of the ‘90s by R. Santonico and R. Cardarelli.
Easy to build and not expensive
2 mm gap, 8-10 HV applied
Ar/isobutane/CF3Br mixture
Full efficiency
Time resolution around 1-2 ns
Immediately used in many experiments, both at accelerators and for cosmic rays.
Made planar gaseous detectors very «democratic», i.e. easy to build

## Slide 28
Some experiment of the past using RPCs
28
Marcello Abbrescia
DRD1 school 2025
Argo-YBJ experiment, on the Tibet, fully implemented with RPCs
E771
Three planes of RPCs
Used for trigger and simple reconstruction
E771 at Fermilab

## Slide 29
Avalanche and discharge processes in RPCs
29
Marcello Abbrescia
DRD1 school 2025
Avalanche: it grows because of subsequent ionization processes due to the drifting electrons.
The separation between avalanche and streamers decreases as the voltage increases.
Streamer: because of space charge effects, secondary avalanches are created via photo-ionization
Spark: short circuit between anode and cathode

## Slide 30
The problem of the rate capability
30
Marcello Abbrescia
DRD1 school 2025
At the beginning of ‘90s it was urgent to design the experiment for the (future) LHC. Given the expected fluxes, the limitation in rate capability of RPCs was relevant. RPC were NOT a «fast» detector.
RPCs represented an attractive solution for the muon system of the LHC experiments, but they were to be operated at fluxes around hundred(s) Hz/cm2.
The limitation in the time constant of an RPC canNOT be overcome (in principle):
Reduce resistivity
On the AVERAGE, the voltage drop in the resistive plates is given by:

## Slide 31
The solution: another change of paradygm
31
Marcello Abbrescia
DRD1 school 2025
The localized voltage drop in and RPC is proportional to the size of the avalanche/streamer developed.
Note: an RPC is NOT a proportional counter: the final size of the avalanches depend on the distance from the anode the are originated.
The solution was reducing as much as possible the percentage of streamers, and reducing the size of the avalanches. In practise:
Reduce the operating voltage
Transfer the needed amplification from the gas to the front-end electronics.

## Slide 32
The role of “Freon”
32
Marcello Abbrescia
DRD1 school 2025
It was found that using strongly quenching gas mixtures helped in obtaining a «Pure avalanche» mode of operation.
Increasing fractions of CF3Br
Then replaced with mixtures made almost all of C2H2F4 (tetrafluoroethane)
CF3Br 0%
<qind>=500pC
CF3Br 8%
<qind>=60pC
Increase of the rate of a factor more than 10
Passing from 100 Hz/cm2 to 1-2 kHz/cm2

## Slide 33
Summarizing…
33
Marcello Abbrescia
DRD1 school 2025
The idea was to pass from «streamer» mode of operation to «avalanche» mode of operation (or «saturated avalanche»).
  The term «saturated avalanche» derives from the fact that the size of the avalanche in RPCs is such that space charge effects are not negligible  the avalanche growth is no more exponential.
This passage implied the use of more sophisticated electronics (widely available in the 90’s)

## Slide 34
RPCs at the LHC experiments: CMS
34
Marcello Abbrescia
DRD1 school 2025
The RPCs at the LHC experiments have contributed to the discovery of the Higgs boson.

## Slide 35
Problems to be addressed: Aging effects in RPCs
35
Marcello Abbrescia
DRD1 school 2025
unreacted molecules
+ radiolytic products
+ HF
e- ;  ; UV ; etc.
avalanche
+
+
R134a
C4H10
SF6
The gas used in RPCs, and specifically tetrafluoroethane, can partially dissociate because of avalanche processes and UV production.
Chromatogram of the INPUT gas to an RPC
R134a
Isobutane
SF6
H20
When you install RPC at the LHC experiments you want them to last the experiment lifetime (≈30 years)

## Slide 36
Aging effects in RPCs
36
Marcello Abbrescia
DRD1 school 2025
Chromatogram of the OUTPUT gas from an RPC
Many stange compounds appear, the most dangerous being hydrofluoric acid (HF), whose production resulted to be roughly proportional to the average avalanche charge.

## Slide 37
Conductive processes in bakelite
37
Marcello Abbrescia
DRD1 school 2025
Experimentally, bakelite resitivity seems to increase with time.
This is increase can be controlled by enriching with H2O vapor the gas mixture used.
Marcello Abbrescia - Universitá di Bari, Italy
Time when H20 vapor was added
Current conduction in bakelite is ionic, and therefore requires H2O to be sustained (J. Va’Vra, who cited a young M. Abbrescia in his diaries(.

## Slide 38
The advent
OF
Multigap Resistive Plate Chambers (MRPCs)
38
Marcello Abbrescia
DRD1 school 2025

## Slide 39
The huge dynamic range of RPCs
39
Marcello Abbrescia
DRD1 school 2025
TRUE: in RPCs, ALL electron avalanche processes start immediately: the induced signal (due to movement of charge) is the sum of all avalanches: thus all ionisation produced in chamber plays a role.
However the avalanches grows across the full gap width.
This is an exponential process, depending on the distance from the anode.
The avalanches originating close to the anode might not grow large enough to give rise to a detectable signal.

## Slide 40
The introduction of Multigap-RPCs
40
Marcello Abbrescia
DRD1 school 2025
To get all these avalanches to produce EACH a detectable signal, the gain (namely the electric field) is set very high.
This implies production of streamers or sparks from the avalanches starting close to the cathode.
Solution: add barriers within the gas gap to stop the development of the avalanche.
Reduce the dynamic range
Since the gap is narrow, the gain can be set very (VERY) high.

## Slide 41
Structure of a Multigap-RPC
41
Marcello Abbrescia
DRD1 school 2025
Stack of equally-spaced resistive plates with voltage applied to external surfaces (all internal plates electrically floating)
Pickup electrodes on external surfaces (resistive plates transparent to fast signal)
Internal plates take correct voltage - initially due to electrostatics but kept at correct voltage by flow of electrons and positive ions – feedback principle that dictates equal gain in all gas gaps
The signal is the analogic SUM of the signals from all the gaps.

## Slide 42
Performance of MRPCs
42
Marcello Abbrescia
DRD1 school 2025
Using tiny gap, the electric field can be increased quite high
The first Townsend coefficient is really (REALLY) high.
250 μm gas gaps (10 gaps in ALICE-TOF)
Excellent time resolution

## Slide 43
The importance of the configuration
43
Marcello Abbrescia
DRD1 school 2025
It might seem that increasing the number of gaps to infinte we would get the perfect detector. Actually the contribution of each gap to the induced signal reduces increasing the number of gap.
Vw=1V
Vw=1V
Vw=1V
Vw=1/3V
Vw=1/3V
Vw=1/3V
Single gap
Double gap
Multigap (3 gaps)
Ratio between induced and drifting charges
Ramo theorem

## Slide 44
And now…
What’s next???
44
Marcello Abbrescia
DRD1 school 2025

## Slide 45
Use of GreenHouse Gases in HEP
45
Marcello Abbrescia
DRD1 school 2025
GHGs are used in several gaseous particle detectors due to their characteristics suitable for optimal detector performance AND long term operation
30 years ago we had to get rid of Ozone Depletion gases
Now we have to get rid of GHGs

## Slide 46
The replacement of GHGs with eco-friendly gas
46
Marcello Abbrescia
DRD1 school 2025
We need to replace:
  C2H2F4 = R134a = TFE mainly used in RPCs
  SF6 mainly used in RPCs
  CF4 used in CSCs, GEMs, RICH, etc.
with more ecological gases, namely with a much lower Global Warming Potential.
Difficult problem: gases are the core of gas-filled detectors.
We also need:
  to get the same performance
  not to change the electronics and HV (for existing systems)
Of course we can also re-circulate
the gases used, after purifying them,
and reduce leaks
HEP experiments, present and future, last several (dozens) of year
 A good performance must be mantained for an adequate period of time
 Aging tests are needed as well.
It’s not a problem concerning just the RPC community

## Slide 47
The importance of collaborative effort
47
Marcello Abbrescia
DRD1 school 2025
47
All high energy experiments (ALICE, ATLAS, CMS, LHCb, etc.) and the CERN gas group (CERN EP-DT) started, already several years ago, an intense R&D program to find suitable gas mixtures.
Practically all research trendlines concentrate around the idea of replacing:
C2H2F4 (GWP=1430) C3H2F4ze (GWP=4)
+ CO2 (GWP=1) or He
EEE
C3H2F4 (here indicated as HFO for short) is the molecule most similar to TFE but with low GWP
CO2 (or He) are essentially added to reduce the operating voltage.
The RPC EcoGas@GIF++ is a Collaboration transversal to ALICE, ATLAS, CERN EP-DT, CMS, and LHCb willing to put together expertise and resources in order to test potential candidates of eco-friendly gas mixtures with different detectors and electronics.

## Slide 48
Yeah…
But what about the REAL future???
48
Marcello Abbrescia
DRD1 school 2025

## Slide 49
Recent and future trendlines
49
Marcello Abbrescia
DRD1 school 2025
We are now in a phase similar to the ‘90s, namely we need to develop detectors suitable for the next generation accelerators (FCC, ILC, Muon Collider…)
- Much larger energy and luminosity wrt. LHC
In general, one wants to push the detector perfomance forward in terms of:
Rate capability
Time resolution
(spatial resolution)
Longevity
What would you do?
Suggestions are welcome!
Here I have some considerations about what the community is doing: but let us hear what would YOU do!

## Slide 50
Conclusions
50
Marcello Abbrescia
DRD1 school 2025
Using a planar geometry in gaseous detectors, in place of using cylindrical or more geometries, is a change of paradygm: it has advantages and drawbacks, but it was something NEW.
The introduction of resistive elements in gaseous detectors was a breakthrough, which rapidly expanded beyond the realm of planar gaseous detectors: again, it was something NEW.
Further refinements came: passing from streamer to avalanche mode, the introduction of MRPCs: again, NEW IDEAS.

## Slide 51
Lesson to be learnt
51
Marcello Abbrescia
DRD1 school 2025
A particle detector is not made by putting together pieces of hardware.
A particle detector is made by putting together IDEAS: chose them well, assemble them in the right way, and it will go like wind.