## Slide 1: SPS-BGI Model to LHC Tunnel Impedance Investigation
10/03/2025
H. Bursali on behalf of Impedance Team
hikmet.bursali@cern.ch
SY-RF-BR

## Slide 2: Outline
First Result
  Model with 1 kΩ NEG coated ceramic cathode
Studied Options
  Decreased NEG coating resistivity on ceramic cathode
  Model with/without cathode
  Model with ferrites
  Model with beam screen
Conclusion
1

## Slide 3: First Result
Broadband contribution
2
SPS - BGI with tapers (120 mm to 80 mm diameter)
Tank
Internal View
1 kΩ NEG coated ceramic cathode
393 W

## Slide 4: Studied Options
3
1 kΩ
300 Ω
50 Ω
Coating Resistivity
Tapers
Broadband contribution
Coating resistivity | Beam-induced RF power loss
1 kΩ | 393 W
300 Ω | 298 W
50 Ω | 203 W
Different Coating Resistivities

## Slide 5: Studied Options
4
With/without Steel Cathode
Beam aperture
Ø -> 120 mm
Model with cathode
Model without cathode
Resonances from chamber itself
-> RF absorbers can be studied!

## Slide 6: Studied Options
5
Ferrite usage
May break due to the high intensity beam!
115 W
170 W
With cathode
Without cathode
TT2-111R

## Slide 7: Studied Options
6
Model with Beam Screen
With cathode
Without cathode
565 MHz
1.01 GHz
1.45 GHz

## Slide 8: Studied Options
7
Model with Beam Screen
Tapers attached to the tank
Tapers at the end

## Slide 9: Conclusion
Decreased resistivity on cathode coating is still causing the broadband impedance, thus excessive power loss.
Ferrites may break due to the high intensity beam.
Best option till now is the model with beam screen and no cathode.
  Power loss is low for both models with different taper locations.
8

## Slide 10: Thanks for your attention!
SY-RF-BR

## Slide 11: Backup Slides

## Slide 13: Beam Screen and Cathode

## Slide 14
15.8 W
51.9 W
48.2 W
Steel Cathode
1 kΩ NEG coated ceramic cathode
50 Ω NEG coated cathode
Model with Beam Screen and Cathode
RF power loss

## Slide 15: Comparison of Taper Locations
Tapers at the end
Tapers attached to the tank

## Slide 16: Studied Options
Beam aperture
Ø -> 80 mm
No cathode
No cathode + RF absorbers on sides
SPS-BGI design (tapers attached to the tank)
50 Ω NEG coated macor

## Slide 17: Possible Options
Model with beam screen and no cathode (tapers attached to the tank)

## Slide 18: Possible Options
698 MHz
Model without cathode (tapers attached to the tank) + RF absorbers

## Slide 19: Possible Options
565 MHz
1.014 GHz
Model with beam screen and steel cathode (tapers at the end)

## Slide 20: Possible Options
6.14 W