## Slide 1: LHC configuration MD’s
S. Fartoukh
What is left for 2025/2026 ?
ATS optics development for the future
Summary

## Slide 2
What is left for 2025/2026? (1/2)
2026 CYCLE (further optimized cycle and pushed b*)
Test the mechanics and measure/correct the optics of a new cycle with:
Full squeeze in the ramp requesting (i) a change of the ATS optics gymnastic in the ramp (anti-telescope starting @2.5 m vs. 2.0 m).and. (ii) the new parabolization procedure (see MD15003 posted by Michi)
ATLAS/CMS/LHCb rotation in the ramp
Beta*-leveling extended down to 40/12 cm after X-angle anti-levelling (or 50/15 cm only @ nTCT=8.5 sigma, but “super-tight settings” are continued on the collimation side)
Intensity ramp up to 1-2 trains would be great for the ramp (to observe the lifetime with the rotation embedded). Not more than probe beam needed for the squeeze extension (or set-up beam if aperture measurement is deemed to be necessary).
3-4 shifts requested, out of which 1 shift is already requested for MD15003.
Optics not ready (first shift of the program to be scheduled in MD2 at the earliest).

## Slide 3
What is left for 2025/2026? (2/2)
Missing D1
The LHC should be ready to operate with the MBWXA modules disconnected in IR1 (radiation), and the other 5 modules pushed up by 20% (~900 A, which is beyond ultimate), but ideally less (~820 A) to minimize the risks and remain compatible with the existing FMCM system.
Dedicated orbit bumps (optics dependent knob acting on MCBXH3, D2 and CODs @ Q4/5/6) can meet this goal (see appendix).
The idea is to mimic this failure scenario by testing the 2026 cycle with the D1 strength reduced by ~10% + new special knob to compensate.
Can be included in the previous program (if 4 shifts allocated) to test the new knob over the full 2026 cycle; or simple test(s) at injection and/or EoR using the 2025 cycle (therefore for the injection and/or the FT optics only).

## Slide 4
ATS optics development and MD for the future
More than a decade ago, the ATS optics concepts were invented to provide a solution for the HL-LHC optics, then developed, heavily tested in MD, and implemented gradually in the LHC since 2017.
The focus was put on IR1 and IR5, for boosting the beta* beyond 50-40 cm, otherwise limited by matching quadrupoles and sextupoles, while keeping under perfect control the chromatic aberrations induced (off-momentum beta-beating, spurious dispersion from crossing bumps)
Limits on these chromatic aberrations were first observed in the LHC
in 2023 during the ion run (on_disp knobs missing inducing background in Alice),
then in 2024 for the proton run (uncorrected vertical spurious dispersion in IR7 from Alice/LHCb + machine imperfections, inducing collimation hierarchy breakage).
Limits on off-momentum beta-beating are not (yet) known/observed, but should come when (if?) Alice and/or LHCb will request even lower beta* in the future.
The ATS optics concept should therefore be generalized to Alice & LHCb as well
Concept .and. corresponding new ATS optics NOT ready (many approach can be imagined). But as soon as available, 1 or 2 shifts in 2025 or 2026 would be welcome to test the next ATS optics generation before HL-LHC.

## Slide 5
Summary
As of MD2 (2025): 4 shifts for the 2026 cycle (including the preventive action against D1 failure), out of which 1 is already requested in MD15003
As soon as available (in 2025 or 2026): 1-2 shifts for testing the next ATS optics generation

## Slide 7
Appendix (MBXWA failure mitigation)

## Slide 8: D1 transfer function (D1 made of 6 MBXW modules in IR1, powered in series left and right)
Chart: HCMBXW_001-BI000027 Integrated field (SSW typical std over 3 reps < 0.3 unit)
| 100.00360609905201 | 200.00429591503899 | 300.026492050652 | 399.98712439523098 | 499.99515687152598 | 599.94816725239104 | 684.93619197875103 | 699.88748445605995 | 749.89190658760197 | 799.87723397538105 | 829.86244435940398 | 849.83449533475505 | 899.80474645536503 | 949.75234501524801 | 999.70073836898098
SSW | 0.65733 | 1.3133 | 1.9686 | 2.6228 | 3.2747 | 3.9188 | 4.4116 | 4.4886 | 4.7256 | 4.9351 | 5.0506 | 5.1246 | 5.2997 | 5.4629 | 5.615
Hall probe | 0.65952 | 1.3159 | 1.9727 | 2.6271 | 3.275 | 3.9164 | 4.3921 | 4.47 | 4.7036 | 4.9135 | 5.03 | 5.0972 | 5.274 | 5.4299 | 5.5723
Linear 0 - 600 A | 0.65891 | 1.3122 | 1.9657 | 2.6188 | 3.2721 | 3.9252 | 4.4804 | 4.5781 | 4.9048 | 5.2313 | 5.4272 | 5.5577 | 5.8842 | 6.2105 | 6.5368
Strong saturation beyond I_ultimate=810 A: ITF reduced by ~ 2
(even not talking about b3)
IPNO=662 A
@ 6.8 TeV
810 A
(ultimate)
890 A (w/o MBWXA)
Courtesy of Pierre Thonet

## Slide 9
Beam1
Beam2
Disconnecting the MBXWA modules (L/R) and increasing the D1/2 strength
+ 23.05% more strength needed in the 5-remaining MBXW modules: 890 A +/- uncertainty (%)
+2.55% more strength in D2 (irrelevant @ 6.8 TeV)
Orbit bump in between D1 & D2 (irrelevant for aperture, especially for flat optics with ~ 60-50 cm)
Note: this optics independent orbit bump will be strongly mitigated when the H crossing is ON (after the ATLAS/CMS
rotation) and is only needed towards the EoR (e.g. could be ramped up from 0 to 1 as of 5 TeV only)
Option 1

## Slide 10: Option 2
Beam1
Beam2
Disconnecting the MBXWA modules (L/R), limit the D1 current to 815 A, and match the orbit with D2 & MCBXH3
D1@815 A (~ultimate current)
+1.55% more strength in D2 (decreases w.r.t. option 1)
+ 385 A needed in MCBXH3 (vs. 400 A for the radial MCBXH/V spec), reduced when the H-crossing is ON
Note: this optics independent orbit bump will be strongly mitigated when the H crossing is ON (after the ATLAS/CMS
rotation) and is only needed towards the EoR (e.g. could be ramped up from 0 to 1 as of 5 TeV only)

## Slide 11: Option 3
Beam1
Beam2
Disconnecting the MBXWA modules (L/R), limit the D1 to 815 A, MCBXH3 to 250 A, and use the usual MCBY/C (at Q4/5/6) to match the orbit
D1@815 A (~ultimate) & D2 even reduced by 5.0% w.r.t. 2024 (optimize for minimizing the usage of the CODs @ Q4/5/6)
MCBXH3@250A: OK for the 400 A radial spec., accounting for 100/200 A more in MCBXH3 for the flat machine
MCBC (@Q5/6) and MCBYS (@Q4) not more than 50% of nominal, then reduced with H crossing ( no impact on lumi knob)
Note: this optics dependent orbit bump will be strongly mitigated when the H crossing is ON (after the ATLAS/CMS
rotation) and is only needed towards the EoR (e.g. could be ramped up from 0 to 1 as of 5 TeV only)