## Slide 1: MDs on Incoherent effects for 2025: Beam-Beam, luminosity, tails, losses, emittance growth, noise & more
H. Bartosik, X. Buffat, R. Bruce, R. De Maria, I. Efthymiopoulos, P. Hermes, M. Hostettler,
B. Karlsen-Baeck, S. Kostoglou, L. Mether, C.E. Montanari, N. Mounet,
M. Rakic, A. Radoslavova, S. Redaelli, G. Sterbini, R. Tomas, H. Timko
18/03/2025 LSWG

## Slide 2: Motivation
Focusing on HL-LHC intensity & beams, main issues to address in 2025/2026:
  Transverse beam quality (emittance, tails, intensity, bbb spread) reaching the LHC from SPS for the different HL-LHC optimized beam variants (BCMS, standard, hybrid, 8b4e; 4x72, 5x48..)
  Emittance growth at injection: validate whether 2024 observations apply to 2.3e11 ppb (+0.2 um/h of unknown origin, brightness independent, even with single bunches).
  Tail population increase for HL: observed during 2024 high-intensity MDs at injection with HL trains.
  Emittance growth during ramp: quantify emittance growth during ramp for HL-LHC beams, interplay between IBS and extra growth.
  Emittance growth during collisions: understand why vertical emittance evolution agrees with model during VdM fills but not during nominal physics fills. Determine whether this is driven by beam parameters or machine configuration.
  Losses at end of collapse/start of collisions, tails and impact on performance: quantify effective cross section with low tail vs nominal tails and measure experimentally the gain (%) in integrated luminosity. Can we achieve 90mb for HL?
  Noise: 8 kHz amplitude increase systematically 3-4 minutes before the end of ramp both for proton and ion fills, not observed during ppref fills.
  Lifetime correlation with DA for ion operation: opens the way towards crossing angle reduction, beta* reduction..
Lots of synergies with RF/e-cloud/collimation/stability/optics teams to minimize number of requests while extracting maximum amount of information during MD blocks. We will clearly need support from BI (BSRT, WS, dBLM..).
Some of these MDs will require preparation time in the injectors.

## Slide 3: MD1
MD A (6h):
Fill 1 Energy: Injection Study: emittance growth and tail evolution at injection, noise Beams: several INDIVs with 2.3e11 ppb.
  Extended stay at injection with several INDIVs, 2.3e11 ppb and different tails (q=1 and q=1.5).
  Will allow to:
    Setup bunches with different transverse distributions, needed for next MDs.
    Measure emittance growth at injection for HL-LHC due to IBS & additional growth of unknown source.
    Tail evolution.
    Enough statistics as measurements will be done with BSRT, not WS.
  Bunches will be distributed around the machine to measure impact from EPC MB PC active filters.
  End with scraping for halo measurements, complementary to tails measured by BSRT but for higher amplitudes.

## Slide 4: MD1
MD A (6h):
Fill 1 Energy: Injection Study: emittance growth and tail evolution at injection, noise Beams: several INDIVs with 2.3e11 ppb.
Fill 2 Energy: Collisions Study: emittance growth during ramp, impact of tails on losses at end of adjust, noise, RF studies parasitically Beams: 6 INDIVs with 2.3e11 ppb.
  6 INDIVs/beam with 2.3e11 ppb and different tails (3 with q=1 and 3 with q=1.5)
  4 colliding HO in IP1/5 and 2 non-colliding, extended stay at 1.2 m where losses are critical (no leveling).
  Will allow to:
    Quantify emittance blowup during ramp with WS for HL-LHC.
    Compare losses for q=1 and q=1.5; measure gain in integrated luminosity for the low-tail type.
    First short study of emittance growth for colliding and non-colliding bunches with same initial conditions and constant β*.
    Crosscheck BSRT with WS.
  Bunches distributed around the machine for EPC MB PC active filters tests.

## Slide 5: MD1
MD A (6h):
Fill 1 Energy: Injection Study: emittance growth and tail evolution at injection, noise Beams: several INDIVs with 2.3e11 ppb.
Fill 2 Energy: Collisions Study: emittance growth during ramp, impact of tails on losses at end of adjust, noise, RF studies parasitically Beams: 6 INDIVs with 2.3e11 ppb.
MD B (8h):
  Energy: Collisions Study: emittance growth during collisions, impact of tails on losses at end of adjust & integrated luminosity, noise, RF studies parasitically Beams: several INDIVs with 2.3e11 ppb.
  Will allow to:
    Quantify difference in losses and integrated luminosity for low and nominal tails with high statistics.
    Emittance growth for colliding/non-colliding bunches and high statistics.
Depending on results of MD B:
  1 fill or 1 injection during VdM period/fills (outside of MD blocks) with >0.9e11 ppb, to be discussed with experiments.
  Will allow to:
    Understand if emittance growth during collisions is related to beam parameters or machine configuration.

## Slide 6: MD2 & MD3 & MD4
MD2: Ramp up to 2 TeV (8h, driven by RF): Energy: Ramp to 2 TeV Beams: trains with 2.3e11 ppb.
Starting from best optimized beam types from the injectors for 2.3e11 ppb (36b, 48b, 72b, BCMS, standard) – to be discussed and determined.
Will study transverse beam quality evolution with HL-LHC trains from SPS  LHC and throughout LHC cycle until 2 TeV, while RF is studying start of ramp losses and improved cleaning of debunched beam.
Hopefully new dBLM in IR3 will bring more insights.
MD3: Collisions with HL-LHC trains + BBLR Wires (8h, in collaboration with ecloud and RF): Energy: Collisions Beams: trains with 2.3e11 ppb.
8b4e@2.3e11ppb + 12b@2.3e11ppb + 24b@2.1e11ppb in the same fill if all flavors in a good state from injectors.
3 trains of each flavor (for steering and test non-colliding train case)
Aiming for leveling at HL-LHC PU.
Wire compensation at EOL. Combined with halo measurements from collimation
MD4: Noise studies
Strategy strongly depends on results of measurements from oscilloscope currently installed in sector 12, dipole A34L2, waiting for measurements without beam when powered..

## Slide 7: MD5
In MD5: Lifetime vs crossing angle reduction for ions
  Proposed both in 2023 and 2024, but could not be done due to machine problems.
  Goal: Study lifetime reduction due to long-range beam-beam during crossing reduction.
  Benefit: establish correlation between simulated DA and measured lifetime for ions – is the 6 sigma DA criterion adequate for ions?
In 2026: beam-beam for p-Pb
  Background: p-Pb under consideration for 2026. Potential performance increase from using high-intensity 25ns beam, but feasibility not proven.
  Goal: Study lifetime for asymmetric collisions - strong 25 ns proton beam colliding with weak 50 ns Pb beam with every second 25-ns bunch not colliding at given IP.
  Expensive MD in terms of setup and validation – consider to do in 2026 if we do p-Pb, when we anyway have a validated p-Pb machine setup

## Slide 8: Various
We are interested & will parasitically observe in:
  Injection with 2.3e11ppb trains > 1000 bunches from ecloud team: observe tail population at injection due to ecloud as observed in 2024.
  High tele-index optics by optics team: important for noise studies if it can be validated for a few INDIVs (5-10 distributed around the machine).
  Collapsing with flat optics by optics team: important for beam-beam studies if it can be validated for trains.
  Collapse-separate-collapse x N times by stability team: important to better understand correlation of tails and losses during collapse.
  Ramp in steps by OP/collimation: would be very important for noise studies (and emittance growth studies) if it can be validated for a few INDIVs (5-10 distributed around the machine).
MDs “on standby”: Done once last year successfully. Simple tests at injection with single bunches in case of empty time slot (~30 mins/1h), no specific pre-requirements, will have detailed procedure in asm. Examples:
  Emittance growth at injection and sensitivity to transverse distribution (will control tails & emittance through steering).
  ADT excitations with white noise or excitations at specific frequencies to benchmark our noise and ripple models (will discuss with D. Valuch).