## Slide 1
Entanglement distribution of photon pairs coexisting with White Rabbit synchronization signals on the same optical fiber
White Rabbit workshop 25/06/2025
Annick Teepe

## Slide 2
Quantum Technology Initiative
HYBRID QUANTUM COMPUTING AND ALGORITHMS
QUANTUM NETWORKS AND COMMUNICATIONS
COLLABORATION FOR IMPACT
CERN QUANTUM TECHNOLOGY PLATFORMS
https://quantum.cern/
Initialized in 2020
“Phase 2” started in 2024

## Slide 3
Quantum Technology Initiative
Notes: -Explore how quantum tech can be useful for CERN
-Explore how CERN can be useful for quantum tech
The quantum networking CoC is in these first years focussing on the second question.
In future, we could imagine CERN could be interested in a network of quantum computers or sensors, connected by quantum networks.

## Slide 4
Contents
      How It Works?!
      1) Background Quantum physics
        2) Entanglement distribution and White Rabbit
      Experiments in Berlin (with Deutsche Telekom – Qunnect)
      1) Experimental set-up
      2) Results “Compensating Mode” without coincidence detection
      3) Results “Compensating Mode” with coincidence detection
      Summary
      Outlook

## Slide 5
Contents
      How It Works?!
      1) Background Quantum physics
        2) Entanglement distribution and White Rabbit
      Experiments in Berlin (with Deutsche Telekom – Qunnect)
      1) Experimental set-up
      2) Results “Compensating Mode” without coincidence detection
      3) Results “Compensating Mode” with coincidence detection
      Summary
      Outlook

## Slide 6
Quantum is everywhere…

## Slide 7
Classical bits:
0 or 1
Superposition Principle
Quantum bits:
0 and/or 1

## Slide 8
Classical bits:
0 or 1
Quantum bits:
0 and/or 1
Quantum states are normalised
Superposition Principle

## Slide 9
Classical bits:
0 or 1
Quantum bits:
0 and/or 1
Superposition Principle
A measurement ‘collapses’ the state to one of the two outcomes, 0 or 1!

## Slide 10
Photons as qubits
Qubit = Two Level System
  Quantum dots
  Trapped ions
  Superconducting
  And photons!
Photon = light particle
  Polarisation
  Distinct polarisation state = Qubit!
Polarized sunglasses remove “glare”
Notes: Qubits are created by manipulating and measuring quantum particles

## Slide 11
Entanglement
A
B
Measure A

## Slide 12
Entanglement
A
B
Measure A
Outcome 1
Corresponds to
State
100% probability!!!

## Slide 13
Using Entanglement
Source emitting entangled photon pairs over two fibers, to two locations
Source
A
B
A
B
A
B
…
…
Alice
Bob
Notes: Qubits are created by manipulating and measuring quantum particles

## Slide 14
Using Entanglement
Measuring yields Quantum Key!
Source
A
B
A
B
A
B
…
…
Alice
Bob
0
1
1
1
1
0
K = 011
K = 011
“Entanglement-based Quantum Key Distribution”
Notes: Qubits are created by manipulating and measuring quantum particles

## Slide 15
The need for synchronization
Emission is simultaneous, detection is not !
Source
A
B
A
B
A
B
Alice
Bob
0
1
1
1
1
0
Bandwidth of biphotons : 0.1 - 10 GHz  10 – 10e3 ps
Notes: Qubits are created by manipulating and measuring quantum particles

## Slide 16
Entanglement distribution and WR in practice
Source
White Rabbit Switch
DWDM
DWDM
White Rabbit Switch
Photon detector
Pol. Optics
Photon detector
Pol. Optics
Alice
Bob
15xx nm
15xx nm
1320 nm
1320 nm
785 nm
TimeTagger
TimeTagger
Notes: Explain 2 node versus 3 node network (with source at different location)

## Slide 17
Multiplexing
 usage existing fiber infrastructure
 use WR light as real-time indicator of changes in the link/fiber
White Rabbit
   sub ns clock synchronisation between nodes
   increase suitability for quantum networks
Why?

## Slide 18
Contents
      How It Works?!
      1) Background Quantum physics
-superposition principle
        -photons as qubits
        -entanglement
        2) Entanglement distribution and White Rabbit
      Experiments in Berlin (with Deutsche Telekom – Qunnect)
      1) Experimental set-up
      2) Results “Compensating Mode” without coincidence detection
      3) Results “Compensating Mode” with coincidence detection
      Summary
      Outlook

## Slide 19
Part 2 : Experiments in Berlin
Matheus Sena
Deutsche Telekom
Maël Flament
Qunnect
Photon detectors
Caution ! VERY fresh results !
Adam Wujek for WR support

## Slide 20
      Distribute entangled photon pairs over deployed fiber with high fidelity AND minimize downtime of network
      Active polarisation compensation  ensure high fidelity
      When compensating  network is down!
      Solution : only compensate “When Needed”  Trigger
      Extend role WR beyond time synchronisation
  Continuously monitor link delay, optical power levels, and polarisation at 15xxnm
   Trigger compensation quantum signal at 1320 nm
Goal
Trade-off!
Extension of work M. Sena et al., “High-Fidelity Entanglement Distribution Through Berlin Using an Operator’s Fiber Infrastructure,” OFC 2025.

## Slide 21
Experimental set-up
Source
White Rabbit Switch
TimeTagger
DWDM
DWDM
White Rabbit Switch
TimeTagger
APC inj
1320 nm
APC cmp
1320 nm
APC cmp
1550 nm
Photon detector 785nm
Pol. Optics
785nm
Photon detector 1320nm
Pol. Optics
1320nm
Grandmaster
polarizer
Trigger

## Slide 22
Experimental set-up

## Slide 23
Measurement with triggers – without coincidences
Source
White Rabbit Switch
TimeTagger
DWDM
DWDM
White Rabbit Switch
TimeTagger
APC inj
1320 nm
APC cmp
1320 nm
APC cmp
1550 nm
Photon detector 785nm
Pol. Optics
785nm
Photon detector 1320nm
Pol. Optics
1320nm
Grandmaster
polarizer
Trigger
Real deployed fiber; ~ 27km

## Slide 24
Results ~1 hour

## Slide 25
Results ~1 hour

## Slide 26
Results ~1 hour

## Slide 27
785 nm
Laser
Fiber coupler
½ waveplate
¼ waveplate
Fiber coupler
WRS1
WRS2
PowerMeter
Intermezzo : power fluctuations with WR in Free Space
Dependency of delay on transmitted power
Linear fit yields slope of:
-0.101 ns per mW

## Slide 28
Measurement with triggers – with coincidences
Source
White Rabbit Switch
TimeTagger
DWDM
DWDM
White Rabbit Switch
TimeTagger
APC inj
1320 nm
APC cmp
1320 nm
APC cmp
1550 nm
Photon detector 785nm
Pol. Optics
785nm
Photon detector 1320nm
Pol. Optics
1320nm
Grandmaster
polarizer
Trigger
Real deployed fiber; ~ 27km

## Slide 29
Results ~ 70 hours

## Slide 30
Results ~ 70 hours

## Slide 31
Results ~ 70 hours

## Slide 32
How It Works ?!
  Background quantum physics
  Entanglement distribution and WR
Joint experiments Deutsche Telekom & Qunnect
  Extend role WR beyond time synchronisation:
  monitoring link delay, optical powers and polarisation state of WR signal to trigger for compensation in quantum signal
Summary
It is possible that WR can provide live network metrics that improve the performance of quantum networking testbeds, beyond just time synchronization, without additional hardware

## Slide 33
Further analysis of Berlin data + gather more data
Local experiment @ CERN : Collaboration Single Quantum – Qunnect
  In-kind contribution of EPS and detectors
  Test different White Rabbit wavelengths and powers
Outlook

## Slide 34
Questions?

## Slide 35
Monitoring only set-up
White Rabbit Switch
DWDM
DWDM
White Rabbit Switch
APC inj
1320 nm
APC cmp
1320 nm
APC cmp
1550 nm
Grandmaster
polarizer
Real deployed fiber; ~ 40km

## Slide 36
Results monitoring only