## Slide 1: Fast failures in fcc-ee
Layout and optics overview, tapering, powering failures
TE-MPE-CB section meeting 17-03-2025 Delphine Domange

## Slide 2: Outline
Layout and optics overview
  FCC-ee layout
  Powering scheme
  Optics
  Synchrotron radiation
  Machine protection consideration
Tapering
  What is tapering ?
  Realistic tapering
  Algorithm and implementation
  Results
Powering failure
  Main dipole powering failure
  Simulation
  Results and criticality
  Next steps

## Slide 3: Layout and optics overview

## Slide 4: Layout and optics overview
Booster: acceleration from 20 GeV to collision energy
Electron – Positron collider
90.65 km circumference
4 technical insertions
  PB - Injection / Extraction to beam dump
  PF - Collimation
  PH - Collider RF
  PL - Booster RF
4 interaction points – experiments (PA, PD, PG and PJ)
Physics mode | Energy
Z | 45.6 GeV
W | 80 GeV
Zh | 120 GeV
t | 182.5 GeV
Physics mode | Energy
Z | 45.6 GeV
W | 80 GeV
Zh | 120 GeV
 | 182.5 GeV

## Slide 5: Layout and optics overview
V24.3 GHC layout
Normal conducting magnets (except for the final focusing insertion)
60 mm
Arc dipoles
  Twin aperture
  2840 units (of 2 magnets)
  Half-arc powering
  16 circuits in total
Arc quadrupoles
  Twin aperture
  2836 magnets
  Half-arc powering
  32 circuits (16 FQ + 16 DQ)
Arc sextupoles
  Single aperture
  600 magnets at Z
  2336 magnets at
  584 circuits (292 FS + 292 DS)
Cell configuration and magnet cross-sections from the FCC midterm report May 2024.

## Slide 6: Layout and optics review
Synchrotron radiation
Particles lose energy via photon emission when (transversely) accelerated
  Particle energy varies along the machine
  RF cavities restore the energy but located in a single technical insertion
  Sawtooth shape of the closed orbit
  Damping of the beam
Physics mode | Energy | Energy loss / turn
Z | 45.6 GeV | 39.1 MeV (0.086%)
W | 80 GeV | 374 MeV (0.47%)
Zh | 120 GeV | 1.88 GeV (1.57%)
t | 182.5 GeV | 10.29 GeV (5.64%)
Physics mode | Energy | Energy loss / turn
Z | 45.6 GeV | 39.1 MeV (0.086%)
W | 80 GeV | 374 MeV (0.47%)
Zh | 120 GeV | 1.88 GeV (1.57%)
 | 182.5 GeV | 10.29 GeV (5.64%)

## Slide 7: Layout an optics review
Sawtooth shape orbit
Z-pole energy
energy

## Slide 8: Layout and optics review
Damping (anti-damping) of the beam
Very small transverse beam size
Physics mode | Z | W | Zh | t
Horizontal emittance | 0.70 | 2.16 | 0.66 | 1.51
Vertical emittance | 1.05 | 1.20 | 0.57 | 0.82
Physics mode | Z | W | Zh | 
 | 0.70 | 2.16 | 0.66 | 1.51
 | 1.05 | 1.20 | 0.57 | 0.82

## Slide 9: Layout and optics review
Motivations for machine protection
Physics mode | Z | W | Zh | t | LHC
Energy (GeV) | 45.6 | 80 | 120 | 182.5 | 6800
# bunch | 11200 | 1780 | 380 | 56 | 2300
Bunch population ( | 2.14 | 1.45 | 1.32 | 1.64 | 1.6
Stored energy (MJ) | 17.5 | 3.4 | 0.96 | 0.27 | 400
Physics mode | Z | W | Zh |  | LHC
Energy (GeV) | 45.6 | 80 | 120 | 182.5 | 6800
# bunch | 11200 | 1780 | 380 | 56 | 2300
 | 2.14 | 1.45 | 1.32 | 1.64 | 1.6
Stored energy (MJ) | 17.5 | 3.4 | 0.96 | 0.27 | 400
Very small beam emittance () => Large energy density
Large damage potential in case of failure

## Slide 10: Tapering

## Slide 11: Tapering
Ideal tapering
  Individual correction for each magnet
  Minimise the closed orbit
Tapering: local correction of the magnet strength to compensate for variation in particle energy

## Slide 12: Tapering
Realistic tapering
  Mean correction for a group of magnets
  Different configurations studied
Example: D64Q32SCM#

## Slide 13: Tapering
Algorithm and implementation
i
j
i
j
i
j
i
j
*
*
*
*
*
Threading

## Slide 14
Realistic tapering Z-pole energy

## Slide 15
Realistic tapering energy

## Slide 16
Realistic tapering energy
Acceptable tapering for energy is D128Q32SCM#
  Beta beating < 5%
Powering of 5/6 basic cells for the dipoles
Cell configuration from the FCC midterm report May 2024.

## Slide 17: Powering failure

## Slide 18: Powering failure
Main dipole power converter failure
Half-arc powering: 175/180 dipoles in series
Loss of a power converter => Fast decay of the bending magnetic field
~ 10 turns to lose 1% of the bending magnetic field
with
Failing circuit naming convention: Arc PA-PL.1
FCC Xsuite model for simulation
  Synchrotron radiation
  Tapering
  Beamstrahlung
  Beam-beam
  Solenoid

## Slide 19: Main dipoles powering failure
Z-pole energy, Arc PG-PF.2

## Slide 20: Main dipoles powering failure
Z-pole energy, Arc PG-PF.2
Single particle tracking along the machine

## Slide 21: Main dipoles powering failure
Z-pole energy, Arc PG-PF.2
Single particle tracking along the machine

## Slide 22: Main dipoles powering failure
ttbar energy, Arc PA-PL.1

## Slide 23: Main dipoles powering failure
ttbar energy, Arc PA-PL.1
Single particle tracking along the machine

## Slide 24: Main dipoles powering failure
Conclusions
At z-pole energy, particle lost in 6 to 13 turns
At ttbar energy, particle lost in 14 to 18 turns
Fast loss of the particle
Large oscillation in the failing arc => orbit excursion with a possible very large deviation while exiting the failing arc
  Limited orbit excursion followed by a sudden jump that can be larger than 10
Offsets in quadrupoles and sextupoles outside of the failing arc induce horizontal local oscillation
Particle lost in collimator or in bottleneck quad QC4L

## Slide 25: Main dipoles powering failure
Next steps
Improve tracking simulations
  Bunch tracking
  Include beamstrahlung
  Include detailed collimation insertion (waiting input from BE-ABP)
Consider possible protection and mitigation system
Extend the powering failure study to the main quadrupoles and main sextupoles

## Slide 26: Backup slides

## Slide 27: Tapering
Comparison of realistic tapering scheme – Z-pole energy
Tapering scheme |  |  |  |  |  |  | 
D8Q8SCM# | 17.54541 | 3.511352 | 2.150847 | 0.640578 | 0.002154 | 0.064319 | 0.492583
D16Q16SCM# | 8.993656 | 2.142827 | 1.244224 | 0.205046 | 0.001264 | -0.01223 | 0.134788
D32Q8SCM# | 4.573902 | 2.632543 | 0.27018 | 0.191612 | 0.000776 | 0.006152 | 0.239203
D32Q16SCM# | 4.573899 | 2.632487 | 0.229624 | 0.16003 | 0.000744 | 0.006305 | 0.196039
D32Q32SCM# | 4.573888 | 2.63231 | 0.229951 | 0.157819 | 0.000815 | 0.006149 | 0.192405
D64Q16SCM# | 2.037801 | 8.234067 | 0.455197 | 0.146766 | 0.000275 | 0.006805 | -0.12369
D64Q32SCM# | 2.03789 | 8.23297 | 0.455775 | 0.152855 | 0.000198 | 0.006002 | -0.12874
Tapering scheme |  |  |  |  |  |  | 
D8Q8SCM# | 17.54541 | 3.511352 | 2.150847 | 0.640578 | 0.002154 | 0.064319 | 0.492583
D16Q16SCM# | 8.993656 | 2.142827 | 1.244224 | 0.205046 | 0.001264 | -0.01223 | 0.134788
D32Q8SCM# | 4.573902 | 2.632543 | 0.27018 | 0.191612 | 0.000776 | 0.006152 | 0.239203
D32Q16SCM# | 4.573899 | 2.632487 | 0.229624 | 0.16003 | 0.000744 | 0.006305 | 0.196039
D32Q32SCM# | 4.573888 | 2.63231 | 0.229951 | 0.157819 | 0.000815 | 0.006149 | 0.192405
D64Q16SCM# | 2.037801 | 8.234067 | 0.455197 | 0.146766 | 0.000275 | 0.006805 | -0.12369
D64Q32SCM# | 2.03789 | 8.23297 | 0.455775 | 0.152855 | 0.000198 | 0.006002 | -0.12874

## Slide 28: Tapering
Comparison of realistic tapering scheme – energy
Tapering scheme |  |  |  |  |  |  | 
D8Q8SCM# | 341.6634 | 206.9149 | 155.7901 | 6.71668 | 0.031133 | 105.3997 | 4.033965
D16Q16SCM# | 155.643 | 113.9441 | 59.04256 | 18.25795 | 0.016699 | 24.00643 | -0.36861
D32Q8SCM# | 73.78891 | 92.04613 | 37.88255 | 14.83311 | 0.00497 | 9.77096 | -15.062
D32Q16SCM# | 73.81883 | 92.7319 | 40.88278 | 15.23158 | 0.004341 | 11.03241 | -11.6755
D32Q32SCM# | 73.83523 | 92.63805 | 38.09864 | 14.09065 | 0.004317 | 9.642237 | -10.3747
D64Q16SCM# | 38.33747 | 50.06991 | 10.71093 | 3.828585 | 0.002551 | 0.752189 | -2.18372
D64Q32SCM# | 38.33651 | 50.14431 | 8.112392 | 2.668171 | 0.002498 | 0.446192 | -1.09471
D128Q32SCM# | 16.3833 | 201.3616 | 3.968574 | 3.570442 | 0.001795 | 0.085597 | -1.61924
Tapering scheme |  |  |  |  |  |  | 
D8Q8SCM# | 341.6634 | 206.9149 | 155.7901 | 6.71668 | 0.031133 | 105.3997 | 4.033965
D16Q16SCM# | 155.643 | 113.9441 | 59.04256 | 18.25795 | 0.016699 | 24.00643 | -0.36861
D32Q8SCM# | 73.78891 | 92.04613 | 37.88255 | 14.83311 | 0.00497 | 9.77096 | -15.062
D32Q16SCM# | 73.81883 | 92.7319 | 40.88278 | 15.23158 | 0.004341 | 11.03241 | -11.6755
D32Q32SCM# | 73.83523 | 92.63805 | 38.09864 | 14.09065 | 0.004317 | 9.642237 | -10.3747
D64Q16SCM# | 38.33747 | 50.06991 | 10.71093 | 3.828585 | 0.002551 | 0.752189 | -2.18372
D64Q32SCM# | 38.33651 | 50.14431 | 8.112392 | 2.668171 | 0.002498 | 0.446192 | -1.09471
D128Q32SCM# | 16.3833 | 201.3616 | 3.968574 | 3.570442 | 0.001795 | 0.085597 | -1.61924

## Slide 29: Main dipoles powering failure
Z-pole energy, Arc PA-PL.1 failing