## Slide 1: TWOCRYST Validation : Machine Protection
Eloise Matheson [BE-CEM], Pascal Hermes [BE-ABP], Daniele Mirarchi [BE-OP]

## Slide 2: Contents
TWOCRYST Installation
TWOCRYST Interlocks
TWOCRYST Machine Protection Test Plan

## Slide 3: TWOCRYST Installation
TCCS.5R3.B2
DCUM: 6773.9
TCCP.4L3.B2
DCUM: 6653.25
XRPV.A4L3.B2
DCUM: 6652.6
XRPV.B4L3.B2
DCUM: 6651.9

## Slide 4: TWOCRYST Installation
TCCS.5R3.B2
XRPV.B4L3.B2, XRPV.A4L3.B2, TCCP.4L3.B2
ECR: EDMS #2962891

## Slide 5: TWOCRYST Interlocks
EDMS Document #3192097 (will be released pending any feedback from this meeting)
There is one dedicated channel available on the BIC (CIB.UJ33.U3 – Maskable Both Beam input 11) to read the USER_PERMIT from the daisy-chained TCCS, TCCP and Roman Pot device signals

## Slide 6: TWOCRYST Device Status
TCCS: Beam Pipe IN, Crystal OUT
Non-MD Status
MD Status
TCCS: Beam Pipe OUT, crystal can move within limits
TCCP: Crystal OUT, Target OUT
TCCP: crystal and target can move within limits
XRPVs: Detectors can move within limits
XRPVs: Detectors OUT
Approximate beam position

## Slide 7: TWOCRYST BIS Interlocks: TCCS & TCCP
TCCS has same setup as per the TCPC devices. Interlock on:
  Position limits on crystal moveable stage
  Single sided energy limit on crystal moveable stage (minimum/outer position)
  Replacement beam pipe and crystal moveable stages switches
  Note: As the TCCS is a refurbished version 1 TCPC device, there is only 1 switch indicating each extreme position of the crystal linear stage. The beam pipe chamber has 2 switches
TCCP has similar setup as per the TCPC devices. Interlock on:
  Position limits on crystal moveable stage and target moveable stage
  Single sided energy limits on crystal moveable stage and target moveable stage (minimum/outer position)

## Slide 8: TWOCRYST BIS Interlocks: Roman Pot
Each Roman Pot upper jaw has the following interlocks
  Position limits on upper roman pot linear stage based on one* LVDT reading
  Energy limits on upper roman Pot linear stage based on one* LVDT reading
  *This primary LVDT input signal could be swapped to the redundant secondary LVDT signal after remote intervention by a BE-CEM expert

## Slide 9: TWOCRYST SIS Interlocks
  TCCS, switchIn_beampipe == True AND switchOut_beampipe == False (to avoid injecting high intensity beams with pipe open)
  TCCP, switchOut_linear == True, switchOut_target == True (to be sure devices are not on the beam path)
  XRPVs, switchOut == True (to be sure devices are not on the beam path)

## Slide 10: TWOCRYST MP Test Plan
Position Interlock Tests – BIS
Position Interlock Tests – SIS

## Slide 11: TWOCRYST MP Test Plan
Power Cut & PRS Reboot Interlock
Check the access map and protected set (RBAC roles checks)