## Slide 1
Machine Learning
and Radiological Characterization
M. Magistris, A. Gomes, R. Neugebauer, J.B. Potoine, E. Stamati
RP Seminar 17/04/2025 EDMS 3291657

## Slide 2: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 3: Machine learning
Machines mimicking humans
Machines learning from data
Machines using multilayer networks

## Slide 4: Statistics Machine learning
Description from an a-priori model Predictions from (un)labeled data
Statistics
Set the model
Use data to set parameters
Deal with outliers
=> describe the population
Machine learning
Set the data
Identify patterns
Deal with parameters
=> predict individuals

## Slide 5: Machine learning: Deep learning
Interconnected nodes, trained to identify patterns
From many simple inputs to few complex outputs
What is the activity of Ni-63 given the chemical composition and radiological history?
No need for deep learning, ActiWiz can answer!
What is the radiological history given a spectrometry measurement and the type of material?
With deep learning you can swap inputs and outputs

## Slide 6: Machine learning: visualization is king!
Recipe (serves 1-2 plots)
Clean the data
Code (R/Python)
Identify message
Reveal message visually

## Slide 7: Machine learning: Applications
Targeted advertising
Weather forecast
Stock market

## Slide 8: Machine learning: and radiological characterization?
Google search
“machine learning radiological characterization”
Top result
...this seminar!!

## Slide 9: Machine learning: radiological characterization
Until today: slow progress, ML needs:
  Large datasets...
  ...a lot of data...
  ... even more data.
Data from
  gamma-spectrometry: time-consuming
  radiochemical analysis: expensive
  chemical composition: wishful thinking
  radiological history: what did you just say?
More data, please!!

## Slide 10: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 11: Data and tools: Waste management - Traceability
From G.Dumont, EDMS 3026072
Notes: TEST

## Slide 12: Data and tools: TREC - Extraction of statistics & KPIs
From G.Dumont, EDMS 3026072
TREC allows the extraction of reliable data:
- Declaration to French/ Swiss authorities (Tripartite agreement)
- Waste management follow-up
Notes: TEST

## Slide 13
Data and tools: Radioactive waste properties
Data recovered when creating waste packages...
...and used in machine learning models for characterization.
Fig: Estimation of materials in SHERPA waste between 2020-2024
Fig: Distribution of facilities of origin for SHERPA waste and net weight of their packages, as provided by TREC
Notes: TEST

## Slide 14: Data and tools: (Py)ActiWiz
Design:
We extract a population of virtual waste items based on the probability distributions
Operation:
ActiWiz computes the radiological properties of every virtual item

## Slide 15: Data and tools: (Py)ActiWiz
Virtual items can be grouped together into packages
Analysis:
Simulate
  spectrometry measurements
  total gamma counting
Heterogeneous activity
Sampling
Data!! DATA!!!!

## Slide 16: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 17: Scaling factors Systematic vs probabilistic
ActiWiz
Systematic
Probabilistic
Input parameters: material, position, geometry, history....
Old school
Machine learning

## Slide 18: Scaling factors Systematic vs probabilistic
ActiWiz
Systematic
Probabilistic
Input parameters: material, position, geometry, history....
Old school
Machine learning

## Slide 19: Scaling factors Systematic vs probabilistic
ActiWiz
Systematic
Probabilistic
Input parameters: material, position, geometry, history....

## Slide 20: Scaling factors: input parameters Probability distributions
Beam energy
Mass:
Entire waste item
Individual components making up the waste item
Beam loss [p/s] Irradiation [years] Waiting [years]

## Slide 21: Scaling factors Systematic vs probabilistic
Probabilistic
Scaling factors on average 2 x lower than with the systematic approach.

## Slide 22: Scaling factors Systematic vs probabilistic
Probabilistic
Scaling factors on average 2 x lower than with the systematic approach.
For crucial radionuclides, on average 3 x lower.

## Slide 23: Scaling factors: impact on total activity
Systematic
Probabilistic
True activity [Bq]
True activity [Bq]
Predicted activity [Bq]
Predicted activity [Bq]
Third quartile
Ratio PE/TA

## Slide 24: Scaling factors Radiological properties
Dose-rate:
Near the entire waste item
Near individual components making up the waste item
1 nSv/h
See the invisible (< 1 nSv/h)
Analyze properties of components (e.g. plastic) based on DR of the entire item
Mass
Invisible

## Slide 25: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 26: With PCA …
We can predict an item’s waiting time based only on quantities we can measure!

## Slide 27: So what is this “PCA”?

## Slide 28: So what is this “PCA”?
Principal Component Analysis is a method used to simplify complex data by turning it into a smaller set of new variables, called "principal components." These components capture the most important patterns or trends in the data.

## Slide 29: So what is this “PCA”?
Principal Component Analysis is a method used to simplify complex data by turning it into a smaller set of new variables, called "principal components." These components capture the most important patterns or trends in the data.

## Slide 30: Let’s visit a gallery!

## Slide 31: Let’s visit a gallery!
A gallery is hosting an exhibition about Van Gogh and Da Vinci.
We’re approaching the first two painting, carefully reading the guide and this is what it says:

## Slide 32: Let’s visit a gallery!
Painting 1 = Painting of a man seated at a table, dressed in period clothing and a hat. He gazes slightly downward, with an introspective expression.

## Slide 33: Let’s visit a gallery!
Painting 1 = Painting of a man seated at a table, dressed in period clothing and a hat. He gazes slightly downward, with an introspective expression.
Painting 2 = Painting of a man standing, dressed in period clothing and a hat. He is holding a paper and gazes slightly downward, with a serene expression.

## Slide 34: Let’s visit a gallery!
Painting 1 = Painting of a man seated at a table, dressed in period clothing and a hat. He gazes slightly downward, with an introspective expression.
Painting 2 = Painting of a man standing, dressed in period clothing and a hat. He is holding a paper and gazes slightly downward, with a serene expression.
Which one is Van Gogh and which one is Da Vinci?

## Slide 35: Let’s visit a gallery!
But what if …?

## Slide 36: Let’s visit a gallery!
But what if …?
Colour contrast
Movement
Painting 1
Painting 2

## Slide 37: Let’s visit a gallery!
Colour contrast
Movement
But what if …?
Painting 1
Painting 2
Is it obvious now?

## Slide 38: *This* is PCA!

## Slide 39: So how do we use it ??

## Slide 40: So how do we use it ??
Large dataset = Collection of virtual items coming out of our codes (~300 variables)

## Slide 41: So how do we use it ??
Large dataset = Collection of virtual items coming out of our codes (~300 variables)
Simplified dataset = Create fewer, new variables that still describe the dataset

## Slide 42: So how do we use it ??
Large dataset = Collection of virtual items coming out of our codes (~300 variables)
Simplified dataset = Create fewer, new variables that still describe the dataset
We have choice!
We can ask for these new variables to be a combination of features we can measure!

## Slide 43: So how do we use it ??
Linear combinations of gamma emitters activities
Virtual items

## Slide 44
Linear combinations of gamma emitters activities
More ML:
Classification model to predict waiting time
Virtual items
So how do we use it ??

## Slide 45
90% balanced accuracy
Virtual items
81% balanced accuracy
86% balanced accuracy
So how do we use it ??

## Slide 46: And what’s it for?
We have trained models to predict various quantities based on ActiWiz.
We have the tools to also train them based on g-spec results and use for quality control!

## Slide 47: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 48: Clearance Logistic regression
conventional
Electric cables to be cleared
Total gamma counting

## Slide 49: Clearance Bubble chart

## Slide 50: Clearance Two predictors: mass and dose rate

## Slide 51: Naïve Bayes
Log. KDE Bayes

## Slide 52: Naïve Bayes
Log. KDE Bayes

## Slide 53: Outline
Machine learning
Data and tools
Application:
  Scaling factors
  Principal component analysis (PCA)
  Clearance
Conclusions

## Slide 54: Conclusions
Machine learning is here to stay
CERN is at the forefront of ML for characterization:
  TREC + ActiWiz + measurements = Data
Endless opportunities:
  Impact of “authoritative” samples
  Waste sorting criteria (DR)
  Dose if sorting materials after clearance
  Impact of MDA on scaling factors
  Avoid penalizing assumptions
  ....
Machine learning is unreliable...
You should see human learning!!
Ha Ha!!

## Slide 55: Conclusions
Training
  Manuals, Google certificates, Udemy classes....
Networks
  Adasci, Kaggle...
CERN
  Thematic CERN school
  Deep learning, beam dynamics
Radiation protection (current trend)
  Image recognition
  Metrology

## Slide 56: Thank you!!!
Questions are welcome!!