## Slide 2
Introduction to BOND Design March 2025
BOND 14 T Dipole design meeting
Author: Juan Carlos Perez
Date: Tuesday March 18th

## Slide 3: Table of contents
High Field Magnet Program
BOND design status
Tooling and Mock-ups for BOND fabrication

## Slide 4
January 2025
High Field Magnet Programme
E. Todesco (Leader), B. Auchmann (Co-leader)
Programme office
G. Riddone
RD1: Nb3Sn conductor
RD1 line coordinators:
T. Boutboul (CERN)
C. Senatore (UniGe)
1.1 Nb3Sn wire and cable
T. Boutboul (CERN)
1.3 Internal oxidation wires
C. Senatore (UniGe)
1.15 Nb3Sn development
M. Sugano (KEK)
1.18 Internal oxid. studies
A. Leineweber (BAF)
1.19 Nb3Sn characterization
C. Senatore (UniGe)
RD3: Nb3Sn magnets
RD3 line coordinators:
F. Toral (CIEMAT)
Haziot, A. Foussat (CERN)
3.1 12 T cosq CERN
A. Foussat (CERN)
3.2 12 T cosq INFN
S. Farinon (INFN)
3.11 14 T Cosq
M. Sorbi (INFN)
3.4 Technology development
A. Haziot (CERN)
3.5 14 T Block dipole BOND
J. C. Perez (CERN)
3.6, 3.12 Block dipole F2D2
E. Rochepault (CEA)
3.7 Common coil DAISY
F. Toral (CIEMAT)
3.14 CC stress managed
D. M. Araujo (PSI)
RD2:HTS conductor+magnets
RD2 coord: A. Ballarino (CERN)
2.1 REBCO development
B. Holzapfel (KIT)
2.2 REBCO conductor
A. Ballarino (CERN)
2.5 Demonstrator DI coils
A. Baskys (CERN)
2.11 Demonstrator MI coil
T. Lecrevisse (CEA)
2.17 REBCO development
Y. Yang (SOTON)
2.15 IBS development
A. Malagoli (CNR-SPIN)
2.16 HTS laboratory
C. Barth (CERN)
RD4: Integration,
sustainability
RD4 line coordinator:
P. Borges de Sousa (CERN)
4.3 Insulation and HV
R. Piccin (CERN)
4.5 Quench D+P
M. Wozniak (CERN)
4.6 Cryogenics, thermal
P. Borges de Sousa (CERN)
RD5: Infrastructures
5.1 Test
F. Mangiarotti (CERN)
5.2 Conductors, cables
J. Fleiter (CERN)
5.4 Manufacturing
J. Axensalva (CERN)
5.5 MM, modelling
L. Fiscarelli (CERN)
Note: completed WP
not shown
2.6 Solenoids and MuC
L. Bottura (CERN)
2.19 REBCO racetrack
D. M. Araujo (PSI)
2.18 HTS 10 T dipole
M. Statera (INFN)
5.7 CIEMAT lab
C. Martins (CIEMAT)
Collaboration WPs
CERN WPs
HFM steering board
M. Lamont (chair)
P. Vedrine (co-chair)
HFM collaboration board
C. Senatore (chair)
TBD (deputy)
3.3 5-m-long block
J. Ferradas Troitino (CERN)
6.1 Societal impact
E. Chesta (CERN)
2.20 REBCO characteriz.
M. Eisterer (TUWien)

## Slide 5: Scope of the Work Package
WP3.5: Nb3Sn 14 T Block dipole BOND
Demonstrate Nb3Sn performance in a 14 T block-type dipole at 1.9 K
Design and construction of a 14 T accelerator quality dipole model magnet
  The short model magnet should reach 15-15.5 T field
Explore alternatives and develop design and technology for Nb3Sn accelerator dipoles

## Slide 6: 14 T Block dipole BOND
BOND stands for BlOck coil Nb3Sn Dipole
BOND

## Slide 7: 14 T Block dipole BOND
Design requirements:
14 T bore field with ≈ 20 % load line margin
(1.9 K using HFM specs).
Protection time margin*1 > 40 ms.
Aperture = 50 mm.
Eq. coil width*2 < 60 mm → “accelerator coil size”.
Field quality within 10 units at all current levels (excluding PC effects).
Magnet OD:
  Double aperture, inter-beam distance: 250 mm.
  Cold mass OD: 800 mm and Magnet OD: 760 mm.
  For the 1 in 1, we will scale down.
Ti post
Al shell
Coil
Vertical pad
Horizontal pad
Key
Iron yoke
Courtesy of A. Haziot, J. Ferradas & E. Fernandez

## Slide 8: BOND Design Parameters
The 2D & 3D electromagnetic design for the single aperture configuration was completed in January 2025.
Magnet |  | Single | Double
Aperture | [mm] | 50 | 50
Intra-beam distance | [mm] | - | 250
Yoke diameter | [mm] | 540 | 680
Shell diameter | [mm] | 640 | 780
Nominal current | [kA] | 20.005 | 19.340
J overall | [A/mm2] | 360 | 348
J strand (eng.) | [A/mm2] | 526 | 509
Nominal field | [T] | 14.00 | 14.00
Peak field | [T] | 14.85 | 14.81
Ap. to peak field ratio | [%] | 6.0 | 5.7
Load line fraction @1.9 K | [%] | 82.7 | 81.7
Load line fraction @4.2 K | [%] | 92.6 | 91.2
Temperature margin | [K] | 3.99 | 4.11
Inductance | [mH/m] | 4.72 | 10.24
Stored energy | [MJ/m] | 1.031 | 2.064
Coil |  | Single | Double
No. of turns per pole |  | 52 | 
Insulated cable surface | [mm2] | 11572 | 
Equivalent coil width | [mm] | 53.4 | 
Coil efficiency *1 | [T.mm/A] | 0.00073 | 0.00075
Courtesy of A. Haziot

## Slide 9: BOND Coils Configuration and Field Profile
Flared end curvature radius | mm | 750
Flared end angle | º | 7
Flared end straight section | mm | 178.4

## Slide 10: Tooling & components design
Coil components and coil fabrication tooling design is well on track.
The 3D design will be completed by end of April.
First tooling delivered is expected by late summer 2025.
Winding
Reaction
Impregnation
Courtesy of N. Peray

## Slide 11: Mock-up design of sliding reaction tooling
Thanks to the experience gained during the construction of the Race-tracks, FRESCA2 and MQXF magnets, BOND tooling designed to compensate for dimensional variations during heat treatments is currently in the design phase.
The basic concepts will be validated using simplified mock-ups that replicate conditions close as possible to those that will be used during coil manufacturing.
Racetrack coil mock-up with integrated sliding system
Courtesy of N. Lusa, J. Ferradas & B. Pellet
Circular ceramic bearing
Linear ceramic bearing

## Slide 12: BOND Magnet development plan
Tests using Mock-ups
Coil 3D CAD Design
3D CAD Winding, reaction & splicing tooling
Q1_2025
Q2_2025
Q3_2025
Q4_2025
Q1_2026
Q2_2026
Q3_2026
Q4_2026
Trial Copper Coil
1st Nb3Sn Coil Winding
Today
Analysis
Iterative engineering design
Insulated Nb3Sn Cable delivery
First dummy copper cable at CERN
First Single Aperture Magnet #1 assembly
Cold Powering
Tests Magnet #1
Single Aperture Magnet #2 assembly
Powering tests Magnet #2
Double Aperture Magnet #1 assembly
Double Aperture Magnet Magnet #1 powering tests