## Slide 1: Introduction to Sailing part 2
Sebastian Łopieński
e-mail: Sebastian.Lopienski@gmail.com
YCC, http://cern.ch/yachting

## Slide 2: After first outings…
“Where does the wind come from?”
“How to slow down/break?”

## Slide 3: After first outings…
“Where does the wind come from?”
“How to slow down/break?”
Helming
Trimming sails
Is it FUN or just too complicated? 

## Slide 4: Outline
True and apparent wind
Trimming sails
Spinnaker
More on manoeuvres:
tacking, gybing
MOB (man overboard)
leaving and entering port
Priority rules
please interrupt and ask questions!!!

## Slide 5: Do you still remember…?
Courtesy of www.easytolearn.net

## Slide 6: A sail
luff
luff
foot
foot
leech
battens
battens
battens
battens
battens
tack
tack
head
head
clew
Pictures © Sebastian Łopieński
mainsail halyard
outhaul
jib halyard
cunningham
… and obviously: mainsail and jib sheets
vang / kicker
See different types of sails

## Slide 7: Some verbs...
to hoist a sail (fr. hisser) and to lower it (fr. affaler)
to trim a sail (fr. border) and to ease it (fr. choquer)
to luff (fr. lofer) and to bear away (fr. abattre)
to tack (fr. virer) and to gybe (fr. empanner)

## Slide 8: True and apparent wind
boat speed
true wind
apparent wind
„boat wind”
wind

## Slide 9: Trimming a sail
Sail eased completely flatters and generates no force (A)
Sail pulled slightly doesn’t flatter, but still no force (B)
When trimmed some more, sail starts to work (C)
More trimming generates air turbulence and lowers the force (D)
Hard trimming against the wind is highly inefficient (E)
wind
wind
OPTIMUM
Drawings © YCC
Poll “Sail trimming”

## Slide 10: Trimming sails
wind
A sail should be let out until it stops working, …and then trimmed a little to make it stop flatter
Correct sail trim depends on the course, so: Changing your course?  work on your sails!
Both sails (mainsail and the jib) should be (more or less) parallel
Correctly trimmed
Sails not parallel – something is WRONG!
Overtrimmed – WRONG!
Not enough trimmed – WRONG!
wind
wind
wind
Poll “Correct trim”
wind
A
B
C
D
E

## Slide 11: Trimming sails
wind
A sail should be let out until it stops working, …and then trimmed a little to make it stop flatter
Correct sail trim depends on the course, so: Changing your course?  work on your sails!
Both sails (mainsail and the jib) should be (more or less) parallel
Correctly trimmed
Sails not parallel – something is WRONG!
Overtrimmed – WRONG!
Not enough trimmed – WRONG!
wind
wind
wind

## Slide 12: Spinnaker (symmetric)
Pictures © Sebastian Łopieński
spinnaker pole
spinnaker
Moving the pole up and down:
leeward sheet
Controlling the spinnaker to port and starboard:
windward sheet (guy)
uphaul
downhaul

## Slide 13: Tacking
crew:
5. trimming jib on the new side
4. changing place when passing line of the wind
3. easing jib completely when it stops working
2. grabbing other jib sheet “ready!”
1. trimming jib
wind
helmsman:
5. rudder zero
4. changing place when passing line of the wind
3. “tacking!” / “lee-oh!” luffing up more (rudder to starboard *)
2. “ready to tack?”
1. trimming mainsail luffing up to close-hauled course
1.
2.
3.
4.
5.
* in the case drawn

## Slide 14: Gybing
wind
crew:
1. easing jib
2. grabbing other jib sheet “ready!”
3. continue easing jib
4. changing place when passing line of the wind
pulling jib to the new side
5. trimming jib (loosely!)
helmsman:
1. easing mainsail falling off to broad-reach course
2. “ready to gybe?”
3. “gybing!” falling off (very slowly!) bringing mainsail to the middle “watch your head” / “heads down”
4. changing place when passing line of the wind
easing mainsail to the other side
5. rudder zero
1.
2.
3.
4.
5.
Slow rotation!!!
(go almost straight)

## Slide 15: Man overboard (MOB)
From http://www.learn2sail.co.uk/dinghies/section.asp?id=11
From http://www.lalizas.com/products.asp?S0=1&S1=4
2. tack
tack
wind
wind
3. approach upwind, sails eased out (not working)
1. sail away in broad reach

## Slide 16: Leaving and entering a harbour
Land
wind
Land
wind
both maneuvres easy
difficult
dangerous!
Land
wind
typical in Port Choiseul
keep to windward
ready to ease or put down sails (when entering harbour)

## Slide 17: Priority rules
wind
wind
starboard tack boat (wind from starboard)
Port tack boat must keep clear of starboard tack boat
port tack boat
windward boat
Windward boat must keep clear of boats to leeward
Boat clear astern must keep clear of slower boat in front
leeward boat
boat clear astern (behind another boat)
motor boat
sailing boat
Sailing boat has a priority over motorboats
There are exceptions!!!

## Slide 18: Distance, speed etc.
1 nautical mile (nm) is 1852 meters (length of 1 minute of arc on the equator)
1 knot (kn) is 1 nautical mile per hour (2 knots = 1 m/s)
(YCC) boats - usually 3 to 5 knots, up to 7-10 knots (could be more for planing dinghies)

## Slide 19: Wind – Beaufort scale
0 | 0-1 knots | 0-1 km/h | flat water
1 | 1-3 knots | 2-5 km/h | ripple
2 | 4-6 knots | 6-11 km/h | wavelets
3 | 7-10 knots | 12-19 km/h | large wavelets
4 | 11-16 knots | 19-28 km/h | small waves, white horses
5 | 17-21 knots | 29-38 km/h | long moderate waves, many white horses
6 | 22-27 knots | 39-49 km/h | large breaking waves, white foam
7 | 28-33 knots | 50-61 km/h | 
8 | 34-40 knots | 62-74 km/h | 
9 | 41-47 knots | 75-87 km/h | 
10 | 48-55 knots | 88-102 km/h | 
11 | 56-63 knots | 103-117 km/h | 
12 | 64+ knots | 118+ km/h | the air is filled with foam and spray
Hopefully you won’t be sailing in these winds on Lac Leman!

## Slide 20: Further reading
“YCC Sailing Course for Beginners” booklet: http://cern.ch/yachting/courses/YCCSailingCourse.pdf

## Slide 21: Take part in YCC activities
Attend other Theory courses
Come and sail on Thursday practice evenings
  meet people, sail on different boats
Participate in Internal regatta
  best way to learn sailing, even for complete beginners
Register to Surveillance boat shifts
  you’ll have to do two shifts before taking a sailing test
Check the Calendar for other events
  Newcomers Welcome, Opening Dinner, etc.

## Slide 22: The famous Lake Geneva races
Geneve-Rolle regatta Saturday, early June (200+ boats passing by Versoix around 15-16h)
Bol d’Or regatta Saturday, mid-June (600+ boats passing by Versoix around 11h-13h)

## Slide 23: Thank you
…and please
ask questions!!!
also to
Sebastian.Lopienski@gmail.com
Pictures © Sebastian Łopieński
Notes: And enjoy sailing