## Slide 1: The Art of Navigating Part VI: The Tides
Torsten Layda
Yachting Club CERN 31.03.2025
torsten.layda@protonmail.ch

## Slide 2: Overall Curriculum
Charts and GPS
Coastal Navigation (basics)
Beacons and Lights
Meteorology
The Plotter
The Tides
Coastal Navigation (advanced)
Off-shore Passages
Celestial Navigation

## Slide 3: Setting the Scene: The Various Courses
No wind, no current: the easiest situation
Add wind
Add current

## Slide 4: Landscape and Seascape In real life

## Slide 5: Landscape and Seascape On the chart

## Slide 6: The Log (-book)
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
Tides |  | (HT or LT) |  | (HT or LT) |  | (HT or LT) |  | (HT or LT) | 
Port | Coeff | Time | Height | Time | Height | Time | Height | Time | Height

## Slide 7: Position Absolute Position from, e.g., GPS
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
50.4 | 45°N46’.60 002°E25’.35 |  |  |  |  |  |  |  |  |  | 
Latitude:
Longitude:

## Slide 8: Motoring in the Mediterranean True Heading == Course Through Water == Course Over Ground
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
… | ..N .. …E .. |  |  |  |  | 135 |  | 135 |  | 135 | 

## Slide 9: Magnetic North vs True North The Declination, aka Variation
Geographic north pole is not the magnetic north pole
The difference is expressed as the Declination, D
Est-ce plus, ou est-ce moins?
Westerly Declinations are negative, easterly Declinations are positive
D = D(t, L, G)
Nv
Nm

## Slide 10: Magnetic North vs True North True Heading  Compass Course
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
… | ..N .. …E .. | 134 | 0 |  | 1 | 135 |  | 135 |  | 135 | 
Cm = Cv – D
Cc = Cm – d,
Assume Deviation d ≈ 0
So, Cc = Cv – D
use minus

## Slide 11: The Leeway dér.
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
… | ..N .. …E .. |  |  |  |  | 130 | 5 | 135 |  | 135 | 
Wind
Port tack  dér. > 0
Starboard tack  dér. < 0
close hauled: | dér.|  10
beam reach: | dér.|  5
broad reach: | dér.|  3
use minus

## Slide 12: Why there are Tides
The basics

## Slide 13: The Earth-Moon System
Daily Rotation around the common center of gravity
Two maxima, ca. 45 cm
  One maximum “under” the moon, due to the gravitational pull of the moon
  The other on the opposite side, due to the centrifugal force being larger than the gravitational pull

## Slide 14: Moon Going Around the Earth
Daily shift of the tidal curve by ca. 50 min
After 24 hours the moon is in position D+1
Observer needs to travel a tad extra:
day

## Slide 15: Effects of the Geography
Higher amplitude
  Bay of Fundy
  St. Malo
  Solent / southern Brittany / German Bight
Actually, there are also areas with smaller, even 0, amplitude
Different times for high/low water
Distortion of the tide curve

## Slide 16: A Third Body in the System: The Sun
Slightly less effect than moon
The tidal wave remains effectively “under” the moon, i.e., high water when moon is in the south
Superposition leads to neap tides and spring tides

## Slide 17: Monthly Cycle: Springs and Neaps New moon
Addition of the effects of moon and sun — spring tides
High water (moon in the south) at about 12:00 (sun also in the south)

## Slide 18: Monthly Cycle: Springs and Neaps First quarter
Partial compensation of the effects of moon and sun — neap tides
High water (moon in the south) at about 18:00 (sun setting in the west)

## Slide 19: Monthly Cycle: Springs and Neaps Full moon
Addition of the effects of moon and sun — spring tides
High water (moon in the south) at about 00:00 (sun in the “north”)

## Slide 20: Monthly Cycle: Springs and Neaps Third quarter
Partial compensation of the effects of moon and sun — neap tides
High water (moon in the south) at about 06:00 (sun rising in the east)

## Slide 21: Tidal Range Oscillates  (Tidal) Coefficients
Tidal Coefficients: Measure for the tidal range (not only HW!)
  This is about the amplitude (not only high water)
  During springs, high water higher, low water lower
  During neaps, high water lower, low water higher
20 ≤ Coeff ≤ 120
Equinoxes
20
45
70
95
120

## Slide 22: Monthly Cycle: Springs and Neaps Equivalence of coefficient and HW/LW times
Constellation (south up) |  |  |  | 
Phase | New Moon | First Quarter | Full Moon | Third Quarter
Springs / neaps | Spring tide | Neap tide | Spring tide | Neep tide
HW time | 12:00 | 18:00 | 00:00 | 06:00
Average Coeff | 95 | 45 | 95 | 45

## Slide 23: Yearly Cycle: Earth-Moon System Travels around the Sun
Spring equinox | ca. 20th March |  | Strong tides In particular, when coinciding with full/new moon
Summer solstice | ca. 21st June |  | 
Autumn equinox | ca. 22nd September |  | Strong tides In particular, when coinciding with full/new moon
Winter solstice | ca. 21st December |  | 

## Slide 24: Coefficients Over The Year Cherbourg 2025 (Jan-Nov)
Chart: 
 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125
Lag of springs and neaps compared to moon phase: Age de la marée
Note the effects of the equinoxes and the summer solstice
Chart: 
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5 | 24 | 24.5 | 25 | 25.5 | 26 | 26.5 | 27 | 27.5 | 28 | 28.5 | 29 | 29.5 | 30 | 30.5 | 31 | 31.5 | 32 | 32.5 | 33 | 33.5 | 34 | 35 | 35.5 | 36 | 36.5 | 37 | 37.5 | 38 | 38.5 | 39 | 39.5 | 40 | 40.5 | 41 | 41.5 | 42 | 42.5 | 43 | 43.5 | 44 | 44.5 | 45 | 45.5 | 46 | 46.5 | 47 | 47.5 | 48 | 48.5 | 49 | 50 | 50.5 | 51 | 51.5 | 52 | 52.5 | 53 | 53.5 | 54 | 54.5 | 55 | 55.5 | 56 | 56.5 | 57 | 57.5 | 58 | 58.5 | 59 | 59.5 | 60 | 60.5 | 61 | 61.5 | 62 | 62.5 | 63 | 64 | 64.5 | 65 | 65.5 | 66 | 66.5 | 67 | 67.5 | 68 | 68.5 | 69 | 69.5 | 70 | 70.5 | 71 | 71.5 | 72 | 72.5 | 73 | 73.5 | 74 | 74.5 | 75 | 75.5 | 76 | 76.5 | 77 | 77.5 | 78 | 78.5 | 79 | 80 | 80.5 | 81 | 81.5 | 82 | 82.5 | 83 | 83.5 | 84 | 84.5 | 85 | 85.5 | 86 | 86.5 | 87 | 87.5 | 88 | 88.5 | 89 | 89.5 | 90 | 90.5 | 91 | 92 | 92.5 | 93 | 93.5 | 94 | 94.5 | 95 | 95.5 | 96 | 96.5 | 97 | 97.5 | 98 | 98.5 | 99 | 99.5 | 100 | 100.5 | 101 | 101.5 | 102 | 102.5 | 103 | 103.5 | 104 | 104.5 | 105 | 105.5 | 106 | 106.5 | 107 | 108 | 108.5 | 109 | 109.5 | 110 | 110.5 | 111 | 111.5 | 112 | 112.5 | 113 | 113.5 | 114 | 114.5 | 115 | 115.5 | 116 | 116.5 | 117 | 117.5 | 118 | 118.5 | 119 | 119.5 | 120 | 120.5 | 121 | 122 | 122.5 | 123 | 123.5 | 124 | 124.5 | 125 | 125.5 | 126 | 126.5 | 127 | 127.5 | 128 | 128.5 | 129 | 129.5 | 130 | 130.5 | 131 | 131.5 | 132 | 132.5 | 133 | 133.5 | 134 | 134.5 | 135 | 135.5 | 136 | 136.5 | 137 | 138 | 138.5 | 139 | 139.5 | 140 | 140.5 | 141 | 141.5 | 142 | 142.5 | 143 | 143.5 | 144 | 144.5 | 145 | 145.5 | 146 | 146.5 | 147 | 147.5 | 148 | 148.5 | 149 | 149.5 | 150 | 151 | 151.5 | 152 | 152.5 | 153 | 153.5 | 154 | 154.5 | 155 | 155.5 | 156 | 156.5 | 157 | 157.5 | 158 | 158.5 | 159 | 159.5 | 160 | 160.5 | 161 | 161.5 | 162 | 162.5 | 163 | 163.5 | 164 | 164.5 | 165 | 165.5 | 166 | 167 | 167.5 | 168 | 168.5 | 169 | 169.5 | 170 | 170.5 | 171 | 171.5 | 172 | 172.5 | 173 | 173.5 | 174 | 174.5 | 175 | 175.5 | 176 | 176.5 | 177 | 177.5 | 178 | 178.5 | 179 | 180 | 180.5 | 181 | 181.5 | 182 | 182.5 | 183 | 183.5 | 184 | 184.5 | 185 | 185.5 | 186 | 186.5 | 187 | 187.5 | 188 | 188.5 | 189 | 189.5 | 190 | 190.5 | 191 | 191.5 | 192 | 192.5 | 193 | 193.5 | 194 | 194.5 | 195 | 196 | 196.5 | 197 | 197.5 | 198 | 198.5 | 199 | 199.5 | 200 | 200.5 | 201 | 201.5 | 202 | 202.5 | 203 | 203.5 | 204 | 204.5 | 205 | 205.5 | 206 | 206.5 | 207 | 207.5 | 208 | 208.5 | 209 | 210 | 210.5 | 211 | 211.5 | 212 | 212.5 | 213 | 213.5 | 214 | 214.5 | 215 | 215.5 | 216 | 216.5 | 217 | 217.5 | 218 | 218.5 | 219 | 219.5 | 220 | 220.5 | 221 | 221.5 | 222 | 222.5 | 223 | 223.5 | 224 | 225 | 225.5 | 226 | 226.5 | 227 | 227.5 | 228 | 228.5 | 229 | 229.5 | 230 | 230.5 | 231 | 231.5 | 232 | 232.5 | 233 | 233.5 | 234 | 234.5 | 235 | 235.5 | 236 | 236.5 | 237 | 237.5 | 238 | 238.5 | 239 | 240 | 240.5 | 241 | 241.5 | 242 | 242.5 | 243 | 243.5 | 244 | 244.5 | 245 | 245.5 | 246 | 246.5 | 247 | 247.5 | 248 | 248.5 | 249 | 249.5 | 250 | 250.5 | 251 | 251.5 | 252 | 252.5 | 253 | 253.5 | 254 | 255 | 255.5 | 256 | 256.5 | 257 | 257.5 | 258 | 258.5 | 259 | 259.5 | 260 | 260.5 | 261 | 261.5 | 262 | 262.5 | 263 | 263.5 | 264 | 264.5 | 265 | 265.5 | 266 | 266.5 | 267 | 267.5 | 268 | 268.5 | 269 | 270 | 270.5 | 271 | 271.5 | 272 | 272.5 | 273 | 273.5 | 274 | 274.5 | 275 | 275.5 | 276 | 276.5 | 277 | 277.5 | 278 | 278.5 | 279 | 279.5 | 280 | 280.5 | 281 | 281.5 | 282 | 282.5 | 283 | 284 | 284.5 | 285 | 285.5 | 286 | 286.5 | 287 | 287.5 | 288 | 288.5 | 289 | 289.5 | 290 | 290.5 | 291 | 291.5 | 292 | 292.5 | 293 | 293.5 | 294 | 294.5 | 295 | 295.5 | 296 | 296.5 | 297 | 297.5 | 298 | 298.5 | 299 | 299.5 | 300 | 300.5 | 301 | 302 | 302.5 | 303 | 303.5 | 304 | 304.5 | 305 | 305.5 | 306 | 306.5 | 307 | 307.5 | 308 | 308.5 | 309 | 309.5 | 310 | 310.5 | 311 | 311.5 | 312 | 312.5 | 313 | 313.5 | 314 | 315 | 315.5 | 316 | 316.5 | 317 | 317.5 | 318 | 318.5 | 319 | 319.5 | 320 | 320.5 | 321 | 321.5 | 322 | 322.5 | 323 | 323.5 | 324 | 324.5 | 325 | 325.5 | 326 | 326.5 | 327 | 327.5 | 328 | 328.5 | 329 | 329.5 | 330 | 331 | 331.5 | 332 | 332.5 | 333 | 333.5 | 334 | 334.5 | 335 | 335.5 | 336 | 336.5 | 337 | 337.5 | 338 | 338.5 | 339 | 339.5 | 340 | 340.5 | 341 | 341.5 | 342 | 342.5 | 343 | 343.5 | 344 | 344.5 | 345 | 345.5 | 346 | 346.5 | 347 | 347.5 | 348 | 348.5 | 349 | 349.5 | 350 | 350.5 | 351 | 351.5 | 352 | 352.5 | 353 | 353.5 | 354 | 354.5 | 355 | 355.5 | 356 | 356.5 | 357 | 357.5 | 358 | 358.5 | 359 | 359.5 | 360 | 360.5 | 361 | 361.5 | 362 | 362.5 | 363 | 363.5 | 364 | 364.5 | 365 | 365.5
New Moon | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120
First Quarter | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125
Full Moon | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130
Third Quarter | 135 | 135 | 135 | 135 | 135 | 135 | 135 | 135 | 135 | 135 | 135

## Slide 25: Meteorological Effects
Air pressure
Wind
It can happen that water does not recede during the ebb

## Slide 26: Main Problem #1: Depth as Function of Time

## Slide 27: Chart Datum and Related Quantities
Dark Sea Green areas cover and uncover
Bisque areas never cover (“land”)
Depths are with respect to the chart datum
Heights in the uncovering area are with respect to the chart datum
Heights on land are with respect to the average spring high water (coefficient 95)

## Slide 28: Principal Ports High Water Portsmouth, May 2025:
High Water Portsmouth, May 2025
Times per Royal Yacht Squadron, Cowes
  https://www.rys.org.uk/yachting/tides
  In UT/BST as appropriate
More general source: Reeds Nautical Almanac
Tides |  | LT |  | HT |  | LT |  | HT | 
Port | Coeff | Time | Height | Time | Height | Time | Height | Time | Height
Portsmouth |  | 04:43 | 1.2 | 11:42 | 4.3 | 16:47 | 1.2 | 00:00 | 4.5

## Slide 29: Tidal Curves Portsmouth
Including plotting area for graphical determination heights/times

## Slide 30: Approximation of the Tide Curve: Rule of Twelfths
Hour since LW | Tidal Range Fraction | Δh with respect to LW
0 |  | 0
1 | 1/12 | 0.5 m
2 | 2/12 | 1.5 m
3 | 3/12 | 3.0 m
4 | 3/12 | 4.5 m
5 | 2/12 | 5.5 m
6 | 1/12 | 6.0 m
Assume a tidal range of 6 m
So, 1/12 = 0.5 m

## Slide 31: Secondary Ports British Approach, Example 1
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Plymouth (Devonport) | 00:00 and 12:00 | 06:00 and 18:00 | 00:00 and 12:00 | 06:00 and 18:00 | 5.5 | 4.4 | 2.2 | 0.8
Starcross | +00:40 | +01:10 | +00:55 | +00:25 | -1.4 | -1.5 | -0.8 | -0.1
If HW at Plymouth is at midnight or midday, 40 min to be added for Starcross.
If HW at Plymouth is at 06:00 or 18:00, 1 h 10 min to be added for Starcross.
If HW height at Plymouth is 5.5 m, 1.4 m to be deducted for Starcross.
If HW height at Plymouth is 4.4 m, 1.5 m to be deducted for Starcross.

## Slide 32: Secondary Ports Time Interpolation, Example 1
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Plymouth (Devonport) | 00:00 and 12:00 | 06:00 and 18:00 | 00:00 and 12:00 | 06:00 and 18:00 | 5.5 | 4.4 | 2.2 | 0.8
Starcross | +00:40 | +01:10 | +00:55 | +00:25 | -1.4 | -1.5 | -0.8 | -0.1
Say, Plymouth HW at 14:00
Starcross
Starcross
Use pragmatism

## Slide 33: Secondary Ports Height Interpolation, Example 1
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Plymouth (Devonport) | 00:00 and 12:00 | 06:00 and 18:00 | 00:00 and 12:00 | 06:00 and 18:00 | 5.5 | 4.4 | 2.2 | 0.8
Starcross | +00:40 | +01:10 | +00:55 | +00:25 | -1.4 | -1.5 | -0.8 | -0.1
Say, Plymouth HW with a height of 5.1 m (at 14:00)
Starcross
Starcross , use 3.6 m
Use pragmatism — and the pied de pilote

## Slide 34: Secondary Ports Logbook, Example 1
Fill in the deltas or the absolute values
French approach: Coefficients instead of HW/LW times to chose the set of the corrections
Tides |  | HT |  |  |  |  |  |  | 
Port | Coeff | Time | Height | Time | Height | Time | Height | Time | Height
Plymouth |  | 14:00 | 5.1 |  |  |  |  |  | 
Starcross |  | +00:50 | -1.44 |  |  |  |  |  | 
 |  | 14:50 | 3.66 |  |  |  |  |  | 

## Slide 35: Secondary Ports British Approach, Example 2
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Portsmouth | 00:00 and 12:00 | 06:00 and 18:00 | 05:00 and 17:00 | 11:00 and 23:00 | 4.7 | 3.8 | 1.9 | 0.8
Yarmouth | -01:05 | +00:05 | -00:25 | -00:30 | -1.7 | -1.2 | -0.3 | 0.0
If HW at Portsmouth is at midnight or midday, 65 min to be deducted for Yarmouth.
If HW at Portsmouth is at 06:00 or 18:00, 5 min to be added for Yarmouth.
If HW height at Portsmouth is 4.7 m, 1.7 m to be deducted for Yarmouth.
If HW height at Portsmouth is 3.8 m, 1.2 m to be deducted for Yarmouth.

## Slide 36: Secondary Ports Time Interpolation, Example 2
Say, Portsmouth HW at 14:00
Yarmouth
Yarmouth
Use pragmatism
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Portsmouth | 00:00 and 12:00 | 06:00 and 18:00 | 05:00 and 17:00 | 11:00 and 23:00 | 4.7 | 3.8 | 1.9 | 0.8
Yarmouth | -01:05 | +00:05 | -00:25 | -00:30 | -1.7 | -1.2 | -0.3 | 0.0

## Slide 37: Secondary Ports Height Interpolation, Example 2
Say, Portsmouth HW with a height of 4.4 m (at 14:00)
Yarmouth
Yarmouth , use 2.9 m
Use pragmatism — and the pied de pilote
 | TIME DIFFERENCES |  |  |  | HEIGHT DIFFERENCES |  |  | 
 | High Water |  | Low Water |  | MHWS | MHWN | MLWN | MLWS
Portsmouth | 00:00 and 12:00 | 06:00 and 18:00 | 05:00 and 17:00 | 11:00 and 23:00 | 4.7 | 3.8 | 1.9 | 0.8
Yarmouth | -01:05 | +00:05 | -00:25 | -00:30 | -1.7 | -1.2 | -0.3 | 0.0

## Slide 38: Secondary Ports Logbook, Example 2
Fill in the deltas or the absolute values
French approach: Coefficients instead of HW/LW times to chose the set of the corrections
Tides |  | HT |  |  |  |  |  |  | 
Port | Coeff | Time | Height | Time | Height | Time | Height | Time | Height
Portsmouth |  | 14:00 | 4.4 |  |  |  |  |  | 
Yarmouth |  | -00:42 | -1.53 |  |  |  |  |  | 
 |  | 13:18 | 2.9 |  |  |  |  |  | 

## Slide 39: Main Problem #2: Current as Function of Time

## Slide 40: Currents as Function of Time Tidal Stream Atlases
Speed
  1/10 kn
  Neaps, springs
… and Direction
… for every hour relative to HW
  Tidal hour lasts from half an hour before the nominal time to half an hour after
  In the example, from HW+2 ½ to HW+3 ½

## Slide 41: Currents as Function of Time Tidal Diamonds
Direction
Rate at spring tides in knots
Rate at neap tides in knots
 |  | J | ..N .. …E ..
Before High Water | -6 | 064 | 1.0 0.5
 | -5 | 053 | 2.8 1.5
 | -4 | 047 | 3.7 2.0
 | -3 | 045 | 3.9 2.1
 | -2 | 040 | 3.1 1.6
 | -1 | 035 | 2.0 1.0
HW | 0 | 206 | 0.6 0.3
After High Water | +1 | 231 | 2.7 1.4
 | +2 | 226 | 4.1 2.2
 | +3 | 225 | 4.3 2.2
 | +4 | 226 | 3.2 1.7
 | +5 | 236 | 1.7 0.9
 | +6 | 139 | 0.3 0.1
J

## Slide 42: How to go from CTW to COG From Surface to Seabed
Figure out the applicable current vector
Vector addition:
This yields a prediction of where we end up, given a specific Rs
Fill in the missing parts in the logbook:
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
… | ..N .. …E .. |  |  |  |  |  |  | 120 | 185 3.0 | 140 | vs = 8 kn
use plus

## Slide 43: How to go from COG to CTW From Seabed to Surface
Figure out the applicable current vector
Vector subtraction:
This yields a verification of our Rs given a specific Rf
Or a verification of the current:
Fill in the missing parts in the logbook:
Log | Position | Cc | d | Cm | D | Cv | dér. | Rs | Crt | Rf | Notes
… | ..N .. …E .. |  |  |  |  |  |  | 120 | 185 3.0 | 140 | vf = 11 kn
use minus

## Slide 44: Putting it all Together
The preparation of the day
Constant adaptation

## Slide 45: Preparation of a Stage Principle
WP 1
WP 2
WP 3
WP 4
WP 5
WP 7
WP 6

## Slide 46: Preparation of a Stage Basic Checklist
Identity port of arrival, an alternative as well as shelters en route
Take down the weather forecast
Study the chart and plot the Course Over Ground, Rf
Determine noticeable beacons and the appropriate way points
Note
  the features of the noticeable beacons
  the coordinates of the way-points
  the Rf, the Df and the rough Cc for every leg
Enter the way-points in the GPS, just in case...
  verify the Rf and Df with the GPS

## Slide 47: Preparation of a Stage Additional Items for Tidal Waters
Determine the departure window for your current location
In the tidal atlas, note the actual time at which the charts apply (post-it)
Determine the rough arrival times at each waypoint
Determine the current vector for each leg
Make sure you can actually get into the port of arrival
Study the approach to the port of arrival prior to departure
12:23
13:23
14:23
15:23
16:23
17:23

## Slide 48: While at Sea: Continuous Prediction & Confirmation Navigators never sleep
Just in time for the arrival at the next waypoint
  Verify the position (and potentially the current vector for the actual leg)
  Determine the current vector for the next leg
  Determine the Magnetic Heading, Cc, from the envisioned COG and the current vector
It is not a fundamental issue to deviate from the stage plan:
  May even be necessary in case of unsuitable weather, issues with the boat, etc.
  Use the identified alternative arrival port and shelters
  Redo the routing checklist for the new legs

## Slide 49: Some Practical Aspects in Tidal Waters

## Slide 50: Practical Considerations
Avoid current against wind
Avoid running aground during the ebb
Note that current acts below water, and the wind above the waterline
The vector sum of the effect of wind and current is relevant
  Going with the current with wind from astern can lead to zero apparent wind
Mooring maneuvers against the combo of wind/current
  Usually, current prevails
  Mooring infrastructure is foreseen accordingly

## Slide 51: Practical Considerations
Using transits
Switch off the log when moored
Put on life-line when on bathing platform at anchor
Mind eddies
Anticipate the change of water level also, and in particular, when moored
Anchoring is a tactical measure
  Bow and stern anchor
  Bahamian moor (“empenneler”)

## Slide 52: The End

## Slide 53: The Perihelion and Perigee / Aphelion and Apogee
Perigee: Supermoon / Apogee: Micromoon
  Effect ≈5 cm for springs
Perihelion (2)
  02nd – 04th January
  Strong tides, in particular when coinciding with full/new moon
Aphelion (1)
  03rd – 07th July
  Week tides, in particular when, coinciding with half moon