## Slide 1: APPLICAZIONI MEDICHE DELLA FISICA DELLE PARTICELLE D. CAMPI CERN – 2 Settembre 2009 Domenico.Campi@cern.ch domenico.campi@adam-geneva.ch

## Slide 2
La FISICA é Bella ed Utile (U.Amaldi)
Gli acceleratori ed i rivelatori di particelle, sviluppati essenzialmente per la fisica fondamentale, sono alla base di molte applicazioni d’avanguardia specialmente in campo medico
I rivelatori di particelle, gli stessi dei grandi esperimenti come ATLAS o CMS, permettono applicazioni diagnostiche
Gli acceleratori – nelle varie forme – permettono di generare gli isotopi necessari alla diagnostica d’avanguardia ma soprattutto vengono impiegati in applicazioni terapeutiche

## Slide 3
La fisica medica si basa essenzialmente sull’uso delle radiazioni
Con il termine di
RADIAZIONI
si comprendono alcuni fenomeni, tra loro differenti, che hanno in comune
il trasporto di energia nello spazio.
L'energia trasportata dalla radiazioni viene ceduta
quando la radiazione è assorbita dalla materia
attraversata.

## Slide 4: Le radiazioni possono anche essere distinte in: corpuscolate ossia dotate di massa come le particelle cariche elettricamente e i neutroni non corpuscolate come i fotoni ( X o ) che non hanno nè massa nè carica.
Sono radiazioni non corpuscolate la luce visibile, le onde radiotelevisive, le emissioni di “fotoni” (X o ) da parte di un elemento “radioattivo”.

## Slide 5
La radiazione elettromagnetica si propaga per mezzo di onde trasversali con velocità nel vuoto c = 3 108 m/s e in un mezzo di indice di rifrazione n, v = c/n.
Caratteristiche fondamentali:
Intensità o Ampiezza
Lunghezza d’onda, , (o frequenza  = c/n)
Parametri della
Radiazione Elettromagnetica
Notes: L’indagine dell’Universo affascina.
I metodi per studiarlo sono attraverso le particelle che riceviamo, la radiazione elettromagnetica, e sul posto.
Sul posto direi che è difficile se si eccettua lo studio dell’Eliosfera e dei pianeti.
Le particelle interferiscono col mezzo che attraversano, eccetto le particelle neutre (neutroni e neutrini)
Inoltre la Terra è per fortuna nostra ben protetta: magnetosfera, atmosfera..
Questa protezione vale anche per la radiazione, ma parte di questa riesce a penetrare l’atmosfera.
La radiazione ha tre caratteristiche: Intensità, spettro e polarizzazione.
Dualismo onda-fotone.
L’occhio umano è in grado di misurare due di queste tre grandezze: intensità e spettro solo nel visibile.
Chi produce la radiazione? Ci sono le vere e propire sorgenti di luce e quelle sorgenti che si dicono secondarie.

## Slide 6
L’assorbimento di radiazione da parte della
materia attraversata può essere impiegato per :
Creare impressioni su una pellicola fotografica, o generare segnali elettrici in appositi rilevatori
(radio-diagnostica)
Generare, a livelli energetici piu’ elevati ed a seguito dell’assorbimento, danni alle cellule malate dell’organismo umano per distruggerle
(radio-terapia)

## Slide 7
Raggi X e Raggi 
I raggi X (Roentgen 1896) sono prodotti nelle transizioni elettroniche negli atomi di elettroni di orbite interne, per es bombardando con elettroni un bersaglio di Tungsteno.
I raggi  (Rutherford 1914) sono prodotti nelle reazioni nucleari, per esempio nel decadimento naturale del Cobalto.
Spettro delle Onde Elettromagnetiche

## Slide 8
Rivelatori => Diagnostica (essenzialmente Imaging attraverso la ricostruzione computerizzata dei segnali)
Dalle lastre per Raggi X alla CT ed MRI -> Diagnostica Morfologica
SPECT e PET -> Diagnostica Metabolica e Funzionale
Acceleratori => (Ciclotroni, Sincrotroni e Lineari) Servono a produrre gli Isotopi per la Diagnostica Avanzata e vengono impiegati in Radio-Terapia
Terapia convenzionale ed evoluta a Raggi X (IMRT e IORT)
Terapia Avanzata con Adroni (Protoni o ioni Carbonio)
Le nuove frontiere degli acceleratori per Adroterapia
Brachiterapia e Teleterapia

## Slide 9
 |  | YEAR | ENERGY | PHYSICAL PROPERTY | IMAGING
RADIOLOGY | X RAYS IMAGING | 1895 | X RAYS | ABSORPTION | 
ECHOGRAPHY | ULTRASOUND IMAGING | 1950 | US | REFLECTION TRANSMISSION | 
NUCLEAR MEDICINE | RADIOISOTOPE IMAGING | 1950 | g RAYS | RADIATION EMISSION | 
TECHNIQUE
Tecniche di Medical Imaging /1

## Slide 10
TECHNIQUE |  | YEAR | ENERGY | PHYSICAL PROPERTY | IMAGING | 
X RAYS COMPUTERIZED TOMOGRAPHY | CT | 1971 | X RAYS | ABSORPTION |  | MORPHOLOGY
MAGNETIC RESONANCE IMAGING | MRI | 1980 | RADIO WAVES | MAGNETIC RESONANCE |  | MORPHOLOGY /FUNCTION
POSITRON EMISSION TOMOGRAPHY | PET | 1973 | g RAYS | RADIATION EMISSION |  | FUNCTION
Tecniche di Medical Imaging /2

## Slide 11
Henri Becquerel (1852-1908)
1896:
Discovery of natural
radioactivity
Marie Curie Pierre Curie
(1867 – 1934) (1859 – 1906)
1898
Discovery of polonium and radium
Thesis of Mme. Curie – 1904
α, β, γ in magnetic field
Hundred years ago
The beginnings of modern physics and of medical physics

## Slide 12
1897
discovery of X rays
Wilhelm Conrad Röntgen
1897
“discovery” of the electron
J.J. Thompson
The beginnings of modern physics and of medical physics

## Slide 13
A conventional X-ray image is basically a shadow: you shine a “light” on one side of the body, and a piece of film on the other side registers the silhouette of the bones (to be more precise, organs and tissues of different densities show up differently on the radiographic film).
Shadows give an incomplete picture of an object's shape.
Look at the wall, not at the person. If there's a lamp in front of the person, you see the silhouette holding the banana, but not the pineapple as the shadow of the torso blocks the pineapple. If the lamp is to the left, you see the outline of the pineapple, but not the banana.
X-ray image

## Slide 14
C - RECONSTRUCTION
A – LINEAR SAMPLING
X RAYS
TUBE
DETECTOR
COUNTS
B – ANGULAR SAMPLING
X RAYS
COMPUTERIZED TOMOGRAPHY
X-ray computerized tomography (CT)
This is the basic idea of computer aided tomography. In a CAT scan machine, the X-ray beam moves all around the patient, scanning from hundreds of different angles. The computer takes all this information and puts together a 3-D image of the body.

## Slide 15
< 0,4 sec/rotation
Organ in a sec (17 cm/sec)
Whole body < 10 sec
Volumetric CT

## Slide 16
1938-1945
Felix Bloch and Edward Purcell
discover and study
NMR
In 1954 Felix Bloch became
the first CERN Director General
Nuclear Magnetic Resonance
Alineamneto del polo magnetico attreverso un campo esterno imposto ed eccitazione degli atomi alla frequenza di Larmor

## Slide 17: MRI = Magnetic Resonance Imaging
Main magnet (0.5-1 T)
Radio transmitter coil
Radio receiver coil
Gradient coils
Measurement of the density of the protons (water) in tissues thought EXCITATION and RELAXATION
Information on the morphology

## Slide 18
MRI of upper torso (courtesy NASA)
MRI of knee
MRI of shoulder
Magnetic Resonance Imaging (MRI): morphology

## Slide 19: 1973: Positron Emission Tomography (PET) to investigate metabolism
ISOTOPES Half-Life
11-C 20.4 min, “natural”
13-N 10.0 min “natural”
15-O 2.0 min “natural”
18-F 109.8 min “pseudo-natural”
FDG with 18F is the most used drug
Measurement of the density of 18F through back-to-back gamma detection
Information on metabolism

## Slide 20
COVERAGE:
~ 15-20 cm
SPATIAL RESOLUTION:
~ 5 mm
SCAN TIME to cover an entire organ:
~ 5 min
CONTRAST RESOLUTION:
depends on the radiotracer
511keV
511keV
Positron Emission Tomography (PET)

## Slide 21
Positron Emission Tomography (PET)
Cyclotron
Radiochemistry
ISOTOPES Half-Life
11-C 20.4 min, “natural”
13-N 10.0 min “natural”
15-O 2.0 min “natural”
18-F 109.8 min “pseudo-natural”

## Slide 22: PET : one example
18FDG/PET images
The cocaine addict has depressed metabolism

## Slide 23
[11C] FE-CIT
Normal Subject
Parkinson’s disease
PET functional receptor imaging
Courtesy HSR MILANO

## Slide 24
PET
CT
PET/CT scanner
Morfologia + Metabolismo

## Slide 25: PET
Positron emission tomography (PET) is a nuclear medicine imaging technique which produces a three dimensional image or map of functional processes in the body. The system detects pairs of gamma rays emitted indirectly by a positon-emitting radionuclide (tracer) which has been introduced in the body on a biologically active molecule

## Slide 26
CT
PET
PET
CT
CT/PET scanner

## Slide 27
HSR MILANO
18F-FDG PET/CT

## Slide 28: Gli Acceleratori e la Radioterapia
Gli acceleratori di particelle vengono impiegati :
Per produrre gli isotopi necessari alle SPECT e PET
Per accelerare le particelle necessarie alla radio-terapia (elettroni o adroni)

## Slide 29
> 17500
TOTAL
>7000
Ion implanters, surface modification
~1500
Industrial processing and research
~1000
Research acc. included biomedical research
>100
~200
> 7500
Synchrotron radiation sources
Medical radioisotope production
Radiotherapy accelerators
~120
High Energy acc. (E >1GeV)
NUMBER IN USE (*)
CATEGORY OF ACCELERATORS
(*) W. Maciszewski and W. Scharf: Int. J. of Radiation Oncology, 2004
9000
Acceleratori attualmente installati nel mondo

## Slide 30: Principali tipi di acceleratori di Particelle
CIRCOLARI
Ciclotroni
Sincrotroni
LINEARI
Acceleraori lineari di vari tipi

## Slide 31
Use of accelerators in medicine
Low-energy cyclotrons for production of radionuclides for medical diagnostics
Medium-energy cyclotrons and synchrotrons for hadron therapy with protons (250 MeV) or light ion beams (400 MeV/u 12C-ions)
Electron linacs for conventional radiation therapy, including advanced modalities:
Cyberknife
IntraOperative RT (IORT)
Intensity Modulated RT

## Slide 32
1930
Ernest Lawrence invents the cyclotron
M. S. Livingston and E. Lawrence
with the 25 inch cyclotron
Tools for (medical) physics: the cyclotron

## Slide 33: CYCLOTRON
A cyclotron has a constant magnetic field and a constant radio-frequency (electric field) to accelerate particles

## Slide 34: CYCLOTRON
The cyclotron is a very robust and reliable machine even if it can be considered primordial in the world of particle accelerators for High Energy Physics

## Slide 35: Sono normalmente basati su un Cyclotrone ad alta corrente – 200/500 uA e da 18 o 30 o 70 MeV di Energia piu’ un complesso di radiofarmacia capace di produrre lemolecole piu’ adatte a portare e far decadere l’isotopo nella zona bersaglio
Centri di Produzione Isotopi e radiofarmacia

## Slide 36: LINEAR ACCELERATOR

## Slide 37
1939
Invention of the klystron
Sigmur Varian
Russell Varian
William W. Hansen
1947
first linac for electrons
4.5 MeV and 3 GHz
Tools for medical physics: the electron linac

## Slide 38: CONVENTIONAL RADIO THERAPHY WITH X-RAYS

## Slide 39
e- + target  X
Electron Linac
3 GHz
6-20 MeV
[
target
X-rays in radiation therapy: medical electron linacs

## Slide 40: The icon of radiation therapy with charged hadrons
40

## Slide 41
An example of intensity modulated treatment planning with photons. Through the addition of 9 fields it is possible to construct a highly conformal dose distribution with good dose sparing in the region of the brain stem (courtesy of T. Lomax, PSI).
E. Pedroni, Europhysics News (2000) Vol. 31 No. 6
Intensity Modulated Radiation Therapy

## Slide 42
SI PUO’ FAR MEGLIO?

## Slide 43
“hadrons” are
made of quarks
carbon ion =
6 protons + 6 neutrons
atom
Proton or
neutron
quark “u” or “d”
electron “e”
Hadrontherapy: n, p and C-ion beams

## Slide 44: The Bragg Peak and HADRON THERAPHY
Tumours close to critical organs
Tumours in children
Radio-resistant tumours
Physical dose high near surface
DNA damage easily repaired
Biological effect lower
Need presence of oxygen
Effect not localised
Dose highest at Bragg Peak
DNA damage not repaired
Biological effect high
Do not need oxygen
Effect is localised
Photons and Electrons vs. Hadrons

## Slide 45: Single beam comparison
X rays
Protons or Carbon ions

## Slide 46: Effect of ΔE/Δx = LET on many cells for many ‘end-points’
LET > 20 keV/μm = 200 MeV/cm =
40 eV/(2 nm)
Production of many localized double strand breaks
‘Radio Biological Effectiveness’
Mauro Belli et al
ISS
4800 MeV
stop
RBE
200 MeV
stop
p
C
LET (keV/μm)
1 MeV/cm

## Slide 47: Protons are quantitatively different from X-rays
9 X-ray fields 4 proton fields
PSI

## Slide 48: Charged hadrons have a much better energy deposition with respect to X-rays
200 MeV
protons
4800 MeV
carbon ions
which control
radioresistant
tumours
charged hadron beam
that loses energy in matter
27 cm
tumour
target
Photons
Protons
X rays
protons or
carbon ions
tail
cobalt
linac
httt://global.mitsubishielectric.com/bu/particlebeam/index_b.html
Hadrontherapy

## Slide 49
Proton radiation therapy

## Slide 50
COURTESY OF IBA - Louvain

## Slide 51
COURTESY OF IBA - Louvain

## Slide 52
Loma Linda University Medical Center (LLUMC)

## Slide 53: Numbers of potential patients
X-ray therapy (  40 linacs)
every 10 million inhabitants: 20'000 pts/year
Protontherapy
12% of X-ray patients 2'400 pts/year
Therapy with Carbon ions for radio-resistant tumour
3% of X-ray patients 600 pts/year
TOTAL every 10 M about 3'000 pts/year (*)
(*) In Italy : 17'000 patients
5 proton centres and 1 carbon centre (AIRO-2004)

## Slide 54: Present and “near” future of Hadrontherapy
Proton-therapy is “booming”! (for more information see PTCOG, www.ptcog.com)
  Laboratory based centres: Orsay, PSI, INFN-Catania, …
  Hospital based centres: 3 in USA, 4 in Japan and many under construction (USA, Japan, Germany, China, Korea, Italy, …)
  Companies offer “turn-key” centres (cost: 80-90 M Euro)
Carbon ion therapy
  2 hospital based centres in Japan
  Pilot project at GSI
  2 hospital based centres under construction in Germany and Italy
  2 projects approved (France and Austria)
  European network ENLIGHT

## Slide 55: Protontherapy is booming
PT center under operation


## Slide 56: CNAO = Centro Nazionale di Adroterapia at Pavia
56
President: Erminio Borloni
Medical Director: Roberto Orecchia
Technical Director: Sandro Rossi
High-tech building
Hospital building

## Slide 57: CNAO = Centro Nazionale di Adroterapia at Pavia
Synchrotron building
Hospital bulding
May 2009

## Slide 58
CNAO : THE SYNCHROTRON

## Slide 59: CNAO at Pavia
Perspective view of CNAO

## Slide 60: The accelerators used today in Protontherapy
200-250 MeV protons
MGH - IBA
Shizuoka - MITSUBISHI
CYCLOTRONS (Normal or SC)
4-5 metres
SYNCHROTRONS
6-9 metres
BEAM ON
BEAM ON
OFF
1.5 s
BEAM ON
Energy
1 s
15 ns
time
time
Current
CYCLOTRONS
Almost continuous beam
Fixed energy
SYNCHROTRONS
Beam ON and OFF
Continuous energy

## Slide 61: General concept of a cyclinac
61
The energy can be varied in 1-2 ms by changing the power pulses sent to the 20 accelerating modules

## Slide 62: Properties of the accelerated beams
1 second
Yes
No
Synchrotron
-
No
Yes
Cyclotron
Time needed for
varying the energy
Energy variation
by electronic
Means?
Beam always
present during
Treatments?
Accelerator
1 millisecond
Yes
Yes
Cyclinac
The energy is changed by adjusting
the RF pulses to the modules
30-50 ms (*)
(*) With movable absorbers

## Slide 63: The properties of the cyclinac beams are specially adapted to the spot-scanning technique
Energy and 3D-position can be varied every pulse, at variance with
Cyclotrons (fixed energy)
and synchrotrons (energy variation takes 1 s)

## Slide 64: Cyclinac use of the GSI approach to treat moving organs
CYCLINAC: energy variation by electronics and not mechanics
p+1 or C+6

## Slide 65: Brachitherapia, Radioimmunotherapia, Tele-therapia
65
Targeted radio immunotherapy: The radiation is brought by a radioisotope attached to a specifically selective vector
α particles from Bismuth-213 for leukaemia
β particles from Yttrium-90 for glioblastoma

## Slide 66
CONCLUSIONE
I rivelatori e gli acceleratori di particelle che vengono ideati e sviluppati per la fisica delle alte energie vengono impiegati e contribuiscono grandemente allo sviluppo della fisica medica e della clinica medica sia in campo diagnostico sia in campo terapeutico.
Ulteriori applicazioni esistono in campo industriale, per esempio per la sterilizzazione degli alimenti e dei presidi medicali, il cross-linking dei polimeri, la datazione dei reperti archeologici il decadimento accelerato di isotopi a lunga emivita (reflui radioattivi) etc. ma cio’ non fa parte del breve escursus qui presentato.
Nel campo della Adroterapia si stanno facendo molti sforzi, anche a livello industriale, per rendere quanto piu’ accessibile possibile questa terapia.
I futuri grandi progetti della Fisica Fondamentale (come CLIC e SLHC ) contribuiranno sicuramente a raggiungere questi obiettivi

## Slide 67
RINGRAZIAMENTI
Per la preparazione di questa presentazione sono particolarmente grato e debitore ad Ugo Amaldi, Marco Silari, e Giulio Magrin per il materiale da loro fornitomi ed i preziosi chiarimenti sui temi qui presentati .