## Slide 1
ITS3
FOCAL
ALICE 3
Future for Heavy Ions & ALICE 3

## Slide 2: ALICE Upgrade Roadmap
LHC LS3
ALICE 2
ALICE 2.1
ALICE 3
LHC LHC LHC LHC
Run 3 Run 4 LS4 Run 5
2022 2023 2024 2025 2026 2027 2028 2029 2030 2031 2032 2033 2034 2035 2036 2037 2038 2039 2040 2041
LHC
LS5
LHC
Run 6
ITS3
FOCAL
ALICE 3
Today
ALICE 2
Pb-Pb: 6.2 nb-1
O-O: 500 µb-1
Pb-Pb: 6.8 nb-1
p-Pb: 0.6 pb-1
Pb-Pb: ~ 35 nb-1

## Slide 3: ALICE Upgrade Roadmap

## Slide 4
FoCal-E: a compact silicon-tungsten sampling electromagnetic calorimeter with pad (1 x 1 cm2) and pixel (30 x 30 µm2)
  High spatial resolution for discriminating between isolated photons and decay photon pairs
FoCal-H: hadronic calorimeter constructed from copper capillary tubes filled with scintillating fibres
  Photon isolation, energy and jet measurements
Coverage: 3.2 <  < 5.6
5
Front view of a FoCal-H module in simulation
FOCAL TDR
3d view of FoCal, dimensions in mm
FOCAL TDR
Segmentation of FoCal-E
High Granularity (HG) cells
Low Granularity (LG) cells
FOCAL TDR
Longitudinal shower profile of two photons in FoCal-E
FOCAL TDR — CERN-LHCC-2024-004
The Forward Calorimeter (FoCal)

## Slide 5: FoCal — Test Beams
2 ALPIDE pixel layers
Monolithic Active Pixel Sensors
pixel size of ~30 x 30 μm2
two tested prototypes (HIC,pCT)
FoCal-H
9 Cu-scintillating fiber modules
towers size ~ 6.5 x 6.5 cm2
length ~110 cm
readout with CAEN DT5202
FoCal-E Pixels
FoCal-E Pads
FoCal-H
FoCal-E Pads
18 layers Si pad sensors
wafers of 9 x 8 cm2
pad size 1 cm2
readout with HGCROC v2
FoCal-E Pixels
FOCAL TDR
ALI-PERF-569144
7

## Slide 6: ALICE 3 — Concept
14
CERN-LHCC-2022-009
Compact, low-mass all-silicon tracker
Retractable vertex detector
Excellent vertex reconstruction
and PID capabilities
Large acceptance
Super-conducting magnet system
Continuous read-out and online processing

## Slide 7
(multiple scattering regime)
Radius and material of first layer crucial
Minimal radius given by required aperture:
R ≈ 5 mm at top energy,
R ≈ 15 mm at injection energy
→ retractable vertex detector
Key detector characteristics
3 detection layers (barrel + disks)
Retractable: r0 = 5 mm
Material budget: 0.1% X0 / layer
Unprecedented spatial resolution: 2.5 µm
Main R&D challenges
  Light-weight in-vacuum mechanics and cooling
  Radiation hardness* (1016 1 MeV neq/cm2 + 300 Mrad)
  Pixel pitch of 10 µm
R&D will build upon ITS3 experience
Pointing resolution ∝ r0 ⋅ x/X0
At injection energy — r0: 15 mm
102
101
1
10
T
102
p (GeV/c)
101
1
10
102
103
104
pointing resolution (m)

 = 0 R = 100 cm
min
Layout V1
ITS2 ITS3
ALICE 3 study
ALI−SIMUL−491785
ALICE 2
ALICE 2.1
ALICE 3
2x
5x
* LOI values, further simulation studies ongoing
15
ALICE 3 — Vertex Detector (VD)

## Slide 8
(multiple scattering regime)
Radius and material of first layer crucial
Minimal radius given by required aperture:
R ≈ 5 mm at top energy,
R ≈ 15 mm at injection energy
→ retractable vertex detector
Key detector characteristics
3 detection layers (barrel + disks)
Retractable: r0 = 5 mm
Material budget: 0.1% X0 / layer
Unprecedented spatial resolution: 2.5 µm
Main R&D challenges
  Light-weight in-vacuum mechanics and cooling
  Radiation hardness* (1016 1 MeV neq/cm2 + 300 Mrad)
  Pixel pitch of 10 µm
R&D will build upon ITS3 experience
Pointing resolution ∝ r0 ⋅ x/X0
102
101
1
10
T
102
p (GeV/c)
101
1
10
102
103
104
pointing resolution (m)

 = 0 R = 100 cm
min
Layout V1
ITS2 ITS3
ALICE 3 study
ALI−SIMUL−491785
ALICE 2
ALICE 2.1
ALICE 3
2x
5x
* LOI values, further simulation studies ongoing
15
ALICE 3 — Vertex Detector (VD)
At top energy — r0: 5 mm

## Slide 9: NorLHC III application
Covers period 1.7.2027 - 30.6.2032
FoCal
  Integration pixel layers - pad layers - HCAL Installation and commissioning (until 2030)
ALICE 3
  Contribution to R&D, construction, installation and commissioning of VD
    Chip-chip, chip-carrier vertical/horizontal integration
    Development of readout electronics, characterization of sensors and readout chain
20