## Slide 1: Updates on 704 MHz, 3 cells cavity design and breakdown studies at CEA
Juliette Plouin, Sophie Pierron, Guillaume Ferrand, Claude Marchand
MC RF sub-WG on RF systems for muon cooling meeting #6
1st April 2025

## Slide 2
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 3
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 4
Task 6.2
In parallel, a 3-cells cavity has been designed by CEA, based on electric coupling, in order to allow comparison with magnetic coupling structure. A main advantage is to avoid the presence of metallic sheet (beryllium or any other metal) between the cells.
adapted to the MuCol stage B5 requirement
adapted from pill-box structures
adapted from an ESS elliptical cavity
Building 3 cells cavity design with electrical coupling

## Slide 5
 |  | Pill-box | Elliptical
 | MHz | 704 | 704
 |  | 0.884 | 0.884
 | m | 0.188 | 0.188
 |  | 3 | 3
 | m | 0.565 | 0.565
 |  | 0.73 | 0.72
 | W | 286 | 337
 |  | 1.57 | 1.82
 |  | 36777 | 36277
 | MW | 10.5 | 12.3
 |  | Pill-box | Elliptical
 | MHz | 704 | 704
 |  | 0.884 | 0.884
 | m | 0.188 | 0.188
 |  | 3 | 3
 | m | 0.565 | 0.565
 |  | 0.73 | 0.72
 | W | 286 | 337
 |  | 1.57 | 1.82
 |  | 36777 | 36277
 | MW | 10.5 | 12.3
 |  | Pill-box | Elliptical
 | MV/m | 22.5 | 22.5
 | MV/m | 16.4 | 16.2
 | MV | 12.7 | 12.7
 | MV | 9.3 | 9.2
 | MW | 8.2 | 6.8
 | MV | 19.3 | 29.5
 |  | Pill-box | Elliptical
 | MV/m | 22.5 | 22.5
 | MV/m | 16.4 | 16.2
 | MV | 12.7 | 12.7
 | MV | 9.3 | 9.2
 | MW | 8.2 | 6.8
 | MV | 19.3 | 29.5
Figures of merit of pill box type and elliptical cavities
E field in cavity for the pi-mode
Peak field is crucial for breakdown issue
Cavity shape is also important: in a cavity with non-parallel walls, the surface density of emitted electrons arriving on a cavity wall could be decreased due to the walls angle. Elliptical cavities could then be a good choice for lowering the breakdown issues.
Copper walls

## Slide 6
0,94
0,49
1,58
1,91
Kilpatrick ratio
Moretti et al., 2005, 10.1103/PhysRevSTAB.8.072001
Bowring et al, 2020, 10.1103/PhysRevAccelBeams.23.072001
 |  | Pill-box | Elliptical
 | MV/m | 22.5 | 22.5
 | MV | 19.3 | 29.5
Kilpatrick ratio |  | 0.78 | 1.19
 |  | Pill-box | Elliptical
 | MV/m | 22.5 | 22.5
 | MV | 19.3 | 29.5
Kilpatrick ratio |  | 0.78 | 1.19
Kilpatrick ratios and experimental results
704 MHz
29.5
24.7
Kilpatrick ratio

## Slide 7
Kilpatrick ratio
4
2
4
2

## Slide 8
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 9
Distance between solenoids 0,64 m
Lcav=0,565 m
Solenoid radius = 0,35 m
DC magnetic field generated by solenoids
CST M static solver

## Slide 10
E0 [MV/m] | 30,0
Eacc [MV/m] | 21,6
V0 [MV] | 17
Vcav [MV ] | 12
Pdiss [MW] | 12
Epk [MV] | 39,31
Stored energy | 100
RF electromagnetic field for the pi-mode
CST eigensolver

## Slide 11
Electron emission from surface
Emission from 3 points in the iris region of the cavity (where the E field is max)
Model : DC emission
Emission point area ~ 1 mm2
Initial e- energy : some eV
Space charge can be neglected
CST PIC Solver

## Slide 12
With DC magnetic field (superimposed)
Result is the same from B = 1 T
The electrons follow exactly the DC field lines.
Here, most electrons hit the facing iris, and some electron fly up to the window…
Without DC magnetic field
Electron max energy is 10 MeV
Electron emission with DC magnetic field and RF field
CST PIC solver with importation of M static and eigenmode solvers.

## Slide 13
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 14
https://www2.kek.jp/accl/eng/topics/topics190122.html
< Figure 7 > […] A flying bright object appeared near the downstream end plate (right image), moving upstream, and impacted the upstream end plate (left image) at t = 0.081 s. Breakdown occurred at the moment of impact (t = 0.081 s) […]
Fireballs speed ~few m/s
From temperature meas (IR camera) they conclude that the flying object is not copper
« fireball » emission from emitter, Abe et al.

## Slide 15
“In this article, we give insights to the atomic scale
processes taking place in metal nanotips under intense field emission conditions. […]. We find that when a sufficiently high electric field is applied to the tip, the emission-generated heat partially melts it and the field-induced force elongates and sharpens it.”
Molecular dynamics simulations
Static E field
Heat transfer
Formation of Taylor cones
Atoms ejection from an emitter

## Slide 16
Magneto hydrodynamical simulations from an emitter in presence of RF field and DC magnetic field
Taylor cone existing cone model in Comsol : to be adapted to our physics.
Very preliminar…