## Slide 1: Liquid Argon Detector Technologies
Kostas Mavrokoridis
K.Mavrokoridis@liverpool.ac.uk
Nufact25, Liverpool, September 5th 2025

## Slide 2: Outline
Single Phase LAr Neutrino TPCs and R&D
Dual Phase LAr TPCs and R&D
Wire Technology
  (ICARUS T600, MicroBooNE, SBND, Proto/DUNE HD/VD)
Pixelated Charge
  (DUNE ND/LArPix/QPiX/SoLAr)
Perforated PCB anode
  (Vertical Drift)
S2 Optical readout
  (ARIADNE)
Neutrinos
Dark Matter
S1 and S2 Light Readout
  (Darkside-20k)
Knowledge exchange & S1 Light collection optimization efforts (ie APEX, PoWER)
Note: Material presented is the work of many people/collaborations, public links provided where possible

## Slide 3: Why Liquid Argon?
Dense: 40% denser than water
Easy ionization: 55 000 e-/cm for MIPs
High electron lifetime if purified  long drifts
High scintillation light yield: 40k γ/MeV
Pulse shape discrimination ability: (S1:fast 6ns/slow 1.6 μs)
Abundant: ~1% of the atmosphere (needs 39Ar depletion for DM)
Cheap: $2/L ($3000/L for Xe, $500/L for Ne)

## Slide 4: Major R&D challenges toward kton scale LAr TPCs
kton scale
LAr TPCs
Ultra-high purity
liquid argon in non
evacuated vessels
Scalable charge readout methods –high granularity tracking & good energy threshold
Very long e- drift length requires very high voltage
Systems 100kV -600 kV
Scalable light readout methods –high granularity tracking & good energy threshold
multichannel DAQ system & Cold electronics
Cryostats & cryogenics

## Slide 5: LAr Single Phase Wire Technologies
Ionisation readout
Light readout
3D image reconstruction by combining coordinates on different wire planes at the same drift time
No electron gain from the wires

## Slide 6: LAr Single Phase Experiments in the SBN Program
Program aims at solving the “sterile neutrino puzzle” by exploiting the well characterized FNAL Booster ν beamline
[1-4]

## Slide 7: ICARUS T600
1977 - the LArTPC Concept by C. Rubbia
[1-4,19]
Running
First physics result, Phys. Rev. Lett. 134, 151801 (2025)

## Slide 8: ICARUS T600
“warm” low-noise front-end amplifier
Compact layout: both analog+digital electronics hosted on a single flange
Icarus @Fermillab
ICARUS PMTs behind the wire planes (90 per TPC)
Provide t0 of any ionizing event in the TPC
[1-4]

## Slide 9: MicroBooNE
UV calibration LASER
[1-4]
(See slides also from Magnus Handley and
Afroditi Papadopoulou @Nufact 25)

## Slide 10: MicroBooNE
Deep Learning
Convolutional Neural Nets
(Leverage advances in computer vision and AI techniques to identify neutrino interactions or label pixels)
Calibration LASER
(multiphoton ionization)
[1-5]
MicroBooNE is the first experiment instrumented with cold CMOS ASICs
8256 wires/channels

## Slide 11: SBND
Improved Cold electronics similar to ProtoDUNE SP
(FPGA also in cold)
11,264 wires/channels
[1-5,20]
Running (first physics run completed)

## Slide 12: SBND –Photon Detection system
Wavelength-shifting reflector foils (TPB coated) mounted at the cathode to Improve the uniformity of collected light
Modular photon detection system mounted behind APAs
X-ARAPURCA R&D
PMTs
(A device for “trapping” photons to increase the active area of SiPM)
[1-5,20]

## Slide 13: DUNE
First module operational in end 2020s
[6-8,21]
(See also slides from
Pierre Granger @Nufact25)

## Slide 14
Membrane cryostat technology developed for LNG transport ships → re-engineered for LAr-TPC detectors
Used by protoDUNEs, DUNE, SBND and Darkside-20k
[6-8]
Membrane Cryostat Technology

## Slide 15: DUNE Far Detectors: two realizations: HD, VD
[6-8, 22]
HD
Anode Plane Assemblies :
Wire chamber technology
Drift length 350 cm -> ~ 180 KV
9800 m3 = 13.2 ktons active LAr
VD
Charge Readout Planes :
perforated PCB technology
Drift length ~ 640 cm -> ~ 300 KV
10180 m3 = 14.2 ktons active LAr
Photon detectors on the cathode at
300 KV

## Slide 16: DUNE APA Factories
Wiring head
[6-8,21,22]
Daresbury, UK
Chicago, USA
Aiming to produce 150 APAs in total

## Slide 17: Vertical Drift Single Phase LAr TPC with PCBs
[9, 22]
Evolution from ProtoDUNE DP

## Slide 18
[6-8, 22]

## Slide 19: ProtoDUNE SP/HD (Wires)
[6-8,21,22]

## Slide 20: Argon purification
NP04 run in 2024
NP04 run in 2024
[6-8, 22]

## Slide 21: ProtoDUNE VD
Cosmics sample event
[6-8,21,22]

## Slide 22: DUNE Photon Detection System: X-ARAPUCA
Photon trapping through:
✓ Total internal reflection in the WLS
✓ Trapping through dichroic filter
[6-8, 22]
(See also talk by Carmen Palomares @Nufact25)

## Slide 23: Optimising further S1 photon detection efficiency – APEX
R&D for phase II of DUNE
APEX: Aluminum profiles with embedded X-ARAPUCA
2ton prototype @CERN
[23]

## Slide 24: Optimising further S1 photon detection efficiency -PoWER
See slides from André Steklain @Nufact 25
PEN
Field Cage
LDUs
S1
ESR
VUV
Vis.
R&D for phase II of DUNE

## Slide 25: LArTPC single phase Pixel Technologies
Motivation: The anode is made of a grid of pixels, which can directly detect the ionization charge at a specific (X, Y) position without needing projections.
[10,11,25]

## Slide 26: LArPiX
Multi-channel charge processing ASICS: LArPix new generation, speed up, more channels, lower power.
[10,11,25]
Continuous readout, ~100% uptime
LArPix: Design Concept
Each pixel operates as an independent detector
- LAr data is inherently sparse
- Self-triggering and digitization for each pixel [O(100) keV threshold]
- Only digitize and readout pixels with signals
Pixelated anode based on LArPix V2 ASIC (LBNL) Pixel tile: 30x30 cm, 100 ASICs, 4900 pixels
P = 64 uW/ch, Total power 0.3 W/tile or 3W/m2
Pixel rate 0.4 Hz/pixel, Tile rate 2 kHz
Data rate - 32 kB/s per tile or ~1 MB/s/m3
ASICs
Tiles

## Slide 27: LArPix and DUNE ND-LAr
[10,11,25]

## Slide 28: LArPix and DUNE ND-LAr
FSD Anode Assembly
FSD Operation @ Univ. of Bern, 21 Oct – 15 Nov, 2024
[10,11,25]

## Slide 29: QPIX
D. Nygren's Qpix ASIC (time-to-charge approach)
Q-Pix summary:
Measures the time to integrate a pre-defined integrated charge (∆Q).
Average detector current is encoded in the reset rate
Self-triggered, per pixel
64-channel Q-Pix prototype (QPixLAr)
Charge integrate/replenishment circuit
replenishment time difference (RTD)
[25, 26]

## Slide 30: Multimodal pixel readout –SoLAr
A pixel plane which is sensitive to
(UV-VIS) photons (L) and ionizationcharge (Q) simultaneously
Multiple ways to achieve this concept
SoLAr: Integration of conventional light
detectors (e.g. VUV SiPM’s) into the pixel
plane
[25]

## Slide 31: Multimodal pixel readout –aSe photoconductor
Amorphous selenium (aSe)
Direct sensitivity to VUV light with low detection threshold
large area coverage & avalanche gain possible Demonstrated at both room and LAr temperature
(Elena Gramellini et al)
[25]

## Slide 32: Dual Phase LAr Detector Operation Principles
ProtoDUNE DP
ARIADNE
Darkside
Charge amplification and readout
Charge amplification and light readout with fast cameras
Electroluminescence light (no e- avalanche) readout with radiopure SiPM array

## Slide 33: ARIADNE (1ton): Optical LArTPC with TPX3Cam
Instead of reading out the charge from the THGEM, fast TPX3 Cameras photograph the S2 light generated in the THGEM holes
500µm
FR4 THGEM
New Manufacturing glass THGEM technique (patent pending) allows use of large scale radiopure glass opening application also to Dark Matter
New Glass THGEM
[13-15]
1-ton Detector at Liverpool

## Slide 34: ARIADNE: Optical LArTPC with TPX3Cam
Silicon pixel readout chip developed by the Medipix collaboration. Very well established technology at CERN.
Simultaneous 10 bit Time over Threshold (ToT) and 18 bit Time Of Arrival (TOA).
ToT allows accurate calorimetry measurements.
TOA accurate timing and 3D reconstruction.
“Data driven readout”: pixels read out asynchronously, allows very efficient sparse readout.
Possible to have continuous trigger-free readout.
Full 3D Readout
ASI
All pixels read out
No timing data within event
Only active pixels read out
Per pixel timing information
[13-15]
Sensor resolution | 256x256 pixels
Pixel size | 55µm x 55µm
Max readout rate | 40Mhits•cm-2 •sec-1
Time resolution | 1.6 ns

## Slide 35: ARIADNE: LAr Cosmics
1.75 sec streaming (ie equivalent to 3km e- drift)
~1mm/pixel
Raw 3D only ToT cut
Camera can cover 1mx1m at 4mm/pix
TPXCam sensitive to electroluminescence regime (no e- gain)
[13-15]

## Slide 36: ARIADNE+ 15 ton Demonstration @CERN
dE/dx
Sixteen 50cm x 50cm glass THGEMs
cosmic
2mx2m glass THGEM array

## Slide 37: DarkSide-20k
[16-18,27,28]

## Slide 38: DarkSide-20k 39Ar depletion & Large Area SiPM Readout
ARIA project (Darkside Collab.), production of depleted argon, below the UAr levels
ARIA -distillation column
Silicon is intrinsically radiopure
[16-18,27,28]

## Slide 39: DarkSide-20k inner detector
[16-18,27,28]
Outer detector PDUs similar with the inner. Production in UK close to completion.
PDU

## Slide 40: A very Exciting Era for LAr Detectors
MicroBooNe
ICARUS T600
SBND -112t
DUNE- ND LAr
DUNE FD 10kt
ProtoDUNEs 750t @CERN
DarkSide-20k
1-ton prototypes
ARIADNE
Thank You!

## Slide 41: Citations
https://indico.cern.ch/event/768000/contributions/3275101/attachments/1817037/2970272/NeutrinoTelescopes2019Varanini.pdf
https://agenda.infn.it/event/24250/contributions/127449/attachments/79423/103217/Fava_SBN_Neutel_2021.pdf
JINST 13 (2018) P12007
https://indico.cern.ch/event/835190/contributions/3576893/attachments/1941976/3220400/Toups_NNN_2019.pdf
https://indico.fnal.gov/event/14063/contributions/23475/attachments/15115/19246/SBNDUNE.20170515.pdf
https://indico.in2p3.fr/event/19194/contributions/73545/attachments/54180/70812/CERNNP_sbordoni.pdf
https://indico.cern.ch/event/881818/attachments/1972807/3299895/CERN-Colloquium-Jan-20-60MB.pdf
https://indico.cern.ch/event/857610/contributions/3651379/attachments/1957901/3253223/LBNC_Dec19_CTouramanis.pdf
https://edms.cern.ch/ui/#!master/navigator/document?P:100722921:100738064:subDocs
https://indico.cern.ch/event/999815/contributions/4221588/attachments/2223005/3764756/ChargeReadout_Kreslo.pdf
https://indico.fnal.gov/event/21535/contributions/63303/attachments/39668/48006/QpixConceptFEelect2.pdf
https://indico.in2p3.fr/event/19194/contributions/73346/attachments/54154/70767/ProtoDUNE-DP-duchesneau-250619.pdf
https://www.mdpi.com/2410-390X/4/4/35
https://arxiv.org/pdf/1810.09955.pdf
https://iopscience.iop.org/article/10.1088/1748-0221/15/03/P03003
https://indico.fnal.gov/event/19947/contributions/54727/attachments/34154/41785/DarrenPrice_DMUK_DarkSide20k.pdf
https://iopscience.iop.org/article/10.1088/1748-0221/15/03/C03038/pdf
https://indico.cern.ch/event/868940/contributions/3814880/attachments/2080507/3494419/DS_ICHEP2020.pdf
https://inspirehep.net/files/03e6542a060e9e668f35ac140d494387
https://indico-cdex.ep.tsinghua.edu.cn/event/175/contributions/2282/attachments/1116/1700/20250828_sbnd_status_twester.pdf
https://indico-cdex.ep.tsinghua.edu.cn/event/175/contributions/2525/attachments/1115/1699/DUNE_TAUP_2025_MANZANILLASv3.pdf
https://indico.cern.ch/event/1492360/attachments/3006084/5298729/CT-CERNcolloquium25.pdf
https://indico.cern.ch/event/1390649/contributions/6061504/attachments/2916604/5118565/DUNE_APEX_PHASEII_LIDINE2024_v0.pdf
https://indico.fnal.gov/event/67540/timetable/#20250312
https://indico.cern.ch/event/1485254/timetable/#20250211.detailed
Qpix: https://indico.phy.ornl.gov/event/510/contributions/2165/
https://indico.global/event/652/contributions/16971/attachments/57443/110377/CaminataUCLA.pdf
https://indico.global/event/652/contributions/16907/