## Slide 1: Simulation of photonic devices for optical links
Hemalatha Muthuganesan
EP-ESE-BE

## Slide 2: Outline
Introduction
Photonics in particle detectors
Photonic Integrated Circuits
Example of waveguide simulation in MODE
Ring modulators
Lumerical INTERCONNECT
Simulation results
Summary and future work

## Slide 3: Why photonics for optical links?
Particle sensor
PIC
>> 100 m Single-mode fibre
Photodiode
Modulator
Fiber coupler
ASIC
OPTO
FPGA
Silicon Photonic Integrated Circuits (PICs)
  Mass production from CMOS foundries
  Low mass
  Low power consumption
  High bandwidth
  High radiation tolerance
Back-end (Radiation-free zone)
  External Laser Source
  Commercial transceivers
Single Mode fibers connecting BE and FE
Front-end (High-radiation)
  Transmitter based on ring modulators and filters
  Receiver based on photodetectors
System concept under development in the
EP R&D WP6 project
High Energy Physics experiments, require transmission of large volumes of data from particle detectors in radiation environments to radiation-free zones.

## Slide 4: Photonic Integrated Circuit (PIC)
Grating couplers
Edge
couplers
Waveguide
Ring modulators
Wavelength
filters
Photodetector
SOI wafer
Fiber
Fiber

## Slide 5: How to design a PIC?
To design a PIC, foundry provides Process Design Kit (PDK) with building block of optical components.
Some components are used from PDK.
Some components are custom made using optical simulations.
Foundry
Reference elements
PIC Idea
PIC
Simulations
Custom elements

## Slide 6: Optical Simulation software
Ansys Lumerical Suite is a software package to model photonic devices.
To customize photonic components tools from Lumerical are employed.
Lumerical INTERCONNECT
Circuit level solver
Waveguides
Ring modulators
Optical anlayzer
Optical source
Electrical source
Lumerical MODE
Device level solver
Lumerical FDTD
Device level solver

## Slide 7: Waveguides

## Slide 8: Waveguides
Waveguide carries light in a PIC from one element to another.
Dimensions vary with wavelength of choice.
Light is squeezed by choosing a high refractive index material.
Si ncore
nclad_bottom
nclad_top
3D schematic
Cross-sectional view
Refractive index of core > Refractive index of clad

## Slide 9: Waveguide simulations in MODE
SiO2 clad_bottom
Si waveguide
Air clad_top
Materials:
Built in data +
import data (refractive index, absorption coefficient)
Simulation region
Sources
Monitor
Structures

## Slide 10: Waveguide simulations in MODE
Si
SiO2
SiO2
SiO2 index =1.4
Si index =3.5
Refractive index of core > Refractive index of clad

## Slide 11: Waveguide simulations in MODE
Waveguide core is silicon with top and bottom clad as silicon dioxide.
1310 nm light is used as source in Lumerical MODE.
Full length waveguide properties are obtained by doing cross-section.
Mode 1: Higher mode confinement and less lossy.
Mode1
Mode 2
Mode 3
Mode 4
SiO2 index =1.4
Electric filed distribution in silicon waveguide
Only the first mode is propagated for long distance in waveguides
Si index =3.5

## Slide 12: Ring Modulators

## Slide 13: Si µ-ring modulator
Input
laser
V0
V1
Optical
Modulation
Amplitude
Electrical
data
Optical data
Input laser
Δλ(V)
p-n junction
V
Reverse biased pn Junction
+
-
Waveguide cross-section
Selective wavelength filters
Small footprint (radius ~ 5µm)
Optically narrowband (< 1nm)
Thermally sensitive (< 1 K)
CERN custom design
10 µm
Electrical contacts

## Slide 14: Simulation of ring modulator (RM)
Reference ring modulators are provided by the foundry.
Custom RM are designed to improve the performance according to our needs.
These custom RM are already measured in lab.
Aim is to develop accurate analytical models of the custom RM.
Why to do this?
To target better RM designs for next iterations.
To make PIC design compatible with driver requirements.
To simulate a full circuit of optical link.
Currently completed frequency domain models of custom RM.
To do: Time domain simulations based on these models, to evaluate bandwidth, rise time and fall time.

## Slide 15: Frequency domain simulations in INTERCONNECT
Results
Element properties
Elements library
Main workspace

## Slide 16: Frequency domain simulations in INTERCONNECT
Results
Element properties
Elements library
Main workspace

## Slide 17: Frequency domain simulations in INTERCONNECT
Interconnect is a circuit level optical solver.
Ring Modulator:
Basic parameters are used from reference design.
Rest of the properties are optimized.
Power supply:
Bias voltage to RM is provided using a DC source.
For each bias, corresponding inputs are provided.
Analyzer:
The output is measured using Optical Network Analyzer.
From the ONA output, functional parameters are calculated.
ONA Transmission spectrum

## Slide 18: Functional parameters
Free Spectral Range (FSR): Ring resonator supports multiple resonances and FSR is the spacing between them. To achieve larger FSR, rings has to be small.
Quality factor (Q-factor): Measure of sharpness of resonance relative to its central frequency.
A high Q factor means that the ring resonator can store energy for a longer time.
Extinction ratio (ER): The contrast between the optical power coupled into the resonator when it is in resonance (on state) and when it is off-resonance (off state).
Q factor =
FSR
FWHM

## Slide 19: Simulation results of reference RM
Simulated reference RM using values from PDK and compared with measured results.
Modulation Efficiency (ME) is the shift in resonant wavelength for varying bias voltage input.
Functional parameters are matched within permissible tolerances.
Simulation setup is validated by matching simulation and measurement results.
Functional parameters | C band |  | O band | 
 | Measured RM | Simulated RM | Measured RM | Simulated RM
FSR | 19.16 nm | 19.34 nm | 13.54 nm | 13.77 nm
Q factor | ~2600 | ~2500 | ~5000 | ~4700
ER | 22 dB | 30 dB | 20 dB | 21 dB
ME | ~ 40 pm/V | ~ 40 pm/V | ~ 30 pm/V | ~ 30 pm/V
Transmission plots from simulated RM PICv3
ME
Results comparison of reference design PICv3
Modulation Efficiency (ME)

## Slide 20: Custom models RM results
To build custom models, ring radius and gap between waveguide is varied for O band.
Simulated values of FWHM, Q factor are within tolerable range and align with measured results.
Device | Results | Full Width Half Maximum (pm) | Q value
Ref Ring | Measured | 262 | 5000
 | Simulated | 278 | 4700
Ring1 | Measured | 223 | 5820
 | Simulated | 220 | 5750
Ring2 | Measured | 197 | 6600
 | Simulated | 200 | 6581
Ring3 | Measured | 150 | 8600
 | Simulated | 150 | 8643
Ring4 | Measured | 193 | 6700
 | Simulated | 190 | 6712
Ring5 | Measured | 168 | 7750
 | Simulated | 160 | 7957
Ring6 | Measured | 156 | 8400
 | Simulated | 160 | 8401

## Slide 21: Custom models RM results
To build custom models, ring radius and gap between waveguide is varied for O band.
Simulated values of FWHM, Q factor are within tolerable range and align with measured results.
Device | Results | Full Width Half Maximum (pm) | Q value
Ref Ring | Measured | 262 | 5000
 | Simulated | 278 | 4700
Ring1 | Measured | 223 | 5820
 | Simulated | 220 | 5750
Ring2 | Measured | 197 | 6600
 | Simulated | 200 | 6581
Ring3 | Measured | 150 | 8600
 | Simulated | 150 | 8643
Ring4 | Measured | 193 | 6700
 | Simulated | 190 | 6712
Ring5 | Measured | 168 | 7750
 | Simulated | 160 | 7957
Ring6 | Measured | 156 | 8400
 | Simulated | 160 | 8401
~ 3 dB
1550 nm legacy PICv2
Amplitude

## Slide 22: Future work: Time domain simulations
Frequency domain simulations are completed for custom models of O band ring modulators.
Next step is to move on to time domain simulation from these simulated results.
An example is provided below for O band 1310 nm reference design.
Wavelength (nm)
Optical power (a.u.)
Time (ps)
Optical power (a.u.)
Frequency domain results
Time domain results

## Slide 23: Summary
Introduced photonic integrated circuits and optical simulations.
Demonstration of Lumerical MODE software was given with waveguide example.
Conducted frequency-domain simulations of O-band ring modulators.
Confirmed the simulation setup using reference ring modulators from PDK.
Built analytical model for six custom ring modulators.
Simulation results align with measurements within tolerance.
Future work:
Time domain simulations on simulated custom models.
Carry out simulation of wavelength filters.

## Slide 24: Backup slides

## Slide 25: SystemPIC ring modulator characterization results
~ 3 dB
28 nm CMOS driver provides limited modulation voltage swing Vmod
Need to increase modulator efficiency (ƞ) for margin in link power budget
1550 nm legacy PICv2
CW laser
p-n junction
r
Coupling gap
Multiple ring modulators sweeping the design parameter space
  Radius (r), p-n junction type, coupling gap
  Trade-off between efficiency and bandwidth