Presentation title is Arial Bold 50pt
up to three lines
Formal verification in SY-EPC(-CCE)
Electronics forum on Formal Verification in Gateware
Valerio Nappi and colleagues
3rd April 2025

---
We have prepared a short introduction for you on
how to use the
Controls of a power converter
In a power converter we can identify three layers on which a control can act:
- Safety: Protect people from hazards. This layer is not part of the control system. The power converter system is designed to ensure safety, typically with hardwired safe chains.
- Equipment protection: Protect equipment from damage. We must ensure that our system responds correctly and timely to avoid damage, both reacting to power converter faults, and to interlocks.
- Plant control: Ensure the correctness of the output and the performance of the power converter.
FGC4 takes care of part of the equipment protection duties, and of the totality of plant control.
Both are implemented across many layers: hardware, gateware, software.
FGC4

---
Protection functions of FGC4
For our new generation of power converter controllers, three levels of functional integrity were identified:
- Safety Related: functions implemented independently of the converter control system. FGC4 is not a safety instrumented system, so safety related functions are outside the scope of the FGC4 project.
- High Integrity: functions implemented in pure hardware, using discrete circuits and logic, without programmable elements.
- Standard Integrity: functions implemented in software, or gateware.
The standard integrity is the only domain where formal verification could be employed.
At the moment there is no plan to formally verifying these components. Depending on the cost of formal, we may choose to verify some (or all), but it is not critical to this project.
The FGC4 cassette

---
The Protection & Firing Module (PFM) for POPS+
- During LS3 SY-EPC will upgrade the power converter for the PS main magnets (POPS - POwer for PS) → POPS+ will be based on FGC4.
- Due to the very high energies in play, the hazard of equipment damage is big.
- The protection functions will be moved outside the FGC4 controller, in a separate, more stable and verified device, the Protection & Firing Module (PFM).
The PFM:
- Will ensure that the FGC4 does not request illegal combinations of switches, that can lead, for example, to a shoot-through (equipment protection).
- Will ensure that the FGC4 respects the design’s deadtimes (equipment protection).
- Trip the converter if any of the IGBTs fail (equipment protection).
The PFM, being a piece of protection equipment, will benefit from formal verification of it’s logic. Once proven, the protection gateware will be stable and fixed.
The PFM circuit boards

---
Formal Verification in SY-EPC(-CCE)
- At the present time, we do not have the know-how to implement formal verification on our IPs, with specific focus on the PFM project.
- Since it will be a fundamental step for our projects, we organized a course with Yann Thoma over three days, which will cover VHDL verification with PSL constructs.
- We have a strong preference for open source and free tools, so the course will focus on the OSS CAD suite.
- If the course goes well, we will submit a recommendation to make it part of the training portfolio at CERN.
- The final plan is to integrate formal in CI/CD.