## Slide 1
H3D-VISIOnAIR
Head-worn 3D-Visualation of the Invisible for Surgical Intra-Operative Augmented Reality
Jaap Heukelom
I-Med Technology
Quest Medical Imaging (Olympus)
Maastricht University Medical Centre
Amsterdam University Medical Centre
University of Twente
ATTRACT Phase 2 Final Review CERN, May 20-21, 2025

## Slide 2
Contactless 2D spectral dataset of human nerve and adipose tissues
  Ongoing data acquisition in OR for duration of the project
Off-line classification of nerve and adipose tissue
  Identification of wavelength bands that represent nerve and adipose tissue, using annotated spectral datasets and machine learning
Integrated hardware
  Integration of i-Med and Quest components to create 3D headset with 5-channel prism allowing real-time overlay of spectral information
Embedded software
  Software for real-time displaying target tissue recognition, within maximum delay of 30 ms, at 60times per second/per pixel (3D).
Demonstrator TRL 6
  Real-time synchronized high resolution spectral+RGB image augmented reality overlays in a head worn 3D display. Ready for investment in industrialization.
Clinical feasibility
Reminder of the initial project objectives

## Slide 3
Contactless 2D spectral dataset of human nerve and adipose tissues:
Many pilot tests (10+) to optimize lightning, lens focus and minimization of artefacts
55 Contactless 2D spectral datasets of human nerve and adipose tissues recorded in-vivo (human)
Off-line classification of nerve and adipose tissue:
Tissue tags are placed on camera during procedure
Surgeons provide expert annotation after procedure
Tissue spectra are extracted from images
Final Results achieved (1)
1st test: porcine recordings, light tests
Tissue Carpal Tunnel Syndrom

## Slide 4
Final Results achieved (2)
Optimal filter combination for the detection of the nerve and adipose tissue (5 bands)
Offline classification model
Demonstrator TRL 6 Hardware integration for head worn display
LED Array, HAREVA NIR LED synthesizer, Aalto University

## Slide 5
Final Results achieved (3)
 | Objective | Deliverable(s)
1 | Contactless 2D spectral dataset of human nerve and adipose tissues | Dataset 62 images 55 sufficient quality and annotated by expert
2 | Off-line classification of nerve and adipose tissue | Selection 5 filters:
3 | Integrated hardware | CAD design, 3D printed
4 | (Embedded) software | Intensive flow model
5 | Demonstrator TRL 6 | Assembled and tested, new designed prisms
6 | Clinical feasibility | Clinal test with patients No METC allowance in time

## Slide 6
Final tests undertaken (1)
System testing with the Team

## Slide 7
Final tests undertaken (2)
Computer simulation done on the 55 datasets applying the 5 selected bands, and the classification model
Confusion Matrix for rating: True Positives (TP), False Positives (FP), False Negatives (FN), True Negatives (TN)
F1 score: 0.494 = harmonic mean of precision and recall Okay for a TRL Demonstrator

## Slide 8
Commercialization actions taken during ATTRACT
Meetings with Medical OEMs
  Olympus, Bbraun, Zeiss, Lumileds
Conference presentations
  Presentation H3DVisionair at NVEC conference April 11th 2023, Amsterdam, NL (150 participants)
  EAES Conference, Maastricht, June 12th 2024
  invited speaker @ European Association Endoscopic Surgery June 20-23 2023 Rome
  Invited speaker @ European summit on Laser Optics and Photonics Technology, Sept. Barcelona
Article
  Article Life:2023; 13(2):357 “Near-Infrared Spectral Similarity between Ex Vivo Porcine and In Vivo Human Tissue”

## Slide 9
Commercialization actions foreseen after ATTRACT
Meetings with Medical OEMs
  Ongoing contact with Olympus
  New contacts: Carl Storz, 3Shape Dental
Grant funding ITEA, HSI VISIONAIR From TRL 6 to TRL 9
  Approved EU-ITEA 4 Approval Dutch Ministry Economic Affairs: pending 2026 => 2028 NL Consortium: Amsterdam UMC, Leiden UMC, Maastricht UMC, Semlab Quest imaging (Olympus), i-Med Technology

## Slide 10
Thanks and Questions
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 101004462