## Slide 1
h-cube
Micromechanical Bolometers arrays for Terahertz hyperspectral imaging
Alessandro Pitanti
University of Pisa
CNR-NANO
ATTRACT Phase 2 Final Review
CERN, May 20-21, 2025

## Slide 2
Initial project objective: Realization of a false-color THz camera
[Vicarelli, Tredicucci, Pitanti ACS Phot. 2022]
Trampoline membrane
resonator
Optical interferometry
h-cube
Optical read-out  Electrical read-out (via magnetomotive effects)
Single pixel  Matrix array (for scanless imaging)
Hyperspectral/multispectral functionalities (False-color RGB images in the far-infrared range: novel functionality!)
No performance degradation (NEP<10 pW/Hz-1/2, video rate - comparable with some of the state of the art commercial devices)
Novel THz camera

## Slide 3
Final results achieved (1)
Electrical contacts
permanent Nd magnets
300 mm
0.8 cm
1.1 cm
v1
v2
v3
All-electrical prototypes
Custom FPGA electronic board
multitonal control [Elettra]
Final prototype v3:
7x7x1.5 cm sensor
256 pixels
static vacuum operation
Phase-locked loop control (multitonal x 8)
Fast pixel response (<100 ms)
Improved Sensitivity PLL + nonlinearities + absorbers  passive THz radiation

## Slide 4
Final results achieved (2)
Multitonal Phase-locked loop
x8

## Slide 5
Bx2
Final results achieved (3)
Hyperspectral chip
200 mm
Linearly combining the RGB channels

## Slide 6
Final tests undertaken (1) - 100 GHz, scanning
II. Peanut
peanut kernel
I. Envelope inspection
III. Art sketches
pencil
ATTRACT CBI
student project


## Slide 7
Final tests undertaken (2) - 100 GHz, scanless
Coffee bean
Coffee bean + metal (Sn)
Sn contaminant
Ball-lens effect
16x16 scanless imaging
acqusition time from ~hours (single pixel) to ~minutes (with sweep) to ~seconds (with PLL)
laser ON
laser OFF

## Slide 8
Commercialization actions taken during ATTRACT
Crash course in emerging technology entrepreneurship: mix of lectures and hands-on work (8 application verticals assessed by 4 teams of researchers: Security, Food and Pharma Inspection, Infrastructure and Crops, Semiconductors and Coatings)
Interaction ATTRACT-CBI students: evaluated new application ideas (e.g., art inspection)
Initial Business plan (D7.1): application opportunities, revenues potential, early customers identification, competitive advantage, value chain map – priority applications: Security, Food and Art inspection
IP prior art assessment: 56 patents shortlisted and analysed to inform IP and business strategy – identified 2 recent patents likely to constitute prior art
Business Devt. Tools: created video, leaflet and specs sheet to engage industry
Industry outreach: engaged key EU THz players (Teraview, Crisel Instruments, Thruvision); organised academia-industry Thematic Workshop on THz Detectors Research & Applied Frontiers (Venice, Feb 15-16 2024)
Finalised commercialisation strategy (D7.2): a) THz camera know-how transfer (as opposed to patent license) to identified THz system integrators (Thruvision, Teravil); b) marketing of drive & read-out electronics for wider application (Elettra ILO); c) further, application- specific R&D and IP creation (e.g., medical diagnostics)

## Slide 9
Commercialization actions foreseen after ATTRACT
Teravil Ltd (LT) – THz camera:
  Adoption driver: new product opportunity
  “Integrating H-Cube technology enables Teravil to deliver new and impactful capabilities to customers. This provides our company with a fresh competitive edge in the global market for commercial and R&D applications of THz cameras” – Andzej Urbanovic, CEO, Teravil UAB
  Actions: 1) know-how transfer to reproduce hardware (bolometric arrays – FBK, UEF and UniPi; drive and read-out electronics – Elettra); 2) joint applications development and optimisation (diagnostics) – via grant or consultancy
Thruvision Group PLC (UK) - THz camera
  Adoption driver: performance enhancement in existing product
  “We are very interested in the potential that HCUBE’s THz camera technology could have to enhance security applications, particularly in passive detection mode. We have established a relationship with members of the H-Cube consortium to allow follow-up exchanges and further explore the applicability of the technology to Thruvision’s people screening products” - Nick Graham-Rack, CTO, Thruvision
  Actions: 1) ad hoc demo (UniPi, Elettra); 2) define next-gen product specs (Thruvision); 3) development of target performance (Elettra, FBK, UEF and UniPi) – via consultancy
ILO (Elettra’s Industry Liaison Office, IT) - Drive & Read-out electronics
  Driver to act as sale channel: compelling tech and fit with industrial customer pipeline
  “The high-performance drive and multiplexing read-out electronics developed by H-Cube fit well with Elettra ILO’s expertise and track record in selling advanced solutions for QC, process improvement, product development and R&D to commercial and research organisations worldwide. In all these applications the appeal, customisation potential and added value of the H-Cube technology is compelling.” – Marco Perloi, Head of Elettra ILO
  Actions: 1) briefing of ILO; 2) creation of specs sheet & promotional material; 3) marketing (ILO); 4) technical support to sales; 5) customisation and/or product delivery (all actions but 3) by Elettra H-CUBE team)– via consultancy

## Slide 10
Thank and Questions
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 101004462

## Slide 11
Backup slides

## Slide 13
Food inspection
Sunflower seed
SEED
SHELL
KERNEL

## Slide 14
Crash course on Emerging Tech. Entrepreneurship
1. Market opportunity
    APPLICATIONS, CUSTOMERS, USERS, HOW BIG IS THE MARKET OPPORTUNITY
2. Market-Product fit
    HOW DOES IT FIT THE APPLICATION REQUIREMENTS
3. Competitive advantage
    IS IT BETTER, UNIQUE, IP PROTECTED
4. Business Model
    HOW WILL IT MAKE MONEY
5. Execution / Plan
    HOW TO GET TO MARKET, IN STEPS
6. People
    TEAM and SKILL SET REQUIRED
Focused on 3 of
the 6 pillars of emerging technology commercialisation.

## Slide 15
Combined bus. dev. work with consortium training
WHAT - Summary of activities
“From Lab to Market”
  MBA-style, introduction to emerging technology ventures and commercialisation
  workshop open to all consortium members
Market research with trainees
Further Bus Dev interviews
Market opportunity prioritisation
IP due diligence
HOW – Format of work
Identified 7 volunteers to work alongside C. Marinelli - split in four, 2-people application teams
Market research conducted independently by teams – periodic reviews with C. Marinelli
Clear tasks and calendar of meetings – instructions and support provided
  first discussion of collated results
  second discussion of collated results
  third discussion incl. technical feasibility aspect with A. Pitanti
  presentation to all partners
  final merging and wrap-up
Security
Infrastructure; Soil and Crops
Pharma; Food
Coatings; Semiconductors

## Slide 16
Market Due Diligence – key, initial takeaways
Confirmed applicability of H-Cube’s hyperspectral THz cameras across all identified areas
Established THz camera market: H-CUBE doesn’t face the challenge of having to create a new market, companies such as Teraview and Thruvision have paved the way
Hyperspectral (RGB-like) operation is a key differentiating feature: gives us second mover’s advantage - opportunity to roll out 2nd generation, with increased selectivity and contrast for target materials/chemicals
First prioritisation of market opportunities – next slide

## Slide 17
Prioritised market application opportunities
Pharma (drug manufacturing): active compound dissolution, tablet coatings thickness, blister packaging integrity
Food packaging: ripeness, ingredients, foreign object, sealed packaging integrity
Top
Priority
Coatings: polymeric, multi-layer coatings, opaque
Semiconductor packaging: defects, delamination areas, epoxy variations
Remote infrastructure: dams, bridges, buildings, motorways and railways
Soil and crops: irrigation, pesticides, harmful substances; foliage, flowers and fruits evolution
Security: bomb, chemicals, concealed threat at borders, airports, ports, couriers depot
Lower
Priority
Large number and diversity of customers and applications.
Strong economic drivers for adoption
Straight B2B sales – equipment or service
Some low hanging fruits for easier market entry – e.g. , pet food quality control
Application benefits not too compelling
Technical challenges (e.g., multilayer coatings)
Limited number of customers
Limited number of customers
Technical challenges (far field detection)
Strong competition from satellite imaging
Complexity of field deployment
Limited number of customers
Regulation/legislation driven adoption

## Slide 18
H-Cube camera vis-à-vis competing technologies
 | CMOS | GaAs Heterostructure | Micro Bolometer | Pyroelectric | H-Cube Hyperspectral Bolometric
Number of pixels | 32 x32 | 64 x 64 | 320 x 240 | 320 x 320 | 16 x 16 (30x30)
Pixel Size (um) | 80 | 1500 | 50 | 75 | 300
Operating Range (THz) | 0.3 – 1.3 | 0.05 – 0.7 | 0.6 – 4.0 | 0.1 and higher | 0.1 – visible
NEP (nw*Hz1/2) | 0.4 | 1 | 0.03 | 13 | 0.01-0.1
Hyper-spectral | NO | NO | NO | NO | YES
Responsivity (kV/W) | 140 | 50 | 18 (at peak) | N/A | 187 kHz/W
Frame rate (fps) | 30 | 24 | 25 | 50 | 20

## Slide 19
We conducted an extensive Freedom to Operate analysis. Using selected academic and industrial patent assignees as research key, we identified and assessed 57 patents
Two patents identified which are likely to constitute prior art
  M.L. Roukes, Caltech published on 22nd Jul 2022 . It covers a key aspect of H-CUBE: multiplexing and sensor reading along a single electrical line by exploiting differences in sensor’s resonance frequencies .
  S. Schmid, Danmarks Tekniske Universitet, published on 23rd March 2023: novel miniaturized calorimeter that uses a chain of microscopic hollow structures to detect extremely small amounts of heat with high sensitivity and fast response times. Covers aspects of our “trampoline membranes” design
  Neither patent was visible before the start of H-CUBE (due to 18-month delay between patent filing and publication)
Negates patent filing/protection for HCUBE
IP due diligence – prior art assessment

## Slide 20
Value chain for the THz imaging/scanning industry
THz camera
THz emitter
emitter
emitter
UI
Image Processing SW
Certifications
Customer support
Mechanics
Component Supplier
System Integrator and Solution Provider
Customer / End user

## Slide 21
Revised commercialisation strategy: know-how transfer to THz camera system integrators (plus separate sale of electronics)
Prioritised applications based on demonstrated H-CUBE capabilities, or channels to market created through Bus Dev work:
Food inspection
Art inspection
Security
Further application development opportunity identified:
Diagnostics
Taking stock of :
Prior art and inability to file IP and therefore to commercialise H-CUBE technology through IP licensing
Challenging conditions to launch an H-CUBE spin-off venture (due to lack of lead entrepreneur, lack of IP protection, tough VC investment environment since Q2 2022, )
Companies, contacts and opportunities identified through Bus Dev work
We have devised the following commercialisation strategy:
H-CUBE RGB THz camera to be comercialised through a know-how transfer (i.e., soft IP transfer rather then IP licence) to establish THz camera system integrators, who will in turn serve customer in identified and new THz imaging/scanning applications
HCUBE advanced Drive & Read-out electronics to be separately marketed to industrial customers for wider applications
Further technology and IP development possible in THz cancer skin screening application, but requires additional R&D, potentially starting at lower TRL
Revised application focus
Revised
commercialisation strategy
Steps have been taken to promote commercial uptake of H-CUBE results by selected organisations:
Teravil Ltd
Thruvision Group PLC
Elettra ILO (Industry Liaison Office)
Interest has been confirmed.
Follow-up actions have been identified
Strategy
implementation

## Slide 22
Commercialisation via established system integrators – benefits for the whole value chain
System Integrator and Solution Provider
ADVANTAGES FOR SYSTEM INTEGRATOR:
Fast and cost- effective new product development
Differentiating performance
ADVANTAGES FOR CUSTOMER / END USER:
Track record of the solution provider = less risk
Reduced time to demo and product
ADVANTAGES FOR H-CUBE:
Leverage of existing expertise, assets and capabilities
Fastest and least risky route to commercial prototype
No dependency on equity investment
THz emitter
emitter
emitter
UI
Image Processing SW
Certifications
Customer support
Mechanics

## Slide 23
Commercialisation route 1
Teravil considers the integration of technologies developed by the H-Cube of value for future-generation, THz camera products designed for active detection (with THz illumination source) in applications such as inspection of food, pharmaceutical products and art, as well as research and development.
H-Cube technology delivers advantages over existing solutions in terms of:
  performance (sensitivity, THz range covered, frame rate) and reduced size
  scalability (of pixel array size) and manufacturability (using existing semiconductor foundries and optoelectronic/electronic component packaging companies)
  multiplexing read-out (high number of channels/pixels; high read-out parallelisation)
Anticipated advantages for THz camera customers and users:
  versatility (THz range), scanning speed, deployable in situ and in line;
  in the future, also high contrast and high specificity (RGB THz camera)
To kick-off the commercialisation and transfer of enabling technologies Teravil will be briefed by consortium members on :
  the design and fabrication of bolometric arrays – by FBK, UEF and Univ. of Pisa
  the design of drive and read-out electronics – by Elettra
Follow-up steps: optimisation with the assistance of H-Cube partners for the applications mentioned above and news ones such a skin disease diagnostics
Integrating H-Cube technology enables Teravil to deliver new and impactful capabilities to customers. This provides our company with a fresh competitive edge in the global market for commercial and R&D applications of THz cameras
– Andzej Urbanovic, CEO, Teravil UAB

## Slide 24
Commercialisation route 2
Thruvision uses passive detection techniques to provide fast, accurate, movable, crowd-scale, people imaging solutions for security monitoring at venues, shopping malls, airport and other transport nodes
H-CUBE technology can augment the capabilities of Thruvision current products by:
  Enabling lower cost and more robust system that do not comprise of mechanical moving parts and deliver fast scans
  Extending the spectral window of detection
  Enhancing image contrast and therefore threat detection through false-colour RGB detection
Benefits for Thuvision customers and users:
  Lighter, more robust and more portable equipment
  Reduced false positives/negatives
From demo to custom development:
  Following many in-person and virtual exchanges, a custom demonstration of HCUBE camera in action will be arranged for Thruvision in Q3-Q4 2025 (most likely in Trieste)
  Target camera’s specifications and a development roadmap will be agreed
  Arrangement will be made for follow-on development work - this could be structured as a consultancy service provide by a subset of H-CUBE partners in support of development work carried out by Thruvision or as development project sub-contracted by Thruvision directly to H-CUBE partners
We are very interested in the potential that H-CUBE’s THz camera technology could have to enhance security applications, particularly in passive detection mode. We have established a relationship with members of the H-Cube consortium to allow follow-up exchanges and further explore the applicability of the technology to Thruvision’s people screening products
– Nick Graham-Rack, CTO, Thruvision

## Slide 25
Commercialisation route 3
Elettra Industrial Liasion Office (ILO) sees the advanced digital and analogue electronics developed under H-CUBE as very valuable and appealing for its typical industrial and research customers.
In particular, the high-speed, multichannel, highly parallelised, lock-in based read-out system provides a highly versatile platform for application to THz cameras as well as to multichannel data acquisition, ultra-fast time-resolved spectroscopy, real-time signal demodulation in wireless communications, advanced medical imaging and high-speed financial trading algorithms
ILO’s typical commercialisation process includes the following steps
  Creation of a demo video, explanatory document and specifications sheet
  Outreach to industry and research institution; handling of inbound enquiries from potential customers
  Negotiation of contracts
  Oversight of product/service delivery, including brokering and negotiation with external OEMs and other service provider for outsourcing of manufacturing tasks
Examples of similar technology sold: FAST SPM (SPM add on for fast data acquisitions).
Customers: word wide research centres, industrial and scientific material sciences labs
The high-performance drive and multiplexing read-out electronics developed by H-CUBE fit well with Elettra ILO’s expertise and track record in selling advanced solutions for QC, process improvement, product development and R&D to commercial and research organisations worldwide. In all these applications the appeal, customisation potential and added value of the H-CUBE technology is compelling.
– Marco Peloi, Head of Elettra ILO