## Slide 1: High Pressure (HP) TPCs with Micromegas detectors
Zhiyong Zhang
12th symposium on LTPCs， December 15th-17th，2025
On behalf of USTC MPGD research group
University of Science and Technology of China

## Slide 2
contents
Why high pressure (HP)
01
Micromegas detectors for HP operation
02
03
The HP-TPCs of PandaX-III and MeGaT

## Slide 3
Why do we need high pressure?
Extend dynamic range for energy measurements of charged particles
  From keV to MeV: dark matter, neutrino energy spectrum etc.
  While maintaining the tracking capability compared with liquid one
Enrich target materials for rare event searches
  Dark matter, 0νββ Decay etc.
Improve the detection efficiency for X-ray/γ-rays
  For astrophysics, Medical/industrial imaging etc.
PandaX-III
HARPO
X-ray imaging （75KeV）

## Slide 4
Demands for high pressure TPC
Experiments and applications using high pressures
Physics/application scenarios | Experiment name | Technical features
Dark Matter (Low-Mass WIMPs) | TREX-DM | 10 bar，Micromegas(low background)
0νββ Decay (¹³⁶Xe) | NEXT、PandaX-III | 10 bar, SiPM、PMT、Micromegas(low background)
Gamma-ray astrophysics | SMILES、MeGaT、HARPO | 3-5 Bar, Micromegas/μPIC
Medical imaging/Industrial inspection | X-ray Imaging/Inspection | High pressure for efficiently imaging with high resolution and single photon counting capability

## Slide 5
contents
Why high pressure (HP)
01
Micromegas detectors for HP operation
02
03
The HP-TPCs of PandaX-III and MeGaT

## Slide 6
Micromegas detectors for HP operation
02
Optimization for HP operation
The thermal bonding Micromegas and its performance
01

## Slide 7
The thermal bonding method
It provides a concise and etching-free technology for fabricating Micromegas-like detectors.
Micromegas in a Bulk
User-friendly for laboratory operations
Convenient for constructing new structures
Low cost
Spacer diameter: Φ0.5mm to Φ1mm, with a pitch of ~10mm
  Suitable for large-area fabrication
  Spacer area: less than 1%
Thermal bonding processing
Jianxin Feng et al,. NIM-A 989 (2021) 164958.

## Slide 8
Germanium films
~ m2 coating area, 100 nm -1 μm film thickness
Sheet resistivity versus temperature and film thickness
Jianxin Feng, Zhiyong Zhang, Jianbei Liu et al., NIM-A 1031 (2022) 166595.
Ge films as the resistive anode
Crystal Ge
Amorphous
annealing treatment (high temperature)
Raman spectrum of Ge films
Crystalline Ge
Coated by vacuum evaporation on low temperature, rough substrate
Amorphous Ge
(Low resistivity)
(1000 times higher)
Notes: single crystal Ge

## Slide 9
Basic performance
X-ray test（5.9 keV）
  Gas gain：~105 (Ar+7%CO2)
  Energy resolution：~15% (FWHM)
  Non-uniformity: ~5% for 30×30 cm2
Electron beam（5 GeV）
  Efficiency：>98%
  Spatial resolution：65μm
~105
σX=65 μm
ε >98%
RMS/MEAN=~5%
~15% (FWHM)
Jianxin Feng, Zhiyong Zhang, Jianbei Liu et al., NIM-A 989 (2021) 164958.

## Slide 10
High gain, low IBF with DMM/TMM
DMM：Double Micro-Mesh gaseous structure
Zhiyong Zhang et al., NIM-A 889 (2018) 78–82
Binbin Qi et al., NIM-A 976 (2020) 164282
Kunyu Liang, et al., NIM-A,1070 (2025) 170033.
DMM: ~0.03% IBF for high rate TPC
TMM: ~0.003% IBF at gas gains exceeding 1 × 105 for visible light detection.
TMM：Triple Micro-Mesh gaseous structure
~0.2 mm
~0.1 mm
PA
SA
Drift region
~3-5 mm
~0.2 mm
~0.1 mm
PA
TA
Drift region
~1-3 mm
SA
~0.2 mm

## Slide 11
Detector production
60 × 60 cm2
Micromegas
40 × 40 cm2
Double Micromegas

## Slide 12
Micromegas detectors for HP operation
02
Optimization for HP operation
The thermal bonding Micromegas and its performance
01

## Slide 13
Optimization for HP operation
Optimizing spacers to avoid overflow glue
Spark occurs in local regions with abnormally strong electric fields or high charge densities.
Higher field
Higher field
Similar phenomenon observed in MRPC
(by Ingo Deppner for CBM-TOF)

## Slide 14
Polishing anode plane to get a smooth surface without burrs
Before coating Ge film anode …
Gas gain curves (left) ; The energy resolution (FWHM) versus the gas gain(right)
Sicheng Wen, et al., NIM-A 1062(2024) 169206.
MM03 was not polished
Optimization for HP operation

## Slide 15
A Leica digital confocal microscope device
Larger gain fluctuation needs better gap uniformity
Reconstructed 3D、2D imaging for the avalanche structure
Optimization for HP operation
Non-uniformity versus gains at different gas pressures (using 37Ar source).

## Slide 16
The voltages and leakage currents versus time in 10 bar Ar/Iso (97.5/2.5)
Over 40 days
<1 nA
Yunzhi Peng, Zhiyong Zhang, Sicheng Wen and Jianbei Liu, 2025 JINST 20 C09014.
During 8 days
Results for long-term operation before and after Optimization
Optimization for HP operation

## Slide 17
contents
Why high pressure (HP)
01
Micromegas detectors for HP operation
02
03
The HP-TPCs of PandaX-III and MeGaT

## Slide 18
HP-TPC of PandaX-III experiment
Requirements for detectors
  Low radioactive background
  Long-term stability at 10 bar Xenon (1%TMA)
  Energy resolution 3% @ 2.458 MeV
  20×20 cm2 MMs for charge readout (52)
Neutrino physics
  Lepton number non-conservation
  Neutrino nature: Dirac () or Majorana ()
  Absolute neutrino mass scale
  The type of neutrino mass hierarchy (normal, inverted)

## Slide 19
Low background Micromegas in high pressure gas
Stainless steel mesh
Thermal bonding film
Flexible PCB
  Ge anode
  Copper strip
Pure copper substrate
Development of high radiopurity Micromegas
12/2019
02/2020
04/2020
08/2020
11/2020
V1
V2
V3
V5
V4
V6
06/2021-now
Very low background rate: μBq/cm2
Sample |  |  |  |  | 
Thermal bonding | 3.55±1.64 | <0.01 | 11.98±1.68 | 24.96±9.22 | 0.37±0.31
Micro-bulk | <9.3 | <13.9 | 26.3±13.9 | 57.3±24.8 | <3.1
Sample |  |  |  |  | 
Thermal bonding | 3.55±1.64 | <0.01 | 11.98±1.68 | 24.96±9.22 | 0.37±0.31
Micro-bulk | <9.3 | <13.9 | 26.3±13.9 | 57.3±24.8 | <3.1
Sicheng Wen, et al., NIM-A 1062(2024) 169206

## Slide 20
Micromegas performance for high pressure
<20% (FWHM) energy resolution
>10000 gas gain
Test at 10bar Ar(2.5% Iso) with a 5.9 keV X-ray source
>150 hours
Sicheng Wen, et al., NIM-A 1062(2024) 169206
Test results in high pressure gas

## Slide 21
Construction and test of the HP-TPC
1-10 bar Ar+2.5%Iso gas
Using X-ray sources of 55Fe, 241Am, 137Cs
No-signal channels due to the bad connections

## Slide 22
Construction of 52 detector prototype
Readout plane with 52 Micromegas
Detectors installation completed
There are still many efforts need to be conducted before we can start
Scientific runs

## Slide 23
HP-TPC for MeV Gamma ray Telescope (MeGaT)
EGRET (1991-2000) 271 sources>100MeV
Fermi (2008-) 6000+ sources>100MeV
Comptel (1991-2000) 63 sources 1-30MeV
EGRET
Fermi-LAT
Comptel
T. Takahashi et al., Astroparticle Physics 43 (2013) 142–154
The great scientific potential for MeV gamma-ray gap.

## Slide 24
Compton camera with HP-TPC
It is practical to improve the e-tracking measurement by reducing the material density with gas detectors
The energy is too high to be collimated
It is difficult to measure 3D trajectories of electrons, which are produced in Compton scattering and pair conversion due to Coulomb multi-scattering.
ARM
PSD
Astroparticle Physics 97 (2018) 10-18

## Slide 25
Detector design and prospective sensitivity
Expected Performance:
√Wide Energy Range: 0.3 MeV – 100 MeV; √High Angular Resolution (PSF): 2° @ MeV, 0.5° @ 100 MeV; √ Gamma Polarization Measurement
TPC+CZT： 50×50× 50 cm3，3-5 bar
preliminary
MeV Gamma ray Telescope (R&D)

## Slide 26
Gas options
Good sensitivity needs good angle resolution and high effective area (efficiency)
multi-scattering effect:
σ=
 ∝z
Gas | z | Scattering angle (σ) |  | 
 |  | 0.5MeV | 1MeV | 2MeV
Ar | 18 | 24.2° | 13.4° | 7.4°
CF4 | 42 | 26.6° | 14.6° | 8.1°
Kr | 36 | 50.4° | 28.4° | 15.3°
Xe | 54 | 73.5° | 44.3° | 23.9°
When electrons pass through 1cm thick 5 bar gas
We need gas with low scattering effect and high equivalent z value

## Slide 27
Detector challenges
Operated in high pressure CF4 gas
CF4 is quite special: its electron attachment coefficient increases with the enhancement of the electric field, and this trend precedes the increase in the Townsend coefficient.
Strong electron attachment regions are formed when the relatively weak drift field transitions to the avalanche field.

## Slide 28
Optimization for CF4 gas operation
To enhance electron collection (simulation)
High density, thin meshes have better transparency by narrowing the attachment region!
Electron transparency
Mesh densities (Lines Per Inch)
Opening rate is optimized to ~40%
Counts
ADC channel
A typical energy spectrum tested with 55Fe in 1 bar:
~30% FWHM
1 bar
3 bar
5 bar
19 μm
14 μm
11 μm

## Slide 29
Progress on the MeGaT TPC construction
Construction and test of TPC from 1bar to 5bar
A vessel chamber with very thin stainless steel window (0.4mm) has been built for HP of >5 bar operation
A 30×30×30 cm3 prototype has been developed, and is now under testing

## Slide 30
Summary
HP-TPC has excellent potential in physics experiments and industrial fields
  Dark matter, 0νDBD, neutrino physics and X-ray imaging, etc.
As the operating pressure increases, almost all aspects of the detector's performance become worse
  Optimization on the spacers, mesh type, electrodes, and other components are conducted
  We developed thermal bonding Micromegas for HP operation, indicating high potential in many experiments

## Slide 31
Thank you for your attention!