## Slide 1: Requirements and comparison of readout architectures
Jüri Jõul on behalf of the BGI team
10.04.2025

## Slide 2: Introduction
Overview of the system, data rates and requirements

## Slide 3: Overview of the BIPXL readout system today

## Slide 4: Simplified diagram
Raw data readout
Raw data
Profiles
Users
Slow control
Slow control
Event processing
Publishing

## Slide 5: Requirements
Along with expected data rates

## Slide 6: Definitions/explanations
“Event” = Timepix or timing data packet with additional metadata from the FPGA
  1 event == 128 bits (b) == 16 bytes (B)
“Processing” = constructing beam profiles from raw data.
  Does not include additional post-processing such as ML-based beam loss removal
  Does not directly apply to the telescope (another Timepix-based system)

## Slide 7: Requirements and data rates
BGI
Publish beam profiles every basic period
3–15 Mevents/s
  At least ~1 Mevent/s signal
  At least ~2 Mevent/s beam loss
  Corresponds to at least ~45 MB/s ~= 360 Mbit/s
Almost real-time
Telescope
Perform track reconstruction during measurement
~36 Mevents/s
  All signal
  Corresponds to 550 MB/s ~= 4,400 Mbit/s
Order of 5 seconds of delay between measurements

## Slide 8: Event and data rates explained (BGI)
Assumptions and facts:
  A cycle is at least one basic period (1.2 s) long
  1000 events needed to form a usable profile
  Maximum 1000 profiles per cycle. Therefore, for the worst-case scenario, we should consider the shortest cycle of only one basic period with the maximum number of profiles.
  Beam loss occurs at roughly 5% of the profiles
  Maximum beam loss event rate 43000 events/ms
  An acquisition can cover up to 100% of the cycle's duration. This is not strictly true, considering that we limit the acquisitions not to start before the injection, but for a worst-case scenario, it is good enough.
  This, in turn, means that the duration of each profile is at most 1.2 s / 1000 = 1.2 ms
  The amount of events per profile during beam loss can be up to 43000 events/ms * 1.2 ms = 51600 events
Resulting event and data rates:
    95% or 950 profiles have 1000 events per profile: total of 950,000 events per basic period.
    5% or 50 profiles have 51600 events per profile: total of 2,580,000 events per basic period.
    In total, this amounts to 3,530,000 events per basic period (slightly under 3 Mevents/s).
    Considering that unpacked, each event is composed of 16 bytes (128 bits), we can expect a data rate of up to 56,480,000 B/Basic Period or 47,066,667 B/s ~= 54 MB/BP or 45 MB/s ~= 431 Mb/BP or 360 Mb/s.

## Slide 9: Event and data rates explained (telescope)
Assumptions and facts:
  The beam rate is up to 10 million particles/spill
  One spill is of the order of 5 seconds
  This results in a particle rate of ~2 million/s during the spill
  Each particle optimally triggers a cluster with 3 hits on a single detector
  The telescope has six planes, that is six detectors
Resulting event and data rates:
  Total event rate is therefore ~36 Mevent/s
  Considering again the event size of 128 bits or 16 bytes, the corresponding data rate is ~550 MB/s ~= 4400 Mb/s

## Slide 10: Candidate architectures
Quick overview followed by an in-depth comparison

## Slide 11: Quick overview of architectures
ATS SoC (standalone)
Hosted SoC (FEC + PCIe SoC)
Regular FEC
+ hosted SoC
ATS SoC as FEC
FESA (SC + online DP)
PS
FPGA
PS
PL
PCIe
Dedicated 10 GbE link
Storage + offline DP
Abbreviations:
SC – Slow Control
DP – Data Processing
FESA (SC + online DP)
Readout frontend
(link to detectors)
8 fibres (GBTX)
Optional CCR server for raw data storage and offline processing
(alternative to TN)
FPGA
PL
Readout frontend
(link to detectors)
Storage + offline DP

## Slide 12: Processing capabilities
Device | CPU | CPU-Mark (MT) | CPU-Mark (ST) | Mevents/s (ST)
HP-FEC | AMD EPYC 9124 | 43,681 | 2,690 | ???
CAD Machine | Intel Xeon W-2225 @ 4.10GHz | 10,486 | 2,642 | 11.4–18.3
FEC (Siemens) | Intel Core i5-8500 @ 3.00GHz | 9,537 | 2,444 | 9.8–16.3
FEC (Kontron) | Intel Core i5-3550S @ 3.00GHz | 4,434 | 1,941 | 8.0–13.2
ATS SoC | ARM Cortex-A53 4 Core 1199 MHz | 407 | 181 | 1.3–2.5

## Slide 13: Raw data offloading (recommended by review)
ATS SoC (standalone)
IPbus
    Limited to ~600 Mbit/s == ~75 MB/s == <5 Mevent/s
Alternative: 10 GbE port exposed to PS
    Theoretically possible, feasibility unknown
Hosted SoC (FEC + PCIe SoC)
10 GbE NIC
    Throughput likely limited by disks when using NFS
      <550 MB/s* == <36 Mevents/s
    Straightforward implementation
*Based on experiences with the Head-tail monitor (Tom Levens)

## Slide 14: Maintainability and scalability
ATS SoC (standalone)
Maintainability:
Forced gateware updates ~1/year?
    Likely involves new tooling
    Likely involves regeneration and revalidation
Processing scalability:
Online: none
Offline: external processing (CCR server)
Hosted SoC (FEC + PCIe SoC)
Maintainability:
FEC: standard FEC
PCIe card: see Mark’s talk
Processing scalability:
Online: upgrade to high-performance FEC (HP-FEC)
Offline: external processing (CCR server)

## Slide 15: Comparison table
 | ATS SoC (standalone) | Hosted SoC (FEC + PCIe SoC)
Processing capability | 2.5 Mevents/s | 16 Mevents/s
Raw data availability | Currently up to 5 Mevents/s | Order of 36+ Mevents/s (limited by disks!)
Maintainability | Standard platform Forced gateware updates | FEC: standard PCIe card: see Mark’s talk
Scalability | Online: none Offline: CCR server | Online: HP-FEC Offline: CCR server

## Slide 16: Our preferred architecture
Hosted SoC/FPGA (FEC + PCIe SoC)
Main advantages:
  High performance
    Meets and potentially exceeds BGI performance requirements
    Could offer almost real-time processing for the telescope
    Could support almost real-time beam loss removal (HP-FEC with GPU)
  Scalability: future-proof architecture for LHC BGI and other Timepix4 applications
  Standard solution in particle physics community (e.g. ATLAS)
  Proven environment (FEC)
  Straightforward raw data offloading
  No forced gateware updates
Main disadvantages:
  As of today, no ATS “standard” PCIe carrier board with a suitable FPGA  see Mark’s talk
  Slightly more work on the gateware required

## Slide 18: Backup slides

## Slide 19: Software layout of the readout system
Original diagram by Steen Jensen

## Slide 20: Readout versions
HTTP
PyJapc
IPbus
Application
Legacy library
Library
Utility process
V2–V3
V4
V5