## Slide 1: Target Complex Rough Floor Loading Map
Gemma Humphreys
26/03/2025

## Slide 2
Vacuum Vessel: 190 tonnes
13.14m2
15 tonnes/m2
MHS:
367 tonnes
13.95m2
26 tonnes/m2
Cast Iron Shielding:
561 tonnes, 12.947m2, 43 tonnes/m2
Cast Iron Shielding:
678 tonnes, 16.787m2, 40 tonnes/m2
Concrete Shielding: 190 tonnes, 17.92m2, 11 tonnes/m2
Concrete Shielding:
105 tonnes
5.92m2
18 tonnes/m2
Collimator (including concrete on top):
104 tonnes
3.84m2
27 tonnes/m2
Concrete Shielding:
42 tonnes
3.4m2
12 tonnes/m2
40 tonnes
3.84m2
11 tonnes/m2
40 tonnes
3.84m2
11 tonnes/m2
Concrete Shielding:
42 tonnes
3.4m2
12 tonnes/m2
Concrete Shielding: 51 tonnes, 4.8m2, 11 tonnes/m2
Calculations performed with assumed densities:
Steel – 7.9kg/m3
Cast iron – 7.8 kg/m3
Concrete – 2.2 kg/m3
Complex Floor Load

## Slide 3
7.7m
12m
2121 tonnes total
92.4 m2
22.95 tonnes/m2
Complex Total Floor Load