## Slide 1: CFRP Laminates with Embedded Channels: Project Overview
D. Alvarez
CERN, 4th March 2025

## Slide 2: Introduction
Potential Research Areas:
  Effects of vaporisation treatment and operation environment on laminate properties
    Compatibility of composite laminate with cooling fluid
    Optimisation of vaporisation process/parameters
    Radiation effects (not a top priority at present)
    Cycling Loads
  Technology Optimisation
    Development of alternative channel reinforcements
      Increase design flexibility (e.g. compatibility with complex multi-channel PLA preforms)
      Improved thermo-mechanical performance (better thermal performance, increased pressure resistance)
    Process optimisation (improved performance, quality, repeatability, other resin systems)
    Development of solutions for improved fluid compatibility (e.g. channel coatings)
    Fluid Interconnections
  Modelling the thermo-mechanical response of composite laminates with embedded channels
    Modelling failure of structures with un-reinforced channels
    Modelling failure of laminates with reinforced channels
      Channels reinforced with carbon over-braids
      Other reinforcements (e.g. BMC-based reinforcements to fill resin-rich areas)
    Modelling thermal performance
04/03/2025
d.alvarez.feito@cern.ch
BMC-based reinforcements around channel to replace resin-rich areas?

## Slide 3: Technical Activities
Technical activities will be organised in three different blocks:
04/03/2025
d.alvarez.feito@cern.ch
A. Material Characterisation | B. Desing, Manufacturing and Testing of Representative Structures | C. Modelling
Manufacturing and testing of standardized coupons Assess effects of vaporisation treatment and operation environment (e.g. exposure to coolant) on laminate properties Determine input properties for analytical and/or numerical models | Conception, production and testing of laminates with embedded channels Proof-of-concept for new or improved technological solutions (e.g. alternative reinforcements) Evaluate (thermal, mechanical, long-term) performance of new technology solutions Obtain experimental data for independent test geometries to validate predictive models Technology demonstration | Development and validation of analytical and/or numerical models to predict the behaviour of laminates with embedded channels Predict pressure resistance Predict long-term effects of exposure to cooling fluid Predict thermal performance

## Slide 4: Proposed Activities
04/03/2025
d.alvarez.feito@cern.ch
A. Material Characterisation | B. Desing, Manufacturing and Testing of Representative Structures | C. Modelling
Measure physical, mechanical and thermal properties for epoxy and cyanate-ester laminates in three states: After autoclave curing cycle After vaporization treatment After exposure to CO2 (for different durations and fluid conditions such as temperature and mass flow rate) Bulk-resin and bonded DCBs produced with the resin should be included in this study | Unreinforced Laminates: Produce and test DCB-like specimens with embedded channels Produce and pressure-test laminates with embedded channels using new epoxy and cyanate-ester resin system Reinforced Laminates: Braided Reinforcements: Produce (or procure) braided pipes for pressure tests and/or CO2 exposure Produce and pressure-test laminates with embedded channels using new epoxy and cyanate-ester prepreg Develop alternative BMC-based reinforcement around the channels to improve thermal performance and pressure resistance. Design tooling and produce reinforced laminates with channel to test pressure resistance and thermal performance. Technology demonstrator (e.g. stave equipped with dummy heaters for tests with CO2) | Unreinforced Laminates: Modelling of delamination and debonding DCBs (familiarization with CZM model) Modelling failure of DCB-like specimens with embedded channels Modelling failure in laminates with un-reinforced channels subject to internal pressure Reinforced Laminates: Braided Reinforcements: Develop “homogenised” model for braided pipes and use it to predict burst pressure (validation using pressure test data obtained with pipes) Modelling pressure failure of laminates with channels reinforced with over-braids. Develop numerical model to predict pressure failure of laminates with alternative BMC-based reinforcement around the channels. Develop thermal model to predict thermal performance of technology demonstrator

## Slide 5: BMC-based Reinforcement
Integrate of Carbon/Epoxy BMC in the laminate to fill the “resin-rich” areas surrounding the cooling channel
  Improve mechanical performance (pressure resistance) wrt un-reinforced channels
  Improve thermal conductivity (KBMC>Kresin)
  Maintain some level of design flexibility for complex channel network geometries (more versatility than braided preforms)
28/03/2025
d.alvarez.feito@cern.ch
Resin-rich Area
Channel
Carbon/Epoxy BMC

## Slide 6: BMC-based Reinforcement
Step 1: Pre-compact BMC reinforcement around PLA preform using dedicated mould (vacuum / pressure) to shape the BMC
Step 2: Integrate BMC+PLA in the lamination process of the final CFRP structure
Step 3: Cure the CFRP structure and Vaporise PLA
28/03/2025
d.alvarez.feito@cern.ch
PLA
BMC+PLA Pre-compaction Mould
PLA
Mould for CFRP Structure
(Rigid Part + Silicone Counter-mould)

## Slide 7: BMC-based Reinforcement
How to start:
  Thermal conductivity measurements of Carbon/Epoxy BMC (use samples extracted from ATLAS gussets) for thermal FEA model
  Design and 3D print “BMC+PLA Pre-compaction Mould”
  Manufacture structure with single channel for pressure tests using existing single-channel moulds built by Matheo
  Perform CT scans, microscopy and pressure tests with prototypes (potentially also non-reinforced channels with M55J/ER450)
28/03/2025
d.alvarez.feito@cern.ch