## Slide 1: S5-like DEMO Cell Coil Search Scheme Update Optimization Tool New Configurations
Giuseppe Scarantino
11/04/2025

## Slide 2: Lattice / Single Cell Operation
LATTICE OPERATION
(nominal, beam operation)
SINGLE CELL
ONE CELL
FORCE
FORCE
RF cavity
Solenoid
absober
Dipole
Periodic cell array: magnets with alternated polarity.
Test of each cell at full field is mandatory.
A magnet design fulfilling both operative conditions looks challenging!
In this presentation: results for lattice conditions.

## Slide 3: Updated Cell Layout: “inter-cell cryostat”
Cooling Cell
Target field on axis for a 1 m cell
Axial forces on coils
(lattice operation)
Target field harmonics
z

## Slide 4: Magnet configuration nomenclature
Numbering of magnet configurations studied for cell integration
“B5-DEMO MAG X.Y”
Cell layout numbering:
0.8 m cell (layout #1)
1 m cell (layout #2)
Magnet configuration #3

## Slide 5: B5-DEMO MAG 2.3 configuration
40 mm
Metal-Insulated Coil
SS spacer
Coil 2
Conductor section:
2 X HTS tape (12mm x 0.0656mm)
1 X SS tape (12mm x 0.026mm)
z
R
R = 285 mm
R = 185 mm
Coil 1
Coil 2
268 mm
70 mm
60 mm
72 mm
45 mm
77 mm
z = 0mm at cell boundary
Spacers:
Coil 1: 4 mm SS spacers
Coil 2: 3 mm SS spacers
Engineering current density:
Coil 1: 328.43 A/mm^2,
N. turns = 445
Coil 2: 300.00 A/mm^2,
N. turns = 382
Baseline magnet configuration currently considered for integration.
SS tape:
HTS
HTS
Conductor Section
N. pancakes: 17
N. pancakes: 5

## Slide 6: B5-DEMO MAG 2.3: EM analysis results
angular dependence considered
z
R
 | Coil 1 | Coil 2
Total Radial Resistance [mΩ] | 30.6 | 12.0
Coil Inductance (lattice op.) [H] | 29.2 | 3.39
Characteristic Time [s] | 954 | 282.6
Power dissipated @ charging [W] (ramp rate: 0.1 A/s) | 278 | 9.58
Margins exceedingly high: non-optimal conductor usage with the selected winding layout (2x 12mm HTS tape + SS tape) considering the coil protection limit (maximum stored magnetic energy density < 150 MJ/m^3).
Mag. Energy Density (lattice)
140.4 MJ/m3
Total Mag. Energy - full cell
12.2 MJ

## Slide 7: B5-DEMO MAG 2.3: Mechanical analysis results
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Free radial expansion
Radial precompression
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation
Radial pressure applied on the external coil boundary:
10 MPa on Coil1
60MPa on Coil2
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers

## Slide 8: B5-DEMO MAG 2.3: Local Stress Components
Evaluate the local stress components on the most loaded coils.
Coil#1.17
Coil#2.1
Coil#1.17
Coil#2.1
Free radial expansion
Pre-compression

## Slide 9: B5-DEMO MAG 2.3 : Magnets Main Parameters
B5-DEMO MAG 2.3 | 
J_eng Coil1/Coil2 (A/mm^2) | 328.6 / 299.8
B2/B1 (%) | 14.9
Focusing strength per cell length (T^2*m/m) | 24.0
Axial Force on Coil1/Coil2 (MN) | +4.12 / +8.25
Net Axial Force (MN) | +12.4
Net Torque applied on centroid of forces (MN*m) | -0.558
Peak Hoop Stress on Coil1/Coil2 (MPa) | +231 / +374
Peak Positive Radial Stress on Coil1/Coil2 (MPa) | +1.77 / +9.48
Peak Von Mises Stress on SS spacers (MPa) | +353 / +508
Magnetic Energy Density Coil1/Coil2 (MJ/m^3) | 148.7 / 92.92
Total HTS length (full cell) (km) | 71.2
Coil Current Coil1/2 (A) | 620.0 / 565.4
Note: peak stress values referred to radially unconstrained coils.

## Slide 10: B5-DEMO MAG 2.3: Coil Support Structure
Von Mises Stress
Total Deformation
Mechanical analysis of the coil support structure in lattice operation

## Slide 11: First Stage Evaluation: EM Analysis Results at full current
R
z
6D lattice
Begin of Cell
Peak Field >> Target

## Slide 12: First stage evaluation: reduced current on external coils
Parametric sweep of the currents in Coil#1, Coil#2 facing the “beginning of cell” side.
0.1 x I_coil steps: 0.5 – 1.0 range
Parametric sweep of the currents in Coil#1, Coil#2 facing the “beginning of cell” side.
0.05 x I_coil steps: 0.7 – 0.9 range
~ Target Peak Field

## Slide 13: Coil Search Scheme Update: Optimization Tool
Coil configuration search via optimization methods (gradient-based / genetic algorithms).
Conflict between different optimization targets  objective weighting.
Re-evaluate the 150 MJ/m^3 limit for magnet protection: consider thermal stability during charging/discharge transients.
As a first approximation, we are considering the enthalpy increase to reach the limit temperature of 200 K.
Cost Function parameters
In case of quench, assuming the energy of the magnet is dissipated uniformly in the entire volume, we get:
However, this hypothesis may lead to non-conservative results for NI-coils.
Ongoing discussion on better criteria to use

## Slide 14: Optimization Tool: Cost Function Definition
Optimization with patternsearch(), Matlab built-in function. Cost function is:
Higher weight has been given to the field harmonic constraints and peak field on axis. For the iterations with the 150MJ/m3 limit, to find solutions within this energy density value a higher cost has been used for .
High cost on the polynomial definition of geometrical constraints, to be sure that no solutions outside the space available are considered.
Cost of tape consumption
Field harmonics constraints
Geometrical Constraints
B peak on axis constraint
Cost on margins
Cost on mag. energy density
Cost on Axial Forces

## Slide 15: Coil Search Scheme: Results Comparison (I)

## Slide 16: Coil Search Scheme: Results Comparison (II)

## Slide 17: Coil Search Scheme: Results Comparison (III)

## Slide 18: Coil Search Scheme: Results Comparison (IV)
Results in equivalent 12 mm tape length

## Slide 19: Summary Table: Margins
 | Current Margin (%) | Temperature Margin (K) | Load-line Margin (%)
12 mm tape 150 MJ/m3 Limit | 40.4 | 13.2 | 19.6
12 mm tape 200K Limit | 38.7 | 12.8 | 20.4
8 mm tape 200K Limit | 37.1 | 12.4 | 19.0
6 mm tape 150 MJ/m3 Limit | 34.6 | 11.5 | 18.3
6 mm tape 200K Limit | 31.1 | 10.0 | 14.8
12MN-40mm gap Option | 68.6 | 27.2 | 48.6
Target minimum temperature margin > 10K
SS tape:
HTS
HTS
Conductor Section
B5-DEMO MAG 2.4

## Slide 20: Configuration Comparison: Summary Table
 | Coil Current Coil1/Coil2 (A) | SS spacer width Coil1/Coil2 (mm) | Axial Force on Coil1/Coil2 (MN) | Net Axial Force (MN) | Net Torque applied on centroid of forces (MN*m) | Peak Hoop Stress on Coil1/Coil2 (MPa) | Peak Positive Radial Stress Coil1/Coil2 (MPa) | Peak Von Mises Stress on SS spacers (MPa) | Magnetic Energy Density Coil1/Coil2 (MJ/m^3) | Total HTS tape length (full cell) (km)
12 mm tape 150 MJ/m3 Limit | 761.2 1193 | 7.9 13.7 | -4.61 11.7 | 7.09 | -0.319 | 207 435 | 3.50 9.51 | 560 | 151.7 147.0 | 50.9
12 mm tape 200K Limit | 1132 957.8 | 4.7 2.0 | -0.010 7.13 | 7.12 | -0.202 | 391 573 | 9.96 12.2 | 749 | 303.1 179.3 | 35.7
8 mm tape 200K Limit | 582.8 828.3 | 12.5 13.1 | 0.069 10.1 | 10.2 | -0.768 | 170 380 | 2.26 8.37 | 525 | 119.4 113.8 | 54.7
6 mm tape 150 MJ/m3 Limit | 566.5 669.6 | 11.3 14.8 | 2.66 8.72 | 11.4 | -0.347 | 208 332 | 3.65 7.37 | 454 | 150.5 92.99 | 43.4
6 mm tape 200K Limit | 575.7 707.6 | 11.7 15.7 | 2.61 8.73 | 11.3 | -0.371 | 205 321 | 3.56 6.96 | 453 | 148.4 93.47 | 42.2
12MN-40mm gap Option | 620.0 565.4 | 4.00 3.00 | +4.12 +8.25 | +12.4 | -0.558 | +231 +374 | +1.77 +9.48 | +353 +508 | 148.7 92.92 | 71.2
B5-DEMO MAG 2.4

## Slide 21: New B5-DEMO MAG 2.4 configuration
Conductor section:
2 X HTS tape (12mm x 0.0656mm)
1 X SS tape (12mm x 0.026mm)
z
R
R = 285 mm
R = 185 mm
Coil 1
Coil 2
211 mm
76.19 mm
71.67 mm
63.4 mm
56.422 mm
146.25 mm
z = 0mm at cell boundary
Spacers:
Coil 1: 7.9 mm SS spacers
Coil 2: 13.7 mm SS spacers
Engineering current density:
Coil 1: 403.51 A/mm^2,
N. turns = 485
Coil 2: 632.31 A/mm^2,
N. turns = 456
SS tape:
HTS
HTS
Conductor Section
12 mm
13.7 mm
12 mm
7.9 mm
N. pancakes: 11
N. pancakes: 3

## Slide 22: B5-DEMO MAG 2.4: EM analysis results
 | Current Margin (%) | Temperature Margin (K) | Load-line Margin (%)
12 mm tape 150 MJ/m3 Limit | 40.4 | 13.2 | 19.6

## Slide 23: B5-DEMO MAG 2.4: Mechanical analysis results
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Free radial expansion

## Slide 24: Lorentz force distribution on the coil pancakes
R
z
Coil 1.1
Coil 1.11
Coil 2.1
Coil 2.3
-6.28 MN
5.55 MN
7.16 MN

## Slide 25: Note: Coil + Spacers model - contact stabilization & friction
Radial Displacement Magnitude
Shear Stress, Coil 2
Pressure applied on Coil Boundary
Shear Stress on Coil Boundary
Bonded contact hypothesis non verified !!
Radial displacement values differs from the stabilized models and rigid SS spacers approximation.
Zoom on radial displacement magnitude
+ deformation
Model inter-turn contact to evaluate the single turn mechanical behavior

## Slide 26: B5-DEMO MAG 2.4 : Magnets Main Parameters
B5-DEMO MAG 2.4 | 
J_eng Coil1/Coil2 (A/mm^2) | 403.5 / 632.3
B2/B1 (%) | 14.3
Focusing strength per cell length (T^2*m/m) | 25.9
Axial Force on Coil1/Coil2 (MN) | -4.61 / +11.7
Net Axial Force (MN) | +7.09
Net Torque applied on centroid of forces (MN*m) | -0.319
Peak Hoop Stress on Coil1/Coil2 (MPa) | +207 / +435
Peak Positive Radial Stress on Coil1/Coil2 (MPa) | +3.50 / +9.51
Peak Von Mises Stress on SS spacers (MPa) | +273 / +560
Magnetic Energy Density Coil1/Coil2 (MJ/m^3) | 151.7 / 147.0
Total HTS length (full cell) (km) | 50.9
Coil Current Coil1/2 (A) | 761.2 / 1193
Note: peak stress values referred to radially unconstrained coils.

## Slide 27: B5-DEMO MAG 2.4: Coil Support Structure
Peak Von Mises Stress: 648 MPa
Von Mises Stress
Displacement Magnitude
NOTE: Strong axial forces with opposed directions!!!
11.7 MN
4.61 MN

## Slide 28: Rough estimate of dipole dimensions
saddle coil option
same polarity on both dipoles: consider a single dipole magnet across the absorber wedge.
Dipole dimensions:
Inner radius: 140 mm
Radial thickness: 15 mm
Axial length: 236 mm (maximum length available for the inter-cell layout).
Number of turns: 30
Current: 629.6 A
Data to be checked with more detailed analyses.
Dipole z center position at the center of the absorber wedge.

## Slide 29: Backup

## Slide 30: Gradient-based Optimization

## Slide 31: Coil Search Scheme: Results Comparison (IV)
Results NOT normalized in terms of equivalent 12 mm tape