## Slide 1: Beam Instrumentation for FCC injector
T. Lefevre

## Slide 2
FCC-ee Injector TDR by 2028

## Slide 3
FCC-ee Injector sub-systems
Electron source
Electron linac
Electron TL to DR
Positron souce
Positron linac
Positron TL to DR
Damping Ring
TLs to HE Linac
Merging and bunch compressor
HE linac

## Slide 4
FCC-ee Injector sub-systems
One BPM per quad / triplet in linac
Diagnostic station at entrance / exit of each sub-systems
Charge
Energy&Energy spread
Emittance and bunch length

## Slide 5
FCC-ee Injector sub-systems
Target & cryostat
Positron linac 2 GHz, 13.3 (12.8) MV/m
100 Hz, 20+52 RF structures
Positron/Electron
Separation at 170 MeV
Energy collimator
and compressor
2.86 GeV electron beam
from e- linac
Injection section
E = 2.86 GeV
Q = 13 nC (considering 60% losses for transport, collimation and injection into DR)
E = 2.86 GeV
Q = ~3.8 nC
DC solenoid
DC solenoid
Electron/Photon dumps
Capture linac 2 GHz, 13.3 MV/m
100 Hz, 6 RF structures
Damping Ring
E = 2.86 GeV
Qb = 5 nC
Positron complex by IJCLab

## Slide 6
FCC-ee Injector sub-systems
Damping ring by INFN

## Slide 7
FCC-ee Injector sub-systems – towards first functional specifications

## Slide 8: Next steps
List all BI needs in FCC injector complex
Establish preliminary functional specifications for all sub-parts of the complex
    Contact person for each part of the machine
Identify possible synergies with the rest of the instrumentation in FCCee complex
Identify the resource needs for the Technical Design phase

## Slide 9: Thank you for your attention.
9